## Slide 1: Developments of optical systems for X/gamma ray Compton machines at LAL

## Slide 2: Outline
Compton Scattering
Standard Resonant Cavity (High average power, high rep. rate)
Resonant Burst Cavity (High peak power, medium rep rate)
Laser Beam Circulator (High peak power, low rep rate)
Notes: I will present you the progress of Mighty Laser experiment
Limitations that we are confronted to
Then; next; later; afterward(s); subsequently
To begin

## Slide 3: Applications
http://en.wikipedia.org/wiki/X-ray
http://en.wikipedia.org/wiki/Radiation_therapy
http://www.tunl.duke.edu/documents/public/higs2_prospectus_31aug2012.pdf
X-ray Imaging
Radiotherapy
Nuclear Physics

## Slide 4: Compton Scattering
Cross-section ≈ physics
luminosity ≈ geometry
δ (mrad)
Eγ (keV)
γ = 98 (Ee = 50 MeV)

## Slide 5: Compton Scattering properties
Angular acceptance
Nonlinear
effects
Laser beam
parameters
Electron beam
parameters
M. Gambiccini, P. Cardarelli et al. technical design meeting collimation and characterisation system review
V. Petrillo et al., NIM A 693 (2012) 109–116

## Slide 6: Trade-off
Accelerator:
  ↑ bunches, electrons, rep. Rate
   ↓ beam quality (emittance, energy spread)
Laser:
  ↑ rep. rate
   ↓ peak power, ↑ average power
 Trade-off X-ray flux  X-ray bandwidth

## Slide 7: Standard Resonant Cavity
(High average power, high rep. rate)

## Slide 8: Optical Cavity
Electron beam
…
time
frep
Gain = =
High power enhancement factor reachable in permanent regime
 G~10 000 for the ThomX project
Efficient with Storage ring
But laser frequency control at for ‘high finesse’
Implementation of metrological techniques in accelerator environment

## Slide 9: Stored Power
State of the art
Cavity average power = 670kW@10ps ; 400kW@250fs
Laser + amplifier : 420W @ 250 MHz
Cavity enhancement factor ~ 2000
LAL record
4-mirror high finesse cavity tested at KEK on ATF (1.3 GeV ring) French-Japanese collaboration
100kW stored power (before the earthquake)
Mirror surfaces degradation  runs with 45kW at most
Carstens et al. Opt Lett 39 (2014) 2595
‘Huge’ average power can be stored inside the optical cavity
mirror thermoelastic deformations & damage
To further increase circulating power
Reduce fluence on the mirrors

## Slide 10: ThomX project
3 GHz gun and linac delivering 1 bunch of 1 nC at (50 or 70 MeV) every 20 ms (50 Hz)
The bunch is stored in a compact ring (Rev. Freq. ~17 MHz)
An Optical Resonant Cavity to store the laser pulse (max ~1 MW)
Up to 1013 photons/s (max energy 90 KeV)

## Slide 11: ThomX cavity
Laser oscillator rep. rate & CEP locking
Parameters | Typical values
Laser repetition frequency | 33.3 MHz
Laser wavelength | 1031 nm
Cavity optical length | 8.994 m
Cavity finesse | 30 000
Cavity waist size | 70 µm
Injected power | 150 W
Circulating power | ~600 kW

## Slide 12: Painting / archeology analyses
J. Dik et al., Analytical Chemistry, 2008, 80, 6436
http://www.vangogh.ua.ac.be/
(Pbwhite, Hg vermillion…) of a Van-Gogh’s painting
‘K edge imaging’
Heavy chimical elements are contained in painting pigments Characterised by K absorption edges
X-ray attenuation

## Slide 13: Phase contrast
1st Phase contrast image at Lyncean CLS
standard absorption
phase-contrast
[ Synch. Rad. 16, 2009, 43-47 ]
Proof of principle (long acquisition time, high dose, not soft tissues …)

## Slide 14: medical application as at ESRF (ID17)
Search for glioblastoms therapy
  Locate platinum (cisplatine) inside tumor cells (rat brains)
  Shoot with 78keV X-ray (platinum K-shell)
  Observed ~700% increase of life time
  Observed 34% survivals after 1 year … (Biston et al. Cancer reas.64(2004)2317)
X-ray imagery/therapy can also use contrast agent: e.g. iodine (ongoing human trial at ESRF)
Adam et al Int.J.Rad.Onc.Biol. Phys.57(2003)1413
But
relative to water absorption
50 keV

## Slide 15: Resonant Burst Cavity
(High peak power, medium rep. rate)

## Slide 16: Optical Cavity
Electron beam
…
…
…
~100 Hz
~1000 pulses
time
e- bunch duration
Power
Time
Cavity filling
Cavity decaying
t = 0
t2
t1
Laser Burst duration
A simple continuous model
Efficient with linac (low frep)
But cavity maintain at resonance
Implementation of advanced techniques for locking

## Slide 17: Stored Power
Fine tuning of e_burst structure may lead to effective laser burst enhancement factor ~500

## Slide 18: Experiments at LUCX

## Slide 19: LUCX recent results
K. Sakaue, Development of a burst mode enhancement cavity for linac-based Laser-Compton source (LUCX), LAL meeting, 2016/03/24-25
K. Sakaue et al. NIMA637(2011)S107
M. Fukuda et al., IMPROVEMENT OF X-RAY GENERATION BY USING LASER COMPTON SCATTERING IN LASER UNDULATOR COMPACT X-RAY SOURCE(LUCX), to be published

## Slide 20: Laser Beam Circulator
(High peak power, low rep rate)

## Slide 21: Resonant to non resonant cavities

## Slide 22: Optical system
Principle from:
“Dragon-Shape”
2D
3D
Circulator principle:
2 high-grade quality parabolic mirrors No spherical aberration
1 Mirror-Pair System (MPS) per pass  Optical plan switching
 Constant Crossing angle + Unique Interaction Point

## Slide 23: ELI-NP
Parameters | Value
Nb of passes | 32
Crossing angle | 8°
Corona radius | 166.2 mm
Waist size | 28.3 μm
Laser Energy / pulse | 400 mJ
Pulse duration | 3.5 ps
Frep | 100 Hz
Equivalent Power | 1.28 KW
Ee ≈ 600 MeV
Laser 200 mJ
Laser 400 mJ
Ee ≈ 280 MeV

## Slide 24: gamma-ray Applications
AIP Conference Proceedings 1462, 177 (2012)
~8 MeV
~30 MeV
Gamma-beam specifications:
  Energies γ (Eγ) : 0,2 – 19,5 MeV
  Bandwidth (ΔE/E) : <0.5%
  Spectral density (TASD) : >5000 γ/(s.eV)
  Linear polarization: >95% + switching

## Slide 25: Nuclear Resonance Fluorescence
NIM A 507 (2003) 527–536
Parity measurement
Material detection
Require small bandwidth
= Quasi-monochromaticity
 Require polarized γ-ray
γ-ray linearly
polarized

## Slide 26: Conclusion
Standard Resonant Cavity (High average power, high rep. rate)
Resonant Burst Cavity (High peak power, medium rep rate)
Laser Beam Circulator (High peak power, low rep rate)
X-Ray Flux
X-Ray Bandwidth
Storage ring
Linac
Accelerator Type
X-Ray parameters
Optical system
Nb of e- bunches
∞
~100’s - ∞
~10’s - ∞

## Slide 27: Thank you for your attention