## Slide 1: Accelerators for pedestrians a tutorial
Uli Raich
CERN BE - BI
(Beam Instrumentation)

## Slide 2: No stupid questions
A proverb:
There is no such thing as a stupid question.
There are only stupid answers!
Lecturers take a big risk!

## Slide 3: Beam Diagnostics
What do you expect from a lecture on „Beam Diagnostics“
Show how to measure beam parameters
Which beam parameters?
Beam presence
Beam intensity
Mean position
Trajectory
Transverse distribution in horizontal and vertical
Longitudinal distribution
Transverse and longitudinal emittance
Beam Tune, Resonances
Chromaticity
Beta function …..

## Slide 4: Student lecturer
Who wants to come in front and explain to your fellow students what
Transverse emittance
Longitudinal emittance
Betatron Tune …
is?
Who thinks she/he would be able to do so?
Who of you has ever been at CERN or in one of the other big labs?
Who has ever seen an accelerator?

## Slide 5: Introduction to accelerator for my grandma
Find answers to these questions in the film:
Where do the particles come from?
What is done to them to prepare them for acceleration?
Which type of field is used to accelerate?
How much is 1 eV?
At which speed do they enter the Booster?
What happens to the electric/magnetic fields when you accelerate in the Booster
What is the size of the Booster with respect to the PS
What is the circumference of the LHC?
How big is the current in an LHC magnet?
What is the revolution frequency in the LHC?

## Slide 6: Introductory film: CERN‘s Accelerators

## Slide 7: Answers to the questions
Where do the particles come from?
What is done to them to prepare them for acceleration?
Gas Bottle
By Evan Mason - Own work, CC BY-SA 4.0, https://commons.wikimedia.org/w/index.php?curid=49972388
Ionization (stripping off electrons)

## Slide 8: Answers to the questions (2)
Which type of field is used to accelerate?
How much is 1 eV?
proton
Electric field
+++++++++++++++++
- - - - - - - - - - - - - - - - -
Magnetic field
The energy gained by a particle of charge 1 when it falls through a potential of 1 V
Electric field: F=q*E Magnetic field: F=q*v x B

## Slide 9: Answers to questions(3)
At which speed do they enter the Booster?
What happens to the electric/magnetic fields when you accelerate
The magnetic field must increase with increasing particle energy
The magnets are ramped.
At β=0.3 the particle speed increases and the revolution frequency increases
The accelerating RF must also increase

## Slide 10: Answers to the questions(4)
What is the size of the Booster with respect to the PS
The PS is exactly 4 times bigger in circumference than the Booster. The particles in each of the 4 Boosters rings fill the circumference of the PS

## Slide 11: Answers to the questions (5)
What is the circumference of the LHC?
What is the current in an LHC magnet?
What is revolution frequency in the LHC?
27 km
Additional question: Why is it so big?
Difficulty to make magnetic fields stong enough to keep the particles on their orbit
11 kHz: 11000 revolutions per second
12000 A, you see why we need supraconducting magnets!

## Slide 12: More questions
How far does a proton travel when it stays in the LHC for 1 h?
If a particle has an angle of 0.01 degree and the vacuum chamber has a diameter of 10cm How far does it travel before it crashes into the vacuum chamber?
Number of revolutions * no of seconds in 1 h * LHC circumference:
11000 * 3600 * 27 km = 1.069.200.000 km
or 300.000 km *3600 = 1.080.000.000 km
For comparison:
Distance earth to the mars: 119.000.000 km
φ
l
d
d=0.05 m
l= 286.5 m

## Slide 13: Magnets in the lattice
Which type of magnets are these?
Do we need bending magnets in an
Accelerator?
Bending (dipole) magnet
Focusing (quadrupole) magnet

## Slide 14: Why defocussing in the other plane?

## Slide 15: The Beta function
Inject a particle into a lattice and observe ist orbit.
This is a simple fodo lattice

## Slide 16: Betatron Tune
Tune Q = number of oscillations during
one turn
Q =1 is forbidden: small dipole error always gives a kick at the same position
Q= ½ is forbidden small quadrupole error
gives a repetitive error
Same for Q=1/3, 1/4, 1/5 …

## Slide 17: Acceleration
Acceleration is done in cavities with oscillating electrical fields.
Question: What is the revolution frequency of a particle when going at β=0.3 and the circumference is 150 m?
Time for 1 revolution:
Frequency: f = 1/T = 666 kHz
If you have several bunches in your machine the frequency is a harmonic if this basic frequency

## Slide 18: Non-synchronous particles
A synchronous particle P1 sees a phase fs and get a energy kick DEs
A particle N1 arriving early with f= fs-d will get a lower energy kick
A particle M1 arriving late with f= fs+d will get a higher energy kick
Remember: in a synchrotron we have bunches with a huge number of particles, which will always have a certain energy spread!

## Slide 19: More questions (2)
How long is a particle bunch if the accelerating frequency is
40 MHz, the stable regions corresponds to 10% of the RF wave
and the particle travels at the speed of light?
Time for 1 RF oscillation = 25 ns
length [ns] of 1 bunch: 2.5 ns

## Slide 20: Emittance measurements
A beam is made of many many particles,
each one of these particles is moving with
a given velocity. Most of the velocity
vector of a single particle is parallel to the
direction of the beam as a whole (s).
There is however a smaller component of
the particles velocity which is
perpendicular to it (x or y).
Design by E. Bravin

## Slide 21: Phase Space
x’
x
x is the position of the particle
x‘ is ist angle
Projection to the x axis gives the position distribution and rms beam size
Projection to the x‘ axis the angular distribution of the particles

## Slide 22: Emittance measurements
If for each beam particle we plot its position and its transverse angle we get a particle distribution who’s boundary is an usually ellipse.
The projection onto the x axis is the beam size
x’
x
Beam size

## Slide 23: Transforming angular distribution to profile
When moving through a drift space the angles don’t change (horizontal move in phase space)
When moving through a quadrupole the position does not change but the angle does (vertical move in phase space)
x’
x
slit
x’
x
slit
x’
x
slit
Influence of a drift space
Influence of a quadrupole

## Slide 24: Photo CERN and its Accelerator Chain

## Slide 26: Proton Linac

## Slide 27: Booster

## Slide 28: Proton Synchrotron

## Slide 29: SPS

## Slide 30: … finally the LHC