## Slide 1: ADS and Accelerator Requirements
Yacine Kadi
CERN Engineering Department
Geneva, Switzerland
ASP16 – 4th African School of Fundamental Physics and Applications
University of Rwanda, Kigali, Rwanda
August 17, 2016
Application of Accelerators to Nuclear Energy

## Slide 2
Outline
Brief historical account of ADS
Sub-critcal Reactor core physics
Accelerator and the physics of spallation
Motivations and global constraints on ADS

## Slide 3: Accelerator Driven Systems
The basic process in ADS is nuclear transmutation
  1919 Rutherford (14N7 + 4He2  17O8 + 1p1) 210Po accelerator!
  1940 E.O. Lawrence/USA and W.N. Semenov/USSR proposed to use a particle accelerator as a neutron source
  1941 G. Seaborg produced the first μg of 239Pu with the Berkeley 60 inch cyclotron
  1950 E.O. Lawrence proposed the Materials Testing Accelerator (MTA) at the Lawrence Livermore Radiation Lab, to produce 239Pu from Oak Ridge depleted uranium
  1952 W.B. Lewis in Canada proposed to use an accelerator to produce 233U from thorium for CANDU reactors (electro-breeder concept)
Notes: The making of the Atomic Bomb by Richard Rhodes
Seaborg used the 60 inch cyclotron at Berkeley, with 6 MeV deuteron on 238U

## Slide 4: Accelerator Driven Systems
MTA and Lewis’ projects dropped or slowed down when (a) rich uranium deposits were discovered in the USA, and (b) it was realized that it required several hundred mA of beam intensity, hundreds of MW to produce the beam! [Pu, no amplification] today ≤ 10 MW beams seem sufficient
Renewed interest in ADS in the 1980’s, when the USA decided to slow the development of fast critical reactors (Fast Flux Test Facility @ Argone National Lab.):
  H. Takahashi at Brookhaven National Lab: several proposals of ADS systems (PHOENIX), including the idea of burning minor actinides (Fast neutrons – ks~0.99);
  Ch. D. Bowman at Los Alamos: thermal neutron ADS (ATW) with thorium & chemistry on-line for FP and 233Pa extraction;
  Japan launches Options for Making Extra Gains from Actinides (OMEGA, now JPARC) at JAERI (now JAEA).
Notes: Options for Making Extra Gains from Actinides?? Japan Proton Accelerator Research Complex (JPARC) JAEA (Japan Atomic Energy Agency)
MTA 500mA 350 MeV deuteron linac: 175MW => several hundred MW tom produce such a beam. No multiplication in the target!
JPARC: Japan Proton Accelerator Research Complex; Fast Flux Test Facility (FFTF) sodium cooled fast neutron reactor : stopped in 1993 (IFR Itegral fast reactor project) Extenede burnup

## Slide 5: Accelerator Driven Systems
In the 1990s, Carlo Rubbia gave a big push to the ADS, by launching a vigorous research programme at CERN based on:
  development of innovative simulation of nuclear systems
  specific experiments to test basic concepts (FEAT, TARC)
  construction of an advanced neutron Time of Flight facility (n_TOF) to acquire neutron cross-section data, crucial to simulate reliably any configuration with new materials
  Followed by proposals for demonstrators
C. Rubbia triggered a major R&D effort on ADS worldwide
Notes: Simulation integrating the spallation process, neutron transport and evolution of fuel.
Next step is temperature evolution
He is mainly responsible for our

## Slide 6: Basic elements of an ADS system
A particle accelerator, to provide a neutron source
A core in which both source neutrons and fission neutrons are at work – restricted here to the case of a moderator allowing for a fast neutron spectrum
Two main areas of physics:
  Neutron production by spallation from the beam
  Neutron transport and interaction in the core
Physics also drives other ADS elements:
  Cooling (possibility of natural convection)
  Electric power production efficiency (go to highest possible temperature)
Fission
Spallation
Non negligible contribution from the high energy tail (n,xn)

## Slide 7: Simplified model of subcritical systems
Theory of subcritical systems interesting in itself, to get insights into the physics. Properties are quite different from those of critical systems. (C. Rubbia, CERN/AT/ET/Internal Note 94-036)
Neutron flux geometry important to determine the generated power distribution and the uniformity of fuel burnup
Some simplifying assumptions (uniform material and mono-energetic neutrons, small absorption) to get a basic equation similar to that of a critical reactor, but with an external neutron source term in addition:
Fission
Spallation
Absorption
Leakage
Notes: Several ways to be subcritical: kinfinity < 1 or > 1; gives rise to different types of solutions
You really need a MC for fast neutron spectra (n, xn), etc.

## Slide 8: Simplified model of subcritical systems
Example of finite system at equilibrium:
Two regimes corresponding to two classes of solutions:
  k∞ < 1: the system is intrinsically subcritical (FEAT experiment: k∞ ~ 0.93) – Solution is an exponential
  k∞ > 1: subcriticality comes from the lack of confinement, it is a geometrical issue – Solution is oscillatory (C. Rubbia’s EA: k∞ ~ 1.2-1.3)
All modes are excited Theorem:
Diffusion length
Notes: For instance for a paralellepipedal box B**2; l,m,n = Pi**2(l**2/a**2+m**2/b**2+n**2/c**2), a quickly increasing function of the mode
B**2 increasing with increasing modes, => kl,m,n decreasing with increasing mode

## Slide 9: Time dependence
Diffusion equation (with Φ = βn, where β is the neutron velocity):
Case of a neutron pulse, given by C0δ(t), and substituting provides an equation for the time dependence: , and the general solution
Characteristic decay time is shorter as modes become higher. At the criticality limit (k1,1,1=1), the mode is infinitely long. Fermi used this to measure the approach of criticality in his Chicago Pile 1 in 1942, and the method can be used for an ADS.

## Slide 10: Neutron multiplication factor
The neutron multiplication factor depends on the source:
The CERN LHC beam can be switched off in three turns of the machine, that is up to 270µs. The CERN SPS can be switched off in 46 µs. On a (much) smaller machine, such as foreseen for ADS, the switching off time is much shorter. So the reaction time will not be limited by the accelerator. The typically response time of a critical system to reactivity insertion is of the order of 5 ms.
Switching off the neutron source not only stops the main power generation, but also moves the system to a smaller k, from ks to keff.
Fission
Spallation
Absorption
Leakage
For fast neutron systems,
(n,xn) reactions are not negligible, in particular
for the source neutrons

## Slide 11: Critical versus Subcritical Systems

## Slide 12: ADS energy gain
A source neutron is multiplied by fissions and (n,xn) reactions. Since ks<1, neutron production stops after a limited number of generations:
The energy gain G is a characteristic of ADS:
G0 includes information from the spallation process (G0 ~ 3 for uranium; G0 ~ 2.7 for lead, etc.)
n/p
n/fission
Beam energy
Energy/fission
Notes: G = (ε/Eb)(1+ksEf/(1-ks)) where ε is the number of neutrons per proton, Eb is the kinetic energy of a proton, Ef is the energy released per fission

## Slide 13: FEAT at the CERN PS (1994)
The goal of the First Energy Amplifier Test (FEAT) at the CERN PS was to check the basic concept of energy gain, and validate the innovative simulation developed by C. Rubbia and his group.
3.62 t of natural uranium; keff ~ 0.9
– Count fissions
– Measure temperature

## Slide 14: Main results from FEAT
Two important results from FEAT:
  Optimum beam energy reached at about 900 MeV, with slow decrease at higher energies (ionization vs nuclear cascade production). Above 900 MeV, the neutron yield scales with proton energy. At much higher energies the gain drops because of pion production.
  Simulation validated from spallation to energy production
k∞ < 1: exponential
Energy gain well reproduced by simulation

## Slide 15: Energy gain in ADS systems
For a given power output, the energy gain (choice of ks and G0) determines the accelerator power. Trade-off between accelerator power and criticality margin
Modulating the beam intensity allows variations in the power output (complementary with a fluctuating renewable energy source)
Neutronics with thorium very favourable compared to uranium t1/2 (233Pa) ~ 27d; t1/2 (239Np) ~ 2.3d! What was a problem in the use of thorium in critical reactors becomes an advantage in the case of ADS
1500 MW
1000 MW
500 MW
100 MW
Rubbia’s EA
MEGAPIE
With PSI separate turns cyclotron (3 mA and 1.8 MW, with 0.59 GeV protons). PADS = 243 MWth with k = 0.98 PADS = 486 MWth with k = 0.99.
Assuming Pb target
Margin of
present
PWR

## Slide 16: Guidelines for ADS parameters choice
Safety:
  Eliminate criticality accidents by making the system subcritical (void coef., T coef., βeff no longer “critical” parameters) This requires an external proton source!
  Operate system with passive safety elements to avoid core melting or limit its consequences, borrowing features from US advanced fast critical reactor designs;
  Avoid dangerous coolants such as liquid sodium (use lead) Generation IV?
Waste management:
  Use (1) fast neutrons, (2) thorium fuel, and (3) recycle long-lived transuranic actinides (TRU) to minimize waste.
Military proliferation:
  Use thorium fuel (small Pu prod., 233U very difficult mixture)
  Avoid Pu separation (Purex), use pyroelectro reprocessing instead (developed for uranium at Argone N.L.)

## Slide 17: Physics of subcritical systems
C. Rubbia’s EA with natural convection
Subcritical systems are insensitive to delayed neutron fraction (β); safety margin (distance from prompt criticality) is a design choice, it is not imposed by Nature!
ks = 0.975 makes the system subcritical under all conditions (after 233Pa decay)
The reactivity changes only very slowly; the beam can be switched off very quickly, reducing ks to keff. It is possible to choose a higher ks in order to reduce the load on the accelerator (Takahashi, ks = 0.99)
Delayed neutron
fraction
Deterministic
control
Notes: LICE ~ 4.5 Mio nodes / 5000 volumesA; TLAS ~ 29 Mio nodes / 7000 volumes; CMS ~ 1.5 Mio nodes / 1500 volumesL; HCb ~ 18 Mio nodes / 700 volumes
From 1995 to 2009 computing power increased by factor 500 (Moors’s law)
170$/s for 15ms

## Slide 18: Guidelines for ADS parameters choice
Safety:
  Eliminate criticality accidents by making the system subcritical (void coef., T coef., βeff no longer “critical” parameters) This requires an external proton source!
  Operate system with passive safety elements to avoid core melting or limit its consequences, borrowing features from US advanced fast critical reactor designs;
  Avoid dangerous coolants such as liquid sodium (use lead) Generation IV?
Waste management:
  Use (1) fast neutrons, (2) thorium fuel, and (3) recycle long-lived transuranic actinides (TRU) to minimize waste.
Military proliferation:
  Use thorium fuel (small Pu prod., 233U very difficult mixture)
  Avoid Pu separation (Purex), use pyroelectro reprocessing instead (developed for uranium at Argone N.L.)

## Slide 19: Partitioning &Transmutation
P/T applies to TRU (Pu and Minor Actinides) and Long Lived Fission Products.
It should be kept in mind that Plutonium is a special case: it can be considered as a valuable resource or part of the wastes.
However, P/T technologies must apply to all fuel cycles.

## Slide 20: Physics of a thorium core
Thorium in a fast neutron flux:
  It takes 7 neutron captures to go from 232Th to 239Pu!
  233Pa decay 10 times slower than 239Np
Pu equilibrium concentration ~ 10–4 as opposed to 15% in a U-Pu system!
Thorium is a major asset to minimize waste production or to destroy waste
Notes: 231Pa bump after 250000 years; in once through cycle factor 100 at t ≤ 250000 years: => recycle TRU
Could be impurities in thorium ore from uranium => 230Th (231pa by capture or n2n on 232Th (main)

## Slide 21: Why fast neutrons
Use fast neutrons:
  Enhances TRU fission probability
  No need to separate out Pu! (Pyro-Electro reprocessing)
  Reduces captures on FF, extends burnup (120 GW.day/t achieved in fast electro- breeder at Argonne N.L., in EA simulation)
Notes: Minor actinides are the only thing that Nuclear Industry admits would requires ADS!

## Slide 22: Common Deployment Scenario
The objectives of GEN-IV include P/T (waste minimization), as consistent with sustainability and non-proliferation: it is the path towards “Advanced Fuel Cycles”.
Implementation: currently related to Fast Reactor deployment. However, ADS is the only option for Minor Actinide elimination
2020
Implementation of MA partitioning
Waste minimization (Vitrified FP)

## Slide 23: MA Transmutation
Typical transmutation rates (~ 50 kg/TWh) using MA based fuels.
Doping with Pu will sensibly decrease the transmutation efficiency of such systems

## Slide 24: Alternative Deployment Scenario
ADS
LWR with reduced waste generation
232Th
Nuclear
waste
232Th+ 233U
STAGE 1
STAGE 2

## Slide 25: Fast track by Integration of Consolidated Technologies … by 2030 !
UO
2
+PuO
2
UO
2
2+
PuO
2
2+
Technology of pyrochemical reprocessing of fuel
Technologies of fast reactors with lead-bismuth coolant
High power accelerators technology
Liquid metal targets technology

## Slide 26: Europe ADS: MYRRHA
Hamid Aït Abderrahim
In principle MYRRHA should be the flagship of ADS projects.
Strong support from the Belgian government, however:
– several challenges faced at the same time: the accelerator, the subcritical core and their coupling
– no thorium in the plans
– only partially funded
– not before 2025?
– will not remain an ADS, and will be turneds into a critical reactor
Hamid Aït Abderrahim
SCK•CEN, Boeretang 200, 2400 Mol, Belgium

## Slide 27: China ADS: ADANES
The Chinese Accelerator-Driven System (CADS) project includes the accelerator, the target and the blanket. Accelerator-Driven Advanced Nuclear Energy System (ADANES) proposed as a complete energy system, integrating nuclear waste transmutation, nuclear fuel multiplication and energy production, aiming at 1000 MWe.
ADANES has the potential to reach the requirements of sustainable development, safety, economic competitiveness, and nuclear weapon non-proliferation.
Innovative spallation target R&D
Two injector solutions developed in parallel
in 2022
5-10MW
100MW
1000MW
Also a linac approach for the accelerator

## Slide 28: India ADS at BARC
Shashikant Degweker
Other AD R&D activities in may countries such as Venezuela, Turkey, Korea, Japan, Ukraine, UK (Aker Solutions with C. Rubbia) – Many activities in the world but a lack of cooperation
India is mostly concentrating on the accelerator at this time
Study of a high-current, high-energy proton accelerator (1 GeV and 30 mA), in collaboration with the USA (Old Fermilab Project X).
First phase: development of a 30 mA, 20 MeV linac injector (LEHIPA).
Second phase: accelerating the beam to an energy of 1 GeV by way of a superconducting linac.

## Slide 29: A brief history of ADS projects
Project | Neutron Source | Core | Purpose
FEAT (CERN) | Proton (0.6 to 2.75 GeV) (~1010p/s) | Thermal (≈ 1 W) | Reactor physics of thermal subcritical system (k≈0.9) with spallation source - done
TARC (CERN) | Proton (0.6 to 3.5 GeV) (~1010p/s) | Fast (≈ 1 W) | Lead slowing down spectrometry and transmutation of LLFP - done
MUSE (France) | DT (~1010n/s) | Fast (< 1 kW) | Reactor physics of fast subcritical system - done
YALINA (Belorus) | DT (~1010n/s) | Fast (< 1 kW) | Reactor physics of thermal & fast subcritical system - done
MEGAPIE (Switzerland) | Proton (600 Me) + Pb-Bi (1MW) | ----- | Demonstration of 1MW target for short period - done
TRADE (Italy) | Proton (140 MeV) + Ta (40 kW) | Thermal (200 kW) | Demonstration of ADS with thermal feedback - cancelled
TEF-P (Japan) | Proton (600 MeV) + Pb-Bi (10W, ~1012n/s) | Fast (< 1 kW) | Coupling of fast subcritical system with spallation source including MA fuelled configuration – reactivated
SAD (Russia) | Proton (660 MeV) + Pb-Bi (1 kW) | Fast (20 kW) | Coupling of fast subcritical system with spallation source - cancelled
TEF-T (Japan) | Proton (600 MeV) + Pb-Bi (200 kW) | ----- | Dedicated facility for demonstration and accumulation of material data base for long term – reactivated
MYRRHA (Belgium) | Proton (600 MeV) + Pb-Bi (1.8 MW) | Fast (60 MW) | Experimental ADS – under design, not fully funded, 2025?
CADS (China) | Protons (0.6 – 1.5 GeV) | Fast (100–>1000MW) | Four phase project: 2011 – 2032
U-ADS (Ukraine) | Electrons (100 MeV) | 100 kW | Uranium-based ADS prototype (KIPT) Status??
ADS (Russia) | Protons (250-500 MeV) | 1-5 MW | Using an existing facility at Troitsk – under consideration promoted by iThEC

## Slide 30: Accelerator requirements
Choices for an industrial system will rely on specifications in terms of:
  Beam power: 1-10 MW depending of choice of k value, and desired unit power; Ebeam ≥ 900 MeV
  Beam losses: minimize irradiation of the accelerator and of the environment; impact on the maintenance (minimize and localize beam losses)
  Reliability, minimize beam trips (have multiple sources); ease of maintenance
  Beam stability and control: 1% fluctuation on beam intensity is 1% fluctuation on the thermal power; beam intensity to be varied by a factor ≥ ?2
  Energy efficiency: maximize fraction of electric grid power stored into the beam) Improves with increasing beam power.
  Size, cost

## Slide 31: Development is Time-Consuming

## Slide 32: Concluding remarks
Accelerator-driven systems offers a unique level of safety, which give operational flexibility to future systems for safe and clean energy production and waste transmutation
Present accelerator technology offers the possibility of closing the thorium fuel cycle. The Energy Amplifier is one of the examples with high potential
iThEC aims to promote the deployment of these technologies

## Slide 33
Thank You

## Slide 34: How to use thorium in practice?
Thorium blankets around fast critical reactors to breed 233U: the Indian approach, at the cost of maintaining three different nuclear reactor technologies
Continuously circulating fuel to always have fresh fuel in the core Pebble bed or molten salt critical reactors (MSR) or Traveling wave reactors?
Provide extra neutrons with an accelerator: ADS
Pebble-bed and Molten salt reactors have both severe issues to be resolved, mainly in terms of safety, in addition to the fact that they do not provide (so far) a fast neutron flux
Pebble bed Scheme
Molten Salt Reactor Scheme

## Slide 35: Thorium blanket: Indian strategy
India, with little uranium resources but a lot of thorium, has the most advanced practical scheme for using thorium (including front-end and back-end of the fuel cycle):
  Use heavy water reactors (CANDU) or LWR to produce plutonium
  Use sodium cooled U-Pu fast reactors with a thorium blanket to breed 233U
  Reprocess blankets and manufacture 233U-Th fuel for advanced fast reactors or heavy water reactors
The Indian scheme works. However, several issues remain concerning the complexity (three technologies), the sustainability and nuclear waste management.

## Slide 36: Pebble bed critical reactors
Proposed by Farrington Daniels at Oakridge, in the 1940s. Initial developments in Germany (AVR Jülich), followed by THTR-300MW (1983-1989). New developments in South Africa, now in the United States and Turkey.
  Presented as passively safe, as high temperature systems can be cooled by natural air convection
Several severe issues to be resolved:
  No containment building if cooling by natural air convection
  Uses flammable graphite as moderator
  Produces more high-level nuclear waste than current nuclear reactor designs
  Relies heavily on pebble integrity and fuel handling (pebble accident in THTR-300)
  Water ingress, reprocessing virtually impossible, etc.
Notes: The THTR-300 was a thorium high-temperature nuclear reactor rated at 300 MW electric (THTR-300). The German state of North Rhine Westphalia, in the Federal Republic of Germany, and Hochtemperatur-Kernkraftwerk GmbH (HKG) financed the THTR-300’s construction.[1]
Operations started on the plant in Hamm-Uentrop, Germany in 1983, and it was shut down September 1, 1989. The THTR was synchronized to the grid for the first time in 1985 and started full power operation in February 1987.[2]
Whereas the AVR was an experimental pebble bed high-temperature reactor (HTR) used to develop the pebble fuel, the THTR-300 served as a prototype HTR to use the TRISO pebble fuel.
670,000 spherical fuel compacts each 6 centimetres (2.4 in) in diameter with particles of uranium-235 and thorium-232 fuel embedded in a graphite matrix

## Slide 37: Molten salt critical reactors
This is clearly a technology that is concentrating interest (10 talks related to the subject at ThEC13): China, India, UK, USA, Czech Republic, France, Switzerland
Pioneered at Oakridge in 1960 (Molten Salt Reactor Experiment, UF4, 7.4MWth)
Advantages:
  Liquid fuel allows extending burnup indefinitely, because of reprocessing on-line
  High temperature (500˚C – 600˚C), heat produced directly in heat transfer fluid
  Passive cooling for decay heat removal
Several severe issues: neutrons emission, on-line chemistry failure, corrosion, licencing issues, etc.
Presently not using a fast neutron spectrum (R&D should be extended to other salts – PbCl3, to minimize waste)
There is a particularly well focussed and ambitious effort in China (Xu Hongjie, Shanghai Institute of Applied Physics)
Elsa Merle-Lucotte @ ThEC13
F-Li-Be salt (Flibe)
Chemistry on-line
Notes: This cracking could be reduced by adding small amounts of niobium to the Hastelloy-N.
SINAP: Shanghai Institute of