## Slide 1: GBT-FPGA Tutorial
Creation of a reference design in standard mode

## Slide 2: Outline
Demo setup and configuration
How to implementation the GBT-FPGA IP using records
How to implementation the required additional modules
How to make my design versatile (multi-links, enable/disable features)
How to debug the design

## Slide 3: Demo setup and configuration
What is my demo setup ?
Optical fibber
(SFP)
Clock in (LHC Clock)
LHC Clock (to FPGA)
Transceiver Clock (to MGT REFCLK pins)
TTC PON FMC
Altera Arria 10 GX Development kit
Xilinx FMC (HW-FMC-105-DEBUG)
SMA OUT

## Slide 4: Demo setup and configuration
What are the clock and data schemes ?
SI5338
FrameClk (LHC Clock)
MGT RefClk (240MHz)
LHC Clock
Data Tx
Data Rx
SFP Connector

## Slide 5: Demo setup and configuration
How to initialize the SI5338 PLL ?
  Using the ClockBuilder tool from SILabs
  I2C bus located on the card
  I2C OpenCore IP
JTAG Server
Avalon MM
OpenCore I2C
SDA
SCL
Arria 10
On-board osc.
RESET
TCL
JTAG cable

## Slide 6: How to implementation the GBT-FPGA IP using records
What is the content of the GBT bank instance?
gbt_bank
gbt_tx
multi_gigabit_transceiver
gbt_rx
gbt_tx_scrambler
gbt_tx_encoder
gbt_tx_gearbox
mgt_std
mgt_latopt
gbt_rx_framealigner
gbt_rx_decoder
gbt_rx_gearbox
gbt_rx_descrambler
gbt_rx_status
*
*
*
*
*: Contains device specific instances

## Slide 7: How to implementation the GBT-FPGA IP using records
What are the GBT Bank interfaces ?
Records
Configuration
Warning: configuration can be made using two different ways ! Do not mix these to avoid bugs.
First way: Specify only the GBT_BANK_ID parameters when you implement the module. In this case, the information are get from the gbt_banks_user_setup package (gbt_bank/your_device/xxx_xxx_gbt_bank_user_setup.vhd)
Second way: Specify all the parameters except the GBT_BANK_ID (its value shall be 0, default value).

## Slide 8: How to implementation the GBT-FPGA IP using records
How to find records definition?
  GBT-FPGA User guide
    2.5. Operating the GBT-FPGA Core
  VHDL files
    gbt_bank/core_sources/gbt_bank_package.vhd: records generic for all the devices
    gbt_bank/<device>/xxx_xxx_gbt_bank_package.vhd: device specific records

## Slide 9: DEMO

## Slide 10: How to implementation the required additional modules
GBTBank reset
Generates the reset signal for the different part of the GBT Bank: TX, RX and MGT
GBT_TX_RESET_O
MGT_TX_RESET_O
MGT_RX_RESET_O
GBT_RX_RESET_O
INITIAL_DELAY
TIME_N
GAP_DELAY
TIME_N
GAP_DELAY

## Slide 11: DEMO

## Slide 12: How to implementation the required additional modules
GBT Data pattern generator
gbt_pattern_generator
RESET_I
TX_FRAMECLK_I
TX_ENCODING_SEL_I
TEST_PATTERN_SEL_I
STATIC_PATTERN_SCEC_I
STATIC_PATTERN_DATA_I
STATIC_PATTERN_EXTRADATA_WIDEBUS_I
TX_DATA_O
TX_EXTRA_DATA_WIDEBUS_O

## Slide 13: How to implementation the required additional modules
GBT Data pattern checker
GBT_RX_READY_I
RX_ENCODING_SEL_I
RESET_GBTRXREADY_LOST_FLAG_I
RESET_DATA_ERRORSEEN_FLAG_I
gbt_pattern_checker
RESET_I
RX_FRAMECLK_I
RX_DATA_I
RX_EXTRA_DATA_WIDEBUS_I
STATIC_PATTERN_SCEC_I
STATIC_PATTERN_DATA_I
STATIC_PATTERN_EXTRADATA_WIDEBUS_I
GBTRXREADY_LOST_FLAG_O
RXDATA_ERRORSEEN_FLAG_O
RXEXTRADATA_WIDEBUS_ERRORSEEN_FLAG_O
RXDATA_ERROR_CNT
RXDATA_WORD_CNT

## Slide 14: DEMO

## Slide 15: How to make my design versatile (multi-links, enable/disable features)
Generate statement for multi-links:
Generate statement to enable/disable features:

## Slide 16: DEMO

## Slide 17: How to debug the design
ISSP and Signal tap

## Slide 18: DEMO