## Slide 1
Microscopic and fluid modeling of Resistive Plate Chambers
Danko Bošnjaković and Saša Dujko
Institute of Physics, University of Belgrade, Serbia
RD51 collaboration meeting CERN, June 2016

## Slide 2
Outline
Introduction
Microscopic Monte Carlo model
Classical fluid model
“Corrected” fluid model
Conclusion and future work

## Slide 3
Resistive Plate Chamber (RPC): principles of operation
Developed by Santonico and Cardarelli (1981).
Consists of two parallel plate electrodes made of material of high volume resistivity for supression of destructive discharges.
Resistive material:
  glass (ρ = 1012-1013 Ωcm).
  bakelite (ρ = 1012-1012 Ωcm).
Operating conditions:
  atmospheric pressure, room temp.
  reduced electric fields: 200 to 400 Td.
  timing resolution: 50 ps to ~1 ns.
  spatial resolution: ~1 mm.
  counting rate capability: up to ~1 kHz/cm2
Gas mixtures:
Ar, C2H2F4, iso-C4H10, SF6.
incoming particle
(taken from C. Lippmann, PhD thesis)

## Slide 4
Simulation and modeling of RPCs
Model(s) | Advantages | Disadvantages
Analytical e.g. Riegler NIMA 602 (2009) 377; Fonte JINST 8 (2013) P11001 | Can provide general conclusions | Often approximate
Fluid equations e.g. Moshaii NIMA 661 (2012) S168; Fonte IEEE TNS 43 (1996) 2135 | Space charge effects, photoionization and recombination can be relatively easily included Computationally efficient | Provide average quantities (deterministic)
Macroscopic stochastic e.g. Riegler et al. NIMA 500 (2003) 144; Salim et al. JINST 7 (2012) P11019 | Provide stochastic quantities such as efficiency, timing resolution and charge spectra Computationally efficient | Based on different models of avalanche fluctuations (e.g. Legler, Polya) which can be approximate
Microscopic stochastic e.g. Bošnjaković et al. JINST 9 (2014) P09012 | Provide stochastic quantities Accurate | Computationally demanding

## Slide 5
Our “microscopic” Monte Carlo model of RPC †
Based on tracking of each electron and its collisions with the background gas in a bounded space between the cathode and the ’absorbing’ anode
Includes primary ionization and signal induction
Electron path is determined using an analytical solution for the equation of the electron motion
Determination of a probability and nature of a collision;
Probability density that the collision occurs in the time interval (t,t+dt)
Relative probabilities of collisional processes
The nature k of collisional process occurs
Procedure for the collision dynamics
Isotropic scattering is assumed
f
q
electron
molecule
vi
The azymuthal angle f
The polar angle q
The change in the electron energy after an elastic collision
† D. Bošnjaković, Z.Lj. Petrović and S. Dujko (2014), J. Instrum. 9, P09012.

## Slide 6: C2H2F4 cross sections
Cross sections for C2H2F4 were developed by our group† using measured swarm data from Urquijo et al. (2009).
† O. Šašić et al. (2013), J. Phys. D 46, 325201.

## Slide 7
Results: Single-electron avalanches†
† D. Bošnjaković, Z.Lj. Petrović and S. Dujko (2014), J. Instrum. 9, P09012.
‡ W. Riegler (2009), Nucl. Instrum. Meth. A 602, 377.
We simulated 2×104 single-electron avalanches in a gas mixture of 85% C2H2F4 + 5% iso-C4H10 + 10% SF6 (a timing RPC mixture)
Threshold: 10000 electrons
E/N = 439 Td
An analytical model for time response functions‡
Legler’s model
Deviation from the exponential dependence
(t = 290 ps)
Legler’s model of avalanche statistics

## Slide 8
Primary ionization
1/l = 7.5 cl/mm
(MIPs)
taken from W. Riegler, C. Lippmann, R. Veenhof, NIMA 500 (2003) 144
† I.B. Smirnov (2005), Modeling of ionization produced by fast charged particles in gases, Nucl. Instrum. Meth. A 554, 474.
Signal induction (Ramo’s theorem)
Primary ionization consists of point-like clusters. The distance between neighboring clusters is exponentially distributed. Mean distance between clusters and cluster size distribution are calculated using HEED.
Induced current:
mean electron velocity
“flux drift velocity”

## Slide 9
Temporal evolution of an RPC signal for 3 primary clusters consisting of 1, 10 and 100 electrons, respectively. The reduced electric field is set to 421 Td and the gas mixture of C2H2F4:iso-C4H10:SF6=85:5:10 was considered.
Our “microscopic” Monte Carlo model of RPC †
Initial positions of primary clusters.
† D. Bošnjaković, Z.Lj. Petrović and S. Dujko (2014), J. Instrum. 9, P09012.
CATHODE
ANODE
Notes: Tezinsko polje je 1.48 po mm koje je izracunato u rieglerovom radu za rastojanje od 0.3 mm (Riegler 2003).

## Slide 10
Results: Realistic RPC events. Timing and efficiency †
† D. Bošnjaković, Z.Lj. Petrović and S. Dujko (2014), J. Instrum. 9, P09012.
Gas mixture of C2H2F4 (85%), iso-C4H10 (5%) and SF6 (10%); 3 different cross section sets for C2H2F4
Primary ionization: 7.5 cl/mm; 1/n2 and HEED cluster size distributions
0.3 mm gas gap
Threshold was set to 2 fC (corresponds to about 106 electrons in the gap, no space charge)
Comparison with measurements by Lopes et al. (2012)
HEED
our
C2H2F4
set
HEED
(2012)
(2012)
E/N = 439 Td

## Slide 11
Computing requirements
Our MC RPC simulation with 10000 events takes about 2 days of computation time on 300 CPU cores (14400 CPU hours).
The calculations were performed on our lab’s computing system:
5 nodes x 4 CPUs AMD Opteron 6272 @ 2.1GHz (16 cores)
Total # CPU cores: 320
Total RAM: 768 GB

## Slide 12
Numerical scheme
Spatial derivative: 2nd order central finite difference
Time integration: 4th order Runge-Kutta method
1.5D classical fluid model
Transport equations for electrons and ions
Electric field (the charge is deposited inside the cylinder with radius R0 and distributed uniformly in the radial direction)
Induced current (Ramo’s theorem)
Photoionization source term
‘first-order’
model
model based on hydrodynamic approximation
Transport data
bulk
flux
Boundary conditions
Initial conditions

## Slide 13
Avalanche and streamer development in ATLAS triggering RPC
gas mixture: 94.7% C2H2F4 + 5% i-C4H10 + 0.3% SF6
E0/N = 196 Td (operating field)
bulk data are assumed
1.5D classical fluid model: an example

## Slide 14
1.5D classical fluid model: induced current (flux vs bulk data)
ATLAS triggering RPC
94.7% C2H2F4 + 5% i-C4H10 +
0.3% SF6
gas gap: 2 mm
ALICE timing RPC
90% C2H2F4 + 5% i-C4H10 +
5% SF6
gas gap: 0.25 mm
Timing RPC 2
85% C2H2F4 + 5% i-C4H10 +
10% SF6
gas gap: 0.3 mm

## Slide 15
ALICE TOF
1.5D classical fluid model: induced charge (flux vs bulk data)
ALICE TOF
The maximum difference between induced charges calculated using flux and bulk data is about 80% for the ATLAS RPC and few hundred percent for timing RPCs
Due space charge effects at higher electric fields, this difference is about 6% for ATLAS RPC and about 30% for timing RPCs

## Slide 16
1.5D classical fluid model: different C2H2F4 cross sections
ATLAS triggering RPC
gas mixture 94.7% C2H2F4 + 5% i-C4H10 + 0.3% SF6
2 mm gas gap
E0/N = 196 Td (operating point)
the observed differences stem from different drift velocities and effective ionization rates
t = 6.29 ns
t = 10.76 ns
t = 13.13 ns

## Slide 17
8 kV
(160 Td)
9.8 kV
(196 Td)
10.7 kV
(213 Td)
1.5D classical fluid model: different C2H2F4 cross sections
Induced signals in ATLAS triggering RPC
gas mixture 94.7% C2H2F4 + 5% i-C4H10 + 0.3% SF6
2 mm gas gap

## Slide 18
1.5D fluid model based on hydrodynamic approximation (“corrected model”)
Calculation of source term coefficients
Source term due to ionization/attachment
Photoionization source term
and
Transport equations
Electric field
where
flux data

## Slide 19
1.5D corrected fluid model: avalanche and streamer evolution
t = 0.45 ns
t = 0.92 ns
t = 1.07 ns
ALICE timing RPC gas mixture: 90% C2H2F4 + 5% i-C4H10 + 5% SF6
0.25 mm gas gap
E0/N = 415 Td (operating point)
during the avalanche phase, profiles match with those from bulk case
positive streamer velocity is also similar to that from bulk case

## Slide 20
1.5D corrected fluid model: induced signals
ATLAS
ATLAS
ALICE TOF
ALICE TOF
Induced current
Induced charge

## Slide 21
1.5D corrected fluid model: induced signals
Application of Ramo’s theorem
In general, should total flux be included i.e.
where flux density ?
Hydrodynamic approximation
Implementation in fluid model
vs
ATLAS RPC
max=0.33%
ALICE TOF RPC
max=0.95%

## Slide 22: Conclusion and further work
We have developed a 3D Monte Carlo microscopic model for timing resolution and efficiency of RPCs with low signal discrimination threshold
A full microscopic model for RPCs would have to be able to simulate realistic thresholds. It should also follow the signal development until the end so that charge spectra can be obtained. This would require the inclusion of space charge effects. Problem: limited computing resources Possible solution: PIC/MC simulation with super particles
We have developed a 1.5D classical fluid model and also a model based on hydrodynamic approximation. Using these models we have shown how different transport data used as input affect the calculated RPC signals.
These models should be compared with local mean energy model and PIC/MC simulation.