## Slide 1: LINAC5 A New Linear Accelerator for OPENMED at CERN
Jimmy Garland
Linear Accelerators Group, CERN

## Slide 2: My background:
Studied at University of Manchester, UK.
PhD in accelerators for medical and energy applications.
Postdoc. designing a circular accelerator for proton therapy and other FFAGs.
Nature Physics 8, 243-247 (2012)
EMMA - Electron Model for Many Applications
2.5 m radius
0.5 μs acceleration from 10 – 20 MeV
Came to CERN in 2015 to work on a linear accelerator for medical applications...
Fixed-Field Alternating-Gradient
KURRI, Japan. 150 MeV proton FFAG

## Slide 3
OPENMED
CERN’s study group on accelerators for medical applications.
Aim to build a facility for studying multiple ion species in a medical-use context.
Biomedical studies: tissue/cell exposure, detector studies, precision statistical experiments.
What is OPENMED?
Why study ions?
Protons and other ions utilise ‘Bragg peak’ to treat cancer tumors.
Ions potentially more precise and more effective.
Less fundamental research has been carried out with ions to date.
H, He, Li, Be, B, C, N, O
Plot author: Cepheiden

## Slide 4
OPENMED Facility Plan
Existing infrastructure
LEIR
LEIR
(Low Energy
Ion Ring)
New extraction line
Experimental
area
LINAC5
To switching
beam lines
Injection
into LEIR
PS complex
Early-stage design.
Facility will use existing LEIR accelerator to reach up to 430 MeV/u for ions.
New extraction system and experimental area in building 150.
New front-end and linear accelerator: LINAC5.

## Slide 5
LINAC5 Design Considerations
What structure should the LINAC have?
to LEIR
Alvarez Drift Tube Linac (DTL)
Inter-digital H (IH)
Quasi-Alvarez
Long
Good focusing control
Quadrupoles in each drift tube
Short
Limited focusing control
No quadrupole in drift tubes
In between!
Variable focusing control
Quadrupoles in nth drift tube
Focusing is important: particles are often transversely defocused by an RF field.

## Slide 6
LINAC5 Design Progress
Parameter | DTL | Quasi-Alvarez | IH
Linac length [m] | 8.2 | 5.4 | 3.5
Frequency [MHz] | 202.56 | 405.12 | 202.56
x/y emittance [π.mm.mrad] (rms norm.) | 0.158 / 0.179 | 0.135 / 0.135 | 0.136 / 0.136
Longitudinal emittance [π.mm.mrad] (rms norm.) | 0.095 | 0.19 | 0.19
Aperture radius [mm] | 8.0 | 6.0 | 10.0
Max. 5rms envelope [mm] | 2.9 | 2.9 | 6.5
Max. 5rms phase envelope [deg] | 10 | 20 | 23
Transmission [%] | 99 | 99 | 97
Tank Power [MW] | 1.0 | 0.5 | ?
Three design studies were made.
Ions with charge to mass ratio (q/m) of ¼ are the ‘heaviest’ -> baseline design.
Quasi-Alvarez provides more focusing capability than IH with shorter length than DTL.

## Slide 7
LINAC5 Design Progress
Position [m]
X & Y [mm]
One half period
Beam envelope
Blue = x
Red = y
RF electric field map
Emittance
Green = longitudinal
Blue = horizontal
Red = vertical
Quasi-Alvarez

## Slide 8
Phase [deg.]
W [MeV]
x [mm]
X’ [mm]
100
50
0
-50
-100
-15
-10
-5
0
5
10
15
-15
-10
-5
0
5
10
15
X’ [mm]
100
50
0
-50
-100
x [mm]
Acceptance
Longitudinal
Horizontal
Vertical
Area in phase space which traverses the whole structure in a given plane.
Black: acceptance
Blue: initial input
White: RFQ beam

## Slide 9
LINAC5: Next Steps?
Design compact magnets for drift tubes.
Error studies in the structure.
Many ion species to be studied, look at different optimised scenarios for OPENMED.
Design a matching section from RFQ to Linac.
Full electromagnetic 3D modeling.

## Slide 10
Thank you for your attention!

## Slide 11
Ions species (q/m) | Final total kinetic energy [MeV] | Kinetic energy needed for constant rigidity [MeV]
1/4 | 16.8 (4 MeV/u) | 16.8 (4.2 MeV/u)
1/3 | 12.6 (4 MeV/u) | 22.4 (7.5 MeV/u)
1/2 | 8.4 (4 MeV/u) | 33.4 (16.7 MeV/u)
Backup 1.