## Slide 1: On the Possible use of Califes for Beam Instrumentation tests
BI Technical Board, 1st September 2016
T. Lefevre on behalf on the BI group

## Slide 2: Outline
Motivation for a Beam instrumentation Test Facility on Califes
Requirements for the infrastructure
Few examples of possible tests
Conclusions
T. Lefevre, BI Technical Board, 1st September 2016

## Slide 3: Motivations
Why do we need a(nother) test facility at CERN for beam Instrumentation R&D ?
What can be achieved on Califes ?
How relevant is it for CERN accelerator projects ?

## Slide 4: Why ?
Machine operation schedule @ CERN
  Long periods with no beam available
  Limited beam time available for Machine Developments

## Slide 5: Why ?
Hardware installation periods on OP machines are limited
  Any improvements/modifications can not be implemented quickly
    Testing on test Facility will faster the developments and ensure that we installed well-understood devices on operation machines
Developing new concept versus Reliable operation
  Operational machines have strict requirements in terms of vacuum-outgassing performance/ bakeability not always compatible with R&D needs
    e.g. Testing gas ionization monitor and their performance as function of gas pressure
    Very limited opportunities to make changes on beam line equipements

## Slide 6: What for ?
A Test facility can not address all issues. But ….
Address system’s performance under realistic conditions (not achievable in laboratory)
  Testing state of the art electronic with realistic signals
    i.e. Response to short pulses with high signal amplitude
  Testing of UV, optical, X-ray monitors where no other source can reproduce beam induced radiation
    Imaging technique and Beam halo monitoring, …
  Validation of particle detector design (e.g. Beam loss monitor/ Luminosity monitor, detector for Experimental Areas)
    Sensitivity checks, linearity (or non-linearity) checks, ..

## Slide 7: What for ?
All CERN accelerators and possibly interest from other labs
  OP machines including Experimental Areas
  Projects: HL-LHC, LIU (SPS, PS, PSB)
  Studies, i.e. CLIC/ILC, AWAKE, FCC-hh/ee …
Beam tests for
  Calibration of existing BI OP instruments during long Shutdowns
  Upgrades of existing devices and/or understanding of OP issues
    e.g. behavior of devices to bunch length or beam position ..(fBCT@LHC)
  Development of new systems/concepts
    e.g. Electro-optical BPM or Optical Transition Radiation Interferometry

## Slide 8: What for ?
Future Challenges in BI
  Unprecedented request for precision
    Positioning down to below the micron level
  Treatment of increasingly more data
    Bunch by bunch measurements for all parameters:: Test of state of the art acquisition system (electric or optical domain)
  Dealing with high beam powers
    Non-invasive techniques (Gas profile monitor, Quadrupolar PU, ..)
    Robust and reliable machine protection and beam loss monitoring systems
  Dealing with the (ultra) fast
    Sub-picosecond bunch lengths in AWAKE and CLIC
    Longitudinal tomography in LHC (picosecond range)
    Fast transverse beam position monitors (beam Instability diagnostics)

## Slide 9: Why Califes ?
Electron linac is the cheapest way to provide relativistic beams
  Beam energy higher than 200MeV (3.5GeV max) – similar g as on SPS (LHC)
Photo-injector provides a modular bunch spacing
  Single bunch capability for impulse response
  Bunch spacing similar to CERN beams (1ns, 5ns, 25ns, 50ns, .. )
  Pump – probe experiment (wakefield study, impedance measurement, ..)

## Slide 10: Why Califes ?
Achievable Beam parameters
  Good emittance to reach small beam size (<50um)
  Short and long bunches (300fs up to 50ps)
    requiring add. Magnetic chicane
  Easy and full control the beam position over large distance
  Large range of bunch intensity and density
    Possibility to have very weak beams (below 105part/cm2) as for SEU study
Applications requiring high beam current can be performed on Hiradmat@SPS that has been designed for High intensity beam tests

## Slide 11: Modifying Califes
Magnetic chicane
Shorten or lenghthen
RF deflector
for crabbing
Collimator
Reducing the bunch intensity
Beam current monitor
Beam position monitor
Beam profile monitor
Short and long bunches (100fs up to 200ps)
Large range of Bunch intensity
Time to position correlation
+ Adequate beam monitors for beam tuning and cross-calibration

## Slide 12: BI test stand
Synchrotron radiation test stand
In-air DUT area
Synchrotron radiation test stand
Under vacuum DUT area
DUT: Device under Test
Including SR test stand for mm, infrared, visible, UV light, X-ray generation
Including Electronic test stand using Pick-up (BPM, WCM) and seg-Dump for Electrical signal generation (short cable to the location of electronic under test)
Permanent installation for testing beam screens and EM devices (ceramic vacuum chamber)
Including Testing area for beam instruments – Under Vacuum DUT -
Including Testing area for particle detectors – In-air DUT – low intensity option

## Slide 13: Possible Applications
Synchrotron radiation Test Stand
  Imaging system for HL-LHC and FCC (visible, UV, X-ray ?..)
  Beam halo monitor, longitudinal density monitors, …
Electrical signal Test Stand
  Electronic for bunch-by-bunch BPM acquisition system of HL-LHC, ….
Under vacuum DUT area
  Independent vacuum zone with easy access and fast pumping capabilities
  Including steering magnets to move the beam around
  Equipped with a permanent instrumentation test stand
    Used for beam cross calibration: beam size, position and bunch length
    Station for screen and imaging system development
  Testing Gas ionization monitors for PS and SPS, new LHC IR BPM strip-line, fast BPM for LHC crab cavity monitoring, Longitudinal tomography for LHC, Quadrupolar pick-up, …

## Slide 14: In-Air DUT Area on Califes
Possibility to decrease the beam intensity to low or very low values (large beam sizes)
Possible use for developing Beam Loss monitors and Particle detectors
    Study of MIP response, Time response, Signal saturation
    Radiation hardness (Total Integrated Dose or Single Event)
Dark current from gun is used for irradiation
  Stability, low bunch charge (< 0.2 pc), long train 600 ns FWHM: 1800 bunches, higher emittance
  Rep. rate 5 Hz, 0.3 nC per pulse, 16 x 21 mm2 Gaussian size downstream to scattering screen

## Slide 15: Conclusion
Strong motivation for having a test facility at CERN beam instrumentation needs
All CERN (and outside CERN) projects and studies could benefit from such facility
It should be easily accessible, offering flexible set of beam parameters and reliable operation
A modified version of CALIFES could be implemented re-using existing CTF3 hardware (layout and cost have to be worked out in detail)
Excellent training ground for ‘young’ scientists (CERN and collaborators) and students

## Slide 16
Thanks for your attention

## Slide 17: Motivation for Testing screens
To compare light yield/saturation and spatial resolution of screens made of different materials (scintillators, Optical Transition Radiation) and thickness;
To choose an appropriate screen for a beam halo measurement in AWAKE experiment → same beam type (single p+ bunch of 400 GeV/c, 5·1010/2·1011 protons, RMS ~2 mm);
One first test in October 2015 – Now HRMT32

## Slide 18: Measurement setup
Diaphragm
beam
Al foils
Oct 2015 – HRMT30
June 2016 – HRMT32

## Slide 19: Screens tested
Scintillator:
  Alumina (Al2O3) – Purity: 96% & 99%
  Chromox (Al2O3:Cr2O3)
  thicknesses: 3 mm, 1 mm, 0.5 mm
  YAG – thicknesses: 0.1 mm, 0.5 mm
  both coated and uncoated
OTR
  Titanium, Aluminium, Silicon coated by aluminium & silver

## Slide 20: BLM test @ HRMT19-BLM2
LHC ionization chamber (IC) : 1.5l active vol.@ 1.1bar
Little Ionization Chamber (LIC) : 0.05l active vol.@ 1.1bar
for LHC in high losses region
Flat Ionization Chamber (FIC) : 0.05l active vol.@ 1.1bar
new detector for Booster
Tested with 3-5 shots using respectively
1, 36, 72, 144, 216, 288 nominal bunches
Measuring linearity and dynamic range

## Slide 21: BLM test @ HRMT19-BLM2
IC
FIC
LIC
FIC
LIC

## Slide 22: Possible Future BI tests @Hiradmat
Continue the test and characterization of new BLM sensor
Continue the test and characterization screens for BTV
  Limitation with in-air assembly system
    BTV system in secondary vacuum ?
    Reusing the last BTV in the line – adding a valve ?
    Consider as a permanent installation just upstream of the Exp. tables
  Characterizing screens better with an Optical line and Spectrometry and decay measurement
  Measurements in IR for Diffraction radiation monitoring for HL-LHC, FCC studies
Permanent installation for WCM, WCT, inductive BPM development
  Need a 30cm long Ceramic chamber
Permanent installation of BI DUT for new developments : 50cm reserve chamber
  SEM detector for TBIU/TBID renovation
  Electro-optical monitors for HL-LHC (pulling of optical fiber)

## Slide 23: Possible Future BI tests @Hiradmat
Quad
Trim
Trim
BCT
BPM
BTV
BPKG
Exp. A
Exp. B
Exp. C
BPM
Modifying this zone ?

## Slide 24: Gas-jet R&D with ULIV
Beam ionises gas molecules, ions are extracted by electric field
Sufficiently thin gas jet would allow 2D image: if not used as a gas scanner
Initial forwards momentum of gas jet separates gas jet ions from residual gas ions

## Slide 25: Gas-jet R&D with ULIV
Matter-wave focusing for a thin gas jet (down to Tens of micrometers) – Fresnel Zone plate principle
Design (ZEMAX) and fabrication of Apodised Photon Sieve reduces higher order diffraction, increases central maximum
The path difference between each successive light ring is equal to 1 wavelength (at the focal point) constructive interference.
Each zone is equal in area
Focal spot size is roughly the width of the narrowest (outer) zone
Compared to traditional lens: no spherical aberration, large chromatic aberration

## Slide 26: CLIC related BI developments
Transverse beam profile monitoring
  Developing OTR / ODR emittance station at ATF2
  R&D on gas jet technology at Cockcroft and CTF3
BLM developments
  Detector developments i.e. cherenkov fibers, MPPC, ..
  Understand the influence on BLM performances of
    RF breakdown in Acc. Cavity
    X-ray background in damping rings
Finalising developments at CTF3
  High resolution Cavity BPM
  DB strip-line BPM

## Slide 27: OTR interference studies
R. Kieffer
Experimental measurement of the shadowing of the electromagnetic field.