Influence of jets on femtoscopic correlation radii in ultrarelativistic heavy ion collisions
I. Lokhtin, L. Malinina, A. Snigirev
HYDJET++ heavy ion event generator: physics frames
Hadron production and correlation radii at RHIC
Hadron production and correlation radii at LHC
Outlook

---
HYDJET++ Monte-Carlo model for
relativistic heavy ion collisions
HYDJET++ - event generator to simulate heavy ion event as
merging two independent components (continuation of HYDJET):
soft hydro-type part (adapted FAST MC code) +
hard multi-parton part (PYQUEN partonic energy loss model,
medium-modified PYTHIA)
first version 2.0 (September 2008)
latest version 2.1 (September 2009)
http://cern.ch/lokhtin/hydjet++
I.Lokhtin, L.Malinina, S.Petrushanko, A.Snigirev, I.Arsene, K.Tywoniuk, Computing Physics Communications 180 (2009) 779

---
HYDJET & HYDJET++
(HYDrodynamics + JETs)
Calculating the number of hard NN sub-collisions Njet (b, Ptmin, √s) with Pt>Ptmin around its mean value according to the binomial distr.
Selecting the type (for each of Njet) of hard NN sub-collisions (pp, np or nn) depending on number of protons (Z) and neutrons (A-Z) in nucleus A according to the formula: Z=A/(1.98+0.015A2/3)
Generating the hard part by calling PYTHIA/PYQUEN njet times
If nuclear shadowing is switched on, the correction for PDF in nucleus is done by the accepting/rejecting procedure for each of Njet hard NN sub-collisions: by comparision of random number generated uniformly in the interval [0,1] with shadowing factor S ≤ 1, which is taken from the adapted impact parameter dependent parameterization based on Glauber-Gribov theory (K.Tywoniuk et al.,, Phys. Lett. B 657 (2007) 170).
Generating the soft part according to the corresponding “thermal” model (for b≠0 mean multiplicty is proportional to # of N-participants)
Junction of two independent event outputs (hard & soft) to event record

---
HYDJET++ (hard):
PYQUEN (PYthia QUENched)
        Initial parton configuration
        PYTHIA6.4 w/o hadronization: mstp(111)=0
↓
Parton rescattering & energy loss (collisional, radiative) + emitted g
 PYQUEN rearranges partons to update ns strings: ns call PYJOIN
↓
        Parton hadronization and final particle formation
        PYTHIA6.4 with hadronization: call PYEXEC
Three model parameters: initial QGP temperature T0, QGP formation time τ0 and number of active quark flavors in QGP Nf (+ minimal pT of hard process Ptmin)
I.P.Lokhtin, A.M.Snigirev, Eur. Phys. J. 45 (2006) 211

---
HYDJET++ (hard): physics frames
General kinetic integral equation:
1. Collisional loss and elastic scattering cross section:
2. Radiative loss (BDMS):
“dead cone” approximation for massive quarks:
%DELTA E (L,E) = int from {0} to {L}dx {dP} over {dx}(x)%lambda (x) {dE} over {dx} (x,E),~ {dP} over {dx}(x) = {1} over {%lambda (x) } exp(-x/%lambda (x))
{dE}over {dx} = {1} over {4T%lambda %sigma} int from %mu^{2}_{D} to t_{max} dt {d%sigma}over{dt}t, ~{d%sigma}over{dt} simeq C{2%pi %alpha_{s}^{2}(t)}over {t^{2}},~%alpha_{S}={12%pi}over {(33-2N_{f})ln(t/%LAMBDA^{2}_{QCD}) },~C=9/4 (%gg), 1 (gq), 4/9(qq)
{dE} over {dx} (m_{q}=0) = {2%alpha_{s}C_F}over {%pi%tau_{L}} int from {E_{LPM}sim %lambda_{g}%mu_{D}^{2}} to {E} d%omega left [ 1-y+{y^{2}} over {2} right] ln left lline cos (%omega_{1}%tau_{1}) right rline,~%omega_{1}=sqrt{i left( 1-y+{C_{F}over {3}y^{2} }right) {bar k} ln {16}over {bar k}}, ~{bar k}={%mu_{D}^{2}%lambda_{g}}over {%omega (1-y)}, ~%tau_{1}={%tau_{L}}over {2%lambda_{g}},~y={%omega}over {E},~C_{F}={4}over {3}
{dE} over {dx} (m_{q} neq 0) = {1}over {left( 1+(l%omega)^{3/2}right)^{2}} {dE} over {dx} (m_{q} = 0),~~~l = left( %lambda over %mu_{D}^{2}right)^{1/3}left({ m_{q}} over {E} right)^{4/3}

---
HYDJET++ (hard):
partonic energy loss MC procedure
 Distribution over jet production vertex V(r cos, r sin) at im.p. b
 Transverse distance between parton scatterings li=(i+1-i) E/pT
 Radiative and collisional energy loss per scattering
 Transverse momentum kick per scattering
{dN} over {d%psi dr}(b)={T_{A}(r_{1})T_A(r_{2})}over {int from {0} to {2%pi} d%psi int from {0} to {r_{max}} rdrT_{A}(r_{1})T_{A}(r_{2})}
{dP}over {dl_{i}}=%lambda^{-1}(%tau_{i+1}) exp(- int from {0} to {l_{i}} %lambda^{-1}(%tau_{i}+s)ds), ~~%lambda^{-1}=%sigma %rho
%DELTA E_{tot, i}=%DELTA E_{rad, i} + %DELTA E_{col, i}
%DELTA k^{2}_{t, i} = left( E-{t_{i}}over {2m_{0i}}right) ^{2}-left( p-{E}over {p}{t_{i}}over {2m_{0i}}-{t_{i}}over {2p}right)^{2}-m_{q}^{2}

---
HYDJET++ (soft): physics frames
Soft (hydro) part of HYDJET++ is based on the adapted FAST MC model:
Part I: N.S.Amelin, R.Lednisky, T.A.Pocheptsov, I.P.Lokhtin, L.V.Malinina,
A.M.Snigirev, Yu.A.Karpenko, Yu.M.Sinyukov, Phys. Rev. C 74 (2006) 064901
Part II: N.S.Amelin, R.Lednisky, I.P.Lokhtin, L.V.Malinina, A.M.Snigirev, Yu.A.Karpenko, Yu.M.Sinyukov, I.C.Arsene, L.Bravina, Phys. Rev. C 77 (2008) 014903
fast HYDJET-inspired MC procedure for soft hadron generation
multiplicities are determined assuming thermal equilibrium
hadrons are produced on the hypersurface represented by a parameterization
of relativistic hydrodynamics with given freeze-out conditions
chemical and kinetic freeze-outs are separated
decays of hadronic resonances are taken into account (360 particles from
SHARE data table) with “home-made'' decayer
written within ROOT framework (C++)
contains 15 free parameters (but this number may be reduced to 9)

---
HYDJET++ (soft):
main physics assumptions
A hydrodynamic expansion of the fireball is supposed ends by a sudden system breakup at given T and chemical potentials. Momentum distribution of produced hadrons keeps the thermal character of the equilibrium distribution.
 Cooper-Frye formula:
- FAST MC avoids straightforward 6-dimensional integration by using the special simulation procedure (like HYDJET): momentum generation in the rest frame of fluid element, then Lorentz transformation in the global frame → uniform weights → effective von-Neumann rejection-acception procedure.
Freeze-out surface parameterizations
1. The Bjorken model with hypersurface
  2. Linear transverse flow rapidity profile
3. The total effective volume for particle production at
-

---
HYDJET++ (soft):
hadron generation MC procedure
Initialization of input model parameters
The particle 3-momenta in the fluid element rest frame
  accord. to the probability
  by sampling uniformly distributed cos(θ*p) and φ*p
von Neumann rejection/acceptance procedure to account for diff. between the true and gen. (3-5)
 prob. Residual weight simulated x, p
are accepted W> ξ- a test variable randomly
simulated in [0,Wmax], otherwise -> 3
Calculation of Veff and particle densities
The mean multiplicities
Multiplicities by Poisson distr.
the hadron four-momentum is
boosted to the lab system
Simulation of particle freeze-out 4-coordinates in the fireball rest frame:on each hypersurface segment according to element
by sampling uniformly distributed r,η,φ
Calculation of the corresponding
collective flow four-velocities
The 2- and 3-body
resonance decays are simulated
(resonances – from SHARE table)
The particle 3-momenta in the fluid element rest frame
  accord. to the probability
  by sampling uniformly distributed cos(θ*p) and φ*p
von Neumann rejection/acceptance procedure to account for diff. between the true and gen. (3-5)
 prob. Residual weight simulated x, p
are accepted W> ξ- a test variable randomly
simulated in [0,W_max], otherwise-> 3
    Simulation of particle freeze-out 4-coordinates
    in the fireball rest frame :
 on each hypersurface segment accord. to element
        by sampling uniformly distributed r,η,φ

---
HYDJET++ (soft):
thermal and chemical freeze-outs
1. The particle densities at the chemical freeze-out stage are too high to consider
 particles as free streaming and to associate this stage with the thermal freeze-out
2. Within the concept of chemically frozen evolution, assumption of the conservation of
the particle number ratios from the chemical to thermal freeze-out :
3. The absolute values are determined by the choice
of the free parameter of the model: effective pion chemical potential at
Assuming for the other particles (heavier then pions) the Botzmann approximation :
Particles (stable, resonances) are generated on the thermal freeze-out hypersurface, the hadronic
composition at this stage is defined by the parameters of the system at chemical freeze-out

---
       HYDJET++ (soft): input parameters
1-5. Thermodynamic parameters at chemical freeze-out: Tch , {µB, µS, µC,µQ} (option to calculate
Tch, µB and µs using phenomenological parameterization µB(√s), Tch( µB) is foreseen).
6. Strangeness suppression factor γS ≤ 1 (the option to use phenomenological parameterization
γS (Tch, µB) is foreseen).
7-8. Thermodynamical parameters at thermal freeze-out: Tth , and µπ- effective chemical potential
of positively charged pions.
9-11. Volume parameters at thermal freeze-out: proper time τf , its standard deviation
(emission duration) Δτf , maximal transverse radius Rf .
12. Maximal transverse flow rapidity at thermal freeze-out ρumax .
13. Maximal longitudinal flow rapidity at thermal freeze-out ηmax .
14. Flow anisotropy parameter: δ(b) → uμ = uμ (δ(b),φ)‏
15. Coordinate anisotropy: ε(b) → Rf(b)=Rf(0)[Veff(ε(0),δ(0))/Veff(ε(b),δ(b))]1/2[Npart(b)/Npart(0)]1/3
For impact parameter range bmin-bmax: Veff(b)=Veff(0)Npart(b)/Npart(0), τf(b)=τf(0)[Npart(b)/Npart(0)]1/3

---
HYDJET++ : particle ratios at RHIC
Tch=0.165 GeV, µB=0.028 GeV,
µS=0.007 GeV, µQ=-0.001 GeV
Tth=0.100, 0.130, 0.165 GeV
Particle number ratios near mid-rapidity in central Au Au collisions

---
HYDJET++: radial flow at RHIC
 ρumax =1.1

---
HYDJET++: correlation radii at RHIC
        →
Weights for QS only: P12=C(q)=1+<cos qx>
8
5
4
Rout
0-5%
τf = 8 fm/c, Δτf =2 fm/c, Rf =10 fm
8
5
4
size 12{ ital "C" \( q\) ={ {N rSub { size 8{2} } \( k rSub { size 8{1} } ,k rSub { size 8{2} } \) } over {N rSub { size 8{1} } \( k rSub { size 8{1} } \) N rSub { size 8{2} } \( k rSub { size 8{2} } \) } } } {}
Rside
8
5
4
Rlong
side
CF=1+exp(-Ro2qo2 –Rs2qs2 -Rl2ql2 -2Rol2qo ql)
The corresponding correlation widths
are parameterized in terms of the
Gaussian correlation radii Ri
0.8
0.6
0.4
0.2
out  transverse
pair velocity vt
λ
long  beam
τf = 8 fm/c, Δτf =2 fm/c, Rf =10 fm

---
HYDJET++: rapidity spectra vs. event centrality at RHIC
Width of the spectra allows one to fix ηmax =3.3,
Centrality dependence of multiplicity allows one to fix ptmin=3.4 GeV/c and μπ=0.06

---
HYDJET++: transverse momentum spectra at RHIC
PYQUEN energy loss model parameters: T0(QGP)=300 MeV, τ0(QGP)=0.4 fm/c, Nf=2

---
The coordinate information for
“jet-induced” particles in HYDJET++
Transverse coordinate smearing of hadron formation in NN (XNN, YNN) << than in HI and can be neglected as a first approximation
(optionally one can randomize positions around the jet origin
Xj, Yj with radius 1 fm);
zh=τhard_processSinh(ηh)
th=τhard_processCosh(ηh)
τhard_process= 1/Q
x, y, z & t with assumption space rapidity =
coordinate rapidity – rather “toy” estimation.

---
Influence of jet fragmentation on
correlation radii at RHIC
At RHIC the
contribution of
jet part to total
multiplicity is
~ 15%.
 Influence of jets
on CFs is
neglidgible.
At RHIC the
contribution of
jet part to total
multiplicity is
~ 15%.
 Influence of jets
on CFs is
neglidgible.

---
Extrapolation of HYDJET++ parameters for
soft hydro-part to LHC
    SPS ( = 8.7 - 17.3 GeV)
▲ RHIC ( = 200 GeV)‏
    LHC ( = 5500 GeV)‏
■
○
The extrapolated values :
R ~ 11 fm,
 τ ~ 10 fm/c,
Δτ~ 3.0 fm/c,
ρ umax ~ 1.1,
Tth ~ 130 MeV.
Tch=170 MeV,
µB=0, µS=0, µQ=0 MeV
The extrapolated values :
R ~ 11 fm,
 τ ~ 10 fm/c,
Δτ~ 3.0 fm/c,
        ~ 1.1,
Tth ~ 130 MeV.
Tch=170 MeV,
µB=0, µS=0, µQ=0 MeV
 Extrapolation of HYDJET++ parameters for soft hydro-part to LHC
    SPS ( = 8.7 - 17.3 GeV)
▲ RHIC ( = 200 GeV)‏
    LHC ( = 5500 GeV)‏

---
     HYDJET++: hadron spectra at LHC
1000 events Pb+Pb (0-5 % centrality) at √s=5.5 A TeV
(default parameters, ptmin=7 GeV/c: ~55% jet contribution )

---
     HYDJET++: hadron spectra at LHC
1000 events Pb+Pb (0-5 % centrality) at √s=5.5 A TeV
(default parameters, ptmin=10 GeV/c: ~25% jet contribution)

---
Influence of jet fragmentation on
correlation radii at LHC
0-5%
Pure hydro (no jets):
R(LHC) > R(RHIC)
Ptmin=10 GeV/c
(~25% jet contribution):
R(LHC) ~ R(RHIC)
Ptmin=7 GeV/c
(~55% jet contribution): R(LHC) < R(RHIC)!
(especially Rlong)
due to the significant influence of “jet-induced” hadrons, which are emitted on shorter space-time scales than soft hadrons.
It seems quite
non-trivial prediction...
STAR
HYDJET++, ptmin>7 GeV/c
HYDJET++, ptmin>10 GeV/c
HYDJET++, hydro only

---
Outlook: jets.femtoscopy@LHC
Influence of jet quenching: softening the hadron spectra (mostly from partons coming from the center of the nuclear overlapping region, but much less for partons coming from peripheral regions) - “surface emission” at relatively high pT - can we see it on correlation radii?
Influence of nuclear shadowing: hardening the hadron spectra (since shadowing factor S depends on the jet production vertex r, parton production in the nuclear centre is more suppressed then in periphery; but the dependence S(r) is rather weak as compared with the r-dependence of quenching) - imitation of partial “surface emission” at intermediate pT - can we see it on correlation radii?
Note. In our best knowledge, the first study of the influence of hard processes on momentum correlations: G.Paic, P.K. Skowronski and B. Tomasik, Nucleonica 49 (2004) S89

---
BACKUP SLIDES

---
Nuclear geometry and QGP evolution
impact parameter b≡ |O1O2| - transverse distance between nucleus centers
(r1,r2)  TA(r1) ∗ TA(r2) (TA(b) - nuclear thickness function)
Space-time evolution of QGP, created in region of initial overlaping of colliding nuclei, is descibed by Lorenz-invariant Bjorken's hydrodynamics J.D. Bjorken, PRD 27 (1983) 140

---
Angular spectrum of gluon radiation
Three option for angular distribution of in-medium emitted gluons:
Collinear radiation
Small-angular radiation
(default)
Broad-angular radiation
%theta = 0
{dN^{g}} over {d%theta} prop sin %theta exp(-{{(%theta-%theta_{0})}^{2}} over {2%theta_{0}^{2}}), ~~%theta_{0} sim 5^{o}
{dN^{g}} over {d%theta} prop 1 over %theta

---
PYQUEN: mean energy loss
      (√s=5.5 A TeV, Pb+Pb, T0, QGP (b=0) = 1 GeV, 0=0.1 fm/c )
E-dependence
-dependence
L-dependence

---
PYQUEN: energy loss fluctuations
      (√s=5.5 A TeV, Pb+Pb, T0, QGP (b=0) = 1 GeV, 0=0.1 fm/c )

---
HYDJET++ (soft):
hadron multiplicities
1. The hadronic matter created in heavy-ion collisions is considered as a hydrodynamically expanding fireball with EOS of an ideal hadron gas.
2. “Concept of effective volume” T=const and µ=const: the total yield of particle species is .
3. Chemical freeze-out : T, µi = µB Bi + µS Si + µc Ci + µQ Qi ; T, µB –can be fixed by particle ratios, or by phenomenological formulas
4. Chemical freeze-out: all macroscopic characteristics of particle system are determined via a set of equilibrium distribution functions in the fluid element rest frame:

---
HYDJET++ (soft):
thermal charm production
Thermal charmed mesons J/ψ, D0, D0, D+, D- , Ds+, Ds-, Λc+, Λc- are generated within the statistical hadronization model
(feed-down corrections and meson 2- and 3- body decays are performed)
ND=γcNDth(I1(γcNDth)/I0(γcNDth)), NJ/ψ=γc2 NJ/ψth
γc - charm enhancement factor obtained from the equation:
Ncc=0.5γcNDth(I1(γcNDth)/I0(γcNDth))+γc2 NJ/ψth
where number of c-quark pairs Ncc is calculated with PYTHIA (the factor K=2 is applied to take into account
NLO pQCD corrections)
-

---
The block structure of HYDJET++
particles.data,
tabledecay.txt
(particle properties)
RunInputHydjet
(input model parameters)
     RunHadronSource.cxx
(generate events, create trees)
RunOutput.root
(particle output information for each
event and global output parameters)
        Tree “td”
(final particle output)
 ROOT macros
 (to produce histograms)
ROOT
Histograms

---
  Number of events to generate
10
  C.m.s. energy per nucleon pair, fSqrtS [GeV]
200.
  Atomic weigth of nuclei, fAw
197.
  Flag of type of centrality generation, fBfix (=0 is fixed by fBfix, >0 distributed [fBfmin, fBmax])
1
  Minimum impact parameter in units of nuclear radius, fBmin
0.
  Maximum impact parameter in units of nuclear radius, fBmax
0.55
  Fixed impact parameter in units of nuclear radius, fBfix
0.
  Parameter to set random number seed, fSeed (=0 the current time is used, >0 the value fSeed is used)
0
  Temperature at chemical freeze-out, fT [GeV]
0.165
  Chemical baryon potential per unit charge, fMuB [GeV]
0.0285
  Chemical strangeness potential per unit charge, fMuS [GeV]
0.007
  Chemical charm potential per unit charge, fMuC [GeV] (used if charm production is turned on)
0.
  Chemical isospin potential per unit charge, fMuI3 [GeV]
-0.001
  Temperature at thermal freeze-out, fTthFO [GeV]
0.1
  Chemical potential of pi+ at thermal freeze-out, fMu_th_pip [GeV]
0.06
  Proper time proper at thermal freeze-out for central collisions, fTau [fm/c]
8.
  Duration of emission at thermal freeze-out for central collisions, fSigmaTau [fm/c]
2.
  Maximal transverse radius at thermal freeze-out for central collisions, fR [fm]
10.
  Maximal longitudinal flow rapidity at thermal freeze-out, fYlmax
3.3
  Maximal transverse flow rapidity at thermal freeze-out for central collisions, fUmax
1.1
  Momentum azimuthal anizotropy parameter at thermal freeze-out, fDelta
0.1
  Spatial azimuthal anisotropy parameter at thermal freeze-out, fEpsilon
0.05
  Flag to specify fDelta and fEpsilon values, fIfDeltaEpsilon (=0 user's ones, >=1 calculated)
0.
  Flag to switch on/off hadron decays, fDecay (=0 decays off, >=1 decays on)
1.
  Low decay width threshold fWeakDecay[GeV]: width<fWeakDecay decay off, width>=fDecayWidth decay on; can be used to switch off weak decays
0.
  Flag to choose rapidity distribution, fEtaType (=0 uniform, >0 Gaussian with the dispersion Ylmax)
1.
  Flag to use calculated T_ch, mu_B and mu_S as a function of fSqrtS, fTMuType (=0 user's ones, >0 calculated)
0.
  Strangeness supression factor gamma_s with fCorrS value (0<fCorrS <=1, if fCorrS <= 0., then it will be calculated)
1.
  Flag to include statistical charm productio, fIcharm (=0 no charm production, >=1 charm production)
0
  Flag to include jet (J)/jet quenching (JQ) and hydro (H) state production, fNhsel (0 H on & J off, 1 H/J on & JQ off, 2 H/J/HQ on, 3 J on & H/JQ off, 4 H off & J/JQ on)
2
  Flag to suppress the output of particle history from PYTHIA, fIedit (=1 only final state particles; =0 full particle history from PYTHIA)
1
  Flag to switch on/off nuclear shadowing, fIshad (0 shadowing off, 1 shadowing on)
1
  Minimal pt of parton-parton scattering in PYTHIA event, fPtmin [GeV/c]
3.4
  Initial QGP temperature for central Pb+Pb collisions in mid-rapidity, fT0 [GeV]
0.3
  Proper QGP formation time in fm/c, fTau0 (0.01<fTau0<10)
0.4
  Number of active quark flavours in QGP, fNf (0, 1, 2 or 3)
2
  Flag to fix type of partonic energy loss, fIenglu (0 radiative and collisional loss, 1 radiative loss only, 2 collisional loss only)
0
  Flag to fix type of angular distribution of in-medium emitted gluons, fIanglu (0 small-angular, 1 wide-angular, 2 collinear).
0
RunInputHydjetRHIC200
(input parameter file for Au+Au
collisions at RHIC, default)
7 input parameters;
19 free model parameters
(may be reduced to 13) +
PYTHIA parameters;
12 flags.

---
 Number of events to generate
10
  C.m.s. energy per nucleon pair, fSqrtS [GeV]
5500.
  Atomic weigth of nuclei, fAw
207.
  Flag of type of centrality generation, fBfix (=0 is fixed by fBfix, >0 distributed [fBfmin, fBmax])
1
  Minimum impact parameter in units of nuclear radius, fBmin
0.
  Maximum impact parameter in units of nuclear radius, fBmax
0.57
  Fixed impact parameter in units of nuclear radius, fBfix
0.
  Parameter to set random number seed, fSeed (=0 the current time is used, >0 the value fSeed is used)
0
  Temperature at chemical freeze-out, fT [GeV]
0.170
  Chemical baryon potential per unit charge, fMuB [GeV]
0.
  Chemical strangeness potential per unit charge, fMuS [GeV]
0.
  Chemical charm potential per unit charge, fMuC [GeV] (used if charm production is turned on)
0.
  Chemical isospin potential per unit charge, fMuI3 [GeV]
0.
  Temperature at thermal freeze-out, fTthFO [GeV]
0.13
  Chemical potential of pi+ at thermal freeze-out, fMu_th_pip [GeV]
0.
  Proper time proper at thermal freeze-out for central collisions, fTau [fm/c]
10.
  Duration of emission at thermal freeze-out for central collisions, fSigmaTau [fm/c]
3.
  Maximal transverse radius at thermal freeze-out for central collisions, fR [fm]
11.
  Maximal longitudinal flow rapidity at thermal freeze-out, fYlmax
4.
  Maximal transverse flow rapidity at thermal freeze-out for central collisions, fUmax
1.1
  Momentum azimuthal anizotropy parameter at thermal freeze-out, fDelta
0.1
  Spatial azimuthal anisotropy parameter at thermal freeze-out, fEpsilon
0.05
  Flag to specify fDelta and fEpsilon values, fIfDeltaEpsilon (=0 user's ones, >=1 calculated)
0.
  Flag to switch on/off hadron decays, fDecay (=0 decays off, >=1 decays on)
1.
  Low decay width threshold fWeakDecay[GeV]: width<fWeakDecay decay off, width>=fDecayWidth decay on; can be used to switch off weak decays
0.
  Flag to choose rapidity distribution, fEtaType (=0 uniform, >0 Gaussian with the dispersion Ylmax)
1.
  Flag to use calculated T_ch, mu_B and mu_S as a function of fSqrtS, fTMuType (=0 user's ones, >0 calculated)
0.
  Strangeness supression factor gamma_s with fCorrS value (0<fCorrS <=1, if fCorrS <= 0., then it will be calculated)
1.
  Flag to include thermal charm production, fIcharm (=0 no charm production, >=1 charm production)
0.
  Flag to include jet (J)/jet quenching (JQ) and hydro (H) state production, fNhsel (0 H on & J off, 1 H/J on & JQ off, 2 H/J/HQ on, 3 J on & H/JQ off, 4 H off & J/JQ on)
2
  Flag to suppress the output of particle history from PYTHIA, fIedit (=1 only final state particles; =0 full particle history from PYTHIA)
1
  Flag to switch on/off nuclear shadowing, fIshad (0 shadowing off, 1 shadowing on)
1
  Minimal pt of parton-parton scattering in PYTHIA event, fPtmin [GeV/c]
7.
  Initial QGP temperature for central Pb+Pb collisions in mid-rapidity, fT0 [GeV]
0.8
  Proper QGP formation time in fm/c, fTau0 (0.01<fTau0<10)
0.1
  Number of active quark flavours in QGP, fNf (0, 1, 2 or 3)
0
  Flag to fixe type of partonic energy loss, fIenglu (0 radiative and collisional loss, 1 radiative loss only, 2 collisional loss only)
0
  Flag to fix type of angular distribution of in-medium emitted gluons, fIanglu (0 small-angular, 1 wide-angular, 2 collinear).
0
RunInputHydjetLHC5500
(input parameter file for Pb+Pb
collisions at LHC, default)
7 input parameters;
19 free model parameters
(may be reduced to 13) +
PYTHIA parameters;
12 flags.

---
  td->Branch("nev",&nev,"nev/I"); // event number
  td->Branch("Bgen",&Bgen,"Bgen/F"); // generated impact parameter
  td->Branch("Sigin",&Sigin,"Sigin/F"); // total inelastic NN cross section
  td->Branch("Sigjet",&Sigjet,"Sigjet/F"); // hard scattering NN cross section
  td->Branch("Ntot",&Ntot,"Ntot/I"); // total event multiplicity
  td->Branch("Nhyd",&Nhyd,"Nhyd/I"); // multiplicity of hydro-induced particles
  td->Branch("Npyt",&Npyt,"Npyt/I"); // multiplicity of jet-induced particles
  td->Branch("Njet",&Njet,"Njet/I"); // number of hard parton-parton scatterings
  td->Branch("Nbcol",&Nbcol,"Nbcol/I"); // mean number of NN sub-collisions
  td->Branch("Npart",&Npart,"Npart/I"); // mean number of nucleon-participants
  td->Branch("Px",&Px[0],"Px[npart]/F"); // x-component of the momentum, in GeV/c
  td->Branch("Py",&Py[0],"Py[npart]/F"); // y-component of the momentum, in GeV/c
  td->Branch("Pz",&Pz[0],"Pz[npart]/F"); // z-component of the momentum, in GeV/c
  td->Branch("E",&E[0],"E[npart]/F"); // energy, in GeV
  td->Branch("X",&X[0],"X[npart]/F"); // x-coordinate at emission point, in fm
  td->Branch("Y",&Y[0],"Y[npart]/F"); // y-coordinate at emission point, in fm
  td->Branch("Z",&Z[0],"Z[npart]/F"); // z-coordinate at emission point, in fm
  td->Branch("T",&T[0],"T[npart]/F"); // proper time of particle emission, in fm/c
  td->Branch("pdg",&pdg[0],"pdg[npart]/I"); // Geant particle code
  td->Branch("Mpdg",&Mpdg[0],"Mpdg[npart]/I"); // Geant code of mothers (-1 for primordials)
  td->Branch("type",&type[0],"type[npart]/I")	// particle origin (=0 – from hydro, >0 – jets)
  td->Branch("Index",&Index[0],"Index[Ntot]/I"); // unique zero based index of the particle
  td->Branch("MotherIndex",&MotherIndex[0],"MotherIndex[Ntot]/I"); // index of mother (-1 for primordials)
  td->Branch("NDaughters",&NDaughters[0],"NDaughters[Ntot]/I"); // number of daughters
  td->Branch("FirstDaughterIndex",&FirstDaughterIndex[0],"FirstDaughterIndex[Ntot]/I"); // index of first daughter
  td->Branch("LastDaughterIndex",&LastDaughterIndex[0],"LastDaughterIndex[Ntot]/I"); // index of last daughter
  td->Branch("pythiaStatus",&pythiaStatus[0],"pythiaStatus[Ntot]/I"); // PYTHIA status code (-1 for hydro)
  td->Branch("final",&final[0],"final[Ntot]/I"); // an integer branch: =1 for final particles, =0 for decayed particles
RunOutput.root
(tree structure)

---
HYDJET++ version 2.1 (update note)
Version 2.1 is completed in September 2009
1. Option to get output from full particle history for PYTHIA/PYQUEN generated particles (including partons and strings) is introduced.
   It is controlled by the new flag:
   fIedit=1 - only final state particles are presented in event output,
   fIedit=0 - full particle history from PYTHIA/PYQUEN is produced.
   By default the full particle history is not produced, fIedit(D=1).
2. Option to produce thermal charmed particles (J/ψ and D mesons) is introduced. Total number of c-quarks is calculated with PYTHIA, and then thermal charmed hadrons are generated within the statistical hadronization model.
   It is controlled by the new flag:
   fIcharm=0 - thermal charm production is switched off,
   fIcharm>=1 - thermal charm production is switched on),
   By default thermal charmed particle production is switched off fIcharm(D=1).
   The new input parameter fMuC (chemical charm potential) is introduced.
3. A number of technical improvements and bug fixing are implemented.

---
 HYDJET++: elliptic flow at RHIC