## Slide 1
Focusing and de-focusing magnets are alternatively placed along the ring so that the transverse motion can be controlled
Introduction
Betatron Tune
(m,n,l : integer)
must be avoid
The number of the oscillation in one turn
Real-Time Betatron Tune Correction with the Precise Measurement of Magnet Current
Current Ripple DI/I
Experimental Setup at the J-PARC MR
The AD conversion of the current deviation DI @ each regulator
All digitized DI s are sent to the corrector via optical fibers
The FPGA board converts all DI s to the ν.
Motivation
Large current ripple causes v fluctuation
Dominant current ripple is at < 100 Hz
Direct ν measurement is not possible during the user operation
Precise current regulation is the key to controlling the
The magnet current regulators are located at 3 different buildings
Not predictable
Real-Time Correction
The current ripple is affected by the fluctuation of the grid voltage and frequency
The current regulator of the corrector is located at the 1 building
FPGA : Altera Cyclone V Soc (System-on-a-Chip)
DDR3 : 2 GB, 1 GB for User, 1 GB for OS
Digital IO: LVTTL and Optical
Analog Out : 4ch 16 bit DAC
Others: Giga-bit Ethernet, On-board flash, mSD
Overview
FPGA Board
AD Board
AD Converter : TI ADS8568, 8 CH, 16 Bit, 10 kSPs
Digital IO : Optical, Serial Communication
Others : Daisy Chain
Firmware Design
Comparison with the Direct measurement
ν Correction using the System
Direct ν Measurement
Frequency measurement of the betatron oscillation excited by the stripline kicker.
Direct Measurement
Real-Time prediction with DI s (this system)
The tendencies of the time variations are roughly same
Constraint at the J-PARC MR
Possible reasons for the discrepancies
The precision of the direct measurement
Not all magnet currents are used.
8 current regulators are chosen.
・All 96 bending magnets
・96 ( out of 216 ) quadrupole magents
①
②
③
⑤
④
① Receive DI data from the current regulators
② Convert DI data to Dν and sent it to the corrector
③ Store DI data in the DDR3 connected to FPGA
④ Move DI data to the DDR3 connected to the CPU with DMA
⑤ Send DI data to the upper system
On-line Monitoring
ν correction
Yoshinori Kurimoto, Tetsushi Shimogawa and Daichi Naito
High Energy Accelerator Reaserach Organization
Direct measurement with the corrector turned on.
Sensitive to the ν variations below 250 Hz
The proposed system can reduce the v fluctuation by 43 %
Betatron Oscillation
Real-Time ν Correction with Magnet Current
OFF
ON
Time (s)
Time (s)
Conclusion
Abstract - The betatron tune, which is defined as the number of transverse oscillations in one turn of a ring accelerator, must be precisely controlled by electrode magnets. The ripple of the magnet current directly displaces the betatron tune from its designated value. We have developed a system that corrects the betatron tune displacement using the measured magnet current at the J-PARC (Japan Proton Accelerator Research Complex) Main Ring. We adopted Field Programmable Gated Arrays (FPGA) to convert from the measured magnet current to the betatron tune in real time. Using the system, we have decreased the fluctuation of the betatron tune by approximately 43 % at the frequencies less than 250 Hz.
Quad.
Bend.
Current Regulators
x’
X phase space
x
Ex. nx = integer
Dipole Errors are accumulated
Resonance Condition of
Magnets
Betatron Oscillation
I
B
How to control the
Proposed Method