## Slide 1: Orbit correction status and update for HL-LHC
D. Gamba, R. De Maria, R. Tomas
Thanks to M. Fitterer
73rd HiLumi WP2 Meeting 09/08/2016

## Slide 2: Outline
Aim of the orbit correction studies.
Quick review of earlier works.
Current needs.
Reinventing the wheel:
  My way to get into the subject.
Some new/old results.
  Comparison with earlier studies
Plans for the future.

## Slide 3: Orbit correction for the HL-LHC
Orbit correction studies are needed for:
Specify new orbit corrector strength, ramp rate, acceleration rate.
  Need to study the transfer function error and hysteresis.
Evaluate residual static and dynamic orbit offset after correction, at:
  IP for luminosity loss and fill to fill reproducibility
  Triplet and matching section quadrupoles for aperture
  Crab cavities to be compatible with beam loading
Orbit correction studies taking into account:
  Needs for crossing, separation, offset and luminosity scan
  Tolerances for survey and mechanical transverse and longitudinal alignment.
  Precision, accuracy and reliability of BPMs.

## Slide 4: Previous studies
Detailed study from M. Fitterer:
  19/01/2015: Crossing scheme and orbit correction in IR1/5 for HL-LHC (link)
  Based on HL-LHC optics v1.0 and v1.1
  It includes crossing and separation scheme, knobs for aligning the crab cavities, hysteresis considerations, …
HL-LHC optics v1.2
  24/07/2015 (link) and 25/09/2015 (link)
  Changes in gradient, length, position of IT elements.
  Updated values for orbit correction knobs and corrector strength requirements.
So far orbit correction focused at the IT up to D2 in order to correct triplet misalignments and transfer function errors
  + guess based on LHC data on the matching section correction.
A list of orbit-related talks/paper is being prepared here

## Slide 5: Review of orbit correction for HL-LHCV1.2
Assumptions:
Crossing angle and separation (round and flat)
  Operational for HL-LHC scenario (link)
Static IP Offset for Exp. Movement ± 2 mm
  Using all correctors
Lumi scan at beta*=70cm
  Use correctors to decouple B1/B2.
VDM scan at beta*=30m
Crab cavity alignment (WP2 meeting 19/6/15):
  Alignment should be possible within ±0.5 mm
  Max allowed orbit excursion up to ± 2 mm for short time (losses up to 80 kW).
  Max acceptable orbit excursion up to ± 1 mm.
  Aim is to keep the beam within ±0.5 mm.

## Slide 6: Aperture and knobs effects
 | Coil aperture | Beam1 aperture | H,V2full gaps | Sep. knob | Crossing Knob | Crab shift knob | Crab slope knob | Offset knob
 | [mm] |  | [mm] | [mm] | [mm] | [mm] | [mm] | [mm]
TAXS |  | Circle | 60, 60 | 0.8 | 6.1 | 0.0 | 0.0 | 2.0
MQXFA.[AB]1 | 150 | Octagon | 99, 99 | 0.8 | 11.2 | 0.0 | 0.0 | 2.4
MQXFB.[AB]2 | 150 | Octagon | 119, 119 | 1.2 | 16.7 | 0.2 | 0.0 | 3.6
MQXFA.[AB]3 | 150 | Octagon | 119, 119 | 0.8 | 16.6 | 0.4 | 0.0 | 2.8
MBXF | 150 | Octagon | 119, 119 | 0.5 | 15.5 | 0.5 | 0.0 | 2.4
TAXN |  | Circle | 85, 85 | 0.2 | 5.5 | 0.9 | 0.0 | 3.0
MBRD | 105 | Octagon | 84, 84 | 0.1 | 3.3 | 1.0 | 0.0 | 3.3
MCBRD | 105 | Octagon | 84, 84 | 0.1 | 1.7 | 1.0 | 0.1 | 3.4
MCBYY | 90 | Octagon | 70.8,70.8 | 0.0 | 0.1 | 1.0 | 0.5 | 4.0
MQYY | 90 | Octagon | 70.8,70.8 | 0.0 | 0.0 | 1.0 | 0.5 | 3.9
TCLMB.5 |  | RectEllipse | 57.8, 48 | 0.0 | 0.0 | 0.4 | 0.2 | 3.7
MCBY[HV].5 | 70 | RectEllipse | 57.8, 48 | 0.0 | 0.0 | 0.0 | 0.0 | 3.6
MQY.5 | 70 | RectEllipse | 57.8, 48 | 0.0 | 0.0 | 0.2 | 0.1 | 3.5
TCLMC.6 |  | RectEllipse | 45.1,35.3 | 0.0 | 0.0 | 0.0 | 0.0 | 2.3
MCBC[HV].6 | 56 | RectEllipse | 45.1,35.3 | 0.0 | 0.0 | 0.0 | 0.0 | 2.1
MQML.6 | 56 | RectEllipse | 45.1,35.3 | 0.0 | 0.0 | 0.0 | 0.0 | 2.1
1 Either Beam screen or beam pipe;
2 Mechanical tolerances already removed. Rectellipse types are exchanges the H,V orientation depending on the polarity.
  From 25/09/2015 HL-LHC v1.2 (link)

## Slide 7: Aperture and knobs effects
  From 24/07/2015 HL-LHC v1.2 (link) + updated corrector spec.(8/08/2016)
IP crossing, separation, offset (x: ±295 μrad, , s: ±0.75 mm, o: ±2.0 mm)
beam based alignment of crab cavities: ccp, ccm (shift): ±0.5 mm, ccs (slope): ±0.25 mm
IT alignment and transfer function errors (err): ±0.5 mm transverse, ±10 mm longitudinal, ±2x10-3 relative gradient error, ±2x10-3 D2 relative field error (±2 σ from uniform errors).
orbit correction from the arc (from LHC data to confirmed): arc 0.7 Tm;
lumi scan knobs (single beam IP shift for 100μm)
 | x-scheme [Tm] |  |  | cc alignment [Tm] |  |  | err [Tm] | arc [Tm] | lumi [Tm] | summary [Tm] |  | 
name | x | s | o | ccp | ccm | ccs | err | arc | lumi | tot | max | margin [%]
MCBX1 | 0.14 | 0.11 | 1.16 | 0.19 | 0 | 0 | 0.92 | 0 | 0 | 2.42 | 2.5 | 3.3
MCBX2 | 0.07 | 0.05 | 0.79 | 0.19 | 0 | 0 | 1.40 | 0 | 0 | 2.17 | 2.5 | 1.5
MCBX3 | 2.11 | 0.2 | 0.94 | 0.45 | 0.15 | 0 | 0.78 | 0 | 0 | 4.43 | 4.5 | 1.4
MCBRD4 | 2.97 | 0.09 | 0 | 0.28 | 0.15 | 0.52 | 0.04 | 0.35 | 0.27 | 4.60 | 4.5 → 5 | -2 → 8.0
MCBYY4 | 1.49 | 0.04 | 0.12 | 0.42 | 0.42 | 0.92 | 0 | 0.35 | 0.20 | 4.74 | 4.5 → 5 | -5 → 5.2
MCBY5 | 0 | 0 | 1.35 | 0.40 | 0.40 | 0.35 | 0 | 0 | 0 | 2.46 | 2.7 | 8.8
MCBY5 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.7 | 0 | 0.7 | 2.7 | 74
MCBC6 | 0 | 0 | 0.46 | 0 | 0 | 0 | 0 | 0.7 | 0 | 1.16 | 2.8 → 2.1 | 58 → 44
MCBC7 | 0 | 0 | 1.40 | 0 | 0 | 0 | 0 | 0.7 | 0 | 2.10 | 2.8 | 25

## Slide 8: Comparison global correction vs segment
Past: correction up to D2 of triplet misalignment + guess on matching section correction.
Now: first reproduce the previous results and:
  Simplify the treatment of the problem.
  Extend the correction to neighbor sections including part of the arcs.
  Study if a global correction could be beneficial.
  Be able to verify the next optics versions.

## Slide 9: Optics under study: presqueeze v1.2 (thin)
MS.10R5.B1
MS.10L5.B1
In the following simulation we will consider the area around IP5 within the first powered sextupoles.

## Slide 10: Optics under study: presqueeze v1.2 (thin)
2 mm half separation
0.295 mrad half cros. angle
In the following simulation we will consider the area around IP5 within the first powered sextupoles.

## Slide 11: Simplified treatment of the problem
In first approximation the problem is linear and two are the main equations:
  Orbit variation along the a beamline (Δx) is linear with respect to misalignments/errors (Δe)
  And with respect to correctors strengths (Δc)
  The linear coefficients form the matrices RMe and RMc
The response matrices can be measured/extracted by exciting the MAD-X model and measuring the response on the relevant optics parameters.
One is interested only to correct some key* locations. E.g. in case of misalignments:
  Zero orbit variation at the boundaries of the line (to be “transparent” to the ideal machine)
  No variation of position and crossing angle at the IP
  No orbit excursion at the crab cavity location.
The problem is simplified to the following equation:
  Where the * matrices are a subset of the measured matrices RMe and RMc keeping only the important rows.
The residual orbit at other locations is simply:

## Slide 12: Max and variance of strengths/excursions
The resulting strength of each corrector needed to cope with all misalignment is:
A possible definition of worse scenario could then be:
From linear algebra one also has that:
From witch it is possible to extract the square root of the variances (≈ r.m.s)

## Slide 13: Verify that the system is “linear enough”
One can verify that the measured matrices are able to describe the problem by testing the previous procedure with MAD-X itself.
Here a random machine with
  10^-3 [m] transverse and longitudinal quadrupoles and dipoles misalignments
  10^-3 [rad] roll of quadrupoles and dipoles.
  10^-3 error on the transfer function of dipoles.

## Slide 14: Effect of misalignments on open-line orbit
Assuming the worst scenario on B1: sum of the absolute orbit excursions due to different class of imperfections:
  e.g. ITquad_DX is the effect of all IT quadrupoles being misaligned of 1 mm and such that all errors are “constructive”.
  Unphysical! The beam is “starting” by hypothesis from 0 and collects all the errors.
Apertures from MAD
Apertures minus 12 sigma envelope and abs orbit taken by crossing scheme.

## Slide 15: Effect of correctors on orbit (B1)
Absolute orbit excursion induced by each horizontal kicker available in the line.
  Unphysical!

## Slide 16: Correction of each class of error (Horizontal)
Computed absolute corrector strengths needed in order to correct the worse scenario
  Correction of position/angle at IP; zero orbit at the crab cavities; zero boundary conditions.
MAX
Crossing scheme
B1
B2

## Slide 17: Effect on orbit after correction (Horizontal)
Computed the worse scenario on orbit. Note change of scale, see later for explanations.
B1
B2

## Slide 18: Correction of each class of error (Vertical)
Computed absolute corrector strengths needed in order to correct the worse scenario
  Correction of position/angle at IP; zero orbit at the crab cavities; zero boundary conditions.
B1
B2

## Slide 19: Effect on orbit after correction (Vertical)
Computed the worse scenario on orbit. Note change of scale, see later for explanations.
B1
B2

## Slide 20: First observations
As already seen in previous studies (link) the main contribution to residual orbit and correctors strength comes from quadrupoles misalignments.
D1 and D2 imperfections don’t seem to be critical:
  Note that we were comparing 1 mm transverse offsets with 1e-3 relative field errors.
In the previous plots the orbit outside the IT is asymmetric.
  The right part seems to be affected by bigger orbit excursions.
  One can have a closer look error by error.

## Slide 21: Effect of IT quads misalignments (DX) on B1

## Slide 22: Effect of IT quads misalignments (DY) on B1

## Slide 23: Effect of Ext. quads misalignments (DX) on B1
No constraints in arc BPMs: optimistic for strength,
pessimistic for orbit.

## Slide 24: Effect of Ext. quads misalignments (DY) on B1
No constraints in arc BPMs: optimistic for strength,
pessimistic for orbit.

## Slide 25: Effect of D1/D2 errors on B1 (Horizontal)

## Slide 26: Effect of D1/D2 errors on B1 (Vertical)
The effect of dipoles roll on the vertical plane is similar to the effect of field error in the horizontal.

## Slide 27: Comparison with the Monte Carlo approach
Used in the previous studies:
  Define specific knobs (crossing, separation, offset, lumiscan) and specific procedures for imperfection correction (i.e. “short” and “lim” strategy used in link).
  Generate N (e.g. 10.000) machines in MAD and perform orbit correction.
  Extract extreme values and r.m.s. of correctors/orbit.
In order to compare the results but using the matrices approach:
  Define a matrix of misalignments according to desired distribution in external application (MATLAB now, Python future)
  Simple matrix multiplication for the “correction” matrices
    See introductory slides
  Do necessary statistics on the output values.
Note: much less “a-priori knowledge” in the latest method!
  Need to further improve the correction strategies.

## Slide 28: Comparison with the Monte Carlo approach
Example from the study from M.Fitterer (link):
  ±0.5 mm uniformly distributed IT transverse misalignments (* optics v1.0) (correction method “lim”)
 | MCBX1 [Tm] |  | MCBX2 [Tm] |  | MCBX3 [Tm] |  | MCBRD [Tm] | 
 | max | std | max | std | max | std | max | std
short | 1.31 | 0.46 | 2.55 | 0.7 | 1.44 | 0.39 | 0.07 | 0.02
lim | 0.91 | 0.3 | 0.8 | 0.31 | 1.05 | 0.29 | 0.4 | 0.12
 | MCBX1 [Tm] |  | MCBX2 [Tm] |  | MCBX3 [Tm] |  | MCBRD [Tm] | 
 | max | std | max | std | max | std | max | std
Monte Carlo | 0.79 | 0.30 | 0.72 | 0.27 | 0.97 | 0.29 | 0.47 | 0.15
Analytical | 0.89 | 0.30 | 0.81 | 0.27 | 1.18 | 0.29 | 0.52 | 0.15
Repeating the same exercise with current simplified method

## Slide 29: Comparison with previous studies
  *From presentation of 24/07/2015 HL-LHC v1.2 (link)
  **Computed with analytical method presented here
IT alignment and transfer function errors (err): ±0.5 mm transverse, ±10 mm longitudinal, ±2x10-3 relative gradient error, ±2x10-3 D2 relative field error. Method “short” in *.
Same assumptions here, but no relative quadrupole gradient error included.
  Note: no D1/D2 rolls included here.
 | 2σ [Tm] | 2σ [Tm] | 2σ [Tm] | 2σ [Tm] | max [Tm] | arc [Tm]
name | err* | arc* | Err** | arc** | err** | arc**
MCBX1 | 0.92 | 0 | 0.598 | 0.004 | 0.926 | 0.006
MCBX2 | 1.40 | 0 | 0.537 | 0.003 | 0.845 | 0.005
MCBX3 | 0.78 | 0 | 0.574 | 0.008 | 1.227 | 0.013
MCBRD4 | 0.04 | 0.35 | 0.232 | 0.004 | 0.597 | 0.008
MCBYY4 | 0 | 0.35 | 0 | 0.143 | 0 | 0.325
MCBY5S | 0 | 0 | 0 | 0.073 | 0 | 0.17
MCBY5 | 0 | 0.7 | 0 | 0.073 | 0 | 0.21
MCBC6 | 0 | 0.7 | 0 | 0.091 | 0 | 0.219
MCBC7 | 0 | 0.7 | 0 | 0.168 | 0 | 0.395
MCBC8 | - | - | 0 | 0.532 | 0 | 0.939
MCBC9 | - | - | 0 | 0.388 | 0 | 0.941

## Slide 30: Comparison with knobs
 | Sep. knob* | Crossing Knob* | Crab shift knob* | Crab slope knob* | Offset Knob* | Err** 2σ | Arc** 2σ | Err** max | Arc** max
 | [mm] | [mm] | [mm] | [mm] | [mm] | [mm] | [mm] | [mm] | [mm]
TAXS | 0.8 | 6.1 | 0.0 | 0.0 | 2.0 | 0 | 0 | 0 | 0
MQXFA.[AB]1 | 0.8 | 11.2 | 0.0 | 0.0 | 2.4 | 0.074 | 0 | 0.112 | 0
MQXFB.[AB]2 | 1.2 | 16.7 | 0.2 | 0.0 | 3.6 | 0.819 | 0.003 | 1.023 | 0.006
MQXFA.[AB]3 | 0.8 | 16.6 | 0.4 | 0.0 | 2.8 | 1.654 | 0.009 | 1.743 | 0.013
MBXF | 0.5 | 15.5 | 0.5 | 0.0 | 2.4 | 1.736 | 0.011 | 1.678 | 0.012
TAXN | 0.2 | 5.5 | 0.9 | 0.0 | 3.0 | 0.481 | 0.013 | 0.442 | 0.014
MBRD | 0.1 | 3.3 | 1.0 | 0.0 | 3.3 | 0.157 | 0.008 | 0.203 | 0.014
MCBRD | 0.1 | 1.7 | 1.0 | 0.1 | 3.4 | 0.023 | 0 | 0.027 | 0
MCBYY | 0.0 | 0.1 | 1.0 | 0.5 | 4.0 | 0 | 0.024 | 0 | 0.03
MQYY | 0.0 | 0.0 | 1.0 | 0.5 | 3.9 | 0 | 0.079 | 0 | 0.093
TCLMB.5 | 0.0 | 0.0 | 0.4 | 0.2 | 3.7 | 0 | 0.463 | 0 | 0.409
MCBY[HV].5 | 0.0 | 0.0 | 0.0 | 0.0 | 3.6 | 0 | 0.577 | 0 | 0.518
MQY.5 | 0.0 | 0.0 | 0.2 | 0.1 | 3.5 | 0 | 0.577 | 0 | 0.537
TCLMC.6 | 0.0 | 0.0 | 0.0 | 0.0 | 2.3 | 0 | 0.945 | 0 | 0.868
MCBC[HV].6 | 0.0 | 0.0 | 0.0 | 0.0 | 2.1 | 0 | 1.082 | 0 | 1.083
MQML.6 | 0.0 | 0.0 | 0.0 | 0.0 | 2.1 | 0 | 1.089 | 0 | 1.049
MCBC[HV].7 | - | - | - | - | - | 0 | 2.056 | 0 | 2.002
MQM.[AB]7 | - | - | - | - | - | 0 | 2.061 | 0 | 2.061
MCBC[HV].8 | - | - | - | - | - | 0 | 2.412 | 0 | 3.342
MQML.8 | - | - | - | - | - | 0 | 2.499 | 0 | 3.541
MCBC[HV].9 | - | - | - | - | - | 0 | 0.673 | 0 | 0.716
MQMC.9 | - | - | - | - | - | 0 | 0.832 | 0 | 0.952

## Slide 31: So far
Still getting into the topic.
Built a simplified procedure to attack the problem.
  So far only used on HL-LHC presqueeze optics v1.2
The results presented here seem to be consistent with earlier studies, but:
  Correction procedures still to be improved. What is the goal? Reduce the residual orbit? The corrector strengths? Which ones?
  How realistic is such a correction? Should re-establish study on BPMs performance.

## Slide 32: e.g. lower one corrector.
The correction matrix may have a “null space”
  One can create knobs to lower one or more correctors (and increase the others/the orbit)
Here trying to null the use of MCBRD[HV]4; Horizontal B1:

## Slide 33: e.g. lower one corrector.
Here trying to null the use of MCBRD[HV]4. Same assumptions as before **
 | 2σ [Tm] | 2σ [Tm] | max [Tm] | arc [Tm]
name | Err** | arc** | err** | arc**
MCBX1 | 0.962 | 0.015 | 1.907 | 0.024
MCBX2 | 1.408 | 0.023 | 2.925 | 0.039
MCBX3 | 0.74 | 0.012 | 1.662 | 0.02
MCBRD4 | 0.054 | 0.002 | 0.146 | 0.004
MCBYY4 | 0 | 0.143 | 0 | 0.325
MCBY5S | 0 | 0.073 | 0 | 0.17
MCBY5 | 0 | 0.073 | 0 | 0.21
MCBC6 | 0 | 0.091 | 0 | 0.219
MCBC7 | 0 | 0.168 | 0 | 0.395
MCBC8 | 0 | 0.532 | 0 | 0.939
MCBC9 | 0 | 0.388 | 0 | 0.941
 | Err** 2σ | Arc** 2σ | Err** max | Arc** max
 | [mm] | [mm] | [mm] | [mm]
TAXS | 0 | 0 | 0 | 0
MQXFA.[AB]1 | 0.074 | 0 | 0.112 | 0
MQXFB.[AB]2 | 0.61 | 0.011 | 1.079 | 0.022
MQXFA.[AB]3 | 0.965 | 0.018 | 1.224 | 0.026
MBXF | 0.445 | 0.014 | 0.485 | 0.019
TAXN | 0.115 | 0.014 | 0.115 | 0.016
MBRD | 0.041 | 0.008 | 0.056 | 0.015
MCBRD | 0.009 | 0 | 0.014 | 0
MCBYY | 0 | 0.024 | 0 | 0.03
MQYY | 0 | 0.079 | 0 | 0.093
TCLMB.5 | 0 | 0.463 | 0 | 0.409
MCBY[HV].5 | 0 | 0.577 | 0 | 0.518
MQY.5 | 0 | 0.577 | 0 | 0.537
TCLMC.6 | 0 | 0.945 | 0 | 0.868
MCBC[HV].6 | 0 | 1.082 | 0 | 1.083
MQML.6 | 0 | 1.089 | 0 | 1.049
MCBC[HV].7 | 0 | 2.056 | 0 | 2.002
MQM.[AB]7 | 0 | 2.061 | 0 | 2.061
MCBC[HV].8 | 0 | 2.412 | 0 | 3.342
MQML.8 | 0 | 2.499 | 0 | 3.541
MCBC[HV].9 | 0 | 0.673 | 0 | 0.716
MQMC.9 | 0 | 0.832 | 0 | 0.952

## Slide 34: Next studies
Re-verify knobs.
  Define new knobs able to “remove” power from single correctors or to reduce residual orbit.
Apply procedure to the new HL-LHC design.
Review power supplies ramp rate and acceleration rate taking into account:
  separation collapse
  lumi scan
  orbit feedback
(time scale to be discussed)

## Slide 35: Thank you!