## Slide 1: Vivado HLS
An Overview and not much else…
JJRussell

## Slide 2: Outline
Vivado is a big system
  UG902 – This is the user’s guide
    It is > 700 pages (lots of pictures, but not meant for skimming)
  UG871 – Tutorial Guide
Impossible to cover in 1 hour  take the 20,000 foot view of the
  Development process
  Refinement process
    Time optimization
    Resource optimization
Focus more on the What can be done rather than the How
Go through a simple example
If you retain as much as, “Oh, I know you can do something like that”, it will have served some purpose

## Slide 3: Development Process
Vivado HLS is an Eclipse based IDE
  This allows you to get going quickly
  There are ways to script the development process
You break your code into 2 pieces
  A test harness
    This runs only on the host
  One top-level procedure
    This is the code eventually destined for the FPGA, but
    Only after you debug and simulate on a friendly host

## Slide 4: Development Process
The test harness provides test vectors to the FPGA destined code
The initial development and testing is completely host-based in 3 steps
  No FPGA/hardware is necessary
Step 1. C-Simulator simulates the FPGA using strictly C-code – < minutes
  A fast edit/compile/link/test cycle
Step 2. Synthesis stage – ~10 seconds - 10 minutes
  Produces the VHDL (or Verilog)
  This gives good (but not perfect) timing and resource usage
Step 3. Can now run an analysis and co-simulator on this VHDL/Verilog
  The analysis produces accurate resource usage
  The co-simulator produces detailed timing (waveform)
  Both the analysis and co-simulation are much slower
Final step is producing a downloadable bit file – ~hours

## Slide 5: What it does
Vivado HLS allows one to write algorithms in
  C/C++
  System C.
  OpenCL seems to working itself into the mix
  Would recommend stick to C++
    Looks like the best supported
Just throwing vanilla C/C++ at Vivado HLS will not work
  These are sequential languages
    FPGAs get their power from parallelism
  FPGAs are not constrained to natural 8/16/32/64 - bit boundaries
    Any size integer or fixed point are possible
  Some constructs natural to an FPGA have no counterparts in C/C++
    e.g. multi-port memory
  C/C++ is like a visitor in a foreign country
    They may speak the language, but do not appreciate the culture
    Your job  Absorb/understand the culture,
    Vivado’s role  Help you in bridging this cultural gap

## Slide 6: Decorated C++ How to bridge the gap
Two tools are
  Language augmentations
  Pragmas
Language augmentations
    These are C++ classes during the simulation stage, then…
    Mapped to specific hardware constructs during synthesis
  Most common examples are arbitrary precision classes
    e.g. ap_uint<12>
    Easier in C++ than C because other classes (like printing) understand them
    Advise using typedef’s to make these easy to change
      typedef ap_uint<12> Adc;

## Slide 7: Decorated C++ Bridging the Gap - Pragmas
Pragmas, a very large topic
  Allow creation of multi-port memories
  Loop unrolling
  Pipelining
  Interface specification
  Array partitioning
  Array reshaping
  Dataflow
  Resource control
  …and way more than can be covered
Gaining an understanding of their usage is a key component to success

## Slide 8: Some Fine Print
The language is C/C++, but the target is an FPGA
  Algorithms and styles that work in a sequential machines may or may not translate
Currently,
  A clear leaning towards pipeline style processing
  This may just reflect traditional FPGA applications
Buffering and decimation are trickier
  Xilinx seems to have realized this
  Better tools/techniques to deal seem to be coming

## Slide 9: Even Finer Print
More suited to algorithmic code, not the IO
  Depend on VHDL to handle decoding of raw bit streams
  Currently depend on VHDL to do the DMA to the processor
    This may be relieved in SDSoc – but not for the raw input bit streams
    Locally we refer to this as coding in the donut hole
Have had issues dealing with large codes
  Had to break the waveform extraction code handling 128 channels in 4 x 32 code blocks
    May have learned, current DUNE compression code handles 256 channels
      Synthesis ~ 150 seconds
      Export (with analysis) ~ 30 minutes
      Haven’t built a viable bit-file yet, nothing to report here
Model of 1 test harness and 1 FPGA destined module is limiting
  In the waveform extraction code, would have like to have a 2nd module that recombined the 4 x 32 output streams.
  SDSoc may be addressing this

## Slide 10: Example of Code Development
Will use a very simple example to illustrate the process.
The general cycle is
  Write the test harness and top level code
  Compile and debug it
  Synthesis it to see where the time and resources are going
  Adjust the code
  Add pragmas
Will largely ignore the first two steps
Emphasis again
  You never leave the comfort of your host machine during these steps

## Slide 11: But First… The Anatomy of the IDE

## Slide 12
Synthesis View
Notes: First thing to notice, are the DEBUG, SYNTHEIS, ANALYSIS selections in the upper right corner. These control the major views. You spend most of your time in the Synthesis View, this is where code development takes place. In this view you have a row of buttons. The two most commonly used ones are marked These run the C-simulation and Synthesis.

## Slide 13
Debug View
Notes: Typical full screen gdb based debugger. Find it way to tedious. I generally just run it from the command line.

## Slide 14
Analysis View

## Slide 15: Simple Example
The example is from the Vivado Example area
  Would encourage you to look there
  These are simple examples
    Just illustrate a particular aspect or technique
    They are available off the initial welcome screen
The example merely sums the elements of an array
  Will serve as a way to
    Navigate through the myriad of displays
    Demonstrate a couple of common techniques

## Slide 16: Memory Bottleneck
dout_t array_mem_bottleneck(din_t mem[N]) Note the use of types
{ (N = 128)
dout_t sum=0;
SUM_LOOP: for(int i=2;i<N;++i)  Note the label, this is how one
{ scopes pragmas
sum += mem[i];  Asking for 3 memory references
sum += mem[i-1]; on each iteration. This creates
sum += mem[i-2]; a memory access bottleneck
}
return sum;
}

## Slide 17: Bottleneck
Poor performance
  ~2 cycles per iteration
  The goal is usually 1 cycle
  Note the resource usage

## Slide 18: From Analysis View

## Slide 19: Better Code
dout_t array_mem_perform(din_t mem[N]) {
din_t tmp0, tmp1, tmp2;
dout_t sum = 0;
tmp0 = mem[0];  Move 2 of the references
tmp1 = mem[1]; out of the loop
SUM_LOOP:for (int i = 2; i < N; i++) {
tmp2 = mem[i];  Now, only 1 memory reference
sum += tmp2 + tmp1 + tmp0; per iteration
tmp0 = tmp1;
tmp1 = tmp2;
}
return sum;
}

## Slide 20: Better Code  Better Performance
Improved performance
  1 cycle per iteration
    The extra cycles are loop entrance and exit latency
  Resource Usage has barely changed
    Up by 1 LUT
  This is a good trade off

## Slide 21: Pragmas Overview
To further improve performance, need to help Vivado out by using pragmas
There are many, many pragmas and lots of variations for any given pragma
You can restrict the scope of a pragma
  Functions
  Loops
  Regions
  There are a few exceptions, like PIPELINE which applies all the way down a hierarchy

## Slide 22: Pragmas How to specify
Specification of pragmas can be either
  Directly in the code
    This is appropriate for
      Those unlikely to change, e.g. pragmas defining the interface
      Code to be released
  In named solutions
    This is information (think include files) that are kept separate from the code, but selectively applied to it
    Can be any number of solutions; with multiple solutions
      You can play What if games without hacking the source code.
      Define solutions for different target FPGAs
    You select one of the solutions when you synthesis

## Slide 23: Pragmas Uses
There are 2 main uses
  Improve performance
  Control resource usage
While some pragmas are directly aimed at one or the other of these
  There are some (ARRAY_RESHAPE) that address both
There is a third use
  These attempt to make the diagnostic information more useful
  They do not affect the generated code
    e.g. TRIPCOUNT can be used to specify a min,max and average count on variable iteration loops
      This helps make the timing more meaningful
And yet a fourth use
  These help when Vivado is unable to correctly infer properties
    e.g. DEPENDENCY can be used to express or negate a variable dependency

## Slide 24: Popular Pragmas RESOURCE
Can be used to specify details of the memory
  Memory can be implemented in
    Block Ram (BRAM)
    LUT (LUTRAM)
  It can be any of
    RAM
    ROM
    STREAM
    FIFO
  It may be (where it makes sense)
    Single ported
    Couple of different styles of dual porting
Example
  #pragma HLS RESOURCE variable=arr core=RAM_2P_BRAM
Caveat, this pragma does a lot more than this

## Slide 25: Popular Pragmas ARRAY_PARTITION
Adds ports to memory
  This can relieve memory bottlenecks
  Almost always needed when trying to achieve parallelism
The ports can be added differently to different dimensions of multi-dimensional arrays
They can have 1 of 3 styles
  Complete
  Cyclic  This is the most common
  Block
Example
  #pragma ARRAY_PARTITION variable=d2 dim=2 cyclic factor=4

## Slide 26: Popular Pragmas DATAFLOW
The DATAFLOW pragma allows 2 or more functions/loops/regions to execute in parallel
  Think of it as analogous to multi-threading
Useful in packetized processing, e.g.
  Read in a packet  Process It  Write it out
Unlike multi-threading, overhead is not an issue
  This can be used at very small granularity
Caveat – DATAFLOW, PIPELINE and UNROLL come with lots of terms and conditions
  These must be understood to be used effectively
    No just clicking on the I agree box

## Slide 27: Popular Pragmas INLINE,PIPELINE,UNROLL
Functions can be inlined
  This can help in some cases / hurt in others
  Example
    #pragma HLS INLINE (off)
Functions, loops can be PIPELINED
  Allows these to accept more input as soon as they are able
  Example
    #pragma HLS PIPELINE
Loop unrolling
  Determines the extent to which a loop will be unrolled (or not)
  Example
    #pragma HLS UNROLL factor=4

## Slide 28: Language Augmentations
These are C++ classes that map onto hardware constructs
Examples are
  ap_int<n>, ap_uint<n> - arbitrary precision integer
    These have many bit related methods associated with them
      Bit extract
      Bit concatenation
      Bit reversal
    These are heavily used
      The appropriate width improves time and resource usage
    Also can specify fixed point types
    Strongly encourage that these are captured in typedef’s.
      Make that more than strongly  Do it!
  hls_stream – stream variables
  ap_fifo – fifo variables

## Slide 29: Exploring the Effect of Pragmas
The next few slides show what happens when the code is tweaked with appropriate pragmas.
This simple piece of code can be vastly improved
Of course there is a cost to be paid, so watch both
  The time
  The resource usage

## Slide 30
Using Pragmas:: Synthesis View

## Slide 31
Analysis Summary View

## Slide 32
Analysis Performance View
Reads

## Slide 33
Analysis View - Resource

## Slide 34: Performance Comparison
Can compare the effects of the different solutions
Timing comparisons
Resource comparisons

## Slide 35: Just to show you just can’t turn knobs The following solutions increase the loop unrolling x2 each time. Solution 7 – Unroll x 16 Solution 8 – Unroll x 32 Solution 10 - Complete

## Slide 36: Observations
Vivado HLS can be finicky
  Sometimes it does what you want/expect
  Other times, you wind up with a puzzled look
It can be unstable
  Seemingly innocuous changes can led to large changes in time and resource usage
    I’ve adopted the never make more than 1 change at a time rule
Development is largely a 1 or 2 person activity
  Not exclusively a property of Vivado HLS, but it is contributor
  Stems from the dedicated way FPGAs are used
    Not like a CPU where you have multiple processes and tasks running that come from a cadre of developers

## Slide 37: Going Forward
Xilinx is betting on Vivado HLS to make FPGAs into a viable choice
  It is not just the skill set – i.e. more C/C++ than VHDL coders
  It is the complexity and size of what you want to do
    Will overwhelm you and become unmaintainable
    This akin to coding in assembler vs C/C++
      Some things are appropriate to do in assembler, but…
      No way all of it can be in assembler
  Portability of moving to different FPGAs
For those of us using the RCE,
  The FPGA is where the power of the RCE lies
While there is no free lunch,
  This may make it somewhat cheaper