## Slide 1: Testbeam plans Aug. 24-31

## Slide 2: Devices to test
Clicpix: 50 micron thick planar sensor with active edge
  Bias scan
  Threshold scan
  Edge efficiency measurements
  Rotation scan
Alice investigator (t.b.c)
  Efficiency measurements
  More bias scan points
Cracow SOI chip
  High statistics bias scans on different chips
Timepix3
  300 micron assembly
  675 micron assembly

## Slide 3: Timepix 3 measurements
300 micron:
  Bias scan perpendicular (~30minutes?)
  Threshold scan perpendicular (~30minutes?)
  Edge scan?
300+675micron: angle + bias scan
  -80 to 80 deg, 2deg steps = 81 steps
  5, 10, 20, 30, 40, 50, 75, 100, 150, 200V = 10 steps
 2x810 measurement points: (~800-1000 minutes ) x2
= (13 - 16 hours ) x2
Which 300 micron assembly to use?
  8th telescope plane (spare) broken?
  Use the 7th plane?  worse tracking resolution for the SOI chip

## Slide 4
7 Telescope reference planes
DUT position: CLICpix, Timepix3, Investigator
SOI

## Slide 5: Preliminary schedule
1) Wednesday night to Wednesday morning (between telescope planes 6 and 7, can take data in parallel with other measurements):
SOI pix from Cracow with new firmware, more assemblies, different settings (parameter scans)
2) Wednesday night to Friday:
CLICpix 50 um assembly —> DAQ integration, threshold scan, bias scan, rotation
3) Friday afternoon to Monday:
Timepix3 300 um assembly —> threshold, bias scans, rotation, edge scan?
Timepix3 thick-sensor assembly rotation and bias scans with lower rate
4) Monday morning to Wednesday morning:
ALICE Investigator —> efficiency studies, high-statistics data with more bias points