## Slide 1: LHC Status and Outlook
Mike Lamont for the LHC team

## Slide 2
2016: Overcome a few problems…
WEASEL
PS MAIN POWER SUPPLY
SPS BEAM DUMP
Limited to 96 bunches per injection
2220 bunches per beam cf. 2750

## Slide 3
Thereafter: reasonably quick ramp-up in number of bunches
  Electron cloud still very much with us but effects under control
1034
BCMS
Reduced crossing angle
1.5 x 1034 cm-2s-1

## Slide 4: Design luminosity reached
  Reduced beta* and lower transverse beam sizes from the injectors compensating the lower number of bunches

## Slide 5: Beam from injectors
Standard 25 ns scheme
PS circumference
BCMS (Batch Compression, Merging & Splitting)
Lower intensity, smaller bunches from PSB
Lower than nominal emittance taken a step further
Acknowledgements to Steve Hancock

## Slide 6: Good peak performance
Beta* = 40 cm
BCMS
Reduced crossing angle, bunch length
Limited in number of bunches
Limited in bunch intensity (injection kicker vac.)
Bunch population | ~1.1e11
Number of bunches | 2220
Beta* | 40 cm
Crossing angle | 280 urad
Emittance (BCMS) | ~2.0 um
Peak (CMS) | ~1.5e34 cm-2s-1
Crossing angle reduced end September
X-angle [urad] | F
370 | 0.59
280 | 0.7

## Slide 7: Luminosity lifetime
Excellent luminosity lifetime – main component - proton loss to inelastic collisions in ATLAS, CMS and LHCb
Enjoying effects of synchrotron radiation damping

## Slide 8: Availability: 11th June – 8th September
79 days proton physics
Stable Beams 58%!
Andrea Apollonio et al

## Slide 9: Premature dumps
Almost half of the fills ended by operations
Start to worry about optimum fill length!
Ben Todd

## Slide 10: Fault analysis

## Slide 12: This with > 250 MJ per beam
Operations underpinned by superb performance of the machine protection system

## Slide 13: Limitations
SPS beam-dump
  No of bunches per injection limited to 96
  Total number of bunches: 2200
Injection kicker
  Outgassing from ceramic connection (MKI8D-Q5)
  Bunch population limited to around 1.1 x 1011
Electron cloud
  Still significant heat-load within cryogenic limits
UFOs
  Frequency has happily conditioned down

## Slide 14: Electron Cloud - Heat Loads
Very slow electron cloud reduction despite significant doses
Improved handling of dynamics by cryogenics
Drives instabilities – running with high chromaticity, octupoles and damper gain to successfully counter
Courtesy G. Iadarola

## Slide 15: UFOs
Clear conditioning effect
Not known if conditioning will be lost after venting
At the present rate UFOs are at a very acceptable rate

## Slide 16: Run 2
Complementary objectives:
Prepare for HL-LHC and post-LS2 LIU era
Prepare for 7 TeV operation - operation at over 6.5 TeV in 2018 being explored – see Chamonix
Extended Year End Technical Stop – 20 weeks
- CMS pixel upgrade - dipole exchange in sector 12

## Slide 17: Main Options 2017
Optics
  ATS versus nominal
  From a performance perspective nothing to choose between them (beta*, squeeze length etc.)
  Might worry about commissioning time – strategic choice
Squeeze
  40 cm or lower (33 cm seems popular)
  Luminosity levelling options being explored
Nominal 25 ns versus BCMS
Limits from SPS beam dump and LHC injection kicker vacuum should be lifted

## Slide 18: Possible 2017/18 parameters
 | Nominal | BCMS | BCMS+
Beta* (1/5) [cm] | 40 | 40 | 33
Half crossing angle [urad] | 185 | 155 | 170
No. of colliding bunches | 2736 | 2448 | 2448
Proton per bunch | 1.25e11 | 1.25e11 | 1.25e11
Emittance into SB [um] | 3.2 | 2.3 | 2.3
Bunch length [ns] | 1.05 | 1.05 | 1.05
Peak luminosity [cm-2s-1] | ~1.4e34 | ~1.7e34 | ~1.9e34
Peak pile-up | ~37 | ~51 | ~56
Luminosity lifetime [h] | ~21 | ~15 | ~14
Naively applying 2016’s overall Hübner factor gives between 45 and 60 fb-1
Final configuration following discussion at Evian and Chamonix

## Slide 19: Machine status - summary
Excellent and improved system performance
Magnets behaving well at 6.5 TeV
Good beam lifetime through the cycle
Operationally things well under control
Magnetically reproducible as ever
Optically good, corrected to excellent
Aperture is fine and compatible with the collimation hierarchy.
Collimation can take anything that’s thrown at it

## Slide 20: Conclusions
Reasonable peak performance
  Well above design luminosity (squeeze, beams from injectors)
  Still margin for improvement in Run 2
Good integrated delivery
  Excellent availability (normal caveats apply)
  Electron cloud conditioning slowly
  Fortunate that UFOs have conditioned down
Interesting to note that a machine of this complexity with such a challenging operational regime can work pretty well!

## Slide 21
Looking good | Keep an eye on
Availability and R2E | Electron cloud
Injectors | Instabilities
Optics | Losses at start of fill
Magnet model, magnets at 6.5 TeV | Beam-beam, DA
Aperture | Emittance growth
Reproducibility, stability | Earth faults
Nominal cycle++, turn-around | Robustness of protection devices
Losses through cycle | 
Machine protection, QPS | 
ADT, RF, Power converters | 
Beam instrumentation, feedbacks | 
Collimation, beam cleaning | 
LBDS, Injection | 
Cryogenics | 
Vacuum, UFOs, Beam induced heating | 

## Slide 22
2016: 1% rms beta-beating, C- of 0.0002 and lot more to celebrate!

## Slide 23
Courtesy Daniel Valuch

## Slide 24: Lifetime
Isolated case during intensity ramp up
After reduction of crossing angle.
Mitigation deployed
Lifetime very good in Run 2. Not clear how to scale to HL-LHC.
Belen

## Slide 25: Lifetime in Stable Beams
NB first hour – was worse with higher bunch population in 2012