## Slide 1
Possible improvement of the CLIC accelerating structure.
From CLIC_G to CLIC_K.
25.03.2009
Alexej Grudiev

## Slide 2: Outline
Current CLIC accelerating structure: CLIC_G
Compact coupler design with damping
Comparison of rounded and not rounded cell geometry
New type of waveguide damping for lower pulsed surface heating – a ridged waveguide damping
Constant Sc structure as an optimally tapered accelerating structure

## Slide 3: Parameters of CLIC_G
Structure | CLIC_G
Frequency: f [GHz] | 12
Average iris radius/wavelength: <a>/λ | 0.11
Input/Output iris radii: a1,2 [mm] | 3.15, 2.35
Input/Output iris thickness: d1,2 [mm] | 1.67, 1.00
Group velocity: vg(1,2)/c [%] | 1.66, 0.83
N. of reg. cells, str. length: Nc, l [mm] | 24, 229
Bunch separation: Ns [rf cycles] | 6
Luminosity per bunch X-ing: Lb× [m-2] | 1.22×1034
Bunch population: N | 3.72×109
Number of bunches in a train: Nb | 312
Filling time, rise time: τf , τr [ns] | 62.9, 22.4
Pulse length: τp [ns] | 240.8
Input power: Pin [MW] | 63.8
Pin/CtPp1/3[MW/mm ns1/3] | 18
Max. surface field: Esurfmax [MV/m] | 245
Max. temperature rise: ΔTmax [K] | 53
Efficiency: η [%] | 27.7
Figure of merit: ηLb× /N [a.u.] | 9.1

## Slide 4: WDS cell geometry
Waveguide Damped Structure
(WDS) 2 cells
Minimize E-field
Minimize H-field
Provide good HOM damping
Provide good vacuum pumping

## Slide 5: TD24_vg1.8_disk

## Slide 6: TD24_vg1.8_disk transverse wake

## Slide 7: Parameters of TD24_vg1.8_disk
Structure | CLIC_G | TD24
Frequency: f [GHz] | 12 | 12
Av. iris radius/wavelength: <a>/λ | 0.11 | 0.11
In/Output iris radii: a1,2 [mm] | 3.15, 2.35 | 3.15, 2.35
In/Output iris thickness: d1,2 [mm] | 1.67, 1.00 | 1.67, 1.00
Group velocity: vg(1,2)/c [%] | 1.66, 0.83 | 1.62, 0.81
N. of reg. cells, str. length: Nc, l [mm] | 24, 229 | 24, 229
Bunch separation: Ns [rf cycles] | 6 | 6
Lumi. per bunch X-ing: Lb× [m-2] | 1.22×1034 | 1.22×1034
Bunch population: N | 3.72×109 | 3.72×109
Number of bunches in a train: Nb | 312 | 312
Filling time, rise time: τf , τr [ns] | 62.9, 22.4 | 64.2, 23.1
Pulse length: τp [ns] | 240.8 | 242.7
Input power: Pin [MW] | 63.8 | 66.0
Pin/CtPp1/3[MW/mm ns1/3] | 18 | 18.6
Scmax [MW/mm2] | 5.4 | 5.6
Max. surface field: Esurfmax [MV/m] | 245 | 240
Max. temperature rise: ΔTmax [K] | 53 | 62
Efficiency: η [%] | 27.7 | 26.5
Figure of merit: ηLb× /N [a.u.] | 9.1 | 8.7
Parameters assuming coupler overhead

## Slide 8: Electric field coupler

## Slide 9: Magnetic field coupler with damping
Courtesy of
R. Zennaro
compact coupler (CC)

## Slide 10: CLIC_G + compact coupler
CLIC_G
CLIC_GCC
Prototype is under design

## Slide 11: Rounded and non-rounded cells
Rounded cell Rr=2.5mm
Non-rounded cell
CLIC_G middle cell | rounded | non-rounded
Q(Cu) | 7430 | 6820
vg/c [%] | 1.32 | 1.32
r’/Q [LinacΩ/m] | 17670 | 17750
Es/Ea | 1.9 | 1.9
Hs/Ea [mA/V] | 2.43 | 2.43
Sc/Ea2 [mA/V] | 0.32 | 0.32
~8% difference
in Q-factor

## Slide 12: Rounded and non-rounded structure
CLIC_G NDS rounded
CLIC_G NDS non-rounded

## Slide 13: Rounded and non-rounded damped cells
CLIC_G rounded
idw = 8.75 mm
adw = 11.25 mm
CLIC_G non-rounded
idw = 8.2 mm
adw = 10.1 mm
TD18 cell

## Slide 14: Rounded and non-rounded CLIC_GCC
CLIC_GCC
CLIC_GCC non-rounded

## Slide 15: Ridged waveguide for HOM damping
Rectangular waveguide
Double-ridged waveguide
Ridged waveguide
CLIC_GLDT (low ΔT)
idw = 7.5 mm
adw = 9.25 mm
idw
adw

## Slide 16: EM field configuration in RWDS
Electromagnetic field configuration on the surface of a
Ridged waveguide damped structure (RWDS) cell
Electric field
Magnetic field
Sc

## Slide 17: Structures with ridged waveguide damping
CLIC_GLDT : a = 3.15 – 2.35 mm
CLIC_K : a = 3.3 – 2.35 mm

## Slide 18: Wake field of proposed structures

## Slide 19: Transverse impedance

## Slide 20: Parameters of the structures
Structure | CLIC_G | CLIC_GCC | CLIC_GCC non-rounded | CLIC_GLDT | CLIC_K
Frequency: f [GHz] | 12 | 12 | 12 | 12 | 12
Average iris radius/wavelength: <a>/λ | 0.11 | 0.11 | 0.11 | 0.11 | 0.113
Input/Output iris radii: a1,2 [mm] | 3.15, 2.35 | 3.15, 2.35 | 3.15, 2.35 | 3.15, 2.35 | 3.3, 2.35
Input/Output iris thickness: d1,2 [mm] | 1.67, 1.00 | 1.67, 1.00 | 1.67, 1.00 | 1.67, 1.00 | 1.67, 1.00
Group velocity: vg(1,2)/c [%] | 1.66, 0.83 | 1.66, 0.83 | 1.67, 0.84 | 1.68, 0.86 | 1.97, 0.86
N. of reg. cells, str. length: Nc, l [mm] | 24, 229 | 25, 225 | 25, 225 | 25, 225 | 25, 225
Bunch separation: Ns [rf cycles] | 6 | 6 | 6 | 6 | 6
Luminosity per bunch X-ing: Lb× [m-2] | 1.22×1034 | 1.22×1034 | 1.22×1034 | 1.22×1034 | 1.28×1034
Bunch population: N | 3.72×109 | 3.72×109 | 3.72×109 | 3.72×109 | 3.94×109
Number of bunches in a train: Nb | 312 | 312 | 312 | 316 | 326
Filling time, rise time: τf , τr [ns] | 62.9, 22.4 | 64.7, 22.4 | 63.8, 22.0 | 63.0, 21.6 | 58.4, 21.6
Pulse length: τp [ns] | 240.8 | 242.6 | 241.4 | 242.1 | 242.5
Input power: Pin [MW] | 63.8 | 59.8 | 61.5 | 61.3 | 64.6 (65.2)
Pin/CtPp1/3[MW/mm ns1/3] | 17.9 | 16.8 | 17.3 | 17.3 | 17.5
Scmax [MW/mm2] | 5.4 | 5.1 | 5.3 | 5.2 | 5.1
Max. surface field: Esurfmax [MV/m] | 245 | 233 | 230 | 230 | 244
Max. temperature rise: ΔTmax [K] | 53 | 48 | 45 | 39 | 37
Efficiency: η [%] | 27.7 | 28.8 | 28.1 | 28.5 | 29.5 (29.2)
Figure of merit: ηLb× /N [a.u.] | 9.1 | 9.4 | 9.3 | 9.4 | 9.6
(95% of Cu conductivity)

## Slide 21: Proposal for 4 new test structures
CLIC_GCC: proposal has been already made to do TD25_vg1.7_ccsd (see: http://indico.cern.ch/getFile.py/access?contribId=1&resId=1&materialId=slides&confId=37450 )
CLIC_GCC non-rounded: TD25_vg1.7_disk - an optimized version of TD24-type made in standard disk technology the same as TD18-type.
CLIC_GLDT: TD25_vg1.7_dLDT – structure with ridged waveguide damping
CLIC_K:
  T25_vg2_disk – non-damped structure with higher input group velocity and stronger tapering than CLIC_G
  TD25_vg2_disk – damped version

## Slide 22: RF breakdown constraints
Chart: Structure Number
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 12
X-band TWS, BDR=1e-6/pulse/m | 1.8522 | 1.9003 | 2.0528 | 1.8878 | 1.7908 | 1.5871 | 1.5626 | 2.1331 | 1.3788 | 1.38 | 2.25 | 1.7674 | 2.3169
X-band SWS, BDR=1e-6/pulse/m | 1.2064 | 1.8344 | 2.2291 | 2.1049
Chart: Structure Number
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 12
X-band TWS, BDR=1e-6/pulse/m | 5.7835 | 5.8499 | 6.0305 | 5.6275 | 5.062 | 4.8591 | 5.0526 | 7.1954 | 4.8388 | 3.7531 | 5.248 | 5.2718 | 5.4699
X-band SWS, BDR=1e-6/pulse/m | 0 | 0 | 0 | 0
Chart: Structure Number
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 12
X-band TWS, BDR=1e-6/pulse/m | 135.4243 | 157.0473 | 194.1224 | 159.7384 | 148.0538 | 126.2945 | 129.7908 | 180.3588 | 108.783 | 83.2683 | 248.3468 | 160.2979 | 252.1285
X-band SWS, BDR=1e-6/pulse/m | 131.163 | 165.8891 | 242.3425 | 304.0459
Constraints @ {200ns, BDR=10-6 bpp/m} ~ {180ns, BDR=3x10-7 bpp/m}