## Slide 1: DAQ for BIG
BIG=joint Beam Instrumentation wG

## Slide 2
Common solutions as far as possible for SP and DP protoDUNEs
Configuration of the beam instrumentation still evolving, should be fixed by September
Mixed Hadron+electron beams
Beam momenta from 1 to 7-10 GeV/c
At low energies electrons dominate
Crowded and relatively short beam line
Need to reduce the data throughput selecting events with trigger

  Extremely sensitive to material budget
  Difficult for Cerenkov
  Difficult for ToF
Will be a “variable configuration” beamline

## Slide 3: Starting point
Beam monitors + trigger + spectrometer+tracking
  5 stations equipped with one or two planes of scintillating fibres
  Each plane 200 fibres (square, 1mm)
  Readout by SiPM , one per fibre
  Time stamped
ToF for Particle Id at low energies
  1ns or better needed
  Try to reuse the same devices as above.
  New electronics to be tested for fast timing
PID at “high” energies
  One or two Cerenkovs, standard CERN readout
  Time stamp
Rejection of electrons
  Probably a threshold cerenkov

## Slide 4: Online - offline selections
Trigger:
  From beam monitors, select tracks with signal in at least N of them, where N is probably all
  Electron discrimination from Cerenkov
  Keep open the possibility to add Cerenkov if wish to enrich the proton sample
Stored:
  Signals from every fibre of all beam monitors
  Fast time signal from fibres, at least first and last monitors
  Signals from Cerenkov
  All with CERN-compatible time stamp ( whiteRabbit?)

## Slide 5: Today, and next future
Define participations
Start thinking about requirements to be implemented in the electronics of the beam monitors
Start thinking to the architecture of the trigger, needed hardware, software…
How to merge in the DAQ
We would like to test a prototype of the beam monitors+electronics
………..