## Slide 1
FCC-hh Layout and Parameters
Daniel Schulte for the FCC-hh team
Berlin, May 2017

## Slide 2: Note: FCC-hh CDR
Will consist of two parts for the accelerator:
FCC-hh Design Overview
A concise description of the goals, main concepts, key issues and solutions
Should allow to understand the expected performance
FCC-hh Accelerator Design
Documents the studies performed
A resource to support the baseline concept
The basis for the next phase, highlights remaining R&D, alternatives, …

## Slide 3: Tentative FCC-hh Design Overview
1) Design goals and basic choices
2) Parameter optimisation
3) Key design challenges and solutions
4) Optics design and beam dynamics
5) Machine performance and operation aspects
6) Enabling technologies
7) Site integration
8) Injectors
9) Additional options
- Ion operation
- lepton-hadron operation
- special purpose experiments
10) Detectors and experiments
11) Schedule and cost
12) Detailed Parameter Table

## Slide 4: Tentative FCC-hh Accelerator Design
Experimental insertion region concept
Collimation concept
Injection and extraction concept
RF insertion concept
Arc concept
Integrated optics design
Single beam current limitations
Beam-beam effects
Collimation system performance
Operation cycle (incl. machine protection concept)
Ion operation concept
FCC-he concept
Magnets
Beamscreen
…
Descriptions of the collider areas
Performance evaluation
Options
Technical components, e.g.

## Slide 5: FCC-hh Layout
Layout has changed according to site requirements
Two high-luminosity experiments (A and G)
Two other experiments combined with injection (L and B)
Two collimation insertions
  Betatron cleaning (J)
  Momentum cleaning (E)
Extraction insertion (D)
Clean insertion with RF (H)
Circumference 97.75km
Can be integrated into the area
Can use LHC or SPS as injector

## Slide 6: Beam Parameters
 | FCC-hh Baseline | FCC-hh Ultimate
Luminosity L [1034cm-2s-1] | 5 | 20-30
Background events/bx | 170 (34) | <1020 (204)
Bunch distance Δt [ns] | 25 (5) | 
Bunch charge N [1011] | 1 (0.2) | 
Fract. of ring filled ηfill [%] | 80 | 
Norm. emitt. [mm] | 2.2(0.44) | 
Max ξ for 2 IPs | 0.01 (0.02) | 0.03
IP beta-function β [m] | 1.1 | 0.3
IP beam size σ [mm] | 6.8 (3) | 3.5 (1.6)
RMS bunch length σz [cm] | 8 | 
Crossing angle [s’] | 12 | Crab. Cav.
Turn-around time [h] | 5 | 4
Baseline: 1.25ab-1 per 5 year cycle
considering shutdowns, stops, MDs, …
= 2fb-2 per day
Ultimate: 5ab-1 per 5 year cycle
= 8fb-2 per day
Total 17.5ab-1
Focus on ultimate parameters
Injection energy 3.3TeV

## Slide 7: Luminosity Drivers
Maximise the beam current
Risks:
High stored energy and losses
Impedance and electron cloud
Aperture should be minimised for dipole cost
High synchrotron radiation load due to high beam energy
Limited by emittance growth and particle losses
Somewhat more difficult than HL-LHC due to longer L*
Squeeze the beam as much as possible
Harder than in HL-LHC (scaling with energy)
More collision debris due to higher luminosity and energy
For integrated luminosity:
Fast turn-around critical for luminosity
Minimise time for stops etc.
High availability with more components than LHC
Maximising current also maximises time between new fills

## Slide 8: Power and Choice of Temperature
Can only use some temperatures in order to maintain good vacuum
<20, 40K-60K, 100K-120K, >190K
Proton beams emit about 5MW of synchrotron radiation
2K is cheapest for dipole magnets
Choose 50K
Need 20x5MW=100MW for cooling
100MW
200MW
300MW
Ph. Lebrun, L. Tavian,
V. Baglin et al.

## Slide 9: Beam Screen Concept
Cooling channels
T=50K for efficiency
0.3mm copper layer to reduce impedance
Deflector minimises photons in main chamber
Ribs:
Mechanical strength
Photon stopper
Pumping holes
Hidden from beam
Prevents prohibitive impedance
Magnet cold bore
T=2K
Laser treatment to mitigate electron cloud
26mm aperture to reduce impedance
Magnet aperture is now 50mm
Seems to be tight but OK
Impedance more important than in LHC

## Slide 10: Parameter Optimisation
With our beam current can reach luminosity goal
Not much to be gained
  pushing beam-beam parameter increases risk and requires less noise
  reducing beta-function reduces triplet shielding or tightens collimation (impedance, higher risk)
Will reconsider for 5ns spacing
Example options to be considered
Electron lens
Wires
Pushing collision point beta-functions smaller during run
Important for integrated luminosity are
Turn-around time
Availability
Operational schedule

## Slide 11: Parameter Optimisation
Physics looks for reduction of background
Do not have a clear target, so will explore range of options
Possibilities are a combination of
  Longer bunches
  Smaller bunch spacing and charge
  Luminosity leveling
Will put emphasis on 5ns and 12.5ns bunch spacing parameters
  Makes use of octupoles even harder, will have to use different scheme
  Instrumentation already specified for 5ns spacing
  Have to compensate or accept luminosity reduction
    Main compensation is to use smaller beta-function
    Still a relative loss remains
  More sensitive to noise
Luminosity leveling costs limited amount of integrated luminosity
  E.g. limit to 1035cm-2s-1 leads to 30%-40% reduction

## Slide 12: Conclusion
FCC-hh parameters have been derived systematically
The key design challenges have been identified
Should be able to cope with them
There are interesting alternatives that will be considered to become baseline
In case they are still too premature they will remain alternatives for now

## Slide 13: Reserve

## Slide 14: Parameter Optimisation
Choice of bunch spacing
Put together a set of parameters for the 5ns (or 12.5ns) bunch spacing
Choice of working point
Use LHC working point as starting point
Would like to have a scan of the working point for impedance, dynamic aperture and beam-beam
Round vs. flat optics
Need to see how far we progress with the flat optics
Default will be round
Injection energy
Waiting for the field errors at injection, so no calculation for dynamic aperture
Collimation will be tight for lower injection energy, would require lower emittance

## Slide 15: Parameter Optimisation
Operation of additional experiments under the different conditions
Close interaction with the experiments is required
Operation with moving collimators
Move collimators in as the beam burns off (constant impedance effect)
Allows to reduce IP betafunction

## Slide 16: Parameter Optimisation
Choice of collective effects stabilisation methods
Main problem is transition into collision
Switch off feedback before collision and only use octupoles?
  Total octupoles need to be 20 times stronger than in HL-LHC for the same tuneshift
  Tune shift is expected about up to 3 times higher
  Further increase due to emittance damping (faster than burn-off)
  Would need more than 60 times the LHC octupoles strength
  Potentially further increase by factor 5 for 5ns spacing
Can we use a feedback in spite of beta-beating?
  Requires very low noise
  E.g. proportional gain of 0.01 and resolution of 0.1μm (0.5% of beam size)