## Slide 1: 3.3 TeV beam injection into combined experimental and injection FCC machine insertions
M. Hofer, M.I. Besana, F. Burkart, F. Cerutti, R. Martin, D. Schulte, R. Tomas

## Slide 2: Motivation
Since the last FCC week in Rome 2016 the overall layout of the FCC-hh has changed
The new layout has a reduced circumference of 97.75 km compared to 99.97 km for the previous baseline layout
Low luminosity experiments moved from Points F & H to B & L and are now combined with the injection
The length of these insertion remains at 1400 m
See Talk by Daniel Schulte

## Slide 3: Combined injection and experimental insertion in (HL-)LHC
Example for a combined insertion in the (HL-)LHC
Insertion layout for ALICE
Symmetric design and injection protection close to the experiments
High-Luminosity Large Hadron Collider (HL-LHC) Preliminary Design Report
https://cds.cern.ch/record/2116337/files/CERN-2015-005.pdf

## Slide 4: Strategy
For these insertion a rather conservative approach was chosen separating Injection and Experiments as best possible
Chosen as it seems preferable from a machine protection point of view
Not as deeply interwoven as LHC
Same layout is used for both IPB and IPL
Injection
Experiment

## Slide 5: Injection Layout
Half cell length for injection devices is 150 m
Septum is located right next to the Dispersion Suppressor
Protection elements far away from the experiment
150 m
TDI
MKI
MSI
IPB
Possible additional injection protection elements

## Slide 6: Experiment layout
These Experiments were designed with no specific scenario in mind (e.g. Ions, FCC-he)
For the low luminosity experiments an of 25 m was suggested by the detector design group
Keep separation section length as short as possible
IPB
L* = 25 m
TDI
MKI

## Slide 7: Injection Optics
Predetermined injection cell length adds space constraints
Injection optics requires special matching constraint to ensure optimum protection:
  90° phase advance constraint between the Kickers and the absorber TDI
  vanishing dispersion to mitigate the effect of injection oscillation

## Slide 8: Collision Optics
During collision no special constraints need to be applied
With this layout a minimum round of 3 m has been matched
Crossing angle has been scaled from Main Experiments with the reduced distance IP to D1 which yields

## Slide 9: Energy depositions studies
Energy deposition in the magnets is one of the key factors that defines luminosity reach
The maximum instantaneous luminosity is determined by the quench limit of the superconductivity magnets
The cumulated dose sets the achievable integrated luminosity

## Slide 10: Magnet Models
Unlike in the main experiments, the triplet quadrupoles in these insertions are shorter and require a higher gradient and a significantly smaller aperture
Same magnet model for all triplet quadrupoles and a constant 10 mm tungsten (INERMET180) shielding
An 80 cm long tungsten mask is placed in front of the quadrupole closest to the IP
Tungsten mask
Q1A

## Slide 11: Magnet Models
Triplet quadrupoles also needed to be split and housed in separate cryostats
70 cm shielding gaps were assumed in the interconnects
For the separation section after the triplet a design using superconducting dipoles was chosen to keep the section as short as possible which will also needed to be considered for energy deposition studies
C2
Q3B
Q3A
Q2B

## Slide 12: Energy deposition
For an instantaneous luminosity of the peak power density in the triplet is well below the current design limit of Nb3Sn of
Effect of 70 cm shielding gaps in the interconnects from splitting the triplet quadrupoles clearly visible
Q1
Q2
Q3
C1
C2

## Slide 13: Energy deposition
Total Power for : 4.3 kW per side
  1.7 kW deposited in the triplet
  2.6 kW going downstream
maximum power per meter on Q1A for both crossing schemes: ~14.4 W/m
power on the mask in front of Q1A: ~280 W
Further simulations needed to understand where these particles will impact
  Single diffractive protons (50 TeV) lost further downstream (DS, collimation section)
  Lower energy protons (~25 TeV) and pions expected to be lost in D1, D2, TAN or MS
  Neutral particles lost in TAN or further downstream
Particle Spectra at the exit of Q3B per collision

## Slide 14: Energy deposition
With the current baseline radiation limits seems feasible
In order to survive longer, options like thicker shielding with a higher , switching the crossing plane or swapping the triplet quadrupoles in a LS could be explored
Current FCC-hh target radiation limits | 
Baseline | 30 MGy
Ultimate (R&D Goal) | 250 MGy
Q1
Q2
Q3

## Slide 15: Conclusions and Outlook
Since last FCC-week in Rome new, more compact FCC-hh layout with combined injection and experimental insertions as in the LHC
A design for these insertion has been presented, which uses a L* of 25 m and achieves a β* = 3 m
From energy deposition studies using the current baseline target radiation limits sets the attainable integrated luminosity to
Many things to follow up:
  Dynamic Aperture studies
  Impact on particles escaping the triplet
  Beam-Beam effects
  Impact of injection failures on experiments and Studies for additional masks and injection protection elements

## Slide 16: Thank you for your attention!

## Slide 17: Reserve

## Slide 18: Geology
“The favoured layouts avoid the Jura and Pre-Alps limestone whilst also avoiding exceptionally deep shafts in Points H, G and F, however it has proved difficult to simultaneously fulfil these criteria.”
See J. Stanyard, V. Mertens, J. Osborne, Y. Loo, C. Sturzaker, M. Sykes “Optimisation of the design of the future circular collider from a civil engineering perspective”, in Proc.IPAC2017, Copenhagen, Denmark

## Slide 19: Total Power deposited in triplet
  maximum power per meter on Q1A for both crossing schemes: ~14.4 W/m
  power on the mask in front of Q1A: ~280 W
Magnet | Power [W] vertical crossing |  |  | Power [W] horizontal crossing |  | 
 | Total | Shielding | Cold Mass | Total | Shielding | Cold Mass
Q1A | 248.8 | 100.9 | 147.9 | 251.3 | 101.9 | 149.4
Q1B | 267.9 | 182.7 | 85.2 | 269.0 | 183.7 | 85.3
C1 | 27.1 | 18.9 | 8.2 | 27.7 | 19.3 | 8.4
Q2A | 118.1 | 82.3 | 35.8 | 119.3 | 83.3 | 36.0
Q2B | 204.4 | 147.1 | 57.3 | 190.9 | 137.3 | 53.6
Q3A | 111.1 | 76.7 | 34.4 | 112.9 | 80.3 | 32.6
Q3B | 112.6 | 81.2 | 31.4 | 132.1 | 95.2 | 36.9
C2 | 14.7 | 10.7 | 4.0 | 17.5 | 12.8 | 4.7
Total on Magnets | 1104.6 | 700.6 | 404.1 | 1120.7 | 713.9 | 406.8

## Slide 20: Peak dose: Angular Position
Q1
Q2
Q3

## Slide 21: Magnets
Type | Gradient [T/m] | Field [T] | Aperture [mm] | Length [m] | Units per IP
Triplet Q1 | 270 | - | 64 | 10 | 4
Triplet Q2 | 270 | - | 64 | 15 | 4
Triplet Q3 | 270 | - | 64 | 10 | 4
Separation Dipole D1 | - | 12 | 100 | 12.5 | 4
Recombination Dipole D2 | - | 10 | 60 | 15 | 4
Matching Quadrupole Short Type MQM | 200 | - | 70 | 9.1 | 4
Matching Quadrupole Long Type MQML | 300 | - | 50 | 12.8 | 6
Orbit Corrector | - | 3 | 64 | 1 | 6

## Slide 22: Parameters
Normalized emittance | 
Closed Orbit uncertainty | 
Momentum offset | 
β-beating coefficient | 
Relative parasitic dispersion | 
Normalized emittance | 
Closed Orbit uncertainty | 
Momentum offset | 
β-beating coefficient | 
Relative parasitic dispersion | 
β* during collision | 3 m
β* during injection | 27 m
Full crossing angle | 39 µrad
Separation during injection | 1.5 mm