## Slide 1: European XFEL Status
Hans Weise & Winni Decking, DESY
On behalf of the European XFEL Accelerator Consortium
work supported by the respective funding agencies of the contributing institutes; for details please see http://www.xfel.eu
TTC Meeting 02/2017
Notes: How to edit the title slide
Upper area: Title of your talk, max. 2 rows of the defined size (55 pt)
Lower area (subtitle): Conference/meeting/workshop, location, date, your name and affiliation, max. 4 rows of the defined size (32 pt)
Change the partner logos or add others in the last row.

## Slide 2: First Lasing.

## Slide 3: One Kilometer of Cold Linac

## Slide 4: With almost 800 Superconducting Cavities

## Slide 5: The European XFEL Built by Research Institutes from 12 European Nations
Some specifications
Photon energy 0.3 - 24 keV
Pulse duration ~ 10 - 100 fs
Pulse energy few mJ
Superconducting linac 17.5 GeV
10 Hz (27 000 b/s)
5 beam lines / 10 instruments
  Start version with 3 beam lines and 6 instruments
Several extensions possible:
  More undulators
  More instruments
  …….
  Variable polarization
  Self-Seeding
  CW operation
SASE2
(= SASE1)
SASE1, lu= 40 mm
0.2 – 0.05 nm
17.5 GeV
SASE3, lu= 68 mm
1.7 – 0.4 nm

## Slide 6: European XFEL Layout
Injector at DESY campus
Linear Accelerator
1.9 km - 17.5 GeV
Undulator/Photon Tunnels
Experiment Hall
in Schenefeld

## Slide 7: Accelerator Complex with Challenging Parameter Set
* normalized emittance:
electron beam energy | 8/12.5/14/17.5 GeV
macro pulse repetition rate | 10 Hz
RF pulse length (flat top) | 600 ms
# of bunches/second | 27,000
bunch charge | 0.02 – 1 nC
electron bunch length after compression (FWHM) | 2 – 180 fs
normalized slice emittance* | 0.4 - 1.0 mm mrad
beam power | 500 kW
simultaneously operated SASE undulators | 3

## Slide 8: State of the Art 3 Stage Bunch Compression
R56=60-120mm
R56=
60-120mm
R56=30-100mm
ss = 2 mm
Ipeak= 50 A
sE = 0 %
E = 130 MeV
ss = 1 mm
Ipeak= 100 A
sE = 1.5 %
E = 130 MeV
ss = 0.1 mm
Ipeak= 1 kA
sE = 1 %
E = 600 MeV
ss = 0.02 mm
Ipeak= 5 kA
sE = 0.3 %
E = 2400 MeV
3 stage bunch compression: flexible and less sensitive to noise from RF system
= 40 mm
harmonic system
bunch compressor
beam diagnostics

## Slide 9: X-ray Beamlines for Different Wavelengths with Different Time Structures
HED
MID
FXE
SPB
SQS
SCS
SASE 1
3 – 24 keV
SASE 2
3 – 24 keV
SASE 3
0.26 – 3 keV
photon tunnel
electron bend
undulator
electron dump
electron tunnel
electron switch
experiments
LINAC
17.5 / 14 / 10.5 GeV
~
~
~
2 hard x-ray undulators and beam transport with 4 instruments
1 soft x-ray undulator and beam transport with 2 instruments
all undulators planar and tunable

## Slide 10: The Suite of Instruments
SASE 2
SASE 1
SASE 3
U 1
U 2
SQS
SCS
SPB
FXE
MID
HED
FXE Femtosecond
X-ray
Experiments
SPB Single Particle &
Biomolecules
SQS Small Quantum
Systems
SCS Spectroscopy &
Coherent Scattering
MID Materials Imaging &
Dynamics
HED High Energy
Density Science
More about experiments: http://www.xfel.eu

## Slide 11: Project History
2000: First lasing at 109 nm at the Tesla Test Facility (TTF), now FLASH
2001: TESLA Linear Collider TDR with XFEL appendix
2002: TESLA TDR supplement with stand-alone XFEL
2006: European XFEL TDR
2009: Foundation of the European XFEL GmbH
Start of underground construction
2010: Formation of the Accelerator Consortium
16 accelerator institutes under the coordination of DESY
2012: End of tunnel construction
Start of underground installation
2016: Finish of accelerator installation
Start of commissioning

## Slide 12: Commissioning Plan (include as many systems as early as possible)
12/16 Linac Cooldown
01/17 Injector at 130 MeV (3 RF stations)
01/17 L1 commissioning (+1 RF station)
02/17 L2 commissioning (+3 RF stations)
02 - 04/17 L3 commissioning (+15 RF stations)
05/17 Beam through SASE1 & SASE3 undulator sections
end 05/17 Milestone “First Lasing Possible”
06 - 08/17 Commission SASE1 photon beamline and experiment Consolidate FEL operation at 8-10 keV photon energy
09/17 First user experiments (total 800 hours)
2018 Continue facility commissioning + 2000 user hours
2019 Routine operation with 6 experiments + 4000 user hours

## Slide 13: Injector in Operation 2015 / 2016
Spectrometer Diagnostic Section Laser Heater 3.9 GHz Module 1.3 GHz Module Gun
Dump Transverse Deflecting Structure
Photoinjector conditioned and characterized at PITZ, DESY-Zeuthen
Injector cool-down 12 / 2015
First Beam on Dec 18th 2015 - commissioning till Q2/2016
Full bunch train length (27,000 bunches/s) reached for 20pC - 1000pC bunch charges
  Photocathode laser with excellent up-time
  (Yb:YAG laser from Max-Born Institute Berlin; 257 nm ≤ 4 μJ; 3 ps)
3.9 GHz system operational from day 2
Laser heater commissioned

## Slide 14: View along L3 accelerator section

## Slide 15: Overview of XFEL Cryogenic Equipment
Cryo plant with cold compressors and extended distribution system
Cooling capacity:
2K : >1.9 kW
5/8K : 4 kW
40/80K : 24 kW
Linac is one 1.5 km long cryo-string
Cryo Plant
Cold Compressors He Distribution
Linac

## Slide 16: First Cooldown of XFEL Linac during Dec 2016
Start asymmetrical operation of two cold boxes to speed up cooldown
Entry of cold return flows in cold boxes to enhance cryogenic capacity
Fast cooldown at temperatures below liquid nitrogen (no more thermal stress)
10.12.2016
24.12.2016
No Cold Leaks!!!

## Slide 17: Cryogenics is very challenging
Complexity of cryogenic system asked for sufficient commissioning time; experts had to establish / optimize operation and to gain experience with new machines, especially the used cold compressors.
How to deal with…
  671 control valves
  >3,800 sensors (temperature, pressure, flow, level)
  433 regulation loops
  >22,000 records and >220,000 properties
  and last but not least … >300 tons of material to be cooled down
Required 2K pressure stability of 2% peak from LLRF requirements (cavity detuning)
Tedious adjustment of regulation loops
Inner-system heaters to counteract dynamic processes

## Slide 18: We cooled down all 96 accelerator modules
54
XM 4
L2
L1
XM 5
XM 1
XM 2
XM -1
L3
L3
L3
L3
L3
L001
A2.1.L1
BC1
L2
L3
L3
BC2
XM 7
XM 6
XM11
XM 3
XM 13
XM 9
XM 10
XM 19
L002
A2.2.L1
L003
A2.3.L1
L004
A2.4.L1
L005
A3.1.L2
L006
A3.2.L2
L007
A3.3.L2
L008
A3.4.L2
L009
A4.1.L2
L010
A4.2.L2
L011
A4.3.L2
L012
A4.4.L2
L013
A5.1.L2
L014
A5.2.L2
L015
A5.3.L2
L016
A5.4.L2
L017
A6.1.L3
L018
A6.2.L3
L019
A6.3.L3
L020
A6.4.L3
L021
A7.1.L3
L022
A7.2.L3
L023
A7.3.L3
L024
A7.4.L3
L025
A8.1.L3
L026
A8.2.L3
L027
A8.3.L3
L028
A8.4.L3
L029
A9.1.L3
L030
A9.2.L3
L031
A9.3.L3
L032
A9.4.L3
L033
A10.1.L3
L034
A10.2.L3
L035
A10.3.L3
L036
A10.4.L3
L037
A11.1.L3
L039
A11.3.L3
L040
A11.4.L3
L041
A12.1.L3
L042
A12.2.L3
L043
A12.3.L3
L044
A12.4.L3
L045
A13.1.L3
L046
A13.2.L3
L047
A13.3.L3
L048
A13.4.L3
L049
A14.1.L3
L050
A14.2.L3
L051
A14.3.L3
L052
A14.4.L3
L053
A15.1.L3
L054
A15.2.L3
L055
A15.3.L3
L056
A15.4.L3
L057
A16.1.L3
L058
A16.2.L3
L059
A16.3.L3
L060
A16.4.L3
L061
A17.1.L3
L062
A17.2.L3
L063
A17.3.L3
L064
A17.4.L3
L065
A18.1.L3
L066
A18.2.L3
L067
A18.3.L3
L068
A18.4.L3
L069
A19.1.L3
L070
A19.2.L3
L071
A19.3.L3
L072
A19.4.L3
L077
A21.1.L3
L078
A21.2.L3
L079
A21.3.L3
L080
A21.4.L3
L089
A24.1.L3
L090
A24.2.L3
L091
A24.3.L3
L092
A24.4.L3
L081
A22.1.L3
L082
A22.2.L3
L083
A22.3.L3
L084
A22.4.L3
L093
A25.1.L3
L094
A25.2.L3
L095
A25.3.L3
L096
A25.4.L3
L073
A20.1.L3
L074
A20.2.L3
L075
A20.3.L3
L076
A20.4.L3
L085
A23.1.L3
L086
A23.2.L3
L087
A23.3.L3
L088
A23.4.L3
L097
A26.1.L3
L098
A26.2.L3
L099
A26.3.L3
L100
A26.4.L3
L038
A11.2.L3
XM 18
DEMACO Cryo-connection
1.508 m
XM 27
XM 20
A2
A6
XM 30
A7
A8
XM 31
XM 28
XM 14
XM 34
P
XM 26
XM 35
XM 37
SCB 1
DEMACO Cryo-connection
XM 38
SCB 2
XM 39
XM 40
XM 41
XM 36
XM 43
XM42
XM47
XM44
P
P
XM 49
XM 16
XM 33
XM 45
XM 15
A9
A10
52
53
55
56
57
58
59
61
60
62
63
XM 51
XM 17
XM55
XM 52
XM 53
XM 25
A11
A12
A13
A14
XM 32
XM 67
P
XM 56
P
P
XM 48
XM 23
XM 58
50
XM59
XM 12
P
P
P
SCB 4
XM65
68
67
70
74
73
72
75
69
66
64
76
XM 64
XM 60
SCB 3
XM 57
XM 71
UV XTL-2AV
XM 63
XM 66
51
XM 21
XM 61
XM 69
XM 68
XM 70
A5
A15
A16
A17
XM 72
XM 73
XM 76
XM 62
A4
A3
P
P
P
P
CS1
CS2
CS2
CS3
CS4
CS5
CS6
CS7
CS8
CS9
65
32
79
78
77
80
81
82
83
84
85
86
87
88
89
XM -2
XM 74
XM 77
SCB 5
XM 79
P
P
P
XM 81
XM 80
XM 78
XM 75
90
91
93
94
100
BC0
Dogleg
Injector
DEMACO Cryo-connection
95
96
97
98
99
102
101
P
SCB 6
P
XM83
XM82
XM 22
XM84
XM 86
XM87
XM 85
<<< Cabling >>>
22
24
25
26
28
P
29
30
31
33
34
35
36
37
71
92
A18
x
x
x
A19
A20
XM 89
XM 88
XM 90
XM 92
XM 54
<<< Rack cabling >>>
<<< Rack cabling >>>
P
P
P
x
x
x
A22
A23
103
XM 95
XM 94
XM 93
104
105
106
107
108
109
110
111
112
113
114
118
XM 91
XM 24
XM 97
XM 96
Last
XM98
P
P
P
CR
A21
A24
23
Water Distribution assembling
116
120
126
x
x
A25
Wave Guide assembling
Wave Guide assembling
117
119
121
122
123
125
127
Wave Guide assembling
Wave Guide assembling
Interlock-door 1.102m
115
124
128
parked
End cap
CR
129
133
137
Cryo stage

## Slide 19: L3 RF Stations on the Status Pannel
All RF stations including CS7 are commissioned at moderate gradients.
Detailed measurements will show the path towards higher beam energies.
CS8 is meanwhile ready for LLRF commissioning; thanks to maintenance days.
The last two stations (CS9) require still longer tunnel access.
in operation
dito. but shifted off beam
off

## Slide 20: LLRF Commissioning includes…
Commissioning milestones
  Initial checks (LLRF system ready for commissioning)
  Cold coupler conditioning (optional)
  Cavity Forward and Reflected RF signal integrity (cabling issues? signal saturation?)
  Frequency tuning (from parking position)
  Cavity Probe RF signal integrity (cabling issues? signal saturation?)
  Coupler tuning (target QL)
  Power-based gradient calibration (coarse)
  Cavity phasing (using waveguide phase shifters)
  Closed-loop operation (feedback, learning feedforward)
  Beam-based gradient calibration (fine)
Reached goals by now
  Handed over to operations and controlled via FSM
  Inner loop RF stability <0.01 deg, < 0.01%
  Preliminary measurements of beam energy jitter ≈ 10-4
Example: beam induced transient during cavity phasing
Beam loading transient
Notes: Before you start editing the slides of your talk change to the Master Slide view: Menu button “View”, Master, Slide Master:
Edit the following 2 items in the 1st slide: 1) 1st row in the violet header: Delete the existent text and write the title of your talk into this text field 2) The 2 rows in the footer area: Delete the text and write the information regarding your talk (same as on the Title Slide) into this text field.
If you want to use more partner logos position them left beside the DESY logo in the footer area Close Master View

## Slide 21: XFEL RF System
KLYSTRON
CM1 (8 cav.)
CM2 (8 cav.)
CM3 (8 cav.)
CM4 (8cav.)
HV Modulators in surface hall
Connected to pulse transformer via up to 2km long pulse cables
Klystron and modulator
below module

## Slide 22: XFEL LLRF System
KLYSTRON
CM1 (8 cav.)
CM2 (8 cav.)
CM3 (8 cav.)
CM4 (8cav.)
LLRF master
LLRF slave
Drift compensation
Reference synchr. + distr.
Clocks + local oscillator
Main controller crate (MicroTCA)
Piezo*
Power supplies
* not installed yet
LLRF master
LLRF slave

## Slide 23: Energy Reach of European XFEL Modules
maximum energy reach
  according to accelerator module test
  after tunnel installation
  ignoring bunch compressor set-points
Design: 17.5 GeV
L2
L3
L1
Average accelerating gradient after pre-installation module test and waveguide tailoring
  26 MV/m, (design 23.5 MV/m)
Some additional gradient reduction due to tunnel waveguide distribution
Excess energy reach will enhance operation reliability

## Slide 24: Operating Gradients used so far
L2
L3
L1
exp. status of 10.04.17
12 GeV
Design: 17.5 GeV
maximum energy reach
  according to accelerator module test
  after tunnel installation
  ignoring bunch compressor set-points
After initial commissioning design gradient almost reached
Operation of RF stations “off beam” allows final commissioning of single stations parallel to XFEL lasing operation
Quite some RF cavities needed short multipactor processing around 16 to 20 MV/m.
So far 4 couplers were disconnected due to temperature rise at warm window; RF conditioning was not easily possible.

## Slide 25: Warm Beam Line Sections Bunch Compressor Sections – Challenging Installation

## Slide 26: Bunch Compressor BC1

## Slide 27: Transverse Deflection System in Bunch Compressor BC2
The BC2 TDS system is one important system to be used to verify short bunch lengths during linac setup.

## Slide 28: Both Bunch Compressors BC1 / BC2 include Commissioning Beam Dumps

## Slide 29: Linear Accelerator

## Slide 30: Post Linac Beam Lines upstream of XS1
1.508m
DACHS
door
1.520m
1.530m
1.540m
1.550m
1.560m
1.570m
1.580m
1.590m
1.600m
1.610m
1.620m
1.620m
1.630m
1.640m
1.650m
1.660m
1.670m
1.680m
1.690m
1.700m
1.710m
1.720m
1.730m
1.740m
1.750m
1.760m
1.770m
1.780m
1.790m
1.800m
1.810m
1.820m
1.830m
1.840m
1.850m
1.870m
1.880m
1.890m
1.900m
1.910m
1.920m
1.930m
1.940m
1.950m
1.960m
1.970m
1.990m
2.000m
2.010m
2.020m
2.030m
2.040m
2.050m
2.060m
2.070m
2.080m
2.090m
1.740m
1.860m
1.860m
1.980m
1.980m
2.100m
2.100m
2.110m
2.120m
2.130m
XS1
XTL
DUMP
Wall
143
148
144
145
146
147
152
151
149
150
153
154
155
156
158
159
157
Container for condensed water
450 ltr.
160
<<< Cabeling >>>
161
162
163
164
<<< Cabling >>>
<<< Cabling >>>
<<< Cabling >>>
166
167
169
168
170
200 m transport line (eq. to 4 + 12 modules)
200 m collimation
200 m beam distribution
100 m XS1 dump line

## Slide 31: Transfer Lines at the End of the Main Linac Tunnel (XTL)
XDU2
XDU2
XDU2
XS1
All beam lines are suspended from the ceiling
Engineering of ‘hanging’ system needed some effort but result is very satisfying

## Slide 32: Warm Beam Line Sections Transport Line to XS1 Beam Dump
Three 300 kW main beam dumps
Special vehicles to exchange activated dumps
XDU2
XDU2
XDU2
XS1

## Slide 33: Installation on Top of XS1 Dump Cave
XS1 installation includes transport towards XTDs

## Slide 34: Final Installation Activities SASE2 Undulator Section
Mechanical vacuum work in the southern branch almost finished.
Technical commissioning in Q3/2017.

## Slide 35: SASE Undulator Sections with special air conditioning hutch
courtesy of XFEL.EU

## Slide 36: Installation of Photon Beamlines
1st and 2nd offset mirrors in XTD2
Fast valves and 500 m pipes in XTD9
Differential pump + XGM in XTD9
courtesy of XFEL.EU

## Slide 37: Photon Beam Diagnostics Status SASE1 – XTD2
Filter Ch. & IMGTR
Pop-in Monitor
XGM
IMGSR
MCP-detector
K-mono
Gas supply
courtesy of XFEL.EU

## Slide 38: Photon Beam Diagnostics Status SASE1 – XTD9
XGM@XTD9
Pop-in Monitors Type I and II-45
XGM@XTD9
HIREX diagnostic spectrometer system
HIREX crystal chamber
grating chamber
crystal chamber
courtesy of XFEL.EU

## Slide 39: XHEXP – SASE1 science instruments
courtesy of XFEL.EU

## Slide 40: SASE1 - Femtosecond X-ray Experiment (FXE)
courtesy of XFEL.EU

## Slide 41: Beamline Commissioning Progress
13/01*
15/01 @ 130 MeV
19/01 @ 600 MeV
02/02 @ 600 MeV
22/02 @ 2.5 GeV
25/02 @ 2.5 GeV
19/03 @ 6 GeV
08/04 @ 12 GeV
27/04*
* Beam permission on 13/01
* Beam permission on 26/04
27/04 Beam spot before dump
0m 30m 230m 480m 1430m 2100m 3100m
L1
L2
L3
keen on lasing…

## Slide 42: First signal from FEL radiation 02.05.17 - 03.05.17
E = 6.4 GeV
K = 3.5
9 Å
low energy 6.4 GeV working point for beam based alignment
no undulator beam based alignment yet, no laser heater
some tweaking of compression and trajectory

## Slide 43: Systematic approach towards short wavelengths
After first lasing a systematic approach (BBA and commissioning of undulator ctrl) was chosen.
Photon beam diagnostics was commissioned. Well prepared for lasing at short wavelength…
x
y
charge
SASE1
300µm
500pC

## Slide 44: Lasing at 2 Angstroem
photon beam at the end of XTD9
orbit & compression feedback in operation
transport to SASE1 exp area is next

## Slide 45
General Assembly of the European XFEL Accelerator Consortium
04.05.2017
THANK YOU TO ALL CONTRIBUTORS TO THE
EUROPEAN XFEL
Guest Scientists during commissioning