## Slide 1: FCC-hh vertex detector optimization status of fast simulation studies
Dominik Dannheim (CERN),
Estel Perez (CERN), Philipp Roloff (CERN), Rosa Simoniello (CERN)
Special thanks to Zbynek Drasal (CERN)
FCChh meeting , 16th November 2016

## Slide 2: Outline
Constraints of the background occupancy on:
Detector’s granularity (pixel size)
Pattern recognition
  Trade-off between number of layers and single point resolution

## Slide 3: Fluence map
Number of particles per pp collision per unit area
For B field = 4 T
  (scaled from the 6T map used by Zbynek in his past studies)
  Does not include tracker material (small effect)
  Includes EM calorimeter (acts as source of back scattered particles)
  Assumes HAD calorimeter absorbs all particles
Up to z=8m
  Fluence in forward region not available: depends on the layout which is not yet fixed
Irradiation map available
Zoomed-in area in the next slide
Provided by M. Ilaria Besana

## Slide 4
Given the fluence map, what is the minimum granularity needed in each part of the detector, to make sure there will be only one particle firing a pixel?
Assume we need the occupancy <=0.01 (for consistency with prev. results, to be reviewed)
Assume # Pile up interactions per bunch crossing =1100
Assume no diffusion (cluster size for a perpendicular track = 1)
if we Assume squared pixels and no charge sharing, can express the area in terms of σ:
For a given single point resolution, how close to the beampipe can we go?
maximum Fluence= 0.01/1100 /(σ * √12)2
 Draw constant fluence curves in the R vs Z plane
1) Constraints from fluence on detector granularity
Occupancy = Fluence * Pile up * PixelArea
# particles per unit area, per pp collision
# of pp collisions per Bunch Crossing (BC)
per Bunch Crossing
PixelArea = (PixelPitch)2 = (single point resolution * √12 )2

## Slide 5: 1) Constraints from occupancy on detector granularity
10x25
10x30->PixelArea=3600
40x40
10x100
25x25
10x20
10x15->PixelArea=1800
eta=6
20x20
single point res σ [μm] | pitch* [μm] | pixel area [μm^2] | max Fluence [mm^-2]
5x5 | 17.3 | 300 | 0.03030
10x10 | 34.6 | 1200 | 0.00758
10x15 | 42.4 | 1800 | 0.00505
10x20 | 49.0 | 2400 | 0.00379
10x25 | 54.8 | 3000 | 0.00303
10x30 | 60.0 | 3600 | 0.00253
20x20 | 69.3 | 4800 | 0.00189
25x25 | 86.6 | 7500 | 0.00121
10X100 | 109.5 | 12000 | 0.00076
40x40 | 138.6 | 19200 | 0.00047
For layers and rings with R<35mm, pixel area should go down to 1800μm2 -> single point resolution =10x15 μm (for first inner barrel layer and innermost ring of all endcap disks)
eta=5.7
Outer
Endcap
Forward
# particles in a pixel <=0.01
σ = Pitch/√12
#PU =1100 int. per BC
Inner
Which single point resolution is needed in each part of the tracker?
* pitch = sqrt(pixel area), even for non-squared pixels

## Slide 6
Current baseline
10x15
10x30
10x100
σ

## Slide 7
Proposal 1 (from occupancy point of view)
10x15
10x30
10x100
σ
Need to review also where the transition to σ=10x100 should happen (consider also z0 and d0 resolution)

## Slide 8: 1) Constraints from occupancy on detector granularity - requests
Do we have a baseline estimate of max occupancy and cluster size, for FCChh envisaged technologies?
  Assuming 1% occupancy is probably not realistic:
  HL-LHC already requires to go down to 0.2%
    RD53 aims at 50x50μm pixel pitch coping with 3 GHz/cm2
      Sensors of area= 50x50μm = 2500 μm2
      3 GHz/cm2 = 75 KHz/pixel -> in 25 ns: 0.0019 particles
  Propose to use occupancy 0.2% as benchmark for the future
    Factor of 5 in the max occupancy -> factor of 2.2 in the single point resolution
    Go down to 7x5 μm single point resolution for the innermost layers and disks
Would need an estimation of the fluence values up to z=16000mm to realistically assess the minimum granularity in the forward part of the detector.

## Slide 9: 2) Pattern recognition
How does the single point resolution of the forward disks and the gap distance affect pattern recognition
Outer Endcap
Forward disks
gap
Steps:
Project track covariance matrix on the last encap disk
Calculate fluence at such position
If there is another particle in the error ellipse area, it will cause confusion in the tracking algorithms
LiC Toy uses outside-in tracking

## Slide 10: # of background particles in the error ellipse ?
Area of the error ellipse projected at the last endcap disk:
Multiply by fluence at the last endcap disk
Note: In this study the upper and lower part of the disks have the same material budget and resolution
θ=5.49 deg;
η=3
Gap
θ=0.39 deg;
η=5.7
EllipseArea = ¼ π σRφ σz tanθ
Endcap
Forward
θ
R
Rφ
z
A=1/4 π σRφσR
σR=σz tanθ
# bkg particles in error ellipse = Fluence * Pile up * EllipseArea
Study, for forward tracks: (going through all fwd layers)
Area as a function of the single-point resolution of the forward layers
Area as a function of the gap distance (endcap – forward)

## Slide 11: Bkg in error area vs single-point resolution
pT [GeV]
In order to have less than 0.01 particles per bunch crossing in the error ellipse area, would need σ=10x10μm.
Not possible to go below pT=0.5 GeV with this layout
Assume we need the # bkg particles in the error ellipse to be <=0.01, which single point resolution is required for the forward layers?
Assume # Pile up interactions per bunch crossing =1100
Assume squared pixels (single point resolution: 5x5, 10x10, 25x25, 50x50 100x100 μm)
Show results for the forward-most angle that hits all layers (theta = 0.39 deg; eta=5.7)
# bkg particles in error ellipse = Fluence * Pile up * EllipseArea
θ=0.39 deg; η=5.7

## Slide 12: Adding an extra disk in the middle of the gap
If we add one(two) extra layer(s) in the middle of the gap, we can go down to σ=25x25 μm single point resolution for the forward disks and down to pT=0.5 GeV tracks.
extra disk in the middle of the gap
 factor of 5 less background
Baseline
pair of extra disks in the middle of the gap
(5cm apart)
 extra material is counter-productive for low pT tracks
θ=0.39 deg; η=5.7
Line at max # particles in the error ellipse area per BC = 0.01
Assume #PU/BC = 1100
pT [GeV]
pT [GeV]
pT [GeV]
Endcap
Forward
extra disk

## Slide 13: Dependance on track η
σ=25x25μm
Yes, even if highest η does not always mean highest #particles
Show # particles per BC vs η for different single point resolutions (σ) of the forward disks.
σ=10x10μm
σ=5x5μm
Line at max # particles in the error ellipse area per BC = 0.01
Assume #PU/BC = 1100
1 extra disk in the middle of the gap
Would σ=25x25μm work for every η?
pT [GeV]
pT [GeV]
pT [GeV]

## Slide 14: Dependance on track η
pT
p
equivalent for η=5.7
σ=5x5μm
1 extra disk in the middle of the gap
Assume #PU/BC = 1100
At high η the higher fluence is compensated by smaller ellipse area (less multiple scattering: at constant pT, higher η means much higher p)
pT [GeV]
p [GeV]

## Slide 15: Conclusions
Detector granularity close to the beampipe driven by fluence, while at larger R the limitations of the pattern recognition will start to play a role
Need finer granularity in the area close to the beampipe
  For layers and rings with R<35mm, single point resolution should be about 10x15 (7x5) μm for occupancy<1% (0.2%)
Need at least one extra disk between the endcap and the forward disks
  Decreases background in the error ellipse by a factor of 5

## Slide 16: Next steps
Plan to also check pattern recognition constrains between
  inner and outer barrel
  inner and outer endcap
Note:
Having time resolution of the order of 0.1 ns would allow to decrease background for pattern recognition.

## Slide 17: Backup

## Slide 18
Proposal 1b (from occupancy point of view)
10x15
10x30
10x100
In terms of occupancy , one could use lowest resolution down to R<200mm. To be checked: pattern recognition and d0,z0 resolution

## Slide 19: Occupancy
Occupancy map from Ilaria
Notes: ----- Meeting Notes (27/10/16 14:59) -----
disk projection
ask which prjection ilaria used
check if integrated over time
16 Nov next FCChh meeting

## Slide 20
Irradiation map provided
  Independent of the orientation of the surface
  http://www.fluka.org/content/course/NEA/lectures/Scoring.pdf
  Original map interpolated to obtain more precise values

## Slide 21
Given the fluence map, what is the minimum granularity needed in each part of the detector, to make sure there will be only one particle firing a pixel?
Assume we need the occupancy <=0.01 (to be reviewed)
Assume cluster size due to difussion = 1
Assume # Pile up interactions per bunch crossing =1100
1) Constraints from fluence on detector granularity
Occupancy = Fluence * Pile up * PixelArea * ClusterSize(Diffusion)
# particles per unit area, per pp collision
# of pp collisions per Bunch Crossing (BC)
per Bunch Crossing
# hit pixels per perpendicular particle
Cluster size has 2 components:
geometric:
diffusion:
included in the fluence calculation
assumed to have no diffusion (size=1)

## Slide 22: RD53
https://indico.cern.ch/event/527359/contributions/2158545/attachments/1278486/1898346/LHCC_status_report_2016_v5.pdf

## Slide 23
Irradiation Map [cm^-2] (original)

## Slide 24
Interpolated Irradiation Map [mm^-2] (zoom in low R, full Z, removed beampipe area)
increases with z

## Slide 25
σ(fwd layers)=25x25
1 middle layer
pile up=1100
EllispeArea
“Occupancy”
versus radius at last encap layer
versus eta
pile up=1100
PRELIMINARY
EllispeArea
“Occupancy”

## Slide 26: occupancy dependence with the angle
pT=1 GeV
pT=2 GeV
pT=5 GeV
pT=10 GeV
Occupancy
Single point resolution
Eta
Gap distance
pT
pile up=1100
pile up=200

## Slide 27
NO MultipleScattering
MultipleScattering
  A= ¼ * π * res(Rphi) * res(z) * tan(theta)
NO MultipleScattering
MultipleScattering
Occupancy = Irradiation[mm^-2] *
10^-6 [mm^2 / um^2] * Area [um^-2]
Cross-checking area and occupancy calculations
pT [GeV]
pT [GeV]
δ RPhi
δ z0
tan Theta
Ellipse area
Irradiation
Occupancy

## Slide 28
eta=-ln[tan(theta/2)] ; p=pT*cosh(eta)
pT
theta=0.39 deg ; eta=5.683
pT=1 GeV  p=146.9 GeV
p
theta=5.49 deg ; eta=3.04
pT=1 GeV  p=10.45 GeV
pT
p
Cross-checking area and occupancy calculations

## Slide 29
p
pT
  A= ¼ * π * res(Rphi) * res(z) * tan(theta)
p
pT
Occupancy = Irradiation[mm^-2] *
10^-6 [mm^2 / um^2] * Area [um^-2]
Cross-checking area and occupancy calculations
p [GeV]
pT [GeV]
δ RPhi
δ z0
tan Theta
Ellipse area
Irradiation
Occupancy
equivalent for eta=5.7

## Slide 30
New baseline geometry from Zbynek: http://fcc-tklayout.web.cern.ch/fcc-tklayout/FCChh_Option3.v01
longer inner barrel layer,
lighter 1st and 2nd barrel (X/X0=0.5%, others 1.5%)
worse single point resolution assumed
Notes: ----- Meeting Notes (27/10/16 14:59) -----
check why worse resolution