## Slide 1: Magnetic design
Michinaka Sugano
D1 magnet review, KEK, 30 June – 1 July 2016

## Slide 2: Outline
Magnetic design for 7 m production magnet
  Optimization of 2 D cross-section
    Management of iron saturation
    Error analysis
    Design change of yoke (rectangular notch)
  Optimization of coil end
  3D field calculation in 7 m magnet
From 7 m to 2m magnet
  Field calculation of 2 m magnet considering KEK vertical test stand

## Slide 3: Optimization of 2D cross-section

## Slide 4: Fixed conditions for optimization
19
13
8
4
44 turns
Coil
  f150 mm bore
Yoke
  OD: 550 mm
  HX hole: f60 mm at R190
Cryostat
  ID: 890 mm, 12 mmt
Based on our early design study, the following conditions were fixed in optimization.
  Single layer coil (for better cooling and maximizing the amount of iron)
  4 coil blocks, totally 44 turns (19, 13, 8, 4 turns from MP)
  Iron cryostat was taken into consideration.
Reference radius in ROXIE calculation: 50 mm
Yoke
Collar
Cryostat
Coil blocks
HX hole

## Slide 5: Features to minimize iron saturation effect
  Triangular notch
  Field tuning holes
Iron saturation effect on multipole coefficients can be more gentle
w and w/o field tuning holes
w and w/o
triangular notch
Triangular
notch
Field tuning hole

## Slide 6: Optimization of coil block arrangement
 | Iron yoke (Ver3.0)
Main field (T) | 5.573
b3 (unit) | -0.059
b5 (unit) | -0.097
b7 (unit) | -0.111
b9 (unit) | 0.284
b11 (unit) | 0.360
b13 (unit) | -0.663
b15 (unit) | -1.115
b17 (unit) | -0.788
b19 (unit) | 0.399
All of multipoles except for b15 can be controlled below 1 unit.
Multipole coefficients
at I=12 kA

## Slide 7: Error analysis
Systematic error
  Packing factor of iron yoke: -1.2 unit
  Stainless collar (mr=1.002): -0.6 unit
  Coil mispositioning
Random error: sb3=0.5 unit for d=25 mm
Change of b3 by each factor
 | Dx = -50 mm | Δy = 50 mm
CB1 | 1.40 | -2.20
CB2 | -1.44 | -1.20
CB3 | -0.81 | 0.68
CB4 | 0.24 | 0.51
Coil mispositioning
Db3 wrt Dx=Dy=0 (unit)
CB1
CB2
CB3
CB4
x
y

## Slide 8: Design change of iron yoke (Rectangular notch)
I=12 kA | Iron yoke w/o rect. notch (Ver3.0) | Iron yoke w rect. notch (Ver3.0.2)
Main field (T) | 5.573 | 5.568
b3 (unit) | -0.059 | 5.161
b5 (unit) | -0.097 | -1.462
b7 (unit) | -0.111 | 0.193
b9 (unit) | 0.284 | 0.224
b11 (unit) | 0.360 | 0.371
b13 (unit) | -0.663 | -0.666
b15 (unit) | -1.115 | -1.116
b17 (unit) | -0.788 | -0.788
b19 (unit) | 0.399 | 0.399
Rectangular notch
ROXIE model
(Ver3.0.2)
After 2D optimization, we needed to add a rectangular notch to yoke as a coil alignment feature.  Increase of b3 and b5 by 5.2 and -1.4 units
Further calculation confirmed that slight coil block re-arrangement can correct these field errors. Coil block arrangement was NOT changed in MBXFS01.
Yoke
Collar
Mechanical model

## Slide 9: Transfer function
Decrease of transfer function by 10% due to iron saturation
Ver3.0.2
(w Rectangular notch)

## Slide 10: Current dependence of multipole coefficients
Variation of b3 is within ±20 units.
Results of Ver3.0.2 (w Rectangular notch)

## Slide 11: Optimization of coil end

## Slide 12: Coil end in “test coil”
Coil end shape was modified from the design of a “test coil” fabricated in 2014.
Issues in the test coil
  Average b3=8.3 unit should be reduced.
   Further optimization of axial position of each coil end block
  Compact coil end resulted in more inclined cables at coil end
   Cable angle, length of curved section and curvature
To reduce peak field and make the prediction of angle of the last turn in a coil block easy
 Subdivision
Test coil (Ver2.1)
1
2
3-A
3-B
4-A
4-B

## Slide 13: Approximation in 3D model
In 3D field calculation, a simplified iron model was used to reduce computational time.
Applying this simplified model to 2D calculation results in difference of b3 by 2.0 units and b5 by -0.39 units in comparison with the full iron model.
Target values of b3, b5 and b7 for 3D field optimization were set based on these differences.
Full iron model for 2D
Simplified iron model for 3D
Optimization was done for the 3D model
without rectangular notch.

## Slide 14: Results on optimization of coil ends
1-A
1-B
2
3-A
3-B
4-A
4-B
4
3
2
1
 | 7 m production magnet (Ver3) | 
(unit) | Target value | Ave. field harmonics
 | — | 10000
 | 2.020 | 2.510
 | -0.387 | -0.116
 | -0.054 | -0.698
 | — | -0.449
 | — | 0.033
 | — | -0.718
 | — | -1.085
 | — | -0.737
 | — | 0.379
 | — | -4.745
 | — | 1.666
Definition of Average multipole coefficients
Large gap between 1-B and 2
Average b3 within 0.5 unit
wrt the target value
Subdivision of the 1st block
Load line ratio at coil end:
78%  76%
Sufficient length of curved section
Average multipole coefficient at I=12 kA

## Slide 15: 3D field calculation in 7 m magnet

## Slide 16: Magnetic field distribution
Positive integrated b3 in SS is compensated with negative one in the coil ends.
Large a1 and a3 due to ramp leads
Mechanical length of 6.57 m for 35 Tm is acceptable for cold tests in the KEK cryostat.
RE
LE
 | Total | RE | SS | LE
z | -4m ~ 4m | -4 m ~ -2.34 m | -2.34m ~ 2.34m | 2.34m ~ 4m
 | 35.4 | 4.60 | 26.2 | 4.59
 | 0.00889 | -0.0065 | 0.0194 | -0.0041
 | -0.00041 | -0.0010 | -0.0001 | 0.0007
 | -0.00247 | -0.0016 | -0.0002 | -0.0007
 | -0.0168 | 0.0000 | 0.0001 | -0.0169
 | 0.00590 | 0.0000 | 0.0000 | 0.0059
 | Total | RE | SS | LE
z | -4m ~ 4m | -4 m ~ -2.34 m | -2.34m ~ 2.34m | 2.34m ~ 4m
 | 35.4 | 4.60 | 26.2 | 4.59
 | 0.00889 | -0.0065 | 0.0194 | -0.0041
 | -0.00041 | -0.0010 | -0.0001 | 0.0007
 | -0.00247 | -0.0016 | -0.0002 | -0.0007
 | -0.0168 | 0.0000 | 0.0001 | -0.0169
 | 0.00590 | 0.0000 | 0.0000 | 0.0059
Field integral for SS and ends at I=12 kA (Tm)
SS

## Slide 17: Influence of coil end on field quality
b3 is not flat at the longitudinal center even in 7 m coil.
 Influence of coil end is not negligible.
Such an effect of coil end is more remarkable in 2 m model magnet.
RE
LE
b3 in SS of 7 m magnet
2D calculation

## Slide 18: Peak field
Peak field appears at the innermost turn in the CB3 (Block 8, 15, 22)
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
19
20
21
23
24
22
LE
RE
Block No. | Maximum field (T)
8 | 6.56
15 | 6.54
22 | 6.55
Peak field
Peak field

## Slide 19: Load line curve
Load line ratio: 75.4% in straight section
76.6% at coil end

## Slide 20: From 7 m magnet to 2 m model

## Slide 21: KEK vertical test stand
The model for MBXFS01 was built only by shortening the straight section of the 7 m magnet. The coil end design is the same.
Iron model with rectangular notch was adopted.
In 2 m model, we replaced the LHC cryostat by the iron pit in the underground test hole at KEK.
Iron pit in the underground test hole
(OD2062 mm, t22 mm)

## Slide 22: 2D calculation of 2 m model
Additional b3 due to rectangular notch is almost cancelled by changing the cryostat condition.
Multipole coefficients at I=12 kA
 | Iron yoke w LHC cryostat (Ver3.0.2) | Iron yoke w iron pit (Ver3.0.2)
Main field (T) | 5.568 | 5.547
b3 (unit) | 5.161 | -0.258
b5 (unit) | -1.462 | -1.856
b7 (unit) | 0.193 | 0.183
b9 (unit) | 0.224 | 0.235
b11 (unit) | 0.371 | 0.378
b13 (unit) | -0.666 | -0.672
b15 (unit) | -1.116 | -1.119
b17 (unit) | -0.788 | -0.791
b19 (unit) | 0.399 | 0.400

## Slide 23: Comparison btw 7 m magnet and 2m model
Design parameters | 2 m model | Production
Nominal current | 12.0 kA | 
Coil aperture | 150 mm | 
Field integral | 9.8 Tm | 35 Tm
Nominal dipole field | 5.57 T | 
Coil peak field | 6.44 T in the straight section | 
 | 6.56 T at coil end | 
Load line ratio | 75.4% in the straight section | 
 | 76.6% in coil end | 
Differential inductance | 3.95 mH/m | 
Stored energy | 340 kJ/m | 
Coil mechanical length | 2.00 m | 6.57 m
Magnet mechanical length | 2.15 m | 6.72 m
Magnetic length | 1.73 m | 6.33 m

## Slide 24: Summary
Magnetic design was performed for 7 m production magnet.
As a result of optimization of 2D cross-section, multipole coefficient was able to be controlled within allowable level including variation during current ramping-up.
The results of 3D field calculation suggest that field quality at the coil center is affected by coil end even in 7 m magnet.
The 2 m model was built by shortening the straight section of the 7 m magnet with the same coil end.