## Slide 1: Mechanical design
Michinaka Sugano
D1 magnet review, KEK, 30 June – 1 July 2016

## Slide 2: Outline
Mechanical calculation with ANSYS
  Calculation for each assembly step, cooling and excitation
  Estimation of required pre-stress
Assembly of 200 mm long mechanical model
  Validation of assembly procedure
  Evaluation of pre-stress of coils
Coil end support
  GFRP collar
  Longitudinal support

## Slide 3: Mechanical calculation with ANSYS

## Slide 4: ANSYS model
0.5 unit thickness
for each layer
Lorentz force
In coil at nominal current
1.5 MN/m
0.6 MN/m
Simulation steps of the ANSYS 2D 2-layer model
Collaring
< 10 MPa pre-stress in coil by applying load on the stainless steel spacer;
Yoking (2 steps)
1. Applying load on the yoke shoulder to close the gap between top and bottom yokes;
2. Remove the load, insert the lock-keys;
Shell welding
Including stress from the stainless steel shell;
Cool-down to 2K;
Excitation.
Boundary conditions
Symmetry condition: UX = 0 in line X = 0;
Friction coefficient of 0.2 for all the internal interfaces;
Mechanical design for 110% of the nominal current;
Shear stress in lock-keys is not included
SS304L Shell

## Slide 5: Mechanical properties in the ANSYS model
Same with MQXC magnet (data from M. Segreti’s ppt file: “Mechanical computation of MQXC magnet”)
Parts | Material | Young's modulus (GPa) 2K/293K | Thermal expansion coefficients (2K - 293K) | 
 |  |  | unit: K-1 | Integrated
Coil blocks | / | 7.7 / 5.5 | 2.42E-05 | 7E-03
Wedge | Copper | 136 / 136 | 1.14E-05 | 3.3E-03
Yoke & keys | Iron | 224 / 213 | 6.82E-06 | 1.97E-03
Ground insu. | Mix Kapton-G11 (50%/50%) | 5.2 / 4.45 | 2.42E-05 | 7E-03
Collar-Spacer | SS316L | 210 / 205 | 9.97E-06 | 2.90E-03
Shell | SS316L | 210 / 205 | 9.97E-06 | 2.90E-03
GFRP wedges were used in the actual coils.

## Slide 6: Yoking – Loading on yoke shoulder
2.3 MN/m load applied on the shoulder of the iron yoke to close the initial gap between top and bottom yokes.
UX = 0
UY = 0
Collar
Coil
Yoke
Required load:
2.3 MN/m
0.5 unit
thickness
Stress in the yoke
Stress in the coil

## Slide 7: Yoking – Key insertion
UX = 0
UY = 0
Collar
Coil
Yoke
0.5 unit
thickness
Remove load from the yoke shoulder and insert the load-key; The gap between top and bottom yokes keep closed at both ends.
Shear stress in lock-keys is not included
Stress in the yoke
Stress in the coil
Highest stress at key slot
< 220 MPa would be feasible.

## Slide 8: Shell welding
UX = 0
UY = 0
Collar
Coil
Yoke
0.5 unit
thickness
Including the shell stress by making a ~1 mm displacement at one end of the shell;
~1 mm displacement in x direction
Stress in the yoke
Stress in the coil

## Slide 9: Cooling down to 2 K
UX = 0
UY = 0
Collar
Coil
Yoke
Cool down to 2 K; The gap between top and bottom yokes keep closed at both ends.
~1 mm displacement in x direction
0.5 unit
thickness
Stress in the yoke
Stress in the coil

## Slide 10: After excitation
UX = 0
UY = 0
Collar
Coil
Yoke
Applying Lorentz force transferred from the magnetic simulation results.
~1 mm displacement in x direction
Simulation model
(top half)
0.5 unit
thickness
Stress in the yoke
Stress in the coil

## Slide 11: Coil stress at each step
Required pre-stress to keep the coils in compression even after excitation to 110% of the nominal current:
  Pole average: 70 MPa, MP average: 94 MPa
The target value of pre-stress at pole was set to be 80 MPa including 10 MPa margin.
Pole
MP

## Slide 12: Assembly of 200 mm long mechanical model

## Slide 13: 200 mm mechanical short model
Validation of mechanical structure of D1
Items to be checked
Variation of coil pre-stress through the processes
Tooling and jigs: collaring mandrel, collaring press, ···
Structure of electrical insulations
4-way split collar concept
Yoking process
  Alignment of collared coil with respect to yoke
  Cantilever mechanism and lock by keys
Process of shell welding
1. Pre-assembly: coil, (QPH), electrical insulations, brass shoe
2. Collaring
3. Yoking
4. Shell welding
5. Cooling test
Assembly steps and tests
4 way sprit collar

## Slide 14: 2 m test coil
2 m test coil fabricated in 2014
  Almost the same 2D cross-section as MBXFS01
  Radiation resistant GFRP wedges
Homogeneous coil size in the straight section was confirmed by coil size measurement.
200 mm long cutouts from the straight section were used for the mechanical model.

## Slide 15: Ground insulations and brass shoes
QPH: 0.25 mm thick
Replaced by polyimide sheets with the same thickness
Ground insulations
  4 layers of 0.125 mm thick polyimide sheet
  Gap in between the insulations to accommodate large coil shrinkage
  Gap position was modified in MBXFS01 to simplify assembly work.
Brass shim and shoe
  1 mm thick brass shim at pole
  0.5 mm thick brass shoe

## Slide 16: Collaring mandrel
Support and help by Glyn Kirby (CERN)
Polyethylene
pushing bar
Central core
Flat roller
O-ring
Pushing bars can move in the radial direction by spring mechanism and support the coil inner radius.
The central core can be pulled out smoothly thanks to the flat rollers after yoking and the pushing bars can be removed.

## Slide 17: Strain gauges
17
Collar
Yoke
Shell
Collar
  To monitor pole stress
  Strain gauges were calibrated at RT and 77 K.
  Measurement of apparent strain between RT and 77 K
Yoke
  To check contact between upper and lower yoke
  Measurement of apparent strain between RT and 77 K
Shell
  To monitor shell strain during shell welding and cooling

## Slide 18: Collaring
Collaring press
(Almost no coil stress)
Preliminary assembly
Insertion of lock pins to link the sub-stacks
Fabricated by fine-blacking
Alternate stack of S- and F- collar
0.2 mm-high emboss and rectangular groove for better cooling
F-vertical
S-vertical
F-horizotal
S-horizotal

## Slide 19: Concept of alignment of collared coil in yoking
Iron yoke
Triangular notch
Rectangular
notch
Side taper
Yoke
Collar
Preliminary yoking test
Collared coil was rotated wrt yoke
Modified collar and yoke design
Side taper to prevent side collars from rotation
Rectangular notch to block rotation of vertical collars
Triangle notch for final alignment
The concept of coil alignment was verified in a yoking trial.
Such a rectangular notch leads to additional b3 of 5 units.

## Slide 20: Yoking
Side tapers and rectangular
notches functioned as expected.
Key insertion
Loading to
yoke shoulder
Before yoke pressing
Three keys in each side
could be inserted at
hydraulic pressure of
44 MPa (4.2 MN/m/side).

## Slide 21: Pole stress during yoking
A
B
C
A: Contact of upper/ lower yoke
B: Key insertion
C: Completion of yoking
Collar (Pole stress)
Yoke
A
B
C
Coil pole stress after yoking: 69±5 MPa
Partial relief of coil pole stress was observed due to creep only by a few MPa over 60 hrs.
Yoke gauges
C1-R
C1-L
C2-R
C2-L

## Slide 22: Shell welding and cooling test
Gap
Strain gauges
Tensile strain
Welded
Direction of thermal stress by cooling
Shell welding
Cooling test (77 K)
Two halves of stainless steel shells (SUS304L) were welded manually.
Tensile strain in the azimuthal direction started to develop when the gap between upper and lower halves was close.
No remarkable change of coil pole stress was observed by shell welding.

## Slide 23: Variation of coil pole stress
Collaring
Applied load to
yoke shoulder
Key
insertion
Before
shell welding
Shell
welding
Before
cooling
Cooling
at 77 K
ANSYS calculation
Measured coil pole stress
Target pre-stress of 80 MPa at RT
Pre-stress after yoking of 69±5 MPa is lower than the target value of 80 MPa.
Stress release after cooling-down: 23 MPa in measurement
13 MPa in calculation
23 MPa
13 MPa
Pre-stress
after yoking

## Slide 24: Mechanical structure at coil end

## Slide 25: Pre-stress at coil end
Dt =
0.24 mm
Linear taper
GFRP end saddle was made thicker at the end so that the pre-stress can be applied during yoking.
Target value: 50 MPa
50 MPa

## Slide 26: GFRP collar at lead end
GFRP collar
Ramp box
Radiation resistant GFRP collars cover the lead end.
Circumference of the GFRP collars was oversized to clamp the ramp boxes with pre-stress of 40 MPa
 Pre-stress was checked in the yoking process.
Four-split GFRP collar

## Slide 27: Longitudinal support
The coils and yokes were longitudinally supported from the end plates with bullets.
Preload applied to the coil was determined to be 5.2 tonf /coil (pressure of 12.3 MPa at coil end) from experience of MQXA.
In MBXFS01, strain of bullets was not monitored.
Red: Bullets for coils
Blue: Bullets for yoke

## Slide 28: Summary
Based on ANSYS calculation, the target value of coil pre-stress at pole was determined to be 80 MPa.
The 200 mm mechanical short model was assembled and validity of assembly process could be confirmed.
Coil pre-stress at pole after yoking was 10 MPa lower than the target value. Stress release after cooling-down of 23 MPa was 10 MPa larger than the calculation.