## Slide 1: HL-LHC Optics Constraints for Dump Region
C. Bracco, B. Goddard, C. Wiesner, M. Fraser, A. Lechner, M. Frankl
Acknowledgment: ABP

## Slide 2: Main Constraints:
Q4 gradient fixed within maximum ±1%
Horizontal phase advance MKDsTCDQ 90˚± 4˚
TCDS: by,min ≥ 200 m (no more than 10% smaller than present value)
TCDQ: by,min ≥ 145 m (no more than 10% smaller than present value), bx,min ≥ 630m and |Dx| ≤0.2m
TDE: (bx X by) ½ ≥ 4500 and bx,min ≥ 4000 m and by,min ≥ 3200 m (no more than 20% smaller than present value)
TCDQ movement during squeeze unidirectional and towards the beam, accumulated mechanical play  degraded alignment precision (required ±0.1 mm)! Need BETS redesign.
Phase advance MKDTCTs 0˚ or 180 ˚(± 10˚)
TCDS-MSD: bx,max ≤ 175 m (aperture limitation extraction channel at injection).
Disclaimer:
Optics constraints related to machine aperture (circulating beam) are not treated in this talk (assumed as part of standard checks performed by ABP team)

## Slide 3: FLUKA calculations at TCDQ
7 TeV, TCDQ Half gap = 8.6 sb  0.5 s (~250 mm) misalignment included  8.1 s = 4 mm (present optics and 3.5 mm mrad normalised emittance)
Close to limits!
A. Lechner
Type 2 erratic

## Slide 4: Present Collimator Settings @ 6.5 TeV (40 cm b*)
TCP
TCSG
TCDQ
5.5 s
7.5 s
8.3 s
2.8 s = 1.4 mm (nom. b)
Present SIS interlock on local orbit at TCDQ = +/- 1.2 mm  possible moving orbit locally towards the TCDQ without losses (beam cut at 5.5 s at TCPs)
Run 2 nominal settings at collision (40 cm b* in IP1 and IP5): TCDQ at 8.3 s = 4.2 mm
Consider 0.5 s setup error  7.8 s = 3.95 mm
SIS on orbit at TCDQ = ±1.2 mm  gap could go down to 2.7mm.
Scaling from FLUKA calculations and assuming a bunch population of 1.15e11 p+ this gives a maximum energy density of 2.2 kJ/cm3 and a maximum temperature of <1000˚C

## Slide 5: HL-LHC Collimator Settings @ 7TeV (20 cm b*)
TCP
TCSG
TCDQ
5.7 s
7.7 s
9 s
3.3 s = 1.7 mm (nom. b)
Assuming a maximum allowed temperature of 1400 ˚C (“grey zone” for graphite, still ANSYS simulations needed!!)  minimum gap = 3.6 mm
0.25 mm setup error  minimum gap = 3.85 mm
SIS interlock 1.2 mm  minimum gap = 5.05 mm  Minimum allowed bx = 630 m
Chart: SIS interlock [m]
| 1.1999999999999999E-3 | 5.9999999999999995E-4 | 2.9999999999999997E-4 | 1.4999999999999999E-4
9 sigma | 629.6914 | 488.9506 | 425.2469 | 395.0617
8.3 sigma | 740.3832 | 574.902 | 500 | 464.5086
630
740
490
575

## Slide 6: Summarising for TCDQ Minimum bx
Need to asses if Type 2 erratic (and any worse case) can be avoided
Need to confirm that SIS interlock on orbit at TCDQ can be reduced and to which level without impacting machine availability
Need to perform ANSYS calculations to assess if Graphite and CFC would withstand the beam impact in case of Type 2 erratic and limit optics conditions (e.g. 0.6 mm interlock and bx = 490 m)
Once defined previous points, decide if upgrading TCDQ with more robust material (3D C-C?)  impact on the cost (not in baseline)!
bx change TCDQ_UP and TCDQ_DW < 5%

## Slide 7: Horizontal Dispersion at TCDQ
Momentum spread at top energy = 1.13e-4
Total Dp/p = momentum offset + 2*momentum spread
bx
bx
bx
bx

## Slide 8: Present TCDQ Real Cut
TCDQ
Global bottleneck
TCDQ
TCSG
TCP
TCDQ set at 8.3 snom (betatron)  x= 4.2 mm
Real cut xCut [snom ] can be calculated from:
x = xCut * snom + Dx* Dp/p + xdump
xCut contains optics and alignment errors during the setup
xdump is the local orbit at the moment of the asynchronous dump (at present up to ±1.2 mm)
Protection of machine aperture always granted!
Hierarchy wrt TCSG broken for xdump > ± 0.120 mm independently on Dx
Hierarchy wrt TCP broken for |Dx| > 0.9 m

## Slide 9: HL-LHC TCDQ Real Cut
TCDQ
TCDQ
TCSG
TCP
TCDQ set at 9 snom (betatron)  x= 4.5 mm
Real cut xCut [snom ] can be calculated from:
x = xCut * snom + Dx* Dp/p + xdump
xCut contains optics and alignment errors during the setup
xdump is the local orbit at the moment of the asynchronous dump (at present up to ±1.2 mm)
Protection of machine not provided! Either reduce SIS interlock or larger machine aperture (phase advance of global bottleneck wrt MKD not taken into account) or closer TCDQ (possible damage in case of type 2 erratic)
Hierarchy wrt TCSG broken for xdump > ± 0.200 mm independently on Dx
Hierarchy wrt TCP ok
Global bottleneck

## Slide 10: HL-LHC TCDQ Real Cut
TCDQ
Global bottleneck
TCSG
TCP
SIS interlock 0.6 mm  |Dx|≤ 0.2 m
Chart: Aperture bottleneck[sigma]
| 11.4 | 11.6 | 11.8 | 12 | 12.2
 | 0 | 0.2 | 0.45 | 0.7 | 0.9
±1.2mm xdump
Chart: SIS interlock [m]
| 0.6 | 0.5 | 0.4 | 0.3
 | 0.2 | 0.5 | 0.7 | 0.9
10.4 s aperture

## Slide 11: HL-LHV1.2 Squeeze Round
Squeeze
Dx @ TCDQ calculated from Dx and DxP @ IP6
Almost all conditions fulfilled but:
  Dispersion @ TCDQ (to be reminded that this constraint depends on the SIS interlock for local orbit @ TCDQ and TCDQ half-gap)
  bx @ TCDQ only for SIS interlock of 0.6 mm and 9 s half-gap
  TCDQ moving away from the beam during the squeeze (4.5 mm  5.5 mm, ~2s movement)
Maximum
http://lhc-optics.web.cern.ch/lhc-optics/HLLHCV1.2/squeeze/

## Slide 12: HL-LHV1.2 Squeeze Flat
Squeeze
Dx @ TCDQ calculated from Dx and DxP @ IP6
Almost all conditions fulfilled but:
  Dispersion @ TCDQ (to be reminded that this constraint depends on the SIS interlock for local orbit @ TCDQ and TCDQ half-gap)
  bx @ TCDQ only for SIS interlock of 0.6 mm and 9 s half-gap
  TCDQ moving away and towards the beam (maximum movement 5.00 mm  5.4 mm, ~0.8 s). If maximum variation < 1 s (< 0.5 mm) TCDQ could be set to the closest position already before the squeeze (possible coll. hierarchy violation)
http://lhc-optics.web.cern.ch/lhc-optics/HLLHCV1.2/squeeze/

## Slide 13: HL-LHV1.2 Squeeze FlatHV
Squeeze
Dx @ TCDQ calculated from Dx and DxP @ IP6
Almost all conditions fulfilled but:
  Dispersion @ TCDQ (to be reminded that this constraint depends on the SIS interlock for local orbit @ TCDQ and TCDQ half-gap)
  by @ TCDS
  bx @ TCDQ only for SIS interlock of 0.6 mm and 9 s half-gap
  TCDQ moving away and towards the beam (4.5 mm  5.5 mm, ~2s movement)
http://lhc-optics.web.cern.ch/lhc-optics/HLLHCV1.2/squeeze/

## Slide 14: Beta @ MKD
Minimum
Present
Minimum
580 m
640 m
C. Wiesner
Minimum
Present
Minimum
125 m
200 m
TDE
TDE
Maximum bx,y (now 540 m and 216 m respectively) defined by available aperture for circulating beam at injection (ABP checks)

## Slide 15: Conclusions 1/2
Present HL-LHCV1.2 optics:
Q4 gradient fixed within maximum ±1%: OK
Horizontal phase advance MKDsTCDQ 90˚± 4˚: OK
TCDS: by,min ≥ 200 m: OK (not OK for FlatHV but probably not critical) (ANSYS calculations needed for final confirmation)
TDE: (bx X by) ½ ≥ 4500 and bx,min ≥ 4000 m and by,min ≥ 3200 m: OK (ANSYS calculations needed for final confirmation).
TCDS-MSD: bx,max ≤ 175 m at injection (aperture limitation): OK
Phase advance MKDTCTs 0˚ or 180 ˚(± 10˚) (not yet checked)

## Slide 16: Conclusions 2/2
Present HL-LHCV1.2 optics:
TCDQ:
  by,min ≥ 145 m: OK (ANSYS calculations needed for final confirmation)
  bx,min ≥ 630 m for present ±1.2 mm SIS interlock on local orbit and 9 s half-gap (to avoid TCDQ damage in case of Type2 erratic): not OK. Need to assess if:
    Type 2 erratic (or worse) can be avoided
    Possible to reduce SIS limit without impacting machine availability: if ≤0.6 mm  bx,min ≥ 490 m: OK (ANSYS calculations needed for final confirmation)
    TCDQ material upgrade  impact on cost (not in baseline)
    TCDQ movement during squeeze unidirectional and towards the beam: not OK. Try to keep total needed displacement <1s  move TCDQ to closest position before squeeze (possible hierarchy violation)  no BETS upgrade needed!
  |Dx| ≤ 0.2 m (TCDQ hg = 9s) provided that either global aperture bottleneck ≥ 11.6s or SIS interlock can be reduced to ≤0.6 mm (aperture 10.4s ): not OK

## Slide 18: Present Optics Parameters
Beam 4 | MKD | MQ4 | TCDS | MSD | TCDQ | MQ4 | MQ5
Bx_min [m] | 248.0 | 217 | 152.2 | 156.1 | 479.2 | 576.0 | 164.2
Bx_max [m] | 568.9 | 218.6 | 154.4 | 230.6 | 510.9 | 576.7 | 165.8
By_min [m] | 192.4 | 583.4 | 240.0 | 147.2 | 158.9 | 193.4 | 578.7
By_max [m] | 531.1 | 586.5 | 247.9 | 234.5 | 169.2 | 193.7 | 581.5
Dx_max (abs) [m] | -0.053 | -0.051 | -0.150 | -0.205 | -0.294 | -0.308 | -0.157
Dmux_MKD_centre [deg] | 0 | 3 | 51 | 64 | 94 | 97 | 103
Beam 1 | MKD | MQ4 | TCDS | MSD | TCDQ | MQ4 | MQ5
Bx_min [m] | 250.9 | 203.1 | 153.3 | 157.2 | 483.5 | 549.9 | 147.1
Bx_max [m] | 542.8 | 219.3 | 156.7 | 235.9 | 505.5 | 570.5 | 162.2
By_min [m] | 215.6 | 588.8 | 224.6 | 134.7 | 161.4 | 197.3 | 602
By_max [m] | 533.1 | 609.5 | 236.9 | 222.9 | 169.8 | 214.4 | 604.6
Dx_max (abs) [m] | -0.143 | -0.093 | -0.063 | -0.061 | -0.023 | -0.017 | +0.002
Dmux_MKD_centre [deg] | 0 | 3 | 51 | 65 | 94 | 96 | 103

## Slide 19
TCDQ
Global bottleneck
TCSG
TCP
Chart: SIS interlock [m]
| 0.6 | 0.5 | 0.4 | 0.3
 | 0.2 | 0.5 | 0.7 | 0.9
SIS interlock 0.6 mm  |Dx|≤ 0.2 m
Chart: Aperture bottleneck[sigma]
| 11.4 | 11.6 | 11.8 | 12 | 12.2
 | 0 | 0.2 | 0.45 | 0.7 | 0.9
±1.2mm xdump
10.4 sigma aperture
Q4
bx
bx