## Slide 1: Multi Purpose Detector at NICA: Status and Prospects
V.Kekelidze,
Joint Institute for Nuclear Research
NICA
Volga river
6-th International Conference
on New Frontiers in Physics
17-29 August 2017
Notes: Ladies and gentlemen, dear colleagues, first of all I would like to express my gratitude for the kind invitation and for the given opportunity to present
a progress in MPD and BM@N experiment preparation

## Slide 2
MPD
NICA major facility
Nuclotron ring (c=251,5 m)
Notes: This is a view of major NICA facilities. The Nuclotron – supercoducting synchrotron with circumference of 250 meters was put in operation 24 years ago. The beams from Nuclotron are extracted to the experimental hall, where the first experiment of NICA program BM@N is located. The plan is to put in operation a booster in 2019, and collider - in 2020 simultaneously with the MPD.

## Slide 3
The Collider
45 T*m, 4.5 GeV/u for Au79+
Double aperture magnets:
dipole & quadrupole
prototypes
MPD
SPD
Ring circumference, m | 503,04
Number of bunches | 22
r.m.s. bunch length, m | 0,6
b, m | 0,35
max. int. Energy, Gev/u | 11,0
r.m.s. Dp/p, 10-3 | 1,6
IBS growth time, s | 1800
Luminosity, cm-2 s-1 | 1x1027
Notes: The lattice design and prototyping of most collider elements are completed. The ring circumference is twice as one of the Nuclotron. For the gold beam a Luminosity at the energy above 10 GeV per nucleon will be 10 to the 27

## Slide 4
Exploration of the QCD PD - Density Frontier
NICA
Exploring high-density baryonic matter: maximum freeze-out density
J. Randrup, J. Cleymans; White Paper
NICA is well suited for exploring the transition between the hadronic and q-g phases at the high net baryon density.
This is the top priority of the NICA program.
Notes: One of the most urgent task for the study of QCD phase diagram is density frontier. According various calculations maximum freeze-out density is reached at the energy range around 10 GeV per n. NICA is well suited …

## Slide 5
STAR F.T.
HADES
CBM
Interaction rate [Hz]
Collision energy √S [GeV]
NN
NICA/BM@N II
Present and future HI experiments
NA-61/SHINE
2022 – 2025: SIS-100 FAIR
energy region of max.
baryonic density
NICA/MPD
STAR BES II
Notes: The landscape of HIC experiments, present and future, in the energy region of max baryonic density are presented in this figure. Among fixed target experiments CBM at FAIR will provide maximum interaction rate& There are only two collider experiments – NICA and STAR BES with a difference in interaction rate 2-3 orders of magnitude.
Two NICA experiments - BM@N with fixed target and MPD at the collider will cover the whole indicated energy region.

## Slide 6
Physics objectives
Bulk properties, EOS
- particle yields & spectra, ratios, femtoscopy, flow
In-Medium modification of hadron properties
- onset of low-mass dilepton enhancement
Deconfinement (chiral) phase transition at high rB
- enhanced strangeness production
QCD Critical Point
- event-by-event fluctuations & correlations
Chiral Magnetic (Vortical) effect, L polarization
Y-N interactions in dense nuclear matter
- hypernuclei

## Slide 7
Strangeness Enhancement: SPS CERN, RHIC
hyperon production
x 2
x 5
x 20
Thermal/Statistical model:
Indication to chiral symmetry restoration
energy region of NICA
NA49 : Phys. Rev. C 77, (2008)
STAR : QM2011 proceedings
“Horn” effect
onset of
deconfinement ?
requires more detailed study
Notes: Strangeness enhancement yield in HIC versus nn-collisons was observed at the SPS experiments and than confirmed at RHIC. This enhancement is rather high. Taking into account that strangeness is mostly produced by gluon fusion, this observation could indicate to chiral symmetry restoration. The NA49 experiment obtained that K+ yield has a pick at the energy around 8 GeV/u in the cms. The possible explanation this effect as “onset of deconfinement” requires more detailed study. NICA could provide corresponding investigation.

## Slide 8
C. Blume,
SQM-2017
Energy Dependence of Total Yields
NICA
Hypernuclei production enhanced at high baryon densities (NICA)
NICA
A. Andronic et al., Phys. Lett. B697 (2011) 203

## Slide 9
NICA
NICA
D. Tlusty, SQM-2017
maximum net baryon density of GCE~ 8 GeV
Randrup, Cleymans, PRC 74, 047901, 2006.
Strange baryon to pion ratios

## Slide 10
H. Oeschler et al.
Physics Letters B615 (2005) 50-54.
NICA
NICA
J. Cleymans, SQM-2017.
a transition from a baryon-dominated
to a meson-dominated media
less studied region
NICA energy region

## Slide 11
NICA
NICA
Production ratios:
hadrons with extra s-quark over others with just one
NICA energies- sub threshold and above
C. Blume, SQM-2017
Non-trivial energy dependence at very low energies:
Surprisingly high Ξ− yield, data clearly above model expectation
Dramatic rise of ϕ/K− ratio towards low energies

## Slide 12
Study phase transition with femtoscopy
- STAR BES
Green triangles - 1st order EoS,
Red triangle - crossover EoS,
3D Femtoscopy radii
SF technique
Hybrid vHLLE+UrQMD model:
Iu.Karpenko, et al, P.R. C91, 2015.
NICA
long
A.Kisiel, WUT
Notes: HIC study using femtoscopy allows one to distinguish between 1PT and XPT by precise measurements of source function, in particular, Radii out and Radii side. Distribution of their ratios for STAR BES data and for model are presented in the plot. NICA energy region allows to identify way of phase transition.

## Slide 13
O. Rogachevsky, A. Sorin, O. Teryaev,
Phys. Rev. C 82, 054910, 2010;
M.Baznat, K.Gudima A.Sorin, O.Teryaev arXiv:1701.00923
STAR Coll.,arXiv:1701.06657
Vorticity & L Polarization
polarization ~ unomalously induced
axial current:
NICA
Notes: High L polarization produced in heavy ion collisions was predicted due to s.c. vorticity effect in the work of Sorin and Teryaev. This polarization is related to anomalously induced axial current. This current is proportional to the square of Baryon ch. potential. Thus the polarization is rising with decreasing an energy. That was recently confirmed in STAR BES results.
The L polarization at NICA is expected rather high.

## Slide 14
Physics targets for the exploration of first order phase transitions in the region of the QCD phase diagram accessible to NICA & FAIR and possible observable effects of a “mixed phase indicated in the release of the “NICA White Paper” as a Topical Issue of the EPJ A (July 2016).
111 contributions,
188 authors
from 24 countries
New issues: NICA White Paper, SQM proceedings

## Slide 15
high net baryon density – density frontier;
maximum in K+/p+ ratio;
maximum in L/p ratio;
transition from a Baryon dominated system
to a Meson dominated one;
maximum of the L polarization;
1-st order transition & mixed phase creation;
Critical Endpoint ?
QCD matter at the NICA energies:

## Slide 16
MultiPurpose Detector (MPD)
Main target:
- study of hot and dense baryonic matter at the energy range of max net baryonic density
JINR, Dubna;
PI Az.AS, Baku, Azerbaijan;
PPC BSU, Minsk, Belarus;
WUT, Warsaw, Poland;
INR, RAS, Russia;
MEPhI, Moscow, Russia;
ITEP, NC KI, Moscow, Russia;
PNPI NC KI, Saint Petersburg, Russia;
CPPT USTC, Hefei, China;
Tsinghua University, Beijing, China;
SS, HU, Huzhou, Republic of South Africa;
MPD Collaboration:
TPC
ITS
DF, US, Mexico;
ICN UNA; Mexico;
DF, CIEA del I.P.N, Mexico;
FCF-M UAS, Sinaloa, Mexico;
FCF-MB UAP, Puebla, Mexico;
CCTVal, Univ. Téch. Federico Santa
María, Chile.
FHCAL
FFD
Notes: The MPD will be the fist detector operated at the Collider. Main target is …..
The collaboration is permanently growing.

## Slide 17
FFD
MPD detector for Heavy-Ion Collisions @ NICA
Tracking: up to |h|<1.8 (TPC)
PID: hadrons, e, g (TOF, TPC, ECAL)
Event characterization:
centrality & event plane (FHCAL)
Stage 1: TPC, TOF, ECAL, FHCAL, FFD
Status: technical design – completed / close to completion; preparation for the mass production
Stage 2: ITs + Endcaps (tracker, TOF, ECAL)
trim coil
cryostat
control dewar
SC coil
weight
~ 900 t
B0=0.66 T
General contractor:
ASG Superconductors,
Genova, Italy
FHCAL
FFD
Notes: The MPD will be put in operation at two stages. At the first one the barrel part will be equipped with major tracking detector TPC, TOF end ECAL. FHC and FD will be operational as well.
At the second stage the detector will be supplemented with IT and end cap subdetectors.

## Slide 18
Magnet production: at ASG (Genova) & Vitkovice HM
winding machine for SC solenoid
from Forgital to the SIMIC
Genova (Italy), June 2017
Notes: 8 contracts have been signed for the construction of large superconducting solenoid. All works are well progressing. The yoke production is going on at Vitkovice heavy machinery in Czech Republic. The cold mass is under production in other European enter[prizes.

## Slide 19
Item | value
Length, vessel | 340cm
R-out , vessel | 140cm
R-inner, vessel | 27 cm
R-out, DV | 133cm
R-inner, DV | 34cm
Length, DV | 170cm (of each half)
Electric field | ~140V/cm;
Drift gas | 90% Ar+10% Methane,
Gas amp factor | ~ 104
Drift velocity | 5.45 cm/µs;
Drift time | < 30µs;
t stability | < 0.5°C
N ROC | 24 (12 per each end-plate)
Number of pads | 95232
Pad active | < 10%
Max event rate | < 7 kHz ( Lum. 1027 )
shaping time | ~180 ns (FWHM)
Signal-to-noise | 30:1
dynamical range | 10 bits
Sampling rate | 10 MHz
Sampling depth | 310 time buckets
TPC
main parameters

## Slide 20: TPC: assembly stage
assembly workshop
(clean room) & tooling
Notes: The TPC is at the assembly stage. Assembly workshop in clean room and assembly tooling are ready. The r/o chambers are at the production stage.
We are planning to cooperate with ALICE on the RO electronics development and on the upgrade with GEM RO chambers at the second stage

## Slide 21
21
TPC read-out chambers
Pad structure:
- pad raw number - 53
rectangle shape
- small pads 5×12 mm2
- large pads 5×18 mm2
Pads layer
Connectors layer
Layout layer
GND layer
Pad plane:

## Slide 22
22
Parameters (rev.2):
cross-talks < 0.5%
noise < 500e-
(for Cdet=(10÷20) pF and G = 20mV/fC)
ADC ENOB = 9 bit
e-links (350 MHz each)
SAMPA chip (rev.3) – > Oct. 2017
Tests of SAMPA chip (rev.2) – on going
MPD TPC FEC32S board: test set up - in operation
TPC electronics

## Slide 23
23
Laser “planes” – 4+4
Points per plane - 4
Beams per point – 7
Laser “tracks”, N - 224
½ TPC
micro-mirror
bundles
TPC laser calibration system

## Slide 24
TDR – OK!
production close
to completion
tests of the trigger electronics & software
at BM@N
Fast Forward Detector - FFD (Cherenkov)
time resolution < 50 ps
80 channels:
lead converter +
quartz radiator
Notes: The construction of FFD is close to completion. It indicated good time resolution (better than 50 ps) during the December technical run

## Slide 25
TOF system
readout board with strips
triple-stack MRPC
efficiency and t – resolution
28 modules
280 MPRC’s
13 440 ch.
Notes: GEANT simulation was carried out for the construction described above. Mainly used QGSM generator.
clic
Indeed, it can be seen from the histograms, the occupancy does not exceed 15% and the geometric efficiency of the TOF detectors in this arrangement is ~ 94%.

## Slide 26
MRPC
TOF Barrel: MRPC ready for mass production
module box housing 10 PRC’s
basic elements - NINO &
HPTDC chips have been
Purchased to produce
read-out electronics
for the TOF
+ reserve
workshop for the MRPC mass-production
Notes: Другим совместным проектов в рамках эксперимента MPD является время-пролетная система, основанная на многоканальных RPC камерах. Такая система позволяет измерять время пролета заряженных частиц с точностью лучше чем 70 пикосекунд. В этом проекте принимает участие Циньхуа университет (Пекин).

## Slide 27
NINO preamp
Molex InfiniBand cables
HV cable
Distribution board
VMEx64 crate
Air cooling
Trigger out
Signal cables
Gas connectors
LV distribution
Slow control
HV connectors
TOF cables & pipelines
Total cabling:
14 VME crates
196 TDC72VHL
=> 14 per crate
560 cables Molex CXP
=> 40 per crate
~70 cm2 / tech. hole
heat ~10 W/m2
inside the barrel!
Notes: A very important part of creating the TOF system is the correct cabling.
This is single module with all communications that should be placed inside it.
The readout electronics must be as close as possible to the detector for achieving best time resolution.
But each crate radiates heat up to 300 W. Therefore we decided to fix them directly on the yoke.
Cables taking the signals from the FEE, LV cables, gas tubes and slow control buses will be routed through the center of the module to its outer ends.
Then they will come out from the external sides of the sector and pass through special holes in the yoke.
The space about 70 cm2 (<1% of total size) is enough in each hole in the yoke for all TOF system cables, tubes.

## Slide 28
Pb+Sc “Shashlyk”
read-out: WLS fibers + MAPD
L ~35 cm (~ 14 X0)
Segmentation (4x4 cm2),
s(E) better than 5% @ 1 GeV;
time resolution ~500 ps
prototype of a module
common project with Tsinghua University, China
Barrel ECAL ~ 43 000 modules
projective geometry
Electromagnetic calorimeter: ECAL
Notes: One of the unique high-tech projects within the framework of the MPD experiment is the large scale electromagnetic calorimeter of the shashlik type with projection geometry. This is a joint project with Tsinghua University (Beijing). It is required to produce more than 40 thousand modules and assemble them into a single cylindrical system, calibrate and put into operation.

## Slide 29
Inner Tracking System
in the workshop
stand for beam tests of boards with sensors – in operation
# layer | R0 mm | Active l, mm | N of staves | N of chips / layer | active area, cm2 | number of pixel cells,
1 | 24,4 | 542,4 | 12 | 216 | 889,9 | 113 246 208
2 | 42,0 | 542,4 | 22 | 396 | 1 087,7 | 207 618 048
3 | 60,0 | 542,4 | 32 | 576 | 1 582,1 | 301 989 888
4 | 107, | 1477,5 | 12 | 2 352 | 4 845,1 | 1 233 125 376
5 | 156,5 | 1477,5 | 18 | 3 528 | 7 267,7 | 1 849 688 064
6 | 206,5 | 1477,5 | 24 | 3 920 | 9 690,2 | 2 055 209 960
Total: |  |  |  | 10 988 | 25 362,7 | 5 760 877 544
ITS MPD layout
workshop for detector assembly & test was put in operation in 2015
cooperation with CBM/FAIR, ALICE/CERN:
manufacturing the ITS carbon fiber space frames for NICA (BM@N & MPD)& FAIR;
construction of ALICE type (MAPS) ITS
Notes: The ITS is based on MAPS technology developed for ALICE.
Structural elements, ladders, are produced in close cooperation with ALICE group. Workshop for microstrip detector assembly and test is in operation now at JINR. It will be used for assembly IT stations for BM@N and MPD /NICA and CBM/FAIR. We are preparing a plan of common activity on these issues with ALICE.

## Slide 30
FHCAL: for determination of reaction plane and centrality
2-arm (left/right) calorimeter (at ~3.2 m from the IP)
arm consists of 45 modules - 15x15 cm2 each
module - 42 lead/scintillator layers
Ein
Eout
FHCal coverage: 2.2<|h|< 4.8
σ(E)/(E) = 53%/√E(GeV) +10%
FHCal provides required resolution
modules production – in progress
responsibility of INR RAS
Transverse granularity allows to measure:
the reaction plane with the accuracy ~ 200-300
the centrality with accuracy below 10%.
Notes: The acceptance of FHC will cover the pseudo rapidity region from 2,2 to 4,8. Simulation shows reaction plane reconstruction with accuracy of 20-30 degree. The construction is progressing well.

## Slide 31
Hadron spectra

## Slide 32: MPD performance: hyperons
production of multi-strange hyperons to study the properties of
the strongly interacting system and signal for QGP
Central Au+Au @ 9A GeV (UrQMD) , TPC+TOF barrel
Realistic tracking and PID, secondary vertex reconstruction
Yields for 10 weeks of running
hyperon | L | L | X- | X+ | W- | W+
statistics | 6 109 | 7.3 107 | 3 107 | 1.6 106 | 1.4 106 | 3 105
Notes: MPD performance study indicates reliable reconstructions of L, cascade and Omega

## Slide 33
~ 106 3ΛH are expected
in 10 weeks
P = 1 GeV/c
d
p
p-
3ΛH → 3He + π –
PID
3ΛH → p + d + π -
Hypernuclei @ MPD
Hypertritons
central Au+Au @ 5A GeV
(DCM-QGSM
Notes: Hypernuclei could be reliably reconstructed and detected using PID based on the measurements of ToF and energy loss due to ionization in TPC

## Slide 34
Good probes to indicate medium modifications of spectral functions due to chiral symmetry restoration in A+A collisions; effect is proportional to baryon density
σω≈14 MeV/c2
MPD performance for dileptons
Hadron suppression
up to 10-5
meson | Yields |  | Yield/1 w
 | 4p | y=0 | 
r | 31 | 17 | 7 . 104
w | 20 | 11 | 7 . 104
j | 2.6 | 1.2 | 1.7 . 104
Yields, central Au+Au st √sNN = 8.8 GeV/u
PID
Notes: In general, MPD performance allows to study vector meson production and its properties

## Slide 35
ECAL tasks
high acceptance & purity e/g identification
in-medium modifications in dilepton spectra
thermal radiation from QGP
bulk properties via study of spectra, flow & correlations of photons
Challenge for electron measurements in Au+Au at NICA:
suppression of hadron background in the region:
M(e+e-) > 0,7 GeV/c2; pT >0.5 GeV/c complementary to TOF
Notes: Ecal implementation allows hadron background suppression in e+e- spectra, additional to ones provided by TOF and TPC, especially for fast hadrons

## Slide 36
Flow performance: vn of charged hadrons (FHCal event plane)
event plane resolution
Good event plane resolution with FHCal
Simulated vn (true) and reconstructed vn (reco) are in a good agreement
flow harmonics (v1/v2)
MEPhI/GSI:
P. Parfenov, I. Svintsov
I. Selyuzhenkov, A. Taranenko
Centrality with TPC estimator
Notes: Flow performance feasibility study indicate good plane reconstruction with FHCal and good reproducibility of generated events

## Slide 37
strategy in 2021-2023
energy and system size scan from 4 to 11 GeV in steps of 1-2 GeV
limitation by the accelerator:
lower luminosity
extra reduction by 40% because of a larger beam diamond
Detector limitation
TPC tracking: |h|<1.8 (N points>10)
TOF coverage: |h|<1.2
PID: combined |h|<1.2, 0.1<pT<4 GeV/c,
limited in 1.2 < |h| < 1.8 (only dE/dx)
ECAL coverage : |h|<1.2
FHCAL coverage: 2.2<|h|<4.8
FFD inside the TPC inner pipe
Notes: The stage one experiment will be running at limited luminosity and detector acceptance. The p/r gap from 1,8 to 2,2 will not be covered at all.
The gap from 1,2 to 1,8 will have limited efficiency

## Slide 38
 | 2015 |  |  |  | 2016 |  |  |  | 2017 |  |  |  | 2018 |  |  |  | 2019 |  |  |  | 2020 |  |  |  | 2021 |  |  |  | 2022 |  |  |  | 2023 |  |  | 
Injection complex |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Lu-20 upgrade |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
HI Source |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
HI Linac |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Nuclotron |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
general development |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
extracted channels |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Booster |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Collider |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
startup configuration |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
design configuration |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
BM@N |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
I stage |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
II stage |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
MPD |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
solenoid |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
TPC, TOF, Ecal (barrel) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Upgrade: end-caps +ITS |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Civil engineering |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
MPD Hall |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
SPD Hall |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
collider tunnel |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
HEBT Nuclotron-collider |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Cryogenic |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
for Booster |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
for Collider |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
NICA schedule
running time
Notes: The NICA schedule foresees:
- Start of the physics program with BM@N experiment already in this year and first colliding beams in the MPD - in 2021

## Slide 39
Concluding remarks
Density frontier is less explored area and its study
will lead to new interesting results
NICA complex has a potential for competitive research
in the field of baryon rich matter
The construction of MPD is going close to the schedule
MPD Collaboration is open for new participants

## Slide 40
Thank you