## Slide 1: Recent target development at Isolde - 2016
M. Delonca on behalf on TISD

## Slide 2: Isolde hall layout
HIE-ISOLDE
HIE-ISOLDE Linac
Target area
Experimental hall
Protons
GPS target
HRS target
CRIS
COLLAPS
REX
ISOLTRAP
Travelling Setup

## Slide 3: Front end layout
Courtesy of J. Montano
Standard ISOLDE target unit with surface ion source – cut view

## Slide 4: Target & Ion source unit - example
Standard ISOLDE target unit with surface ion source
Intensity (ion/sec)
Flux (ion/sec)
Cross section (cm2)
Number of target nuclei (cm-2)
Efficiencies
TISD projects
Primary beam
Ions
Radioisotopes
Primary beam
Animation inspired from A. Andrighetto, EURISOL DF conference

## Slide 5: Target and ion Source Development (TISD) mandate
Who?
What?
Providing a large choice of intense and pure radioactive beams,
How?
Target development:
- target design,
- ion source design and mode of operation,
- material development,
- release study, impact of chemical environment…
+ target yield tests and optimization

## Slide 6: Target overview for 2016
27 targets operated in 2016,
5 targets developed a leak after ~ 5.1018 protons
  Investigations are on-going, o-rings already changed
Interesting results:
New UCx batch confirmed its results: good and constant yields,
Intense n-rich chromium (Z=63) studied for the first time (ISOLTRAP),
132Sn32S broken up before delivery as pure 132Sn to Miniball
Extremely successful 57Mn & 119In runs: >65 individual experiments,
Absolute measurement of the βα decay of 16N using silicon strip detector (ISOLDE Decay Station).
Courtesy of K. Johnston

## Slide 7: TISD projects
8B beam
Germanium Sulfide beam
Negative ion source
Ti-C nanocomposite material
VADIS ion source update
N-converter new generation
The LIEBE target
Carbonyls beams
2015/2016
2017/2018
+ many other collaborative project with the RILIS team
see talk “The ISOLDE RILIS 2016, achievements, developments and future plans”, T. D. Goodacre – Technical session 1 @ 12.15
see poster “Online prototype TiC-carbon nanocomposite target material: constant release properties and material development” – J.P. Ramos
Release study (PhD thesis Dr. C. Seiffert)
Release study (all)
Ion source development (all)
Material development (PhD thesis Dr. J.P. Ramos)
Ion source development (PhD thesis Y. Martinez)
Target development (J.P. Ramos fellowship)
Target development (PhD thesis Dr M. Delonca)
Target development (PhD thesis J. Ballof)

## Slide 8: 8B beam
Context: MWCNT target with VD7 – SF6 gas
Primary beam
Fluor
Boron
Primary beam
Boron form stable bonds with material in the target -> no extraction of B
Adding Fluor to form volatile molecule with Boron (BF2 – BF3)
Standard ISOLDE target unit with VADIS ion source

## Slide 9: 8B beam
Solution: MWCNT target with VD7 – SF6 gas
Fluor
Boron
Primary beam
Boron form stable bonds with material in the target -> no extraction of B
Adding Fluor to form volatile molecule with Boron (BF2 – BF3)

## Slide 10: 8B beams
Results:
Yield measured:
Injection into REX: 11B19F21+  11B4+
    Space charge effect on trap (decrease of efficiency with higher beam current),
    Flat trap, cooling on A=30 only 9% efficiency,
    TOF: many breakups in trap,
    EBIS might accept all masses,
    When taking 8B19F21+ into the trap, radioactive beam is seen after the separator with Geiger counter
 | Yields (ions/µC)
8B | ~ 1e3
8BF | ~ 7e2
8BF2 | ~ 2e4
8BF3 | ~ 4e2
11B
19F
11B19F
11B19F2
Courtesy of J. Pitters, FJC. Wenander

## Slide 11: Neutron deficient Germanium Sulfide beams
Context:
Atomic Ge comes with strong isobaric contaminants (Ga, AlCl, ..)
Proposal: shift to other mass region by adding S with a mass marker (no reaction between S and Ga!)
Mass |  | Yields (ions/µC) |  | 
 |  | Ge | Ga | Factor
66 | Database | 3.6e5 | 4.4e8 | ~ 2
 | New | 5e5 | 2e8 | 
67 | Database | 1.1e6 | 8e8 | ~ 4
 | New | 1.2e6 | 2e8 | 
Ratio 67Ge / 67Ge32S = 1 / 1
Ge + S  GeS
Courtesy of J. Ballof, JPR. Ramos
Results: ZrO2 target with VD5 – S mass marker

## Slide 12: Negative beams @ PSB : Target tests Th/Ta-MK4 576
Context:
Magnet
Electron deflector
Negatively ionized isotopes
Neutral isotopes
Electrons
Ionizer
I source (neg)
Electron thermally generated
MK4 (planar-ionizer) negative ion source
+ 1 kV
Magnetic field

## Slide 13: Negative beams @ PSB
Expected efficiencies:
Higher efficiency expected with LaB6 source,
Good agreement between theory and experiment for MK4 source.
Courtesy of T. Stora
Theoretical and measured efficiencies – MK4 ion source and tubular LaB6 – Saha-Langmuir equations
Yields stable over time for MK4,
Slow release for MK4,
Tubular LaB6 ion source not operated on-line successfully due to poisoning -> instable operation but higher efficiencies expected
Isotope | Half-life | Yield / Production rate [ ions/s/mA 1H+] | 
 |  | 2005 | 2016
38Cl | 37.2 m | 1.6 105 | 1 105
40Cl | 81 s | 4.3 104 | 9 104
41Cl | 38.4 s | 1.4 104 | 3.5 102
42Cl | 6.9 s | 1.1 103 | 1.4 101
85Br | 2.9 m | 9.6 105 | 1.6 106
89Br | 4.4 s | 8.4 104 | 3.6 103
122I | 3.6 m | 4.4 104 | 6 105
137I | 24.2 s | 1.3 105 | 9 104
138I | 6.4 s | 7.3 105 | 9 104
204At | 9.2 m | - | 9 103 (5 103 after 5 days)
206At | 29.4 m | - | 6 103
Measured ion yields from target with MK4 LaB6 surface source (UC target in 2005, Th/Ta in 2016)
Y. Liu, D.W. Stracener, T. Stora, Production of negatively charged radioactive Ion Beams, 2016 (to be published)

## Slide 14: TiC-Carbon Black nanocomposite material
Context:
Standard ISOLDE target unit with surface ion source
Standard material grain size: μm
Reduction grain size to nm!
Reduction diffusion time = Increase yield
Toward ion source

## Slide 15: TiC-Carbon Black nanocomposite material
Application: development of a TiC nanocomposite by adding Carbon black
132 nm TiC grains – 84 % porosity, Stable for T > 2100 °C
Chart: 
| 8Li | 9Li | 20Na | 26Na | 27Na | 36K | 37K | 47K | 39CaF
TiC-CB | 6000000 | 380000 | 490000 | 7600000 | 640000 | 8000 | 1100000 | 450000 | 140
Ti-foils | 1700000 | 320000 | 53000 | 3000000 | 170000 | 90000 | 4900000 | 1300000 | 66000
TRIUMF | 120000 | 13000 | 360000 | 28000 | 7300 | 1600000 | 43000 | 2300
Yield [ions/s]
normalized to μC
(TiC micron)
Courtesy of JPR. Ramos
New nanostructure developed with carbon nanotubes,
Allow for extraction of 35 Ca (t1/2 = 25.7 ms) and 35K (t1/2 = 190 ms)
Yields stable over time (Ti foil targets degrade over few hours)
Good yields on Li and Na
Lower yield of K and Ca

## Slide 16: VADIS ion source development
Context:
Magnets
Magnets
Cathode
Anode
Standard VADIS MK5 (first design from Kirchner in 1976!) use: Anode @ 150V & hot Cathode
Ionization by electron impact
I cathode
150 V
150 V
Joules effect

## Slide 17: VADIS ion source development
Context:
Magnets
Magnets
Cathode
Anode
Electron thermally generated
Ionization by electron impact
Ionized isotopes
Neutral isotopes
Electrons
Neutral isotopes get ionized
BUT not homogeneous electrical field

## Slide 18: VADIS ion source development
Current VADIS efficiencies
Further investigations
    Reproduce with simulations time profile of extracted beam measured experimentally (RILIS mode),
    Optimize the anode geometry, reduce inactive volume for an increased efficiency/faster ion extraction,
    Determine beam emittance and energy spread, compare with experimental results,
    Determine the extraction efficiencies for metals.
Proposed modifications
Beam extraction
Ion source with insulated thermal screens with
variable voltage
Offline measurements – efficiencies noble gases
L. Penescu et al., Rev. Sci. Instrum. 81
Courtesy of Y. Martinez
Beam extraction
Expected increase in efficiency

## Slide 19: Neutron-converter new generation
Context:
Secondary isotopes
Neutrons
Primary beam
Secondary reaction created from neutron impacting onto target material
Secondary isotopes diffuse/effuse out of the material toward ion source
yield gains in neutron-rich isotopes
yield reductions in neutron-deficient isotopes
Less contaminant from the neutron-deficient side -> beam more pure
BUT current design not yet optimized on proton & neutron fluence
Primary beam

## Slide 20: Neutron-converter new generation
Results
Collaboration started between 4 institutes
Online tests foreseen:
  In 2017 in Triumf
  In 2018 in Isolde
Proposed design for ISOLDE target
52 cm3 UCx container
hollow W converter
Converter water-cooled body
Proposed design for TRIUMF target
Courtesy of R. Luis, A. Gottberg and JPR. Ramos
Zinc/Rubidium Ratio improvement

## Slide 21: The LIEBE project: toward short lived isotopes
Context:
! Picture not contractual for a Pb target!
Primary beam
Creation of droplets under specific proton & target conditions: faster release of isotopes

## Slide 22: The LIEBE project: toward short lived isotopes
Current situation:
  Assembly on-going,
  Heating elements installed & tested on sub assembly 1,
  Ion source installed,
  Pump manufactured: modification required (cavitation occurred before the required P-Q)
  On-line pushed to 2017
LIEBE pump – test @ IPUL – August 2016
LIEBE pump – test @ IPUL – August 2016 – P=f(Q)
LIEBE ion source & Sub-assembly 1 with heating elements

## Slide 23: Carbonyls beams @ ISOLDE
Context:
Some reactive species and refractory elements are not extracted -> extraction as volatile species by in-situ volatilization
Proposed solution:
Neutron bombardment
Target in gas
Courtesy of J. Ballof

## Slide 24: Carbonyls beams @ ISOLDE
Beam extraction:
Primary beam
Molecular beam
Neutrons
Primary beam

## Slide 25: New yield database
Current situation:

## Slide 26: New yield database
- Redesign the database structure
SQL
GUI
- Build a new user interface
Coming soon (release foreseen in 2017/2018):
Current situation
Courtesy of J. Ballof, J.P. Ramos, J. Klimo

## Slide 27: Thank you for your attention
And a special thanks to all our colleagues from HSE-RP-AS, BE-OP-ISO and EN-STI-RBS for their collaboration!