## Slide 1: PC Interlock: Recent updates and status
A. Calia,
K. Fuchsberger, M.-A. Galilee, J. Makai, M. Schaumann, Delphine Jacquet, Georges-Henry Hemelsoet, TE-MPE-SW Team

## Slide 2: Outline
Introduction to PC Interlock
Interlocking strategies
Phase Advance Interlock
Result

## Slide 3: Previous Presentations and Material
M. Schaumann, “PC Interlock status, next steps and feasibility of optics interlocking”, MPP 19/02/2016
  https://indico.cern.ch/event/495744/contributions/2016024/attachments/1231246/1805016/MPP_QuadrupoleInterlocking.pdf
Marc-Antoine Galilee, “Optics Interlocking within PcInterlock”, TE-MPE-TM Group Meeting 30/06/2016
  https://indico.cern.ch/event/544818/contributions/2219877/

## Slide 4: Introduction

## Slide 5: PC Interlock - Principle
Principle: Subscribes to Power Converters (PC) and compares measured current to reference functions ± tolerances (1 Hz).
Example: RCBYVS4.L8B2 (Orbit corrector) during COLLISIONS Beam Process:
Blue: k from measured current.
Red: Reference Function ±15µrad tolerances
~ 100 µrad
Slide from “PC Interlock – status, next steps and feasibility of optics interlocking”
Author Michaela Schaumann
https://indico.cern.ch/event/495744/

## Slide 6: PC Interlock - Principle

## Slide 7: PC Interlock - Principle

## Slide 8: PC Interlock - Principle

## Slide 9: Power Converter States
3 interlocking states of a Power Converter are defined:
  Ok: Not interlocking, current is within limits (or PC is in any other state than STANDBY, IDLE, ARMED and RUNNING)
  Warning: Trigger warning when current is 70% of interlock limit
  Interlock: Trigger interlock when current is 100% of interlock limit

## Slide 10: The PC-Interlock ecosystem
PC
PC
PC
PC
PcInterlock GUI
LSA
XTIM
Timing events
SIS
Intensities
Intensity tolerances
(“Itol”)
PcInterlock server
Interlocks & warnings
Global and individual PC statuses
Slide from “Optics Interlocking within PcInterlock”
Author Marc-Antoine Galilee
https://indico.cern.ch/event/544818/contributions/2219877/
Notes: Explicit LSA role of translating KTOL to ITOL, explicit role of XTIM

## Slide 11: Interlocking strategies

## Slide 12: Interlocking Strategy
Strategy for deciding if an interlock should be triggered.
Analysis of one or more Power Converter groups.

## Slide 13: Power Converter Groups
Set of Power Converter logically connected:
  Orbit correctors
  Matching Quadrupoles
  …

## Slide 14: Orbit correctors interlocking strategy
Interlocks when:
  >= 2 PCs per beam and plane are in interlock state
Warning when:
  1 PC per beam and plane is in warning state

## Slide 15: Quadrupoles interlocking strategy
Interlocks when:
  >= 1 PCs is in interlock state
Warning when:
  1 PC is in warning state

## Slide 16: Interlocking strategy example
PC1
PC3
PC2
PC4
isOk = False
isWarning = True
PC1
PC3
PC2
PC4
isOk = True
isWarning = False
PC1
PC3
PC2
PC4
isOk = True
isWarning = True
Example using Quadrupole interlocking strategy

## Slide 17
SIS Channel per strategy

## Slide 18: Latest improvements
Multiple interlocking strategies
SIS: publish additional interlocking status per strategy
Full quadrupole circuits support to allow for phase advance interlocking
New handling of tolerances in the LSA parameters (K_TOL and I_TOL)

## Slide 19: Phase Advance Interlock Prevent damage of tertiary collimators (TCT) and triplets in the event of an asynchronous beam dump (dump kicker (MKD) fires when beam passes). For protection, a phase advance between the MKD and TCTs in IP1 and IP5 should be kept within Δμ ≤ 30°.

## Slide 20: Phase Advance Interlock
An unwanted increment on the Power Converter current may produce a phase advance on the orbit.
Phase Advance Interlock uses tolerances on the Power Converter current to avoid this behaviour.
Generated tolerances are based on simulations of the closed-orbit phase using MADX

## Slide 21: Tolerance Generation
A tool was developed to automatically produce accurate limits, Ktol, in terms of magnet strength (k).
After user confirmation the Ktol values are written to LSA. A make rule generates the corresponding Itol (current) limits.
Ktol values are based on MADX simulations and the maximum allowed phase advance change, Δμ, provided by collimation team.

## Slide 22: Tolerance Generation Families
For easier configuration, the Tolerance Generation tool has a concept of families.
A family is a set of magnets that will share the same Ktol.
For example, the same type of magnets.
The concept of families let the user decide the granularity of the tool according to needs.

## Slide 23: Tolerance Generation Ranges
In order to prevent damage in the TCTs in IP1 and IP5, we have to take into account 4 ranges of the LHC ring, starting from the dump location (IP6):
  From IP6 to IP1 and IP5 per Beam
The simulations of the phase advance are done per range individually.

## Slide 24: Tolerance Generation Ranges
B1
IP6
IP1
IP5
R61B1: IP6  IP1
R65B1: IP6  IP5
Relevant ranges for Beam 1
Image from “PC Interlock – status, next steps and feasibility of optics interlocking”
Author Michaela Schaumann
https://indico.cern.ch/event/495744/

## Slide 25: Tolerance Generation Ranges
Relevant ranges for Beam 2
IP6
IP1
IP5
B2
R65B2: IP6  IP5
R61B2: IP6  IP1
Image from “PC Interlock – status, next steps and feasibility of optics interlocking”
Author Michaela Schaumann
https://indico.cern.ch/event/495744/

## Slide 26: Tolerance Generation
The allowed Δμ budget is distributed over all families.
At the moment defined families are:
MQ, MQT, Matching quads, Triplets, Warm quads.

## Slide 27: Tolerance Generation
The magnet phase response is the ratio of phase change over a segment resulting from a small strength increment.
The resulting family phase response consists of the sum of the member’s phase response. The absolute value is used for taking into account the worst case scenario.

## Slide 28: Tolerance Generation
The Ktol is then the ratio of the Δµ family budget over the family phase response.
The Ktol is calculated per range and the resulting family Ktol corresponds to the minimum.

## Slide 29: Makerules
Ktol values belong to magnets.
The Itol value of the corresponding Power Converters is calculated using a Makerule in LSA.
For most magnets it is a standard Makerule from K to I.
Triplets are special due to their configuration (Itol_nested).

## Slide 30: Makerule: Itol_nested
KQ1
KQ2
KQ3
IRTQX1
IRQX
IRTQX2

## Slide 31: Latest Improvements
Ktol Generation Tool
Make rule (including Itol_nested for the triplets)

## Slide 32: Results

## Slide 33: The PC-Interlock ecosystem
PC
PC
PC
PC
Ktol Generation
Tool
PcInterlock GUI
LSA
XTIM
Timing events
SIS
Intensities
Intensity tolerances
(“Itol”)
Kick tolerances
(“Ktol”)
PcInterlock server
JMAD
MAD-X
Interlocks & warnings
PC properties
New component
Global and individual PC statuses
Slide from “Optics Interlocking within PcInterlock”
Author Marc-Antoine Galilee
https://indico.cern.ch/event/544818/contributions/2219877/
Notes: Explicit LSA role of translating KTOL to ITOL, explicit role of XTIM

## Slide 34: Current Fluctuation in Stable Beams
Current variations ranges:
  From fill-to-fill ~ ΔI ≈ ±3A
  During Stable Beams ΔI ≈±1.5A
from fill-to-fill
during Stable Beams
Slide from “PC Interlock – status, next steps and feasibility of optics interlocking”
Author Michaela Schaumann
https://indico.cern.ch/event/495744/

## Slide 35
Families |  | ΔImeas (2015) | Itol (Preliminary) | Itol (LSA) | Ktol (LSA)
MQ | 5° | ± 0.02A | ± 0.5A | ± ~4.4A | ~7.69E-6
MQT | 15° | ± 4.5A | ± 5A | ± ~22.2A | ~2.45E-4
Matching Quad | 5° | ± 0.02A | ± 0.5A | ± ~[0.8, 5.1]A | ~8.95E-5
Warm Quad | 1° | ± 0.02A | ± 0.5A | ± ~[5.3, 7.7]A | ~1.33E-5
Triplet | 10° | ± 0.02A | ± 0.5A | ± ~3.8A (MQXA3.R8 = 2.2A) | ~3.25E-6
Families |  | ΔImeas (2015) | Itol (Preliminary) | Itol (LSA) | Ktol (LSA)
MQ | 5° | ± 0.02A | ± 0.5A | ± ~4.4A | ~7.69E-6
MQT | 15° | ± 4.5A | ± 5A | ± ~22.2A | ~2.45E-4
Matching Quad | 5° | ± 0.02A | ± 0.5A | ± ~[0.8, 5.1]A | ~8.95E-5
Warm Quad | 1° | ± 0.02A | ± 0.5A | ± ~[5.3, 7.7]A | ~1.33E-5
Triplet | 10° | ± 0.02A | ± 0.5A | ± ~3.8A (MQXA3.R8 = 2.2A) | ~3.25E-6
ΔImeas largest current variation found in 2015 Stable Beams data.
Requirement to avoid unnecessary beam dumps: Itol > ΔImeas.
Ktol values per family are equal, while Itol values can be different, because of the magnet’s calibration curves.
Optics used to generate the Ktol R2016a_A40C40A10mL300

## Slide 36: Phase Advance Interlock Quadrupole
On Quadrupole RQT4.L7
Strategy: Quadrupole Interlocking Strategy
2016.08.23 @ 06:20:04 (MD)

## Slide 37: Phase Advance Interlock Quadrupole

## Slide 38: Phase Advance Interlock COD
On RCBYHS4.L1B1 and RCBCH7.R5B1
Strategy: Orbit Correctors Interlocking Strategy
2016.07.30 @ 05:07:30 (MD)

## Slide 39: Phase Advance Interlock COD
~9.9 A
~11A

## Slide 40: Conclusions
Everything is implemented and deployed.
PCInterlock on quadrupoles is running since spring 2016
Since 9th Aug. the SIS channel was un-masked.
No interlocks occurred during PHYSICS.
Interlocked correctly several times during MD.

## Slide 41: Thank you
Do you have any question?

## Slide 42: References for Java Classes
Strategies configuration
  /lhc-pcinterlock-core/src/java/cern/lhc/pcinterlock/conf/pcinterlock-strategies-beans.xml
PC groups
  cern.lhc.pcinterlock.domain.enums.PcInterlockPcGroup
Interlocking strategies
  cern.lhc.pcinterlock.service.manage.impl.AbstractInterlockingStrategy
  cern.lhc.pcinterlock.service.manage.impl.OrbitCorrectorsInterlockingStrategy
  cern.lhc.pcinterlock.service.manage.impl.QuadrupolesInterlockingStrategy
PC state evaluator
  cern.lhc.pcinterlock.service.decide.impl.WarningEvaluator
  cern.lhc.pcinterlock.service.decide.impl.InterlockEvaluator

## Slide 43: References for Java Classes
Make rules (lsa-core-cern)
  LHCNestedItolMakerule
  LhcKTol2IRefTolMakeRule
Lhc-pcinterlock-tolgeneration project
  svn+ssh://svn.cern.ch/reps/acc-co/trunk/lhc/pcinterlock/lhc-pcinterlock-tolgeneration