## Slide 1: Clock Configuration for GBT Application
GBT application requires 120MHz clock for MGT
HSIO-II:
TTC RMB variable clock generator has 120MHz TTC clock for Artix, but clock to DTM is delivered to a regular fabric clock pin.
Simplest to replace HSIO-II X12 100 MHz Oscillator with 120 MHz part, but only on-shelf part has a central ground pad that can short out HSIO-II board pads. Tried one replacement with central pad taped over.
Possible revision for HSIO-II to redirect TTC RMB clock to DTM REFclock path to replace the X12 oscillator.
Need to check either solution actually works.

## Slide 2
Existing HSIO-II (C03) Clock Configuration
ZYNQ Z030
MGTREFCLK1_112_W5,6
REFCLK1
X5
250 MHz
Pkg=IDT8N4Q001
CLK_SCL/SDA, CLK_SEL
DTM
100 MHz
MGTREFCLK0_112_U5,6
X3
REFCLK0
N/L
Pkg=LCC6
DTM_REFCLK
X12
‘PCIE_REFCLK’
Pkg=LCC6
160MHz
SI5338A
Artix T200
PGP_REFCLK1
PGP_REFCLK0
X9
X3
250 MHz
312.5 MHz
Bank 113
RTM_REFCLK1
RTM_REFCLK0
X10
X5
312.5 MHz
Bank 116
250 MHz
TTC_SCL/SDA
TTC_CLK[0:1]
DTM_RTM_LS0
HSIO-II TTC RMB
TTC
BUSY
DTM_TO_RTM_LS0
IO_L13p/m_T1_MRCC_t/u17
variable clock generator
DTM_CLK[0:2]
DTM_CLK[0:2]
Bank 15 MRCC/SRCC

## Slide 3
Possible revise HSIO-II (C04) Clock Configuration
ZYNQ Z030
MGTREFCLK1_112_W5,6
REFCLK1
X5
250 MHz
Pkg=IDT8N4Q001
CLK_SCL/SDA, CLK_SEL
DTM
MGTREFCLK0_112_U5,6
X3
REFCLK0
N/L
Pkg=LCC6
DTM_REFCLK
‘PCIE_REFCLK’
160MHz
SI5338A
Artix T200
PGP_REFCLK1
PGP_REFCLK0
X9
X3
250 MHz
312.5 MHz
Bank 113
RTM_REFCLK1
RTM_REFCLK0
X10
X5
312.5 MHz
Bank 116
250 MHz
TTC_SCL/SDA
TTC_CLK[0:1]
DTM_RTM_LS0
HSIO-II TTC RMB
TTC
BUSY
DTM_TO_RTM_LS0
variable clock generator
DTM_CLK[0:2]
DTM_CLK[0:2]
Bank 15 MRCC/SRCC

## Slide 4: COB Clock Source Requirements and Constraints
Current COB+RTM rely on external TTC source to generate 160 MHz
Cannot touch the 100MHz oscillator on the COB – needed for PCIe control
Only needs 120 MHz MGTrefclk for DPM, while DTM itself doesn’t need to run GBT on the COB
For DPM to run GBT and TTC at the same time, both 160 MHz and 120MHz clocks are needed and can only come from the DTM TTC distribution
160 MHz and 120 MHz clocks need to be synched to LHC TTC clock in real operation

## Slide 5
Existing COB + RTM Clock Configuration
ZYNQ Z030
MGTREFCLK1_112_W5,6
REFCLK1
X5
250 MHz
DTM
100 MHz
MGTREFCLK0_112_U5,6
X3
REFCLK0
N/L
X5
PCIE_REFCLK
TTC
BUSY
DTM_TO_RTM_LS[0-5]
DPM_CLK[1:2]
Bank 13 MRCC
PCIE_REFCLK
X9
REFCLK0
X10
156.25 MHz
250 MHz
X7
Z045-A
REFCLK0
REFCLK1
X8
250 MHz
156.25 MHz
MGTREFCLK0_110_AA7,8
MGTREFCLK0_111_U7,8
DPM_CLK0
Bank 12
regular I/O
MGTREFCLK0_111_W7,8
REFCLK2
DPM0_CLK0
Bank 12 MRCC
DPM0_CLK[1:2]
DPM_CLK[1:2]
Bank 12 MRCC
MGTREFCLK0_111_W7,8
DPM_CLK[1:2]
DPM1_CLK[1:2]
REFCLK2
DPM1_CLK0
Fan out
REFCLK1
MGTREFCLK0_110_AA7,8
MGTREFCLK0_111_U7,8
DPM Bay 0
Z045-B
Other DPM Bays
COB
0
Bank 13 SRCC
Bank 12 regular I/O
1
DTM_RTM_LS[0-5]
2
3
4
5
TTC
RMB
CLK
DATA
LOL
SD
LOCKED
BUSY
RTM
P3
160 MHz
160 MHz
TTC RX logic

## Slide 6
SD
COB + RTM with new ‘GBT’ RMB
ZYNQ Z030
MGTREFCLK1_112_W5,6
REFCLK1
X5
250 MHz
DTM
100 MHz
MGTREFCLK0_112_U5,6
X3
REFCLK0
N/L
X5
PCIE_REFCLK
TTC
BUSY
DTM_TO_RTM_LS[0-5]
DPM_CLK[1:2]
PCIE_REFCLK
X9
REFCLK0
X10
156.25 MHz
250 MHz
X7
Z045-A
REFCLK0
REFCLK1
X8
250 MHz
156.25 MHz
MGTREFCLK0_110_AA7,8
MGTREFCLK0_111_U7,8
DPM_CLK0
Bank 12
regular I/O
MGTREFCLK0_111_W7,8
REFCLK2
DPM0_CLK0
Bank 12 MRCC
DPM0_CLK[1:2]
DPM_CLK[1:2]
Bank 12 MRCC
MGTREFCLK0_111_W7,8
DPM_CLK[1:2]
DPM1_CLK[1:2]
REFCLK2
DPM1_CLK0
Fan out
REFCLK1
MGTREFCLK0_110_AA7,8
MGTREFCLK0_111_U7,8
DPM Bay 0
Z045-B
Other DPM Bays
COB
0
Bank 13 SRCC
Bank 12 regular I/O
1
DTM_RTM_LS[0-5]
2
3
4
5
GBT
RMB
CLK
DATA
LOL
LOCKED
BUSY
RTM
P3
160 MHz
160 MHz
TTC RX logic
SI5338A
DTM_SCL/SDA
Bank 13 MRCC
120 MHz
TTC_CLK160
TTC_CLK120

## Slide 7: New ‘GBT’ RMB for COB RTM
New GBT RMB design from Larry
Added SI5338A variable frequency clock generator with either local oscillator or TTC 160 MHz clock inputs
Remapped DTM_RTM_LS[0-5]:
  Chan 0,1 (MRCC) = 160 MHz, 120 MHz clocks
  Chan 2 (SRCC) = TTC data
  Chan 3 (SRCC) = New dedicated DTM I2C
  Chan 4 (I/O) split one LVDS pair into two CMOS25 for
        a) TTC link Signal Detector (SD)
        b) RMB CDR locked (LOL)
  Chan 5 (I/O) = BUSY as before
  New DTM I2C controls SI5338A configuration and monitors SD,LOL,LOCKED,BUSY on RMB