## Slide 1: A development of an accelerator board dedicated for multi-precision arithmetic operations and its application to Feynman loop integrals II
Hiroshi DAISAKA(Hitotsubashi University)
Naohito NAKASATO(University of Aizu)
Tadashi ISHIKAWA(KEK)
Fukuko YUASA(KEK)
Keigo NITADORI(RIKEN/AICS)
2017/8/24 ACAT2017 Trac3@washington university
Notes: My name is hiroshi daisaka, from hitotsubashi university.
Here is title of my talk and collaborators..
英語サンプル
progam needs to be done in kind of machine code called VHDL
we have a problem in accuracy.
accuracy is not so small, actually, it is one or two-digit
according to a report of program (QD-pack)
GPU were flexible than GRAPE
but two problems
prgamming, optical way needs special knowledge to memory and hardware structure
even hen done in CUDA
consume much more energy per TeraFlopls
new paradigm , use FPGA
platform

## Slide 2: about myself
original major: planetary sciences, astronomy
  N-body simulations of planetary rings, plant formation, etc
GRAPE technique is being utilized for calculation of Feynman loop integrals.
GRAPE development
GRAPE-8
GRAPE-10
GXHIB
e.g. Daisaka et al. 2001
Kominami, Makino, Daisaka , Fujimoto (2016)
Notes: Let me start with my brief introduction.
My original major is planetary science and astronomy.
N-body simulation of planetary rings, planet formation and so on.
This is one of my simulation results of Saturn’s ring, we can see structure formation,
and this is an animation of planet formation, we can see migration of proto planets by gravity effect of surrounding particles
And I was also involved in GRAPE development as well
Here is pictures of hardware I have developed so far.
Grape technique is being ustilized for calculation of Feynman loop integrals
I was involved in GRAPE development as well

## Slide 3: abstract
We have been developing an accelerator system dedicated for multi-precision arithmetic operations (GRAPE9-MPX).
  Processor elements (PE) with arithmetic logic units for quadruple/hexuple/octuple precision
  implemented on multiple FPGA(Field Programmable Gate Array) boards
  compiler system (LSUMP, Goose)
We report :
  progress of our system
4 FPGA Boards in ACAT2014
64 FPGA Boards in ACAT2017
evaluation of 3-loop selfenergy in a massive case with various masses
Notes: So , We have been … をよむ
we developed PE with …, and PE are implemented on FPGA board
We also developed our own compilers in order to use our system easily
here we report progress and the detailed implementation of our system.
This is previous system presented in acat 2014, and this is current system.
We also report an application, evaluation of 3-loop selfenergy in a massive case with various masses

## Slide 4: Outline
Introduction
Hardware and software of current GRAPE9-MPX system
Application to 3-loop integral
Summary
Notes: This is outline of our talk
Let’s move on to introduction
This is outline of our talk.
First we start with the introduction,
followed by an explanation of hardware and software of our current system.
Next I will show the application to 3-loop integral, and
then last part is summary.

## Slide 5: Outline
Introduction
Hardware and software of current GRAPE9-MPX system
Application to 3-loop integral
Summary
Notes: let us move to introduction

## Slide 6: Evaluation of Feynman Integrals
Analytical Approach
Analytical + Numerical Approach
Fully Numerical Approach
easy to treat arbitrary multi masses
needs huge computing resource
  6, 7-dimensional integrations
  high precision in some cases
Notes: One of the things we want to do is to evaluate Feynman integrals
For the evaluation, there are three approaches, one is analytical approach, second one is analytical + numerical approach, and third one is fully numerical approach
Each approach has merit and de-merit
our choice is fully numerical approach
one of the reason of our choice is that it is easy to treat arbitrary multi masses.
But, one of demerit is that this approach it needs huge computing resources
because we need 6,7 dimensional integrations, and needs high precision in some cases

## Slide 7: Feynman loop integral and DE-DCM
Need fully numerical evaluation for auto calculation
  our method : DE-DCM(Direct Computation Method)
    use Double Exponential Formula(DE) and trapezoidal rule for numerical integration
    extrapolation by Wynn’s epsilon algorithm
Feynman loop diagram with number of loop L, number of lines inside N (scalar integral)
Notes: This is an equation we calculated numerically.
Our numerical method is DE-DCM
In this method, we use Double exponential formula and trapezoidal rule for numerical integration
Also we use extrapolation by Wynn’s epsilon algorithm.

## Slide 8: Difficulties in DE-DCM
need huge CPU power for numerical integrations
  more than 6D integrations
    furthermore , there are wide variety of loop configurations, mass parameters, and physical parameters
need calculation with high precision
  numerical instability appears in double precisions calculation (Yuasa et al. 2007)
  need further huge CPU power to realize high precision calculation in ordinary CPUs
  e.g. addition in QD needs 40 double-double operations
solution : use an accelerator
  GPU
  FPGA
Notes: However, there are some difficulties in DE-DCM.
One is we need huge CPU power ….
This is because, the integrations become more than six-dimensional integration,
Also we need calculation with high precision,
because numerical instability appears in …as in Yuasa et al two thousand seven
also we need further huge CPU power to realize high precision …
the solution is to use an accelerator
such as GPU, and FPGA
here we use FPGA
どれだけの精度が必要？
ソフトウェア実装では計算時間が問題
here we consider a feasibility of FPGA

## Slide 9: Field Programmable Gate Array
http://www.ni.com/tutorial/6097/ja/
designed to be configured with any logic functions
an accelerator with an appropriate hardware design
  use technique that was used in GRAPE
Notes: This is an image of FPGA
FPGA contains logic blocks, programmable interconnects, and I/O blocks.
This is designed to be ….
So it can be an accelerator ….
Here we use technique that was used in GRAPE
fpga からgrape

## Slide 10: Concept of GRAPE(GRAvity PipElines)
Host
computer
GRAPE
Data required
for calculation
Result
accelerator connected to a host computer
computes only computationally intensive part in N-body simulations
  mutual force calculation
dedicated pipelines
(Sugimoto et al., Nature 345, 1990)
Notes: This slide shows the concept of GRAPE
GRAPE is an accelerator connected to a host computer.
GRAPE computes only computationally intensive part in N-body simulation.
That is mutual force calculation.
To do so, dedicated pipelines, like this figure, are implemented on GRAPE
This is a concept of traditional grape.
After that, GRAPE-DR was developed.

## Slide 11: GRAPE-DR
GRAPE-DR was adopted as programmable processor elements instead of the dedicated pipelines
We extend PE to have arithmetic units for quadruple/hexuple/octuple precision → GRAPE-MPX architecture
possible to carry out any calculation like LINPACK (DGEMM)
  top of little GREEN top 500, 2010
    Makino et al., Procedia Computer Science 4 (2011)
Notes: GRAPE-DR was ….
This is block diagram of PE, processor, and GRAPE-DR board.
GRAPE-DR is possible to carry out any calculation like LINPACK
DR cluster got the top of little GREEN top 500
We expend this PE to have artimetic units for qudruple/hexuple octuple precision.
We call it GRAPE-MPX artchiteture

## Slide 12: Our developed accelerators
GRAPE-MP(2011)
Structured ASIC
6PE, quadruple
GRAPE-MPX(2012)
Altera StratixIV
16PE,quad/hex/oct
GRAPE9-MPX(2014-)
Altera ArriaV
quad/hex/oct
Notes: here is accelerators we have developed.
We designed dedicated processer and implemented it on a structured Asic and FPGAs
Next we will explain the details

## Slide 13: Outline
Introduction
Hardware and software of current GRAPE9-MPX system
Application to 3-loop integral
Summary
Notes: let us move to hardware and software of current system

## Slide 14: GRAPE9-MPX cluster system
64 FPGA boards (Altera ArriaV) on 8 host computers
  8 FPGA boards per host
  connected via PCIe
specifications of host PC
  Intel Xeon 2687W v3(6 hosts)
  2687w v4 (2hosts)
  128GB mem
  SuperMicro X10DRX
  GbE for host connection
Peak performance
  422 Gflops for quadruple
  185 Gflops for hexuple
  96 Gflops for octuple
Notes: Here is a picture of GRAPE9-MPX cluster system in KEK.
It has 64 FPGA boards on 8 host computers.
FPGA boards are connected via PCIe interface.
The peak performance of the system is the following.
Here is specification of host PC.

## Slide 15: FPGA board
use Altera(Intel) ArriaV GX starter kit
https://www.altera.co.jp/products/boards_and_kits/dev-kits/altera/kit-arria-v-starter.html
  good cost performance (850 USD, 120000 JPY), rich resources
Main equipment
  ArriaV GX (5AGXFB3H) ALM/MEM/DSP=136880/1726/1045
  DDR3 SDRAM (256MB), SSRAM(2MB)
  Interfaces (PCIe x8, GbE, etc)
  config unit, power supply unit
Notes: This is a FPGA board we use
We use board of Alter ArriaV Gx start kit
This board has good cost …
Here is main equipment of the board,
FPGA chip, DDR memory, PCI-express IF, and so on.

## Slide 16: block diagram of processor
MP processor
  PEs + BM
  PEs: execute same instructions (SIMD)
  BM: 128 w x 2(in/out) (260-bit width)
Control processor(CP)
  MEM+control unit+IF
  Instruction mem:
  4k w (on chip)
  16M w (on DDR)
  if < 4k , use on chip
  EM: 32k w (256-bit width)
  x4 Gen I PCIe (GPCIe from KFCR)
Notes: This is a block diagram of our processor implemented on the FPGA
our processor consists of two parts, MP processor and Control processor.
MP processor consists of many PE and Broadcast memory.
PEs behave as SIMD operations
On the other hands, Control Processor consists of memory units for instruction and data, its control unit, and IF.
CP sends data and instruction to MP processor, then MP carries out calculation,
and CP gets results from MP and sends the results to host PC via PCIe interface
one of the memoy unit is instraction memory
it has 4k words on chip memory, and 16M words on DDR memory.
if number of instruction is less than 4k words, we use only onchip memory
another memory is for data memory, named as EM which has 32 words
For connection to host computer, we use times 4 Generation I PCIe interface, provided by KFCR

## Slide 17: Block diagram of PE
arithmetic units(add, mul, rsq)
+ registers + selector units
add, mul
  quad/hex/oct precision
  operate independently
rsq
  used for initial guess of div
  exp 19-bit, man 32-bit
regs
  128 w for GRF1 and GRF2
  4 w for treg
1 clock for throughput and
4 clocks for latency
  → 4 “logical” pipelines to hide latency
Notes: This is a block diagram of PE
PE consist of …
here
add is to adder umit, and mul is multiplier unit.
These units have quad/hex/oct precision.
This is the key of our hardware.
These unit can operate independently
rsq uniti is to perform root-square calculation,
which is used for initial geuss of division
and has appropriate accuracy
PE has one clock for throughput, 4 clock for latency
so we use as 4 logical pipelines to hide latency
rsq (x^-0.5) exp 19-bit, man 32-bit

## Slide 18
Numerical format used in PE
use 19-bit exponents for IEEE754(2008)binary256 format
truncate 4 bits when sending to host (CP)
  from exp in MP4 -> binary128 format
  from mantissa in MP8 -> binary256 format
Notes: Here we show numerical format used in PE
here is format of quarduple, hexuple, octuple, we call as Mp4, MP6, MP8
We should note we use 19-bit exponent in order to corresponds to IEEE format.
We truncate 4 bits when sending to host (or CP)
If it is from exponent in MP4, it becomes binary 128 format.

## Slide 19: Calculation efficiently accelerated
interaction type
examples
  mutual gravitational force
  multi dimensional integration of Feynman loop diagrams
    need loop fusion (expansion) for efficiency
set xi in register files of i-th PE
broadcast yj to all PE
calculate f(xi, yj) and sum up
large nj for reducing communication overhead
Notes: Our system is possible to carry out any calculation but,
there is a type of calculation efficiently accelerated.
That is a interaction type.
Here is the procedure of calculation.
we set xi in register files in i-th PE
Then we broadcast yj from BM memory to all Pes,
and PE calculate the function with x_i and yj and sum up.
It is important to take large nj for reducing communication overhead.
one of examples is mutual gravitational force calculation.
Another one is a multi dimentional integration of Feynman loop diagrams.
It it crutial that we use loop fusion technique for efficienty

## Slide 20: Logic synthesis
Our processor is written in VHDL
  easy to implement on any FPGAs
Synthesis tool needed for implementation
  Altera FPGA needs QuartusII (here we used ver. 13.1)
  generates binary code for FPGA
  transfers to FPGA
prepare binary codes for MP4, MP6, MP8 individually
Notes: Here is logic synthesis
Our procesoor is …
Synthesis tool is needed for implementation
for altera FPGA, it is quarutsII
It genertes …
and trasfers to FPGA
We prepare binary code …
this table is the synthesis result.
here is values for MP4, MP6, and P8
each of the number of PE are 36, 19, 11
the clock speed are 92, 78, and 68.
and peak speed are 6.6 , 2.9 and 1.5 Gflops
The bottom three lines show the utilization parcentage of logic resourses.

## Slide 21: How to use GRAPE9-MPX
    plus pragma to C/C++
#pragma goose parallel for loopcounter(ixy, iz)
for(ixy = 0; ixy < ni; ixy++) {
sumzG[ixy] = 0.0;
for (iz = 0; iz < nj; iz++) {
xx = dev_xx[ixy];
yy = dev_yy[ixy];
zz = x30_1[iz] * dev_cnt4[ixy];
d = - xx * yy * s
tt * zz * (one - xx - yy - zz) +
(xx + yy) * lambda2 +
(one - xx - yy - zz) * (one - xx - yy) * fme2+
zz * (one - xx - yy) * fmf2 ;
sumzG[ixy] += gw30[iz] / (d * d);
}
}
#pragma goose parallel for loopcounter(ixz, iz)
one-loop box diagram
accelerate !
Notes: Here we show how to use our system.
It’s very simple, just plus pragma to a C/C++ program and recompiling.
Here is a case of one-loop box diagram, this is integral and this is a source code in C corresponding to loop calculation
All we have to do is to add this pragma into the code.
By this, we can accelerate this code by using GRAPE9-MPX

## Slide 22: Goose and LSUMP
Goose compiler
  directive type compiler like OpenMP
  generates kernel code for LSUMP
  inserts communication APIs.
  Goose:
  http://www.kfcr.jp/goose-e.html
LSUMP
  generates the assembler code for GRAPE9-MPX
currently supports MPI/GPU(OpenCL)/PEZY-SC(PEZY-CL)
(please ask to KFCR, if you want to use.)
realized by Goose and LSUMP
Notes: Such a easy programing model is realized by Goose and LSUMP.
Goose is a directive type compiler like OpenMP.
goose analyzes source code, then,
generates kernel code for LSUM and
insterts communication APIs in C/C++ source code
For more information, please go to this website.
LSUM is our DSL compiler which generates the assember code for …
goose currlenty suport MPI/GPU and PEZY-SC

## Slide 23: Comparison to software implementations
case of 12 FPGA boards
compare the execution time for this diagram
Condition for software implementations
  Host: Xeon E5 2687W 16 threads
  Use MPFR C++ (F4, F6, F8 correspond to quadruple, hexuple, octuple precision)
214 times
faster
144 times
faster
80 times
faster
146 times
faster
25 times
faster
226 times
faster
6D integration
N=646
Notes: Here we show performance of our system, comparing to software implementations
here is the case of 12 FPGA boards
We compare the execution time for calculation of this diagram with the same number of integral points.
Here is condition for software implementation, we use 8-core 16 threads Xeon CPU
This table shows the result.
Here is values of our system, here is values of Software
This is result of comparison
we can see the our system is much faster than software implementation

## Slide 24: Outline
Introduction
Hardware and software of current GRAPE9-MPX system
Application to 3-loop integral
Summary
Notes: Lets move on to application to 3-loop integral

## Slide 25: previous applications
We have already used our system to evaluate Feynman loop diagram in a massive case
  3-loop self energy with m=1 for all mass
S. Laporta , Int.J.Mod.Phys.A15:5087-5159,2000
  2-loop box cross with m=1 for all mass
  S. Laporta , Int.J.Mod.Phys.A15:5087-5159,2000
  F. Yuasa et al. CPC vol.183, no.10, pp.2136-2144 2012.
E. de Doncker et al., J. Phys.: Conf. Ser. 523 (2014) 012052
  2-loop box cross with masses from Yuasa et al. (2012)
    unphysical region
Here we evaluate 3-loop self energy diagram with various masses
Notes: We have …
One is 3-lloop
next one is 2-loop box crosse,
and another one is 2-lopp box cross with …
and 2-loop cross with masses from Yuasa et al, of unphysical region.
Here we evaluate 3-loop….
Ghinculov, Phys. Lett. B 358 (1996) 279-283

## Slide 26: 3-loop self energy in a massive case
mass assignment
same as used in Ghinculov 1996
1
2
3
4
5
6
7
8
evaluate the integral by changing manderstum variable s
Ghinculov, Phys. Lett. B 358 (1996) 279-283
Notes: Now I show you a diagram and equation we calculated as an application
here is mass ssignment, which is the same as used in Ghincoulv 1996.
We evaluate the integral by changin manderstam variables s
Ghinculov--analytical + numerical (combine)
計算条件ほか、は our setting とか

## Slide 27: Result of Ghinculov 1996
REAL part
IMAGINARY part
features
unphysical region for s2 < 1
diverse at s2=1, 4
sign change at s2 ~2, 5.5 for RE, at 3.5 for IM
convergence to zero for large s2
Notes: Here we show the result of Ghinculov 1996
this axis is s-square and this is value of integral
There are features to note.
one is unphysical region for s-square less than one
…
It seems to be in his paper, Im part should be Re part, and Re part should be Im part,
because of behavior of unphysical region.
ReとImが逆のように見える
unphysicacl でIm がない
In Ghinculov, it explains that solid line is imaginary and dashed one real part.
But, It seems to reverse

## Slide 28: Our settings
unphysical region (s2 < 1)
  r=0 (fixed, no extrapolation)
  N=25 ( 257 = 6103515625 total )
  h=0.3
  1 board of ArriaV, MP4 mode (36PE, 92MHz)
  elapse time per point of s ~ 300 sec
physical region (s2 > 1)
  r=1.15b, b={-50, -51,..,-80,-81 } for extrapolation
  N=64 ( 647 total )
  h=0.0875, 0.117187
  64 board of ArriaV, MP4 mode (36PE, 92MHz)
  elapse time per point of s ~ 11 hours(including 24 b’s)
  integrate both Re part and Im part with 8 different values of b (16 integrations at the same time)
    C/D are common and can be reused
Notes: Here is our setting
let me skip detail but I would like to point out we use quadruple precision in calculation.
8 beta 計算していることを説明するスライドはバックアップで用意のこと
in order to use Wyns’s epsilon algorithm,
we evaluate the integrals with different values of epislon for fixed value of s
enouth rich for regsters in PE to store the results obtained by reuse of C/D,
and possilble to increase efficienty
once C/D are calculated, since they are common even if epsilon is different,
C/D can be reused in the integration

## Slide 29: Our （preliminary）result
unphysical region for s2 < 1
diverse at s2=1, 4
sign change at s2 ~2, 5.5 for RE, at 3.5 for IM
convergence to zero for large s2
11 hours for each point
64 FPGA boards
647 grids
24 integrations for extrapolation
300 sec for each point
1 FPGA board
257 grids
no extrapolation
Notes: This is our preliminary result
This is very similar to previous work, unphysical region here, diverse here and here
We should note the computational time.
For physical region, it took 11 hours to calculate each point of s-square
under these conditions.
For unphysical region, and it took 300 sec.

## Slide 30: Outline
Introduction
Hardware and software of current GRAPE9-MPX system
Application to 3-loop integral
Summary
Notes: Let me move on to the summary

## Slide 31: Summary
We have been developing an accelerator system dedicated for multi-precision arithmetic operations (GRAPE9-MPX).
  Processor elements (PE) with arithmetic logic units for quadruple/hexuple/octuple precision on FPGA
  compilers (LSUMP, Goose)
  current system : 64 FPGA boards with 422/185/96 Gflops for MP4/MP6/MP8
  compiler also supports MPI/GPU(OpenCL)/PEZY-SC(PEZY-CL)
We showed evaluation of 3-loop selfenergy in a massive case with various masses
  possible to carry out 7 dimensional integration with quadruple precision within acceptable time
    11 hours per point of s in physical region with 647 grids
  also possible to carry out calculation with hexuple/octuple precision
Notes: Here is summary
We have been ….
We showed …
This is end of my talk
thank you very much.
We would like to use our system to evaluate various kinds of Feynman loop integrals in the future.
sixty four to the seventh grids

## Slide 32
backups

## Slide 33: Detail analysis

## Slide 34: example : one-loop box diagram
#pragma goose parallel for loopcounter(ixy, iz)
for(ixy = 0; ixy < ni; ixy++) {
sumzG[ixy] = 0.0;
for (iz = 0; iz < nj; iz++) {
xx = dev_xx[ixy];
yy = dev_yy[ixy];
zz = x30_1[iz] * dev_cnt4[ixy];
d = - xx * yy * s
tt * zz * (one - xx - yy - zz) +
(xx + yy) * lambda2 +
(one - xx - yy - zz) * (one - xx - yy) * fme2+
zz * (one - xx - yy) * fmf2 ;
sumzG[ixy] += gw30[iz] / (d * d);
}
}
#pragma goose parallel for loopcounter(ixz, iz)
Notes: Here is an example of how to use goose
sample code is one-loop box diagram.
only thing we have to do is to add this pragma into the code, and re-compile by goose, that it.
by this, we can accelerate this code by using G9MPX

## Slide 35: How to realize high precision
Software implementation
  ARPREC, GMP, MPFR, MPFUN90, QD/DD, quadmath on gcc, etc
  Easy to use, but performance is …
    Add with Double precision -> 1 operation(cpu has dedicated logic)
    Add with QD -> 40 operations (combination of operations with double-precision)
Hardware implementation
  No consumer products ….
  Series of our dedicated hardware

## Slide 36: Overview of GRAPE9-MPX system
Use Altera ArriaV developing boards with PCIe
Use two PCIe extender boards (G9MG from KFCR co. ) enabling system with upto 16 FPGA boards
Develop compiler system (Goose compiler, LSUMP)
  Program written in C/C++ with pragma
@www.altera.com

## Slide 37: Picture of GRAPE9-MPX

## Slide 38: Feynman diagram used in measurement
Two loop crossed box diagram (Yuasa et al. 2012, Doncker et al. 2014)
result：-0.0853513981
Number of ops.: 128 (including load/store)
6-dimentional integral

## Slide 39: Method of the measurement
Total number of points
Replace 6 loops to 2 loops by loop fusion
To fit GRAPE9-MPX hardware
Measure execution time of overall calculation of loop integral with given (Ni , Nj)
Fix Nj :
Vary Ni :
Maximum problem size :

## Slide 40: Performance with 12 boards
Problem size
26.5 Gflops
(quadruple)
13.6 Gflops
(hexuple)
6.36Gflops
(octuple)
About 36 % of the peak performance
small
large
Influence of
data transfer

## Slide 41: Performance model
Elapsed time required for the calculation per one i-data point
Time for execution of the kernel instruction on GRAPE9-MPX
Time required for the communication between the host and GRAPE9-MPX
Time to process on the host
Number of instructions
Operation clock[Hz]
Number of PE per board
Number of FPGA boards
Number of j-data

## Slide 42: Comparison of the model and measurement
Problem size
small
large
Points: measurements
Lines: model
Good agreement!
Case of octuple
Speed-up of 12 boards
11.6 times
faster
9.3 times
faster
Significantly improved from previous work (1.07 times for 4 boards)

## Slide 43: Example: 1-loop with 3 points
loop integral
analytical result
relative error of I from the analytical result

## Slide 44
Range for the case of double precision
(11-bit exponent)
Range for the case of quadruple precision (15-bit exponent)
error for
A single digit@double
(11-bit exponent)
20-digits@quadruple
(15-bit exponent)
Need precision with more than 10-digits -> need more than quadruple
Example: 1-loop with 3 points(2)

## Slide 45: Precise in DE
Integration
transformation
trapezoidal rule
parameters determining precision
  h (width of grids)
  Nh (cutoff distance in t-variable (tmin /tmax))
    control precision
      double : tmin = -6 (xmin = 10-308)
      quadruple : tmin = -9 (xmin = 10-4932)
Notes: バックアップにまわす
DEはendpoints に あるsingularityが強いときに精度よく計算できる
のセリフを入れる
精度によって取れるtminがある, どこまで寄れるか？ how far can approach
端点特異性が強い場合は、doubleでは足りない可能性がある

## Slide 46: 開発した多倍長精度専用ハードウェア
GRAPE-MP (daisaka et al. 2011)
  Structured ASIC (Nextreme NX2500 , 90nm)にPEを実装
  4倍精度(ただし指数部11bit) 6PE 100MHz動作
GRAPE-MPX (Nakasato et al. 2012)
  Altera StratixIVに4/6/8倍精度PEを実装
  PE数: 22 / 16 / 8, 123 / 95 / 74 MHz動作

## Slide 47: GRAPE9-MPX
  G9MG(KFCR製PCIe extender)を用いてマルチボード化
  Altera ArriaVを使用
  PE数: 36/20/12, 92/81/70 MHz 動作
  IEEE754-2008: binary128 準拠(指数部15bit)
  ソフトウェア実装の100倍の性能
より規模の大きなシステムを構築し、ファインマン図形積分を計算
Notes: ソフトウェアとの比較を書くこと
----- 会議メモ (2014/09/16 16:17) -----
繰り返しはなくす。

## Slide 48: compilation process and functions
possible to generate a exe-file with MPI, GPU(by using OpenCL)
Notes: 英語化すること