## Slide 1
B. Di Girolamo, M. Guinchard, M. Schaumann, J. Wenninger
Acknowledgments:
N. Azaryan, J. Budagov, R. Corsini, P. Fessia, M. Fitterer, D. Gamba, A. Gorzawski,
M. Lyablin, M. Poehler, R. Steinhagen
Review of the needs for a hollow e-lens for the HL-LHC
6th October 2016
Observations and measurements on the impact of earthquakes and cultural noise on the LHC operation and their extrapolation to HL-LHC parameters.

## Slide 2: Outline
  Summary of civil engineering studies for HL-LHC
  Ground motion and measurements at CERN
  Study of long-distance earthquakes
    Correlation of ground motion with LHC data
    Simulation of ring orbit responds
    Simulations using HL-LHC optics
  Simulation of local small seismic activity (Geothermie2020)
  Other observations of beam oscillations

## Slide 3: HL-LHC civil engineering
The HL-LHC civil engineering work implies the construction of new access shafts, underground galleries and caverns in points 1 and 5.
  The distance between the new underground structures and the LHC tunnel is approximately 40 m.
Most of the work must be completed before LS3 for installation of HL-LHC equipment.
  Some work overlaps with LHC operation, which could lead to performance degradation of the LHC due to beam offsets at IP, emittance growth from noise etc.
M. Guinchard & J. Wenninger

## Slide 4: From noise to the beam
Beam stability
H1 (ω)
H2 (ω)
H0 (ω)
To evaluate the impact of CE, the transfer functions of the ground (vertical H2, horizontal H1) and of the triplet support (ground to CM H0) have been determined in a number of test setups.
Parasitic beam observations were made whenever this was possible.
In (ω)
Out (ω)
H1 (ω)
H0 (ω)
H2 (ω)
M. Guinchard & J. Wenninger

## Slide 5: Summary of Civil Engineering Studies
  Vibration tests reveal strong mechanical resonances of the triplet [8 - 20 Hz].
      The resonances can boost ground vibrations to amplitudes that can be problematic for the beams.
      A feasibility study of a fast beam orbit feedback system could be considered.
  The excavation of caverns and underground structures should be made during LS2.
  The convolution of measured transfer functions seems to indicate that the construction of the HL-LHC CE vertical shafts should be compatible with beam operation (2018).

## Slide 6: Outline
  Summary of civil engineering studies for HL-LHC
  Ground motion and measurements at CERN
  Study of long-distance earthquakes
    Correlation of ground motion with LHC data
    Simulation of ring orbit responds
    Simulations using HL-LHC optics
  Simulation of local small seismic activity (Geothermie2020)
  Other observations of beam oscillations

## Slide 7: Waves from Earthquakes
The different types of body (Pressure, Shear) and surface (Rayleigh, Love) waves, the multiple paths and reflections of the wave produce a complex signature of earthquakes at seismic measurement stations – and also at the LHC.
Although the seismic activity in the Geneva area is very low, waves from far away earthquakes can affect the LHC.
L. Braille (Purdue U.) / The IRIS (Incorporated Research Institutions for Seismology) consortium
Slide from J. Wenninger

## Slide 8: Geothermie 2020
Geothermie 2020 is a renewable energy production project
by the Canton of Geneva to exploit geothermal energy
for electricity production and heat generation.
Principle of energy exploitation: water is pumped into a bore hole under high pressure to stimulate a geothermal reservoir.
This may induce seismic activity and earthquakes of magnitude ~2 have to be expected.
  Duration: ~1 second, rate: 1/week – 1/month?
  Amplitude ~1 mm (factor 10 uncertainty).

## Slide 9: Earthquake Monitoring around CERN
Monitoring of the regional seismic activity is poor (from the Swiss side).
In the context of the Geothermie 2020 project (see below) a network is been build to monitor the natural seismic activity down to magnitude ~1.5 (Geneva Univ.).
Ground motion measurements at CERN:
  Network of geophones (EN-MME) will be installed in the
  LHC service areas of Point 1 and 5
    Installation foreseen during EYETS 2016/2017.
    Currently a prototype is installed in TT1, operating since Apr. 2016.
  Precision Laser Inclinometers (PLI, collaboration between CERN, ATLAS, Dubna Institute)
    Long term plan is to install devices in ATLAS cavern.
        Currently a prototype is installed in TT1, operating since Mar. 2015.
Notes: Observation with LHC beam instrumentation: DOROS, Orbit BPMs, ADT ObsBox, BLMs, BBQ, WPS/HLS (position sensors on triplets), Luminosity, Beam intensity…

## Slide 10: LHC Ring Response
Simulations of the amplification of the wave effect on orbit displacement due to the LHC lattice were carried out during the design of the orbit feedback (by R. Steinhagen).
The response of the LHC to ground motion waves depends on wavelength and direction, the amplification can reach a factor ~100 for waves travelling along the LSS in IR1 and IR5 (direction NW SE).
Large amplifications are associated to resonant response of (parts of) the LHC.
R. Steinhagen, CERN Thesis 2007-058
Transverse wave (S), vertical plane, v = 2000 m/s
l = 200 m
Currently this study is been extended in order to obtain the response under HL-LHC conditions.
Slide from J. Wenninger

## Slide 11: Simulation of Ring Response
Input
Measured ground motion (in mm)
Travel direction of the wave w.r.t LHC
  Time evolution of the ring response in terms of RMS and mean orbit.
Simulation tool under development
Output
  “snapshots” of the wave’s passage
  quadrupole offsets
  closed orbit change due to offsets

## Slide 12: Benchmarking Simulations
Results for vertical responds from new simulation tool are in good agreement with the old study.
  All important resonances appear at the same frequencies and with approximately the same ratios to each other.
  In the horizontal plane larger discrepancies are observed.
  The simulation code is still under development and being reviewed.
R. Steinhagen, CERN Thesis 2007-058
V6.503 injection optics,
injection tunes,
V6.5.seq
Vertical plane response to transverse wave excitation, v = 2000 m/s
R. Steinhagen
new simulation

## Slide 13: Outline
  Summary of civil engineering studies for HL-LHC
  Ground motion and measurements at CERN
  Study of long-distance earthquakes
    Correlation of ground motion with LHC data
    Simulation of ring orbit responds
    Simulations using HL-LHC optics
  Simulation of local small seismic activity (Geothermie2020)
  Other observations of beam oscillations

## Slide 14: Observed Earthquakes at the LHC
Location | Date | Mag | LHC | DR (mm) | Int (1013 p/beam)
Italy | 20-05-12 | 6 | 4 TeV collisions | ±60 | 14
Costa-Rica | 05-09-12 | 7.6 | 4 TeV collisions | ±80 | 19
Chile | 16-09-15 | 8.3 | Injection | ±200 | 5
Chile | 17-09-15 | 6.5 | 6.5 TeV collisions | ±15 | 10
Italy | 24-08-16 | 6.2 | Injection (MD) | ±60 | 0.3
Ascension Islands | 29-08-16 | 7.1 | 6.5 TeV collisions | ±20 | 20
Presented at Charmonix 2016
New events with available ground motion measurements in TT1.
Qualitative estimate of RMS orbit distortion impact (LHC):
If beams would be dumped for a certain orbit movement, strongly depends on tail population, wave properties …
Scaling the loss pattern at TCP,
the first Italy event could have dumped under
HL-LHC conditions.
50μm (≈0.25σ@TCP) beam dumps unlikely
>~100μm (≈0.5σ@TCP) beam dumps probable
>~200μm (≈1σ@TCP) beam dumps definitive

## Slide 15: Italy Earthquake, 24th Aug. 2016
Magnitude 6.2 in ITALY Wednesday, August 24, 2016 at 01:36:33 UTC
The prototype ground motion devices in TT1 recorded the event.
LHC
epicenter
Amatrice after the earthquake
Geophone measurement TT1
Inclinometer data TT1
~2min
10min
Main frequencies: 0.1-0.3 Hz (8-3s)

## Slide 16: Italy Earthquake: LHC Observations
The LHC was performing MDs and only Beam 1 was present at the time of the earthquake.
Inclinometer signal
±10mrad
Meas. mean orbit
±60μm
Meas. RMS orbit
no signal visible
TCP BLMs in IR7
nicely correlate with orbit
Noise floor of this BLM
Losses increase with increased mean orbit
Timing and overall shape of ground motion measurement and orbit signal fit.

## Slide 17: Ascension Islands Earthquake, 29th Aug. 2016
Magnitude 7.1 in Ascension Islands Monday, August 29, 2016 at 04:29:57 UTC
LHC
Epicenter
LHC was in stable collisions
1h
Main frequencies: 0.05-0.1 Hz (10-20s)

## Slide 18: Observations on the LHC Beam
Hor. Mean Orbit
BLM TPC CL7
Clear correlations between ground motion in TT1, orbit and losses in IP7.

## Slide 19: Correlations of Ground Motion with Luminosity
Luminosity shows good correlation with ground motion in TT1.
ALICE/LHCb oscillate in phase with the ground motion.
ATLAS/CMS oscillate with π/2 phase difference.

## Slide 20: Simulation of Orbit Responds
Simulation with Inclinometer data
No proper calibration to units of meter (as required for the simulation).
 Amplitude of simulated RMS orbit distortion not reliable.
Assumed same signal for longitudinal and vertical offsets.
 Some frequencies and amplitudes may not be covered in simulation.
 Where orbit and inclinometer show equivalent peaks the simulation follows.
Simulated vertical RMS orbit
measured RMS orbit
measured radial orbit
Inclinometer signal

## Slide 21: Simulations with HL-LHC Optics
Compared to the 2016 LHC optics the sim. RMS orbit response increases by a factor
~2 for round HL-LHC optics
~3 for flat HL-LHC optics

## Slide 22: Outline
  Summary of civil engineering studies for HL-LHC
  Ground motion and measurements at CERN
  Study of long-distance earthquakes
    Correlation of ground motion with LHC data
    Simulation of ring orbit responds
    Simulations using HL-LHC optics
  Simulation of local small seismic activity (Geothermie2020)
  Other observations of beam oscillations

## Slide 23: Seismic activity from Geothermie 2020
Seismic signal (magnitude ~1.8)
measured during a test injection of high pressure water
Report of RESONANCE Ingenieurs-Conseils SA, RT-424.02-1/MK/CB/ST/CL, data provided by Martin Koller, data set used SMZW_093
Amplitude ~4-6μm
Duration <10s

## Slide 24: Simulation Results for 2016 Conditions
Propagation direction: IP1->IP5
Propagation direction: IP3->IP7
2016 Optics
IP1
IP5
IP3
IP7
Earthquake wave
IP1
IP5
IP3
IP7
Earthquake wave
For the simulation it was assumed that plane wave fronts travel parallel to the LHC plane.
RMS orbit strongly dependent on direction of the wave  factor 3
Peak ~120μm
Peak ~40μm
RMS quad. displacement up to ~2μm

## Slide 25: HL-LHC Optics Cases
Propagation Direction: IP1-> IP5
Propagation Direction: IP4-> IP8
Vertical Response
IP1
IP5
IP3
IP7
Earthquake wave
IP1
IP5
IP3
IP7
Earthquake wave
RMS orbit increases by a factor 2-3 for HL-LHC optics, with resonant spikes up to a factor 5 for flat optics.
Peak ~250μm for flat optics
Peak ~100μm

## Slide 26: Outline
  Summary of civil engineering studies for HL-LHC
  Ground motion and measurements at CERN
  Study of long-distance earthquakes
    Correlation of ground motion with LHC data
    Simulation of ring orbit responds
    Simulations using HL-LHC optics
  Simulation of local small seismic activity (Geothermie2020)
  Other observations of beam oscillations

## Slide 27: Luminosity Oscillations of Levelled Experiments
Luminosity oscillations of levelled experiments are frequently observed.
  Period ~15 seconds
  Period ~2.5 minutes
Example
Fill 5345

## Slide 28: Luminosity Oscillations: Fill 5345
~30min
~15min
~15min
~4h
ALICE
LHCb
Effects have often a similar duration (~minutes) and re-appearing intervals (~hours).
 Seems to be caused by a technological source.
~50min
~4h
~15min
~1 - 2h
~4h
both effects overlap

## Slide 29: Effect with ~15s Period
Oscillation of amplitude ~4 mm in vertical at Q1 BPM in IR1 (b = 1200 m)
  amplitude in arcs is ~ 2 mm
Oscillation of amplitude ~1 mm in vertical at Q1 BPM in IR2 (b = 60 m)
  amplitude in arcs is a little larger
 The oscillations of the orbit may be a bit too small to explain the luminosity fluctuations unless the source is a quadrupole.
  The orbit oscillations are due to the beam offset w.r.t. quadrupole axis,
  The luminosity fluctuation due to the b-function modulation. The levelled experiments are much more sensitive !
DOROS BPM B1 – IR1
10 mm
B2 shows similar amplitude in both cases
DOROS BPM B1 – IR2
5 mm

## Slide 30: Effect with ~2.5min Period
A second effect with a different frequency causes:
Orbit oscillations mostly observed in B2-Hor with amplitudes of ~20 mm.
Periodic ‘spikes’ are observed in the RMS orbit of B2.
RMS Orbit B2
RMS Orbit B1
Example Fill 5282

## Slide 31: Conclusions
Civil engineering:
  Strong mechanical resonances of the triplet at [8, 20 Hz].
  Excavation of HL-LHC vertical shafts should be compatible with 2018 LHC operation.
Large earthquakes (M>6) have a clear impact on the LHC.
  So far NO event cased a beam dump.
  (Prototype) ground motion measurements at CERN are under commissioning.
    IP1 and 5 are planned to be equipped with geophones in the EYETS 2016.
Simulations to predict the ring orbit response are being renewed and extended to as well make estimates for HL-LHC.
  Simulations are still in the development phase.

## Slide 32
Backup

## Slide 33: Transfer Function Measurements
In (ω)
Out (ω)
H1 (ω)
H0 (ω)
H2 (ω)
Measurements at SM18
with Q1 triplet spare
Measurements in AWAKE area (TAG41/TT41)
with a shaker
Measurements in ATLAS area (UL16/SR1)
with a vibration truck
40 m
M. Guinchard & J. Wenninger

## Slide 34: Transfer Function Results for H0(ω)
Measurement of Q1 transfer function H0 shows strong modes at 21.5 Hz, 8.4 Hz and 12 Hz.
Vertical
Lateral
21.5 Hz
8.4 Hz
8.4 Hz
12 Hz
Measurements performed using the ADT and the DOROS BPMs at the Q1’s and the 100Hz BLM data confirm the presence of activity in the frequency range of the triplet resonances.
4.5Hz
8.4Hz
12Hz
21.4Hz
22.9Hz
2x22.9Hz
FFT of a sample of the BLM 100Hz data
DOROS
20 Hz
12 Hz
Normalized by b
2015 ADT and DOROS BPM data
M. Guinchard
M. Fitterer

## Slide 35: Transfer Function Results for H1(ω) and H2(ω)
      TT41 (H1(ω)) measurement dominated by shear waves, SR1 (H2(ω)) measurement by pressure waves – confirmed by wave propagation speed.
      Gain for vertical measurement is possibly biased by surface waves.
      The source distance is together with planning decoupling the main ally that we have to minimize / avoid impact on beams.
Chart: Frequency [Hz]
| 2.0 | 3.0 | 5.0 | 8.0 | 12.0 | 18.0 | 24.0 | 28.0 | 35.0 | 42.0 | 49.0 | 60.0 | 70.0 | 85.0 | 98.0 | 127.0 | 148.0 | 174.0 | 198.0
TT41-TAG41@40m | 0.031736 | 0.029141 | 0.027665 | 0.030507 | 0.02103 | 0.010009 | 0.012397 | 0.017184 | 0.019722 | 0.018799 | 0.014632 | 0.0090963 | 0.0094248 | 0.012932
TT41-TAG41@80m | 0.015807 | 0.014477 | 0.01369 | 0.01502 | 0.010274 | 0.0048523 | 0.0059788 | 0.0082131 | 0.0093415 | 0.0088242 | 0.0067716 | 0.0041558 | 0.0042234 | 0.0056987
SR1 to UL16@89m | 0.1279 | 0.090214 | 0.066352 | 0.046012 | 0.017227 | 0.0038986 | 0.0080651 | 0.0048788 | 0.0029787 | 0.0023031 | 0.0010048 | 0.00065902 | 0.0004236 | 0.0006474 | 0.0024909 | 0.0019637 | 0.000501 | 0.0018832 | 0.0026925 | 0.0035294 | 0.0050847
6138 to UL16@141m | 0.065041 | 0.032995 | 0.025375 | 0.059206 | 0.010512 | 0.0065741 | 0.0033845 | 0.0018793 | 0.00039152 | 0.00272 | 0.0016325 | 0.0010921 | 0.00063361 | 0.0010303 | 0.00042911 | 0.00041064 | 0.0003858 | 0.00045965 | 0.00070602 | 0.00073511 | 0.00014337 | 0.00017346 | 0.00016437 | 0.00022994 | 0.00033036 | 0.00046189
Horizontal -40m
Horizontal -80m
M. Guinchard & J. Wenninger
H2(ω)
H1(ω)

## Slide 36: Vibrating truck impact on LHC beam
Beam measurements with the vibrating truck were performed for the squeezed optics (80 cm) at 6.5 TeV and at injection.
  Multi-turn data (all BPMs) & ADT data.
Measurements results:
  Beam oscillations were only observed in the vertical plane  truck location.
  Beam oscillations were only observed for vibration frequencies of 18-22 Hz – consistent with the triplet resonances.
  Observed B1/B2 amplitude ratio of ~2.5 implies that the different triplet quads oscillated with different amplitudes.
  The oscillation amplitudes of the triplet CMs were in the few mm range for a ground motion amplitudes of ~50 nm in the tunnel.
Dark blue = no truck
The observations are consistent with the triplet resonances that enhance the vibrations by a factor >> 10
M. Guinchard & J. Wenninger

## Slide 37: Truck  triplet predictions
Chart: Excitation frequency (Hz)
| 4.0 | 6.0 | 8.0 | 10.0 | 12.0 | 14.0 | 16.0 | 18.0 | 20.0 | 22.0 | 25.0 | 30.0 | 35.0 | 45.0 | 52.0 | 60.0 | 70.0 | 80.0 | 90.0 | 100.0
In (w) SR1 ground motion [um] | 0.33937 | 1.1186 | 1.63 | 2.322 | 4.617 | 3.2314 | 6.3031 | 7.3164 | 12.708 | 20.407 | 19.905 | 25.968 | 21.625 | 9.6353 | 6.111 | 5.4491 | 3.186 | 1.857 | 0.85 | 0.59
Out (w) for IP side | 0.080127 | 0.078269 | 0.31731 | 0.29439 | 0.3154 | 0.11883 | 0.2264 | 0.41637 | 0.85937 | 0.22754 | 0.1173 | 0.040659 | 0.048282 | 0.053149 | 0.072566 | 0.0068158 | 0.0041225 | 0.0081598 | 0.0069373 | 0.030277
Out (w) for Q2 side | 0.072563 | 0.14429 | 0.57757 | 0.39823 | 0.19856 | 0.069194 | 0.040254 | 0.055227 | 0.29406 | 5.1667 | 0.34913 | 0.053017 | 0.041626 | 0.043253 | 0.095001 | 0.012378 | 0.014364 | 0.022555 | 0.020154 | 0.011283
      Expected motion of the triplet magnetic center during truck tests.
2-3 µm @ 22 Hz (average of both sides) – consistent with beam observations !
beam
M. Guinchard & J. Wenninger

## Slide 38: Core drilling  triplet predictions
Chart: Depth [m]
| 10.0 | 20.0 | 30.0 | 40.0 | 50.0 | 60.0
In(22Hz) with Core Drilling | 0.22105 | 0.11814 | 0.092079 | 0.058153 | 0.13786 | 0.10811
Out(22Hz) for Q2 side with Core Drilling | 0.081118 | 0.08138 | 0.081643 | 0.10319 | 0.12448 | 0.13508
Out(22Hz) for Q2 side without Core Drilling | 0.076212 | 0.076212 | 0.076212 | 0.076212 | 0.076212 | 0.076212
38
      The expected motion of the triplet magnetic center vs depth remains at level of ≈ 0.1-0.2 mm – acceptable.
M. Guinchard & J. Wenninger

## Slide 39: Frequencies of Earthquakes
Frequency spectrum of waves induced by earthquakes ranges from ~ mHz (earth oscillations and surface waves) to ~100 Hz for local seismic events.
The signatures of large and distant earthquakes (teleseismic) are dominated by low frequencies < 1 Hz.
Ground motion from local earthquakes (Geothermie 2020) extends to higher frequencies.
Slide from J. Wenninger

## Slide 40: Orbit Stability at TCP
±5μm
±5μm
The orbit at the TCP during stable collisions is controlled to
±5μm.
J. Wenninger

## Slide 41: RMS Orbit over the year
reference mid July
wrong calibration of some BPM crates
single bunch fills
RMS orbit stable <50μm
J. Wenninger

## Slide 42: Luminosity Oscillations of Levelled Experiments
Luminosity oscillations of levelled experiments are frequently observed.
These oscillations correspond to ~2-4 mm of vertical beam separation at the IPs (@ b*= 3 and 10m).
Period ~15 seconds
  Effect also visible on B1 lifetime ( losses at TCP).
Example
Fill 5282

## Slide 43: Luminosity Oscillations: Fill 5282
~31min
~16min
~17min
~17min
~4h
~4h
~4h
ALICE
LHCb
Effect has often a similar duration and re-appearing intervals.
 Seems to be caused by a technological source, which is so far unknown.

## Slide 44: Luminosity change due to beta-beat
Luminosity change due to beta-beating with offset levelling:

## Slide 45: Summary of Ground Motion Studies (1)
Large earthquakes (M>6) have a clear impact on the LHC, even if originating at long distance.
  So far NO event cased a beam dump.
  Potentially only one event would have dumped under HL-LHC conditions.
  Nearby small earthquakes have not been observed.
Prototypes of geophones and high precision laser inclinometers are under commissioning and recording ground motions in TT1.
  Since the ground motion backgrounds in TT1 and the LHC tunnel are quite different, any correlation to LHC beam data can only be meaningful for long-distance earthquakes.
  For systematic correlation studies of the effect of ground motion on LHC operation, ground motion measurement devices are required in the LHC tunnel.
     Geophones will be installed in Point 1 and 5 in the EYETS and the data will be logged to the database from next year on.

## Slide 46: Summary of Ground Motion Studies (2)
Simulations to predict the ring orbit response are being renewed and extended.
  The simulation code is still under development and all new simulation results presented here are very preliminary.
  Long-distance strong earthquakes:
    Clearly observed on orbit, BLM and luminosity.
    Simulation show already a qualitative reasonable agreement.
    Simulation indicate that for HL-LHC optics orbit oscillations are increased by a factor 2-3 w.r.t. the current LHC.
  Potential seismic activity from Geothermie 2020 project:
    No comparison with beam data possible.
    Simulations with current LHC collision optics show rms orbit distortions > 120μm, which could probably be survived.
    For HL-LHC optics the simulation suggests (depending on the direction of the wave) an enhancement of a factor ~2-3,
       which would most probably cause beam dumps.