## Slide 1: Scalable Readout System
SRS was developed by RD51 collaboration for R&D on MPGD gas detectors
Collaborating SRS teams and users in 2016
MPGDs @ GDD-lab CERN, Photon detectors @ NEXT coll., Muon Tomografy @FIT, MICROMegas @ ATLAS MAMMA, DTC links and SRU@ ALICE DCAL, GEMs @ FTBF Coll., Timepix-SRS for ILC-TPC test@Bonn Univ,, GEM stack readout @BNL, GEMs@ CMS GEM collab, optical Readout@ TOTEM, GEM detectors @ PRad Coll., Neutron detectors@ ESS Brightness, Large surface MUST detector @ LSBB, VMM frontend for FOCAL E-PAD@ Univ. Tsukuba, GEMs for CP-Violation @CAPP, … and many more

## Slide 2: SRS concept (since 2009)
choose the best frontend for your detector
low noise, spark protection, dyn. range..
connect X frontends to SRS backend
scalable DTCC links instead of bus
start with few channels (1 hybrid=128 ch.)
get used with DAQ and Analysis software
scale up to X channels with same software
get support by large SRS user base RD51
many SRS systems, much experience
SRS services: detector-HV, amplifiers etc.
SRS Classic: purchase via @CERN store
Commercial SRS starting 2017 *
New SRS frontends: request-driven R&D collaboration based
*exception: APV hybrid, only available through CERN
DTCCP links
default HDMI
DTCC links
Default CAT7
Frontend carrier (hybrids)
ASICs, preamplifiers
on detector
FE Adapter (cards, mezzanines)
( ADC, DVM, Timepix, SiPM, PM)
+ Frontend concentrator (FEC)
Opt. Scalable Readout Unit (SRU)
data MUX/Buffer, TTCrx, clock and trigger source, Busy, Slow Controls
UPD/ 10GBE
PC / Laptop with
DAQ and Analysis SW
Slow controls

## Slide 3: Scalable readout Architecture
SRU
PCs with Online SW
Detector
…..
Laptop
with Test/Online SW
Adapters.)
FECs
Frontend DTCC links
SRS frontend
Backend DTCC links
high BW data
over UDP
trigger
controls over
ethernet
SRS
service
electronics
USB Device
Controls
& readout
HV
1 Vertical Slice
Minimal SRS: 1 or 2 vertical slices
Full SRS: stacks of vertical-slices
UDP Ethernet
Data and Controls
FEC
Adapter (ADC, DVMcard, etc)
(Mini)Crate
SRS Frontend (APV,VMM etc)
Test Detector
Frontend link
Trigger
Trigger Pickup
TC link
Crate(s)
CTF

## Slide 4: xTCX links ( SRS-specific links )
ALICE DCal: DTC links over CAT7 from 40 FEE to 1 SRU
xTCx links make SRS scalable
DTCCP frontend links
PC
10 Gigabit Ethernet / UDP
SRU
BUS
. . . . .
DTCC backend links
FEC
..
FEC
..
FEC
..
LINK scalability features vs. parallel Bus
Data in parallel over p-p links
=>Higher BW & Trigger rates
point-point controlled impedance
=> very high bitrates & lower error rates
overcome bus length limit
=> single point failures = non fatal
less wear-out of contacts
=> more reliable, less cost
xTCx link flavors in use so far
DTC Data+Trigger+Clock (over CAT7, SRU-FEE ) 2009
DTCCP Data+ Trigger+ Clock +Control + Power ( over HMDI*, FEC-Frontend) 2010
TC Trigger + Clock ( over CAT7, CTF - FEC) 2010
DTCC Data +Trigger+ Clock +Control ( over CAT7, SRU - FEC) 2011
DTCCO Data+ Trigger+ Clock+ Control over Optical fibre ( planned , 2017 )
* copper or fibre
hybrids
D T C C

## Slide 5: Table-Top SRS
Powered SRS crate with FEC / Adapter combo
Detector
with APV hybrids
Readout & power
via HDMI link
Laptop connected via
Ethernet cable to FEC
Online Readout systems
DATE, and/or Labview SRS

## Slide 6: SCALABILITY ( a. over types of frontend )
-general-purpose SRS:
APV frontend = 128 analogue ch. on hybrid
VMM frontend= 128 digital ch. on hybrid
-experiment –specific SRS:
SiPM and PM adapter (NEXT)
Octal Timepix-2 adapter (Univ. Bonn)
1 ASIC: 128 analogue ch.
APV wire-bonded, on SRS hybrid
1 ASIC: 64 digital ch.
2 x VMM wire bonded on SRS hybrid
1 APV channel
1 VMM channel
Example of different frontends combined in a single RO system

## Slide 7: Scalability ( B. # channels )
SRS channel unit = 1 hybrid 128 channels
DTCCP readout cable unit = 256 channels
FEC Frontend concentrator unit = 2k ch.
Multi-FEC system with SRU = 4k…16 k ch.
Multi-Crate with SRU(s) > 16k ch
Table-top minimal SRS system
1 ADC adapter card + 1 FEC
8 HDMI ports
Frontend Hybrids
along Detctor frame
SRS slices (FEC+Adapter)
in Euocrate with SRU below

## Slide 8: Frontend links (DTCCP)
HDMI* cables A-D (micro) up 5m
HDMI cables A-A coupled to A-D up 25m
NEW ( tests in preparation )
- active HDMI copper A-A + A-D max 50 m
- active HMDI fibre A-A + A-D max 150 m
* we do NOT use HDMI protocols
SRS Minicrate
DTCC link HDMI A-A
GEM detector with
SRS APV hybrid,
powered over HDMI
Photo: SRS test with RCDAQ at BNL
Laptop with RCDAQ
Commercial
100m active, optical
HDMI cable
5m HDMI standard A to micro (D)

## Slide 9: Small systems
Mini-crate SRS system
> 100 crate systems in use worldwide
mainly by members of the RD51 collaboration
Table-top SRS
= 1 vertical slice
Complete
readout system from detector
up to offline Analysis
HDMI cables max 25 m
(active HDMI up 150m)
Hardware available via CERN store
Firmware included
Software via RD51 database
2017+ commercial SRS sales licences
“SRS Classic”
Crate –based SRS

## Slide 10: SRS frontends
APV25 (128 ch, analog) @ CERN store, standard FE for RD51
VFAT (64 ch, digital) CMS/Totem -> prototype only
Beetle (128 ch, anal +digital) -> prototype only
SiPM and PM frontend @ UPV Valencia for NEXT
VMM (128 ch, digital+ ZS ) @CERN -> testing RD51/ESS
GEMROC (64 ch , digital) in prep @ AGH and EicSys
Timepix R&D for ILC TPC @ Bonn Univ. Proto system
SRS system Hardware
FEC cards ( CERN store + commercial)
analogue adapter (16 x ADC 12 bit) ( CERN store + commercial)
digital adapter for VMM frontend (commercial)
Mini-crates up 4k channels (CERN store)
Eurocrates ( REV2 ) up 16 k channels (commercial)
ATCA crates, RTM cards 10 GBE, SFP (commercial)
ATCA blades ( 2x LX240) (commercial)
ATCA mezzanines (ADC, 6x12fibre ribbon) commercial, CDT (UPV)
CTF clock-trigger fanout (inhouse-> commercial)
Timepix adapter 6U card ( Bonn Univ, prototype )
Optocard VFAT 6U card (Totem)
High Voltage for MPGD’s AVD NIM ( in prep. -> commercial)
SRU LX240, 40xDTCC, NIM, 10GBE, 4x SFP (inhouse-> commercial )
APIC preamp-shaper , battery box ( finalized -> commercial)
Femto online current measurement over 10 decades (in prepar.)
SRS Online SW ( via UDP )
DATE (= default RD51)
MMDAQ (ATLAS MM)
CODA ( PRad)
RCDAQ ( BNL/RHIC)
Labview SRS ( test systems)
Slow controls (via IP )
SDC (Scalable Detector Controls )
scripts via Linux/DATE
Labview (for testing)

## Slide 11: frontend link Adapters
ADC and DVM cards with HDMI ports
HDMI and SFP mezzanines (ATCA)
Optical ribbon mezzanines (ATCA)
Crate environment
Minicrate 19” 3U (CERN store)
Eurocrate 19” 6U (CERN store)
ATCA Minicrate (EicSys )
ATCA 14 slot full crate (EicSys)
Readout Units
Network switch ( small systems)
SRU ( default, large systems)
SRU-ATCA (planned)
SRS firmware
FEC -APV frontend
FEC -VMM frontend
analogue module APV readout
common mode/pedestal correction
Zero Suppression APV
10 Gbit core Virtex6 XAUI ( SRU)
DDL core ALICE
Slink core ATLAS
TTC rx module Virtex-6 (SRU)

## Slide 12: APV 128 hybrid SRS (CERN store SCEM 07.89.00.005.9 )
Micro HDMI-D
readout plug
= SRS chiplink
Wire –bonded,
APV 25 chip,
analogue
128 channels
(below globtop)
MMCX connector
array for GND/click-in
Master-Slave
cable
connector
IEC-61000
Level-4
spark
protection
PLL for clock/trigger
separation
Discrete AC coupling and grounding
Low noise LDO’s

## Slide 13: VMM hybrid SRS ( new digital SRS frontend under test )
HDMI link 1 DTCCP
JTAG
HDMI link 2 DTCCP
Companion FPGA
Photo: 2 x wire-bonded VMM2 chips, VMM3 under work)
AC coupling
&
spark protection
Panasonic 130 pin
connector for MPGDs
to be replaced by new
140 pin HRS connector
Neighbor-channel via MMCX
Detector GND MMCx

## Slide 14: APV(analogue) VMM(digital)
APV (250 nm CMOS)
Pipeline depth: max. 192 clocks
Trigger latency: max. 3 us
Noise: < 500 e- intrinsic >750..1400 e- on detector
dynamic range: 25 fC
Detector capacity: 18… < 60pf
ADC ext. 4096/1000 [counts/baseline]
Gain: fixed CSA gain 100uA/mip, 5 output signal gains (in step of 20%)
Timing jitter : ½(1/fc) [+- 12ns]
Shaping times: 50 ns adjustable to 80 ns
max readout rate: 7 kHz
VMM (130nm CMOS)
Pipeline depth: 64 digital frames (peak)
Trigger latency: (self triggered) or L0 (12.8us)
noise : < 400 e- on 10x10 detector reported
dynamic range: expect >> 25 fC
Detector capacity: 30pF .. .. < 1nF
ADC: embedded, 10 bit
Gains: 8 CSA gains [0.5..16mV/fC]
Timing jitter: 20 bit t-stamp, 1ns resolution
Shaping times: 4 [ 25… 200ns]
max readout rates: estimated 4 MHz/ch

## Slide 15: Eurocrates fOR larger systems
Stacking “of vertical slices”
up to 8K channels
per crate
CTF card for common clock and Trigger (TC link)
HDMI frontend links connected on rear side
Power for APV or VMM via HDMI

## Slide 16: SRS ATCA
ATCA Minicrate
2 slots for SRS blades
shelf manager
2x
SRS mezzanines
Left: optical
Right: ADC/HDMI
RTM (rear Transition Module)
10 GB Ethernet, 3 GB SFP
Meshed backplane
(6 Gbps, 100W links)
SRS ATCA blade
2x FPGA LX240, 2 mezzanine slots

## Slide 17: SRS ATCA overview
RTM I/O card:
2 x 8 SFP+ ports
( 2x 10 GBE FPGA, 2 x 7 4Gbps to mezzanines)
2 x Rj45 (1 DTCC to each mezzanine)
2 x NIM (SMA)
Blade main board:
2 x Virtex 6 LX240 FPGA
2 x DDR3 plugin
2 x mezzaine ports
2 x Mezzanines (ADC):
ATCA Zone 2
backplane connectors
ATCA zone 1 power connector
ATCA Zone 3
RTM comemctor
2 ADC mezzanines:
up to APV 6144 channels

## Slide 18: ATCA - based SRS
ATCA industry standard crates of different size
Very high-speed linked backplanes between blade-slots
3 x channel density compared to FEC
FEC => Blade with 2 x Adapter plugins
Adapter card=> mezzanine card
Photo SRS Minicrate with 1 blade, 24 HDMI ports for 6 kchannels

## Slide 19: SRS Classic versus SRS ATCA
80 k APV channels 4 Eurocrates crates
in a Rack with SRS Classic
80k APV channels in one single 14 slot ATCA crate
with ATCA SRU in slot 1
ATCA blades, RTMs and ADC mezzanines are available
ATCA SRU is a planned design
ATCA:
3 x channel density
FECs, ADC, SRU available
Eurocrates for 8 FEC/ADC require ATX
power upgrade

## Slide 20: SRS in Experiments
PRad GEM with SRS- APV frontend @ UVa
NEXT Collab. SRS-ATCA with photon
Detector frontend
SRS with Timepix frontend
Large surface MUST detector
with SRS Classic and APIC trigger
SRS Totem: optical readout DTC
Detector telescope with SRS readout
@testbeam 2016

## Slide 21: SRS service electronics
APIC: preamplifier -shaper box, solar chargeable
Femto: Femto-ampere meter with realtime signal output
AVD: Active Voltage Divider / generator for MPGD’s
..and more

## Slide 22: Where to GET SRS
SRS procurement until 2016
INHOUSE production RD51 ( basically all early systems )
CERN Store ( from produces like Prisma, NEOHM etc ) https://edh.cern.ch/Document/SupplyChain/MAG
  AVP hybrids, FEC + ADC cards, Minicrates, HDMI cables, SRS accessories
  However !!! Only via team account, delivery only to CERN, APV purchase restrictions
EicSys http://www.eicsys.eu/
  ATCA crates, blades, RTM cards; ADC mezzanines
  However !!! No hybrids, waiting for news and testbeam qualification
  NEXT and ATLAS NSW users have their your own experts for SRS ATCA
believe it or not, this was and still is, the most difficult about SRS
SRS procurement from 2017+
INHOUSE production RD51: stopped
CERN Store: continued
EicSys: no change reported
NEW SRS production licencies* 2017
SAMWAY Electronics: http://www.samwayelectronic.com
FEC and ADC cards, Eurocrates, SRS-ATCA
mezzanines
SRS Technology: http://www.srstechnology.ch
VMM hybrids, DVMcards, SRU, APIC, AVD, Femto

## Slide 23: more possibilities
For example:
optical 3D frontend with CMOS cameras or Timepix-3 chips ( >> 10 kHz frame-rate )
multichannel, low noise photodetector frontend ( APD's, SiPMs, MPCCs etc )
calorimeter frontend with up to 16 bit dyn. range ( high/low gain channel hybrids )
SRS sensor frontends via I2C with new HRS connector ( pressure, temperature, position, currents, gas purity, UV ps pulser, etc )
… possible with active support and collaboration from your team

## Slide 24: SRS Resources and references
SRS documents and binaries database https://espace.cern.ch/rd51-wg5/srs
RD51 electronics school 2014 https://indico.cern.ch/event/283113/
MPGD Applications beyond Fundamental Science, 18 RD51 Collaboration meeting Aveiro 2016
https://indico.cern.ch/event/525268/timetable/#20160912
S. Martoiu, H.Muller, J.Toledo, Front-end electronics for the Scalable Readout System of RD51
IEEE Nucl. Sci. Symp. Med. Imag. Conf. (2011) pp.2036-2038.
K. Gnanvo et al.,
Detection and Imaging of High-Z Materials with a Muon Tomography Station Using GEM Detectors
Nuclear Science Symposium Conference Record (NSS/MIC), Nov. 2010 IEEE
J. Toledo et al., The Front-End Concentrator card for the RD51 Scalable Readout System,
2011 JINST C11028.
S.Martoiu, H.Muller, A.Tarazona, J.Toledo,
Development of the Scalable Readout System for Micro-pattern gas detector and other applications,
2013 JINST 8 C03015
Ignacio Lázaro et al.
Muon telescope based on Micromegas detectors: from design to data acquisition,
IDUST 2014
R. Esteve et al., Readout and data acquisition in the NEX-NEW detector based on SRS-ATCA
2015 JINST C01008
Gianluigi De Geronimo et al, VMM2 - An ASIC for the New Small Wheels,
TWEPP 2014 – Aix en Provence, France, September 2014

## Slide 25: Backup slides

## Slide 26: MPGD-detector-specific hybrids and accessoirs
Master-Slave = 256 channels
per HDMI A-D readout cable
(Farnell 1786338 )
power via HDMI
Panasonic 130-pin socket
on detector
header on hybrid
9 mm above detector
detector plane
128 channels for 0.4 mm
continuous pitch
MMCX click-in Ground system
on detector and hybrid, stackheight 6.5 mm
Typical desktop
MPGD detector*
M-S flat cable
10 cm:
SAMTEC FFSD-08-D0401N
20 cm:
SAMTEC FFSD-08-D0801N
Master
(has HDMI)
Slave
no HDMI
Gas connector

## Slide 27: DTCC link protocol
High Priority ch.
Trigger/Busy/..
Low Priority ch.
Data / Contrl
Framing Control
Framing Detection
8b/10b
ctrl
commas
Ch. request
Flow control
DTCC Tx
8b/10b
DTCC Rx
Latency correction
Time multiplexed DTCC link
Trigger, Busy, Clock = high priority and low latency
Data = low priority
Controls = Ethernet frames @low priority

## Slide 28: Frontend link (DTCCP)
SRS uses HDMI cables A-D
for connection of frontends to
SRS
DTCCP =
Data uplinks
Trigger downlink
Clock downlink
Controls bidir I2C
Power 5V max. 1A
For distances 25m< L <150m
 active HDMI links
copper/ fibre under tests
HDMI-A
HDMI-D (micro)

## Slide 29: Scalable Readout Unit (SRU)
40 x DTCC links
2 LVDS in, 2 LVDS out
4 x LVDS
horizontal synchronization and Trigger
TTCrx optical
4 x NIM in
4 x NIM out
4 x SFP+ ports
3 x 3 Gbit
1 x 10 Gbit Ethernet XAUI
2 GB DDR3
Virtex 6
FPGA
PHOTO SRU
designed for use in magnetic field:
Alu chassis, no transformers, no DC-DC
Jitter cleaner
TTC clock
Hans.Muller@cern.ch

## Slide 30: VMM issues
3x power of APV frontend: direct powering via HDMI is limited in length
VMM Power and HDMI repeater box for long HDMI links is under works
VMM requires cooling on the detector:
cooling strategies under discussion
Standard MPGD connector ( Panasonic 130 pin obsolete)
=> new connector for both MPGD detector frames and VMM3 hybrid in 2017
New 140 pin connector for VMM

## Slide 31: SRS history RD51
SRS, 2009+ standard readout system for MPGD detectors ( GEM, MM, etc)
CERN made MPGD detectors come with SRS connectors for SRS hybrids
2010+ SRS crates, electronics, accessories available trough CERN store
Firmware, Software and Manual download from RD51 server
DAQ systems : DATE (default), Labview
O(100) deployed small and medium-sized SRS systems