## Slide 1
Introduction to the RD51 Collaboration
Workshop on Neutrino Near Detectors based on gas TPCs
CERN, 8-9 Nov. 2016
Theodoros Geralis,
NCSR Demokritos, Greece
On behalf of the
RD51 collaboration
OUTLINE
RD51/MPGD history
Organization/Infrastructures
Technological achievements
Applications

## Slide 2
MSGC: Oed 1988
GEM:Sauli 1997
Micromegas:
Giomataris 1996
~50 μm
~100 μm
~50 μm
~50 μm
μ-PIC
Ingrid
MWPC: Charpak
1968
RD51 Collaboration:
86 Institutions
500 Scientists
From Multi-Wire Proportional Chambers to Micro Pattern Gaseous Detectors
Rates: ~106Hz/mm2
But: Sparks,
irreversible damages
Rates: >106Hz/mm2
σSpatial ~30μm
Rates: >106Hz/mm2
σSpatial ~30μm

## Slide 3
The RD51 Collaboration
Main objectives:
MPGD technological development
  Provide the collaboration framework
  Develop common simulation
  packages
  Develop common read out electronics
Access to “MPGD know-how”
Foster Industrial production
 huge growth in interest in the MPGD
technologies
Collaboration Spotting Software: http://collspotting.web.cern.ch/)

## Slide 4
RD51
Technological Aspects
New Detector Structures
Modeling of Physics Processes
Software Tools
MPGD Electronics
Production and Industrialization
Common Test Facilities
WG5:
WG4:
WG1:
WG2:
WG7:
WG6:
Applications, Training
and Dissemination
Detector Physics and
Performance
RD51 Common Projects
WG3:
The RD51 Collaboration: Working Groups

## Slide 5
RD51 related infrastructures:
EP DT MPT Workshop (Head: Rui De Oliveira)
The heart of the MPGD Globe: Design, prototyping, production
New infrastructure (building, MPGD production machines, clean room etc) will be soon ready
2) GDD Laboratory (RD51)
The Detector R&D laboratory:
- Permanent users (ALICE, ATLAS, ESS)
- Temporary Users stations
- Cosmic stands, X-ray and radioactive sources
- Clean room, Workshop
- Vacuum and Gas System
- MPGD Electronics support
- 15 visiting groups, synergies with companies
3) Test Beam Area (SPS/H4 semi permanent RD51 area)
Workshops
Laboratory (140m2)
Clean
Room
(17m2)
Meeting/
Visitors
Room
5
GOLIATH
(1.5T Max, 1mt gap)
Organize test beam
3 times (2 weeks)/year
R&D for Experiment
HEP Experiments:
LHC upgrades
CERN & Others
Applications
Electronics

## Slide 6
RD51 Technological achievements (I)
Large MPGDs production/industrialization of GEM, THGEM, Micromegas:
single mask GEM Bulk Micromegas
High rates and spark mitigation:
Staged Gain: multiple layers Resistive coating, buried resistors
GEM, THGEM, MHSP Micromegas, RETGEM, RPWELL

## Slide 7
COMPASS RICH
Staggered THGEMs
RD51 Technological achievements (II)
Ion Back Flow (IBF), Application in TPCs (field distortion) and
  photon detection (photocathode protection): Multiple Layers
  Hybrid: THGEM+ CsI and MM Multi layer GEM stack MHSP/GEM/F-R-MSHP
Radiation hardness
LHC MPGD Upgrades (ATLAS NSW project - Resistive Micromegas and CMS GEM
muon chambers) proven to withstand the equivalent of 10 years of operation at the
HL-LHC. Irradiation with: neutrons, X-rays, α and β.
ALICE TPC
IBF ~ 5. 10-2
IBF ~ (5 – 25) . 10-3
IBF ~ (1-3) . 10-4

## Slide 8
RD51 Technological achievements (III)
Sealed detectors (purity) for space and non-laboratory applications
Physics simulations and tools
  Software tools: Magboltz (transport equations), Degrad (cluster size), Garfield++
  (speeding up), optimization of charging up simulation
  Modeling of Physics processes: Penning in Ne mixtures, CO2 impact, GEM gas gain
  dependence on hole diameter, impact of mesh geometry to micromegas
Read-out electronics
  Scalable Readout System: Development of the readout system for MPGDs adaptable
  to various FE ASIC chips (APV25, VMM2, GEMRoc)
Development of generic electronic devices for MPGDs:

## Slide 9
Generic Detector R&D

## Slide 10
MPGD Technologies for Present and Future:
Hadron / Nuclear Physics Experiments-Heavy Ion Facilities
High Energy Physics
Hadron / Lepton Colliders
Photon / Neutron Detection
Neutrino Physics / Dark Matters Detection
X-Ray Detection and γ-Ray Polarimetry

## Slide 11
MPGD Technologies: LHC experiments Upgrades
Challenges: Ultra high rates, radiation harsh environment, longevity, large area detectors
Present:
TOTEM (GEM), LHCb (GEM)
Future:
ATLAS Muon System NSW (μΜ), Muon tagger μ-PIC, CMS Muon System (GEM), ALICE (GEM TPC), FCC Collider (GEM, THGEN, Micromegas, μ-PIC, InGrid)
ATLAS NSW (mm)
CMS (GEM)
ALICE (GEM)

## Slide 12
MPGD Technologies: Hadron and Nuclear and Heavy Ion Physics experiments
Challenges: Ultra High rates, IBF
Present:
COMPASS (GEM, μMegas, THGEM RICH), rates: 100kHz/mm2
First experiment to use MPGDs (GEM, Micromegas and recently THGEM)
KEDR (GEM), Rates: 1MHz/mm2
CLAS12: Cylindrical MM
Future: JLAB: SBS, pRad, SoLID (GEM, NP, tracking), JPARC: E42, E45 (Hadron Physics, ACTAR TPC
4He(12C,3)4He
(gas is used as a secondary target for nuclear reactions):
Goal: Nuclear structure with rare-isotope beams
12C breakup
J. Pancin
MM-based readout
Cylindrical GEM for BESIII Experiment @ e+e- collider Beijing
The ACTAR TPC Project

## Slide 13
MPGD Technologies: Photon detection
Challenges: IBF photocathode protection
Present:
COMPASS (THGEM RICH)
Future: JLAB: SBS, pRad, SoLID (GEM, NP, tracking), JPARC: E42, E45 (Hadron Physics, ACTAR TPC
After a long-term fight for increasing electrical stability at high rates: MWPC robust operation is not possible at
gain~105 because of photon feedback, space charge & sparks
PMTs not adequate  only small demagnification factor allowed; 5 m2 of PMTs not affordable.
F. Tessarotto
Staggered THGEMs
Hybrid: THGEM+ CsI and MM
MWPC’s + CsI
mass production ongoing

## Slide 14
MPGD Technologies: Neutron detectors (ITER spallation sources,
Macromolecular Crystallography
Beam diagnostics)
Challenges: Low mass detectors
Present:
nTOF
Future:
ESS (macromolecular crystallography, neutron scattering)
2D image of thermal neutron
2D image of fast neutron
Pixel detector
Installation on NTOF
4 pad detector
Megas detector:
2 D reconstructed image
M Neutron Monitor applied to fission reactor
F. Murtas
T. Papaevangelou
GEM detector
nTOF at CERN

## Slide 15
MPGD Technologies: Neutrino Physics
Challenges: Large area TPCs
Present:
T2K (Japan), first large scale neutrino experiment with MPGD (9 m2 TPC with micromegas)
Future:
LBNO-DEMO (LAr TPC THGEM), DUNE 720 m2 (LAr TPC THGEM), Ship (26 m2 micromegas, GEM, mRWELL)
T2K experiment
72 Micromegas,120k channels (since 2009)
Charge, momentum and dE/dx PID)
Spatial resolution : 0.6 mm
Momentum res.: 9% at 1 GeV
dE/dx: 7.8 % (distinguish /e, identify νe)

## Slide 16
MPGD Technologies: Dark Matter detection
Challenges: Ultra low background detectors < 10-7cnts/keV/cm2
Present:
CAST (Micromegasμbulk and Ingrid), NEWAGE (Kamioka, TPC GEM, μPIC)
Future:
PANDA-X(TPC μbulk micromegas, DARWIN (THGEM GMPT), IAXO (μbulk micromegas)
μbulk background
NEWAGE
µ-PIC based TPC with electronics Only DM experiment with 3-D tracks
GEM
-31×32 cm2
- 70μm/140m
LCP 100m
made by Scienergy, Japan
-PIC
- 31×31cm2
- made by DNP, Japan
NEWAGE-0.3b’
K. Miuchi, A. Ochi
IAXO: Axion searches

## Slide 17
MPGD Technologies: X and γ ray detection and polarimetry
Astrophysics and fusion plasma monitor
Challenges: Track photoelectrons and low energy e
Present:
KSTAR Korea (Plasma monitor), SMILE II (γ-ray imaging, GEM and μPIC) , ETCC camera (GEM and μPIC) environmental γray monitoring
Future:
PRAXyS (TPC GEM x-ray polarimetry), CALISTE (piggy back micromegas, X-ray polarimetry)
GEMPIX (GEM + Timepix) for fusion
KSTAR Tokamak
PRAXyS X-ray polarimetry
GEM + Readout
GEMs
Photoelectron
track
The first dedicated mission for X-ray polarimetry in astrophysics
US-Japan joint mission (NASA lead)
The space craft carries two identical
GEM-TPC
CALIST-MM:
X-ray polarimetry
Piggyback Micromegas
CALIST
10 x 10 x 20,7 mm3 (Compact)
16x16 pixels : 8 ASICs of 32 channels
Pixel Ø = 500 μm ; Pixel Pitch = 580 μm
Consumption = 850 μW/channel (218 mW in total)
Low Noise (ENC = 50 e- rms)

## Slide 18
Experiment / Timescale | Application Domain | MPGD Technology | Total detector size / Single module size | Operation Characteristics / Performance | Special Requirements/ Remarks
ILC Time Projection Chamber for ILD: Start: > 2030 | High Energy Physics (tracking) | Micromegas GEM (pads) InGrid (pixels) | Total area: ~ 20 m2 Single unit detect: ~ 400 cm2 (pads) ~ 130 cm² (pixels) | Max. rate: < 1 kHz Spatial res.: <150µm Time res.: ~ 15 ns dE/dx: 5 % (Fe55) Rad. Hard.: no | Si + TPC Momentum resolution : dp/p < 9*10-5 1/GeV Power-pulsing
ILC Hadronic (DHCAL) Calorimetry for ILD/SiD Start > 2030 | High Energy Physics (calorimetry) | GEM, THGEM RPWELL, Micromegas | Total area: ~ 4000 m2 Single unit detect: 0.5 - 1 m2 | Max.rate:1 kHz/cm2 Spatial res.: ~ 1cm Time res.: ~ 300 ns Rad. Hard.: no | Jet Energy resolution: 3-4 % Power-pulsing, self- triggering readout
Particle Flow Calorimetry (ILD/SiD):
ILD
Concept:
SiD Concept:

## Slide 19: MPGD Conferences since 2009: 1st MPGD2009, Crete, Greece 2nd MPGD2011, Kobe, Japan 3rd MPGD2013, Zaragoza, Spain 4th MPGD2015, Trieste, Italy NEXT: 5th MPGD2017, Temple University, USA May 22 – 26, 2017
4th MPGD2015, Trieste, Italy
140 participants, 120 abstracts
Special focus MPGD events. Most recent : - Academia-Industry Matching event:
Second special workshop on neutron detection with MPGDs, CERN, March 2015
Rd51 Academia-Industry Matching event:
Special workshop on photon detection with MPGDs, CERN, June 2015
Topical workshop on resistive electrodes, CERN, Dec. 2015
Topical workshop on discharges in MPGDs, CERN, March 2016
MPGD Applications Beyond Fundamental Science Workshop, Aveiro, Portugal, Sept. 2016
- Schools, visits, events
MPGD Conferences and Special focus events

## Slide 20
                CONCUSIONS
RD51 collaboration contribution:
MPGD technologies have received enormous boost over the last decade
MPGDs are used in many scientific domains
MPGDs are used in many applications beyond Particle Physics
Exciting field for creative new ideas, attractive for young scientists !