## Slide 1: Design of a Detector Optimized for DIS at eRHIC
Richard Petti
for the BNL EIC Science Task Force
SPIN2016
September 27, 2016

## Slide 2: Convert RHIC to eRHIC
Add an electron ring to the RHIC tunnel
Main features:
  Collides electrons with protons, light and heavy ions
  Polarized electron and proton/light ion beams
  High luminosity 1033-1034 cm-2s-1
  Wide range in collision energy
Main physics goals (non-exhaustive list)
  Proton spin
  Proton tomography
  Gluon saturation
arxiv:1212.1701

## Slide 3: Detector and IR requirements
Main detector coverage over -3.5 < η < 3.5
  Electron ID from -3.5 < η < 1; π suppression up to 1:104
  π/K/p separation with suppression factors ~100 required
  Spatial resolution of primary vertex ~10-20 microns
  Hcal at forward η for jet studies
Close-to-beam-line acceptance
  Recoil protons
  Neutrons in hadron going direction
  Low Q2 electrons
Luminosity and polarization measurement
  photons from Bethe-Heitler for lumi
  photons and/or electron from Compton scattering for e pol

## Slide 4: Reference detector layout: BeAST
hadronic calorimeters
RICH detectors
silicon trackers
GEM trackers
3T solenoid cryostat
magnet yoke
9.0m
Micromegas barrels
TPC
e/m calorimeters
hadrons
electrons
BeAST: Brookhaven eA Solenoidal Tracker
Hermetic coverage
Tracking and e/m calorimetry in the range |η| < 3.5
Active R&D for detector components
https://wiki.bnl.gov/conferences/index.php/EIC_R%25D

## Slide 5: Tracker details
3T solenoid cryostat
magnet yoke
9.0m
hadrons
electrons
hadronic calorimeters
RICH detectors
e/m calorimeters
~2.0m
~180 mm
GEM trackers
silicon trackers
TPC
Micromegas barrels
~360 mm
~75 cm
Real life module (Saclay)

## Slide 6: Tracker performance in simulation
High redundancy
Low material budget
High resolution up to (at least) |h|~3
Radiation length scan (inner tracking elements only)
Momentum resolution
p+
~2.0m

## Slide 7: Calorimeters
GEM trackers
3T solenoid cryostat
magnet yoke
9.0m
hadrons
electrons
hadronic calorimeters
RICH detectors
e/m calorimeters
silicon trackers
TPC
Micromegas barrels
Electromagnetic Calorimeter
Very backward pseudo-rapidities (h < -2):
PWO crystals with ~2%/√E (or better) energy resolution
Pseudo-rapidity range -2 < h < 3.5:
Tungsten powder scintillating fiber technology with ~7-10%/√E energy resolution
May’2016 test run in FNAL

## Slide 8: Calorimeters
GEM trackers
3T solenoid cryostat
magnet yoke
9.0m
hadrons
electrons
hadronic calorimeters
RICH detectors
e/m calorimeters
silicon trackers
TPC
Micromegas barrels
Hadronic Calorimeter Endcaps
Electron identification in electron-going direction; jet physics in hadron-going direction
Lead absorber scintillating plate sandwich technology
~50%/√E energy resolution looks fine
Monte-Carlo model exists in GEANT
MC: 12 GeV pions: Hcal vs EmCal

## Slide 9: “Purity” in (x,Q2) kinematic bins
Lepton tracking only
Double-angle method
Describes migration between kinematic bins
Important to keep it close to 1.0 for successful unfolding
“Straightforward” lepton tracking can hardly help at Y<0.1
Hadronic final state accounting allows to recover part of the high Q2 range
{PYTHIA 20x250 GeV} -> {GEANT} -> {Kalman filter track fit}
Bremsstrahlung turned on here (and it matters even for detector with ~5% X/X 0!)

## Slide 10: “Purity” in (x,Q2) kinematic bins, cont’d
Assume e/m calorimeter is used in addition to tracking
~2%/√E energy resolution for h < -2 (PWO crystals)
~7%/√E energy resolution for 1 < h < 2 (tungsten powder scint. fiber sampling towers)
Consider “bremsstrahlung off ” case here for simplicity
High-resolution e/m calorimeter allows to noticeably increase available Y range
Lepton tracking only
Lepton tracking + EmCal

## Slide 11: Auxiliary Detectors
In addition to the main detector, there are several auxiliary components being developed which are critical to the program
  Forward proton tagger (Roman Pots, small angle scattered protons)
  Low Q2-tagger (small angle scattered electrons)
  Luminosity monitor
  Electron beam polarimetry
p beam energy dependence from DVCS simulation
detector acceptance: h>4.5
(relative to electron going direction)
PYTHIA 20x250 GeV ep simulation Q2 < 0.01 GeV2
detector acceptance: h>4.5

## Slide 12: Auxiliary Detectors and the IR
0 m
18 m
-15 m
-35 m
-45 m
hadrons electrons
Ongoing R&D and optimization of the IR layout with the machine design group
Much attention given to allow acceptance of forward and backward going particles close to the beam
  Scattered protons and neutrons
  Scattered electrons
  Photons for luminosity measurement
Active R&D for machine induced backgrounds that may be present
  Synchrotron radiation from the electron beam
  Beam-gas interactions

## Slide 13: Auxiliary Detectors and the IR
0 m
18 m
-15 m
-35 m
-45 m
hadrons electrons
Roman Pots
Sensors integrated into the vacuum system
Retractable to move into the beam after stable
Allows to move sensors as close to beam as possible
  Typically around 10sigma beam width
  Defined by beam optics (beta function) at the location of the roman pot
  Want small beta function with large dispersion to pull scattered protons out of the beam
Ongoing R&D with machine developers to give access
MILOU 20x250 GeV DVCS sent into sim
One station at ~20 m
generated flat in space

## Slide 14: Auxiliary Detectors and the IR
0 m
18 m
-15 m
-35 m
-45 m
hadrons electrons
ZDC
Need acceptance for outgoing neutrons
  Centrality determination in e+Au collisions
  Tagging for diffractive events
Expected distributions from DPMJet simulation of neutron evaporation

## Slide 15: Auxiliary Detectors and the IR
0 m
18 m
-15 m
-35 m
-45 m
hadrons electrons
Low Q2-Tagger
  Acceptance for electrons from events with Q2<0.01 GeV2
  Sits close to the beam line
15
electron beam
pythia events
with electron reconstructed in the tagger

## Slide 16: Auxiliary Detectors and the IR
0 m
18 m
-15 m
-35 m
-45 m
hadrons electrons
Luminosity Monitor
  Measure via Bethe-Heitler
    e+p -> e+p+gamma
  Emission cone dominated by beam optics

## Slide 17: Auxiliary Detectors and the IR
Electron Polarimetry
  Measure via Compton Scattering
  Shine laser on electron beam, flip helicity state and measure asymmetry in cross section
  Focus here on measuring longitudinal component of spin, i.e. measure photon energy
  Working on extracting the full polarization vector angle and magnitude by a 2D fit in angle and energy of photon
0 m
18 m
-15 m
-35 m
-45 m
hadrons electrons
cartoon schematic
measure via single photons
measure via electrons

## Slide 18: Summary
Construction of an EIC is deemed a top priority in major facility construction in the US by the NSAC
Major detector R&D programs underway for detector technologies and the planning of the detector to meet the physics goals of the facility
A new detector is being developed to carry out the next generation DIS measurements (BeAST)
The design of detector components, configuration, and technologies guided by physics requirements
  Main DIS detector
  Auxiliary support through down stream close to beam line detectors, luminosity monitors and polarimeters

## Slide 19: Backups

## Slide 20: Physics with a low Q2-tagger
acceptance of electrons from events down to Q2 ~ 10-5 GeV2
allows for further study of photoproduction physics
  represents large portion of total cross section
  probing the quark structure of photons
    direct vs resolved photon
  look for change in event properties associated with transition of real to virtual photon
pythia events
with electron reconstructed in the tagger
Notes: ----- Meeting Notes (8/27/15 10:34) -----
mention that 2D plot is accepted electrons  done!, put Q2 scale as log scale  done!

## Slide 21: Auxiliary Detectors and the IR
0 m
18 m
-15 m
-35 m
-45 m
hadrons electrons

## Slide 22: Scattered Lepton Kinematics
Q2 > 1.0 GeV2: rapidity coverage -4 < h < 1 is sufficient
Q2 < 0.1 GeV2: a dedicated low-Q2 tagger is required anyway
Also notice: as lepton beam energy goes up scattered lepton is boosted to negative h
Cuts: Q2>1 GeV2, 0.01<y<0.95, z>0.1

## Slide 23: Silicon Vertex Tracker
2x2 barrel layers with high resolution MAPS
assume discrete 20x20 mm2 pixels and ~0.3% X0 per layer
The prototype (ALICE ITS TDR page)
Radiation length scan (single layer)
Two innermost layers
ALICE ITS design
~180 mm

## Slide 24: Forward & backward Silicon Trackers
2x7 disks with 30 .. 180 mm radius
for now assume the same building blocks (complete staves) as in the vertex tracker
Final configuration can be a combination of ALICE ITS and MFT upgrades
Design of this subsystem will likely become a topic for a separate R&D effort soon
~360 mm

## Slide 25: TPC
~2m long; gas volume radius [225..775] mm
1.2% X/X0 IFC, 4.0% X/X0 OFC; 15.0% X/X0 end-caps
assume 5 mm long GEM pads and ~250 mm single point {rf} resolution for the max. drift distance of ~1m
A gas mixture like T2K at ~250 V/cm (very small transverse dispersion in 3T field) will do the job
~2.0 m
~1.6 m
A medium size and medium resolution TPC, having in mind current status of the ILD R&D work
Ongoing EIC R&D project

## Slide 26: Micromegas barrel tracker
CLAS12 upgrade project
4 layers; technologically driven azimuthal and longitudinal segmentation
2D readout; assume ~100 mm spatial resolution
Real life module (Saclay)
Internal structure modeled according to the real-life prototypes
~0.5% X/X0 per layer
~2.0 m

## Slide 27: GEM endcap trackers
3 disks behind the TPC end-caps; SBS internal design for now
assume 50 mm {rf} spatial resolution can be achieved
Ongoing EIC R&D project
~75 cm
Well advanced R&D program
A couple of groups have their own large area GEM designs

## Slide 28: Superconducting solenoid
Implement in the same compact design:
homogeneous ~3T field in the TPC
hadron-track-aligned field in the RICH
Keep it simple (no dual solenoid configuration; no reversed current coils; no flux return through HCal; no warm coils between RICH and EmCal)
Central field | 3T
Current density | 23 A/mm2
Full current | 4.6 kA
Main coil radius | 1500 mm
Coil pack length | 3520 mm
Cryostat inner radius | 1350 mm
+/- 4% or so
h = 1.0
h = 1.5
RICH
location
Goal:
Field variation in TPC volume
TPC volume
h = 3.5

## Slide 29: Electromagnetic calorimeters
Ongoing EIC R&D projects
Present status (May’2016 test run)
Very backward pseudo-rapidities (h < -2):
PWO crystals with ~2%/√E (or better) energy resolution
Pseudo-rapidity range -2 < h < 3.5:
Tungsten powder scintillating fiber technology with ~7-10%/√E energy resolution
e- and g energy measurement;
e/p electron ID
H1 : (7..12)%/√E+1%
ZEUS : 18%/√E+1%
Several configurations tested since 2012
Reach energy resolution level of ~{7%/√E + 1%} with the PMTs
See clear path towards getting similar level of performance with a compact readout
May’2016 test run in FNAL

## Slide 30: Hadronic calorimeter(s) in the end-cap(s)
MC: 12 GeV pions: Hcal vs EmCal
Slope ~1.20 perfectly
matches measured data
Lead absorber scintillating plate sandwich technology
~50%/√E energy resolution looks fine
Adequate Monte-Carlo model exists in GEANT
Cost optimization and further R&D may be required (use steel plates instead of lead?)
Electron identification in electron-going direction;
jet physics in hadron-going direction
EIC R&D project

## Slide 31: SIDIS: kinematic coverage for pions (and kaons, protons)
except for the highest h values (1.5 < h < 3.5 range)
p/K/p separation below ~5 GeV/c or so is sufficient
Increasing lepton beam energy boosts hadrons
more to negative rapidity
Increasing hadron beam energy influences max. hadron energy at fixed h

## Slide 32: SIDIS: kinematic coverage for pions (and kaons, protons)
Cuts: Q2>1 GeV2, 0.01<y<0.95, p>1GeV
-3.5 < h < 3.5 covers entire kinematic region in pt & z important for physics
(no difference between p±, K±, p±)

## Slide 33: DVCS photon kinematics
EmCal pseudo-rapidity coverage -4 < h < 1 is sufficient
Cuts: Q2>1 GeV, 0.01<y<0.85
Also notice: increasing hadron beam energy influences max. photon energy at fixed h – photons are boosted to negative rapidities (lepton direction)

## Slide 34: Interaction rate & absolute yields
PYTHIA 20x250 GeV configuration; absolute particle yields for L=1033 cm-2 s-1
Not even close to LHC-HL upgrade (to say the least)
Interaction rate ~50kHz (so 1:200 at ~10MHz bunch crossing frequency)
At most few particles per unit of h per event
Correspondingly low particle fluxes per unit of time
Per unit of {h,f}
Per unit of {q,f}

## Slide 35: Electron ID
15x250 GeV configuration; particle yields versus momentum in the -4 < h < 4 range:
g suppression:
the same h coverage for
tracking & Ecal
h- suppression through E/p
-3.5<h<-1: 10:1 to 103:1
-1<h <1: 104:1
Pseudo-rapidity range [-1.0 .. -3.5] is also covered by the hadronic calorimeter

## Slide 36: Relative pion/kaon/proton yields
20x250 GeV configuration; yields versus momentum in the 4 < h < 4 range:
p/K/p distributions at the same h look similar
p/K ratio is about 3:1 -> depending on the desired efficiency and contamination this defines the required suppression factors

## Slide 37: Jets at mid-rapidities
20x250 GeV; Q2 [10 .. 100] GeV2 ; -1 < h < 1
Absolute number of particles in each class
Fractional number of particles in each class
Fraction of jet Pt carried by different particles classes
EIC jets at |h|<1 are “jetlets”
Fraction of Pt carried by neutral hadrons is small
No way ~50%/√E hadronic calorimeter energy resolution at <40 GeV/c can beat tracker momentum resolution

## Slide 38: Kinematic variable definitions: reminder
Kinematic variables:
  k, k’ are the four-momenta of the incoming and outgoing lepton
  p is the four-momentum of the nucleon
Lorentz invariants (related by ):
  , squared collision energy
  , squared momentum transfer to the lepton (equal to the virtuality of the exchanged photon)
  , determines the momentum fraction of the parton on which the photon scatters
  , the inelasticity which determines the polarization of the virtual photon, fractional energy transfer
Other variables:
  , squared invariant mass of the produced hadronic state
  , the energy lost by the lepton (i.e. energy carried away by the virtual photon) in the proton rest frame

## Slide 39: Kinematic Variable Reconstruction
Lepton method
  Use only the scattered lepton to determine event kinematics
  Resolution goes as:
Double angle method
  Use a combination of information from the scattered lepton and hadronic state