## Slide 1: GeantV – Structure and interfaces
Andrei Gheata and Alberto Ribon (CERN) for the GeantV development team

## Slide 2: Overview
CORE
GEOMETRY NAVIGATION
PHYSICS
USER APPLICATION
EVENT GENERATOR
EVENT SERVER
BASKETIZER
SCHEDULER
CONCURRENCY SERVICES
RUN MANAGER
CONFIGURATION
VecCore
BACKENDS
CONCURRENT I/O
PROPAGATOR
Notes: Main components of the system in the form of an overview. Several bits and pieces of the initial prototype that grew-up in different phases of the project and now are making up a more coherent framework.

## Slide 3: Starting a GeantV application
Create a configuration object
  Configure GeantV: #events, event buffer size, vector size, geometry, physics, ...
  Configure concurrency: max. threads, #propagators, use threads/tasks
Create the user application and primary generator
  Derived from base classes having curently a minimal interface
Create a run manager and initiate event loop
  After connecting configuration, user application and generator
Examples provided as executables or root macros
Notes: We have mainly focused in the R&D phase on demonstrating performance, so the interfaces in GeantV are in the “infancy” stage, providing only the minimum required by the prototype.

## Slide 4: Main concept
Increase the instruction/data locality by “holding” more tracks to be processed by the same instruction sequence
  E.g. particles in the same geometry volume will use the same geometry algorithm for exiting, electrons will undertake the same physics processes
  Will profit cache coherence and vectorization
Increasing the effectiveness of gathering large “baskets” of similar tracks can be done at the expense of keeping many tracks in flight
  Mix tracks from different events
  Do the basketizing concurrently, otherwise we would need <ncores> more events in memory to achieve the same efficiency per thread AND using all resources
  Dealing with more tracks require memory management mechanisms
    Explained in detail in the “Parallelism, transport structure and overall performance” talk

## Slide 5: Workflow
Basketizer
Flow
Controller
Geometry
Interfaces
Physics
(propose step)
Transport
manager
Field
Propagator
Filters
Geom
(Fast)
Phys
Physics actions
(along step, post step, at rest)
Scheduler
Workload manager
User application
User
actions
concurrent
queues
Concurrent
I/O
Hits
MC truth
Event
Server
Physics SOA
Geometry SOA
geometry baskets
physics baskets
in development
Primary generator
Notes: The core of GeantV is the track propagator. This is composed by a workload manager, taking as input a basket of tracks in the same logical volume and calling the geometry and physics methods required to perform a “multi-particle” step, plus a scheduler, doing the filtering and basketizing of tracks coming from transport into vectors of tracks grouped by geometry or physics locality criteria. The work is balanced by a concurrent queue shared by many workers.

## Slide 6: Fast simulation hooks & flow
Fast simulation filters foreseen in the track data stream
  Generating shortcuts exiting to other streams
R&D
fast sim shortcuts
Data stream<Track>
SimulationFilters
<Track>
FastSim filters
<Track>
GeantV scheduler
particle, region, energy, …
Full simulation
FastGeom filters
<Track>
Geometry/mat. parameterizations
Frozen showers/ fast tracking
Hits
Parameterized
det. response
Tracks exiting tracker
Data stream<hits>
Digitizers
<hits>
Digits
Data stream<digits>
Trackers
<reco_event>
The framework may construct the parameter database learning from full sim + response from user module
Reco tracks
User application
Notes: GeantV fast sim approach can be looked as specialized filters inserted in the MCtruth tracks data stream, using parameterized geometry and/or tracking and/or detector response to generate shortcuts to other data streams (e.g. reconstruction). Having access to both MCtruth and response functions from the user application (reco/analysis) the framework may also be used to construct parameterizations for some common use cases.

## Slide 7: CORE

## Slide 8: Core functionality
Provide data structures and concurrent services
  Track AOS/SOA, data factories, pools, queues, basketizers
Dispatch and control the concurrent workflow
  Specialized concurrency services minimizing contention
  Monitor workflow and take actions according the conditions
    Work balancing, flushing pending baskets, switch between vector/scalar modes, prioritizing transport of certain events, …
Enforce work coherence by packing particles in vectors
  Grouped by criteria maximizing code locality (geometry, physics)
Provide vectorization tools for geometry and physics algorithms
  Including back-ends adapted to the machine architecture

## Slide 9: The run manager
Entry point for steering the GeantV run
  The run configuration, event server, physics and I/O (MC truth) managers are connected to it
No static access, the run manager is percolated in GeantV and user code via interfaces
  Member of GeantTaskData, holding GeantV state information
Coordinates:
  initialization (geometry, physics)
  event loop control (internal or external)
  list of propagators (see next)
  work stealing control
  run termination

## Slide 10: Propagators
GeantPropagator – class controlling the GeantV transport core
  Work queue + WorkloadManager + Scheduler
  Steering a fixed number of co-operating working threads
  Re-designed to handle a part of the machine’s hardware
    A cluster of threads on the same processor
    NUMA-aware, using knowledge of the HW threads pinning/ memory partitioning – under development
GeantV can fill a machine with one or more propagators
  The objective is to increase data/processing locality and cut down contention
Propagators handle their own basket queues and generally work standalone
  When propagators are detected to become idle, their work queue is fed by the run manager from the “wealthy” ones

## Slide 11: Data structures: AOS versus SOA
fEvent
fNode
fParticle
fPDG
…
fXpos
fYpos
fZpos
fXdir
fYdir
fZdir
…
Edep
Pstep
Snext
Safety
*fPath
*fNextpath
*fEventV
*fNodeV
*fParticleV
*fPDGV
…
*fXposV
*fYposV
*fZposV
*fXdirV
*fYdirV
*fZdirV
…
*fEdepV
*fPstepV
*fSnextV
*fSafetyV
**fPathV
**fNextpath
00
40
80
C0
00
fEventV
fNodeV
fParticleV
…
fXPosV
fYPosV
fZPosV
fSnextV
fSafetyV
…
fPathV
fNextpathV
vector 1
vector 2
GeantTrack
GeantTrack_v
SOA of fNtracks
Contiguous, aligned buffer
192 bytes + 2*sizeof(VolumePath_t)
32 tracks ~ 7kBytes
Ready to use, SIMD-ized, serializable
Overheads for basketizing, data copy, reshuffle operations, larger memory footprint
  Morphing AOS->SOA needed during transport
AOS
(xyz)(xyz)(xyz)(xyz)…
SOA (needed for vectorization)
(xxx…)(yyy…)(zzz…)
fEventV
fNodeV
AOSOA considered also (more cache friendly):
{(xxxx)(yyyy)(zzzz)},
{(xxxx)(yyyy)(zzzz)},
…

## Slide 12: Synchronization objects
Used in GeantV for concurrent services: data gather/scatter, workload balancing, I/O, data services
  Generally lock-free, minimizing ‘Amdahl’ in low contention regime
Concurrent queues
  Multi-producer/multi-consumer (MPMC) – basket distribution to workers
  Multi-producer/single consumer (MPSC) – concurrent I/O
Basketizers
  Chopping data coming from multiple producers into groups
Data factories – pre-allocated, reusable
  Templated on user data (factories) or specialized pools (e.g. tracks)
  Allocating blocks of multiple objects with lock-free “Get/ReleaseObject”-like interface
Notes: For the primitives implementation, we have tried using existing libraries such as Boost and TBB. Chosen own implementation for most structure, due to their specialization (hard to find an efficient concurrent ‘basketizer’ around). We used C++11 features for dealing with lock-free progrmming, rather than existing libraries.

## Slide 13: Example: Basketizers
Assembling concurrently groups of tracks
  AddTrack() interface
  Filling in lock-free manner a GeantTrack_v container up to a threshold
  Deploying the container in the client propagator work queue
Current scheme using GeantTrack_v SOA to rebasketize
  Highly optimized, lock-free
  Involves important data copying, reducing the basketizing effective throughput
    Generates sizeable Amdahl for high basketizing rates
AddTrack
Basketizer
Recycle

## Slide 14: New: AOS basketizer
Idea: Work with AOS for basketizing, copy to SOA only when deploying to geometry/physics
  Lightweight basketizing: regrouping pointers rather than complete tracks
Now integrated in GeantV
  Circular buffer, fixed size baskets
  No memory barriers
  Better scalability
Push & extract in the same method
  Fills std::vector<Track*>
Ncopy=7
Ncopy=3
ibuf = icrt & buffer_mask
ibasket = ibuf & basket_mask
AddTrack(Track *tr, std::vector<Track*> &extract)
phys. cores
Chart: AOS basketizer, data chopping workload load=35 x time per track
| 1.0 | 2.0 | 4.0 | 8.0 | 16.0 | 32.0 | 64.0 | 128.0 | 256.0
load=35 | 1 | 1.9999 | 3.9944 | 7.9218 | 15.6629 | 30.198 | 48.8641 | 71.2217 | 90.9578
max speed-up SOA basketizer
Notes: The SOA basketizer getting a max speed-up of ~20. AOS->SOA coversion done only when needing to dispatch data to geometry/physics, and ONLY for the required fields. We consider using HW to help this operation in future.

## Slide 15: Concurrent I/O
Not re-inventing the wheel: using ROOT as I/O technology
  Writing standard root tree for hits/MC truth kinematics
2 models tested:
  Many producers of data, one thread responsible for writing to file
    Amdahl problems since writing includes serializing/zipping
  Many producer of memory resident files, one thread responsible of merging them + writing the output
    Much higher throughput achieved since serialization/zipping done per worker
See talk on “Output and utilities for details

## Slide 16: GeantV MC truth
Handling of particle history is problematic per se and multithreading adds complexity
  tracking of daughter particles can completed before mother particle ‘end of life’
GeantV focuses on providing light and flexible interface to particle history
  Framework provides the ‘handles’ to store concurrently event trees
  User has to implement implements his concrete MC ‘selection algorithm’ and conversion to his event record
Concrete example provided, see talk on “Output & utilities”

## Slide 17: USER APPLICATION

## Slide 18: User application
Mandatory user class connected to the run manager
  Used to notify the user code about run/event/stepping actions
Interface define by base class GeantVapplication
  Currently minimal functionality
    Initialize(), StepManager(), FinishRun() – sufficient for performing benchmarks
  To be extended to provide a full suite of user actions similar to G4 one
Interface extended to interact with task-based user framework
  Steering event loop from user application
  Optionally controlled via TBB tasks:
    SpawnEventLoopTask(), SpawnUserEndRunTask()
Notes: As mentioned, the current version of interfaces is in embryonic form, to be extended. StepManager() is equivalent to SteppingAction() in Geant4 language. TBB task mode interacting with user application was recently introduced, will be presented in detail in the concurrency presentation.

## Slide 19: Current implementation
GeantVApplication
Init() = 0
StepManager() = 0
FinishRun() = 0
TBBApplication
SpawnProcessEventsTask() provided
SpawnUserEndEventTask() = 0
SpawnUserEndRunTask() = 0
UserApplication
GeantRunManager
UserPrimaryGenerator
PrimaryGenerator
fApplication
fPrimaryGenerator
optional

## Slide 20: User application: interfaces
GeantV stepping propagates a basket of tracks
  To their individual geometry/physics limited steps
The user application interfaces using vectors rather than scalar objects for the stepping action:
    StepManager(std::vector<GeantTrack*> tracks, GeantTaskData *td)
A task data object is percolated into user code
  Containing GeantV state interesting for the user (e.g. unique task id)
  “Whiteboard” allowing the user code to post state data, managed by GeantV in a single thread access mode
    no need to manage thread safety for user task data
    user code MUST be thread safe and re-entrant
Notes: TaskData is a fundamental concurrency concept minimizing the state to be handled concurrently, by just percolating it via interfaces. Task data is unique per thread in the static thread approach of GeantV, or percolated hierarchically in its task-based approach

## Slide 21: (User) Data factories
User code needs to allocate/use data objects during simulation
  Issues: thread safety, re-usability, efficiency
  Hits, “summable” digits, tracks
GeantV provides a mechanism to allocate large blocks of user data (per event) using templated factories
  GeantFactory<MyData> *MyDataFactory = GeantFactoryStore::Instance()
  ->GetFactory<MyData>(nevt, nwrk)
  MyData *obj = MyDataFactory->NextFree(ievent, taskId)

## Slide 22: Event generators and event server
Events can be injected in GeantV using the PrimaryGenerator interface
  userGenerator->InitPrimaryGenerator();
  GeantEventInfo &info = userGenerator->NextEvent();
  for (int itr=0; itr<info.ntracks; ++itr) {
  GeantTrack &track = trk_mgr.GetTrack();
  userGenerator->GetTrack(itr, track);
  }
Simple functionality available for now:
  Eta, phi, momentum cuts
  Vertex per event
Primary events injected into concurrent GeantV event server at beginning of run
  Or at the beginning of each event loop if steered by user code
UserPrimaryGenerator
GeantEventServer
AddEvent()
track buffer
concurrent clients

## Slide 23: User application: TBB interface
New TBB approach recently developed
  Working on interaction with user task-based framework
  Presented in detail in the parallelism talk

## Slide 24: GEOMETRY

## Slide 25: VecGeom – GeantV geometry package
Geometry algorithms are expensive in the simulation budget
  Optimizing them for the GeantV vector use case was required
Get maximum profit from “multi-particle” requests
Not just another geometry package
  VecGeom emerged from an existing Geant4 + ROOT geometry unification effort, taking it to the next level
  Final goal is to integrate VecGeom with Geant4 and ROOT
See geometry presentations
DistanceToIn
DistanceToOut
Safety
Normal

## Slide 26: Geometry interfaces
GeantV maintains a generic interface to geometry
  Supporting multi-particle interfaces, having both vector and scalar (loop based) implementations
Possible to run GeantV with VecGeom, but also with any other geometry modeller
  TGeo interface supported, mainly to have a stable reference

## Slide 27: PHYSICS

## Slide 28: Tabulated physics
First, very rough “physics” developed for GeantV
  In order to have (in a short time, with a crude interface) something “reasonable” to play with
    for scheduling, basketizing, vectorizing, etc.
  Tabulated cross sections and final states, as extracted from Geant4
    for fixed (energy) production cuts and no multiple scattering
    for all particles and elements, for a grid of energies
  Several, obvious limitations on the physics
    limited final-state possibilities
    energy-momentum conservation only statistically
  Only a temporary solution for developers, until the real physics simulation is implemented

## Slide 29: GeantV Plan for Physics Development
Design of the Physics Interface
Review of the main electromagnetic physics processes
  ionization, bremsstrahlung, multiple scattering
  photoelectric, Compton, pair production
=> needed for simulating electromagnetic showers
Review of the main hadronic physics models
  String model (QGS), intranuclear cascade model (BERT-like), precompound/de-excitation
=> needed for simulating hadronic showers
Start with high-energy applications, but with low-energy extensions in mind
  e.g. low-energy neutrons already considered...

## Slide 30: Goals of the Physics Interface
Create the basic infrastructure to fit the whole physics of GeantV
Decay
Electromagnetic physics
Hadronic physics
Fast simulation
Biasing
etc.

## Slide 31: Strategy
Keep a small coupling between kernel and physics
  Keep transportation in the kernel, outside physics
Leverage as much as possible on the experience in design and development of Geant4 physics
  Trying to streamlining it, e.g. reducing the inheritance depth and the number of classes
  Boosting its CPU performance by replacing, whenever possible, e.g. virtual function polymorphism with static template polymorphism
  Offering thin interfaces for direct calls to cross sections and final-state models
  Two complementary strategies: 1. Reviewing the physics and writing code from scratch 2. Exporting code from Geant4 and adapting it into GeantV, to quickly investigate track vectorization opportunities

## Slide 32: Main ideas
As in G4, any physics process can have 3 “components”:
  Along-step, i.e. continuous part of the in-flight process
  Post-step, i.e. discrete part of the in-flight process
  At-rest, i.e. interaction when the particle stops
Discrete and at-rest processes compete, whereas continuous processes collaborate
As in G4, each continuous process can propose a step limitation; but for discrete processes, the proposed step length takes into account the cross sections of all discrete processes of the particle
  Equivalent to G4, and with the same number of random calls
  More adapted for simplicity, locality and track vectorization
  Individual cross sections of the discrete processes are then used to sample the process
  Similar approach also for the lifetime of at-rest processes

## Slide 33
Outline
KERNEL
PhysicsInterface
PhysicsProcessHandler
Inherits
Calls at initialization
PhysicsManagerPerParticle
ProcessA
ProcessK
PhysicsList
PhysicsProcess
PhysicsListA
PhysicsListN
Inherits
Inherits
PhysicsListManager
Contains a list of physics lists
Contains the list of physics processes of one particle
Uses
Creates objects at initialization
Creates objects at initialization

## Slide 34: PhysicsProcessHandler
Similar to the Geant4 G4SteppingManager concept, this class handles the physics simulation in one step
  It exists only one instance (object) of this class
At initialization, it creates all the physics related objects (managers, handlers, physics tables)
At run time, it decides and calls the appropriate methods to simulate the physics of any given particle happening in one step

## Slide 35: PhysicsListManager
Singleton class that handles the physics-list (per region)
  In nearly all practical cases, only one physics list exists for all regions
  But in special cases, a more sophisticated EM model is needed in one region, e.g. in Geant4:
    Use PAI in ALICE TRD
    Use EM Opt1 (_EMV) everywhere, except in the sampling calorimeter where standard EM Opt0 is used (e.g. ALICE ECAL, CMS HCAL)
Its main work is at initialization
  Creates all the particles and the PhysicsManagerPerParticle objects and all the rest

## Slide 36: Physics list
Abstract base class from which any physics list derives from
Its main work is at initialization
  Creates all the physics processes for all particles and assigns to them
Note:
  we assume that all the GeantV particles are always present in any simulation, but by default they have no physics processes associated to them (i.e. they will be transported without interactions, like “geantinos”)

## Slide 37: PhysicsManagerPerParticle
Similarly to the Geant4 G4ProcessManager concept, this class keeps the list of physics processes associated to one type of particle
For each physics list, there is one object of this class per particle type (e⁻,e⁺, γ, π⁻, π⁺, p, n, etc.)
Keeps the (total and per-process) lambda tables
  Macroscopic cross sections per material or material-cut
  Built at initialization
  Used at run-time to sample the physics step length and the discrete process

## Slide 38: PhysicsProcess
Similarly to the Geant4 G4VProcess concept, this is the (abstract) base class for any physics process associated to one particle type
Main methods
  ComputeMacroscopicXSection
  AlongStepLimitationLength
  AlongStepDoIt
  PostStepDoIt
  AtRestDoIt

## Slide 39: First Physics Result with the New Physics Framework
See dedicated presentation “New electron physics modelling”
M. Novak

## Slide 40: Vector Physics
In parallel to the review and development from scratch of electromagnetic physics processes, on-going work on how to vectorize final-state physics models and evaluating how much we can gain from it
Considered some electromagnetic models (e.g. Compton, photoelectric, etc.), taken from Geant4 and adapted to GeantV, and investigated the replacement of the rejection sampling with alternative sampling techniques
See dedicated presentation “Vectorization of existing physics models”

## Slide 41: Conclusions
GeantV started as a prototype focusing on the proof of principle
  Developing bits and pieces needed by concurrency, vectorization of geometry/physics, data structure and management, new model development
    To demonstrate modelling, algorithmic and HPC improvements
  In most cases functionality not available in other libraries/frameworks, or needing adaptations
Current state: consolidation of the core framework/services and interfaces
  New physics interface ready and successfully used for producing the first electromagnetic physics results.
  High performance vector-aware geometry package interfaced in multi-particle mode with GeantV
  Many products/services developed in this phase could be re-stated as community effort
    Integrated in existing frameworks (e.g. ROOT) or becoming stand-alone products
  The acquired knowledge can be useful to many HEP areas
    Concurrency, data management, vectorization, …
Bottom-up and top-down approaches converging to a coherent framework