## Slide 1
The Physics of Particle Detectors / Future Trends
Lecture I – Tracking Detectors (History, Gas/Si- Detectors)
Artist's View
of a Bubble
chamber by
a CERN
physicist
Ukrainian Teacher Programme,
CERN, April 8-12, 2019
Maxim Titov, CEA Saclay, France

## Slide 2
“This does not necessarily mean
that this is the Higgs mass”
“We have decided now to identify
the particle species by a bar code!”
no comment
“Did you see it?”
”No nothing.”
“Then it was a
neutrino!”
Cartoons by Claus Grupen
Experimental physicist
(analysis
oriented)
Theoretical
physicist
Experimental physicist
(detector oriented)
Accelerator
physicist
How (different) Physicists See the World ?

## Slide 3
Murray Gell-Mann
Mary Gaillard
To do a HEP experiment, one needs:
A theory:
Clear and easy understandable drawings
and a cafeteria
and a tunnel for the accelerator and magnets and stuff

## Slide 4
We will just concentrate on
detectors
and a
Nobel prize
Physicists to operate detector/analyze data
Easy access to the experiment

## Slide 5
The History of Instrumentation is VERY Entertaining
A look at the history of instrumentation in particle physics
 complementary view on the history of particle physics, which is
traditionally told from a theoretical point of view
The importance and recognition of inventions in the field of instrumentation is proven by the fact that
 several Nobel Prices in physics were awarded mainly or exclusively
for the development of detection technologies
Nobel Prizes in instrumentation (“tracking concepts”):
1927: C.T.R. Wilson, Cloud Chamber
1960: Donald Glaser, Bubble Chamber
1992: Georges Charpak, Multi-Wire Proportional Chamber

## Slide 6
Timeline of Particle Physics and Instrumentation
< 1950s: Cloud Chambers,
Nuclear Emulsions + Geiger-
Muller tubes dominated
1960-1985:
peak time for
Bubble Chambers
>1970: Wire Chambers (MWPCs and drift chambers) started to dominate
>1980: solid state detectors
in common use

## Slide 7
Flux of particles
Cloud Chamber
+ Magnet
Observer
Passage of charge particle
would condense the vapor
into tiny droplets,
marking the particle’s path
 their number being
proportional to dE/dx
Classic Particle Tracking Detector: Cloud Chamber
Cloud chamber (1911 by Charles T. R. Wilson, Noble Prize 1927)
  chamber with over-saturated water vapour
    originally developed to study formation of rain clouds
  charged particles leave trails of ions
    water is condensing aound ions
  visible track as line of small water droplets

## Slide 8
1932 C.D. Anderson :
Particle with positive curvature and minimum ionisation (droplets size)
Track length is at least 10 times greater than the possible length of a proton path of this curvature
Energy loss in a 6 mm of Pb:
compatible with that of electron
Hypothesis (discovery !) :
particle with mass ~me
and charge +1, the positron
First anti-particle
Cloud chamber
+ magnetic field
B
Discovery of a Positron e+ from Cosmic Rays
Discovery of the positron by Cloud Chamber
(1932 by Carl Anderson, Noble Prize 1936)
Positron loses
energy in lead:
narrower curvature
23 MeV at exit
lead plate
upward going
positron of 63 MeV

## Slide 9
Nuclear Emulsion (I)

## Slide 10
Nuclear Emulsion (II)

## Slide 11
Nuclear Emulsion (III)

## Slide 12
1952 by Donald Glaser, Noble Prize 1960
(4.8 x 1.85 m2) chamber with liquid (H2) at boiling point (“superheated”)
CERN
Gargamelle bubble chamber
e-
e-
Z0


Bubble Chamber (I)
LBNL Image Library
Similar principle as cloud chamber:
Instead of supersaturating a gas with a vapor
one would superheat the liquid.
A particle leave a trail of ions along its path  make a
liquid boil, and form gas bubbles around ions
was used for discovery of the “neutral current”
(1973 by Gargamelle Collaboration, no Noble Prize)

## Slide 13
Bubble Chamber (II)

## Slide 14
Bubble Chamber
Liquid hydrogen “bubble chamber”
The hydrogen acts as a target (for incoming particles) and a detection medium
Advantages:
liquid (hydrogen) is
BOTH detector medium AND target high precision
(~ 5 mm)
Disadvantages:
- NO TRIGGER ->
has to be in superheated
state when particle is
entering
LOW RATE CAPABILITY
Need FASTER
detector (electronics !)

## Slide 15
1908: FIRST WIRE COUNTER USED BY RUTHERFORD
IN THE STUDY OF NATURAL RADIOACTIVITY
E. Rutherford and H. Geiger , Proc. Royal Soc. A81 (1908) 141
1928: GEIGER COUNTER
SINGLE ELECTRON SENSITIVITY
H. Geiger and W. Müller, Phys. Zeits. 29 (1928) 839
1968: MULTIWIRE PROPORTIONAL CHAMBER
G. Charpak, Proc. Int. Symp. Nuclear Electronics (Versailles 10-13 Sept 1968)
Nobel Prize in Chemistry in 1908
Walther Bothe
Nobel Prize in 1954 for the “coincidence method”
Hans Geiger
Ernst Rutherford
Nobel Prize in 1992
George Charpak
Fabio Sauli
Jean-Calude Santiard
In the Family of Gaseous Detectors with a glorious tradition
1st Revolution: The invention of the MWPC revolutionized particle detection and HEP, which passed from the manual (optical) to the electronic era.
1st revolution:
MWPC

## Slide 16
M. Hoch, 2004 Wire Chamber Conference

## Slide 17
Multi-Wire Proportional Chamber (MWPC)
High-rate MWPC with digital readout:
Spatial resolution is limited to sx ~ s/sqrt(12) ~ 300 mm
S ~ 1 mm
TWO-DIMENSIONAL MWPC READOUT CATHODE
INDUCED CHARGE (Charpak and Sauli, 1973)
Spatial resolution determined by: Signal / Noise Ratio
Typical (i.e. ‘very good’) values: S ~ 20000 e: noise ~ 1000e
Space resolution < 100 mm
Resolution of MWPCs limited by wire spacing
better resolution  shorter wire spacing  more (and more) wires...

## Slide 18
1968: MWPC – revolutionising the way particle physics is done
Detecting particles was a
mainly a manual, tedious and
labour intensive job – unsuited
for rare particle decays
George Charpak developed
the MultiWire Proportional
Chamber, which revolutionized
particle detection and
High Energy Physics - which passed from the manual
to the electronic era.
Electronic particle track detection is now standard in all particle detectors
1992:

## Slide 19
First Large Experiment with MWPCs

## Slide 20
Nobel Prize: W, Z - Discovery at UA1/UA2 (1983)
UA1 used the largest imaging drift chamber of its day (5.8 m long, 2.3 m in diameter)
It can now be seen in the CERN Microcosm Exhibition
Z  ee (white tracks)
Particle trajectories in the CERN-UA1
3D Wire Chamber
Discovery of W and Z bosons
C. Rubbia & S. Van der Meer Nobel 1984

## Slide 21
The 1970’s Dream: Digital radiography with MWPC
1992:
Biospace: Company Founded
In 1989 by Georges Charpak
~ 2000: LOW-DOSE 3D IMAGING
(&à times less)
COMMERCIAL AUTORADIOGRAPHY SYSTEMS WITH GASEOUS DETECTORS
http://www.biospacelab.com

## Slide 22
Cloud Chambers, Nuclear Emulsions + Geiger-Müller tubes  dominated until the early 1950s: Cloud Chambers now very popular in public exhibitions related to particle physics
Bubble Chambers had their peak time between 1960 and 1985
   last big bubble chamber was BEBC at CERN
Since 1970s: Wire Chambers (MWPCs and drift chambers) started to dominate
Since late 1980s: Solid state detectors are in common use
 started as small sized vertex detectors (at LEP and SLC)  now ~200 m2 Si-surface in CMS tracker
Most recent trend: hybrid detectors
  combining both gaseous and solid state technologies
Tracking Detectors: History and Trends

## Slide 23
energy measurement
by creation and total
absorption of showers
muon detection with
improved momentum
measurement (long
lever arm)
electromagnetic hadronic
shower
undetected
neutrinos...
momentum measurement
by curvature in magnetic field
There is not one type of detector which provides all measurements we need -> “Onion” concept -> different systems taking care of certain measurement
Detection of collision production within the detector volume
   resulting in signals due to electro-magnetic interaction
   exceptions: strong interactions in hadronic showers (hadron calorimeters)
   weak interactions at neutrino detection (not discussed here)
Schematical View of a HEP Detector

## Slide 24
Tracking Detector (or Tracker) = momentum measurement
  closest to interaction point: vertex detector (often silicon pixels)
    measures primary interaction vertex and secondary vertices from decay particles
  main or central tracking detector
    measures momentum by curvature in magnetic field
    two technologies: solid state detectors, Si strips or gaseous detectors
Calorimeters = energy measurement
  electro-magnetic calorimeters
    measures energy of light EM particles (electrons, positrons, photons) based on electro-magnetic showers by bremsstrahlung and pair production
    two concepts: homogeneous (CMS) or sampling (ATLAS)
  hadron calorimeters
    measures energy of heavy (hadronic) particles (pions, kaons, protons, neutrons) based on nuclear showers created by nuclear interactions
Muon Detectors = momentum measurement for muons (more precise)
  outermost detector layer, basically a tracking detector
Particle Detectors: Physics Principles

## Slide 25
Particle Physics: Modern Detector Technologies

## Slide 26
3000 scientists from 40 countries
CMS Letter of Intent (Oct. 1992)
Silicon Tracker
Scintillating Crystals
Brass plastic scintillator
Gaseous detectors
CMS Detector: Concept to Data Taking in 18 Years

## Slide 27
The Largest and Most Complex Microscopes we’ve ever built
The “Gothic Cathedrals”
of the 21st Century

## Slide 28
In practice we detect only:
Computer Simulated Event in ALICE

## Slide 29
*real LHC pp event (~50 Vertices, 14 Jets, 2 TeV)
It is very important to determine with precision the
particle trajectories to know their properties (momentum,
position, direction etc) and to reconstruct the event
5 cm
What do We See in Reality – The Challenge of Pileup

## Slide 30
Micromegas
GEM
Thick-GEM, Hole-Type and RETGEM
MPDG with CMOS pixel ASICs (“InGrid”)
Micro-Pixel Chamber (mPIC)
Electrons
Ions
60 %
40 %
Micromegas
GEM
THGEM
MHSP
InGrid
Micro-Pattern Gaseous Detector Technologies for Future Physics Projects
mPIC
Rate Capability:
MWPC vs MSGC

## Slide 31
GEM (Gas Electron Multiplier)
Thin metal-coated polymer foil chemically pierced by a high density of holes
Electrons are collected on patterned
readout board.
A fast signal can be detected on the lower
GEM electrode for triggering or energy
discrimination.
All readout electrodes are at ground potential.
S1
S2
S3
S4
Induction gap
e-
e-
I+
F. Sauli, Nucl. Instrum. Methods A386(1997)531
F. Sauli, http://www.cern.ch/GDD
A difference of potentials of ~ 500V is
applied between the two GEM electrodes.
the primary electrons released by the
ionizing particle, drift towards the holes
where the high electric field triggers the
electron multiplication process.

## Slide 32
CDF Experiment
H1 Experiment
Silicon Detectors in Particle Physics
ALEPH Experiment
DELPHI Experiment
Strip and hybrid pixel detectors are mature technologies employed in almost every experiment in high energy physics.

## Slide 33
1983: First Silicon Strip Detector in HEP
Ratio of detector surface
to nearby electronics
surface 1:300 !
NA11/NA32 Experiment at CERN –Measure Lifetime and Mass of Charm Mesons
1200 diode strips on 24 x 36mm2 active area
250-500 μm thick bulk material
4.5 μm resolution

## Slide 34
1980’s: The post era of the Z and W discovery, after the observation of Jets at UA1 and UA2 at CERN – “To proceed with high energy particle physics, one has to tag the flavour of the quarks!”
b-jet identification is crucial,
making use of 1.5 ps b lifetime:
flight distance few 100 μm
 need hit precision ~ 10 μm
Top Quark Production at Tevatron
(t tbar  bW bbarW):
1995: Discovery of Top Quark at Tevatrion

## Slide 36
Silicon Detectors has transformed the way we look at particles
1950-1970: Pre-Silicon Era-
photo of ionization trails
1990: Si-vertex detector
& gaseous tracking (TPC)
2010s: SiD concept for ILC
• Si vertexing, Si tracking
• Si calorimetry
It might look like we are actually seeing less now,but we can see a lot more than in pre-silicon era !
From Microelectronics to Nanoelectronics:
Detectors are more and more based on
semi-conductor technology
from vertex elements (20 um feature size)
to Si-calorimetry (ILC)
Silicon surface:
  ATLAS and CMS need to exchange
  Si-trackers during LS3 (2022/23) due
  to radiation effects: 400 m2
  CMS ECAL/HCAL Endcap: 600 m2 ?
  ILD/SiD ECAL: 2500 (1200) m2

## Slide 37
Why are Silicon Detectors such a Success ?
Enormous benefit (compared to gaseous detectors):
 Huge technological advances of silicon technology in the IT industry
 Pattern and structure are industry standard

## Slide 38
Si-Detector Electronics and Si-Pixels

## Slide 39
Silicon Detectors in Particle Physics: Evolution of Scale
CMS: ~ 220 m2 Silicon:
 More than all other previous HEP experiments combined !

## Slide 40
Silicon Strip Detectors: 220 m2
25000 silicon sensors
10 M strips = electronic ch.
75376 readout chips
26.000.000 bonds
37.000 analog optical links
The CMS Tracker: Pixels and Strips
Silicon only
tracker solution
10 layers of Si-strip (barrel)
9 endcap Si-strip wheels

## Slide 41
Pixel Detector: ~ m2
3 layers of pixels
1440 pixel modules
66 M pixel =
electronic channels
Half disk of forward pixels:
The CMS Tracker: Pixels and Strips
Silicon only
tracker solution

## Slide 42
The ATLAS Inner Central Tracker (Barrel)
The most critical parts are the sensors, ASICs and system engineering
(mechanics, power, cooling, assembly, etc) and integration

## Slide 43
The CMS Inner Central Detector (Barrel)
The most critical parts are the sensors, ASICs and system engineering
(mechanics, power, cooling, assembly, etc) and integration

## Slide 44
Solid State Tracking: Detector-Electronics Integration Trends
TODAY: Pixels
50 – 100s mm
Trends and Perspectives:
Improve rad. hardness (p-type bulk)
Reduce the thickness to 50 mm
From 6” to 8” and 12” wafers
R&D on SLID/TSV interconnect.
TODAY: Monolithic
25 – 50 mm (e.g. CMOS)
Radiation hardness improvements demand newer technologies
Improved functionality can only be achieved with higher integration
Power dissipation and material budget must be reduced
TOMORROW: 3D
Detectors (25–50 mm)
Day After Tomorrow:
3D TSV (< 20 mm)
Integrated sensor &
electronics: Less X0,
no bonding, low noise
Lower Vdep (power)
Faster charge collection
3D vertical
Integration (TSV)
Motivation to develop new Pixel Detectors:
Decrease fabrication cost
Develop thinner pixel systems
Easy fabrication of large area devices
Integrate More (= denser) Intelligence

## Slide 45
From LHC Particle Detectors to Medicine
Silicon pixel detectors, and crystals of lead tangstate, used for calorimetry, have already found various applications, especially in medicine:
- Silicon pixels are deployed as Medipix, for medical imaging and diagnosis.
- CMS electronics to read out these crystals in a magnetic field opened the way to combined PET/MRI scanners.
MEDIPIX: https://medipix.web.cern.ch/
ClearPET: https://crystalclear.web.cern.ch/crystalclear/pet.html

## Slide 46
75 800 Lead Tungstate Crystals
More (by number & volume)
than all other previous HEP
experiments combined!
Designed for
Ultimate e/
Energy Resolution
of 1-2%
CMS Electromagnetic Calorimeter
1972
1985
1990
1999
2008
Crystal Ball
672 NaI(Tl)
Cleo II
7800 CsI(Tl)
L3
12000 BGO
Crystal Barrel
1380 CsI(Tl)
TAPS
600 BaF2
KTeV
3100 CsI
Babar
6580 CsI(Tl)
Belle
8816 CsI(Tl)
Alice
17920 PWO
CMS
75000 PWO
5
10
m3

## Slide 47
CERN to become established as an important facilitator
of medical physics in Europe

## Slide 49
Future e+e- Colliders: “Higgs Factory” + possible Extension to Higher Energies
Linear colliders: ILC, CLIC (extendable to higher energies)
Circular colliders: CEPC, FCC-ee
Compact Linear Collider (CLIC): CERN
√s = 380 GeV, 1.5 TeV, 3 TeV
Length: 11 km, 29 km, 50 km
International Linear Collider (ILC):
Japan (Kitakami)
√s = 250 - 500 GeV (1 TeV)
Length: 21 km, 31 km (50 km)
Circular Electron-Positron Collider (CEPC):
China
√s = 90 - 240 GeV (1 TeV)
Circumference: 100 km
Future Circular Collider (FCC-ee):
CERN
√s = 90 - 350 GeV (1 TeV)
Circumference: ~100 km

## Slide 50
Large TPC
R~1.8m
Z/2~2.0m
Vertex detector
Inner radius~1.6cm
Outer radius~ 6 cm
Central and forward
Si tracking system
Example: ILC DETECTOR
Sketch of ILD cerntal detector

## Slide 51
~13m
~14m
~13m
~12m
ILD | SiD
Both optimized for PFA PFA Performance ~B･RECAL,inner2 (two-track separation @ ECAL) | 
B = 3.5 T | B = 5 T
RECAL,inner = 1.8 m | RECAL,inner = 1.27 m
Si + TPC tracking | Tracking: Si only
Share interaction point via push-pull | 
Two Validated Detector Concepts: ILD and SiD
ILD
SiD

## Slide 52
CMOS sensors expected to provide an attractive trade-off between granularity, material budget, radiation tolerance, speed and power dissipation
STAR
BT: PLUME
ILC
Sub-atomic Physics:
BT (EUDET, AIDA),
Vertex det. (STAR, ALICE)
X-Ray imagers molecular
biology (nano-science)
Mass spectroscopy (PIMMS)
X-Ray imaging lights sources equipment (SOLEIL)
Industrial quality control (soldering, u-cracks)
Art: C. Monet, Nymphéas et Pont Japonais
ILC CMOS-based sensors for Science and Industry

## Slide 53
A muli-modality approach (PET/CT,PET/MR) will be more and more requested in the clinical practice.
Today’s PET imaging platforms using SiPMs:
GE clinical PET/MR uses analog SiPM
VEREOS Philips PET/CT uses digital SiPM
Multi-channels arrays of crystals + SIPM:
minimum dead material between crystals
SiPM packaging is crucial up to 50%
sensitivity improvement
Monolithic arrays/high density of chan.
SiPMs represent today the future of Nuclear Medical Imaging  the only slowing down factor at the moment being the high associated cost.
2006: ILC Calorimetry (8k ch.):
First large experience
with SiPM operation (2006):
C. Monet, Nymphéas et Pont Japonais
From SiPM-based ILC Calorimeter to Advanced PET-Systems