## Slide 1: Universal adjustment solution for non motorized components in high radiation areas
M.Sosin, J.Jaros EN-ACE/SU
WP15 Meeting – 19.05.2017

## Slide 2: Outline
HL-LHC residual doses vs. access constraints
Typical issues with position adjustment
Alignment system requirements
Universal adjustment platform - CLIC DBQ support example
Standardized adjustment solution
Case of collimators alignment
Universal adjustment platform – R&D schedule
Summary

## Slide 3: HL-LHC residual doses estimation

## Slide 4: Typical issues with position adjustment
Crowded neighbourhood of aligned components
  Difficult access to regulation mechanisms/screws – (circus skills needed for some of components regulation)
  Fragile equipment around workspace – slow an careful manipulation
Ergonomics of adjustment
  Mechanisms not always intuitive
  Simple mechanisms => big backlash => multiple measurement and adjustment iterations needed =>
  Long adjustment time

## Slide 5: Alignment system requirements
Limit the presence of personnel in high radiation areas:
  Easy access from transport zone
  Intuitive kinematics of adjustment system
  Possibility of position measurements from bigger distances
  Option of remote (distance) adjustment using portable motorized adapters
5DOF position adjustment preferred
  Accuracy, resolution, stiffness – application dependent
  Simple robust and cheap solution

## Slide 6: A bit of history – CLIC DBQ adjustment platform
Tight space constraints
  14.5mm for „hexapod” platform integration
  Crowded environment – access from one side needed
  Small distance to neighbouring components
Needs
  +/- 1mm of stroke in X and Y
  µm resolution of X-Y position adjustment
  Rotations adjustment within +/- 4 mrad
  ~20µrad resolution of angular adjustment
  Short adjustment time

## Slide 7: A bit of history – CLIC DBQ adjustment platform

## Slide 8
A bit of history – CLIC DBQ adjustment platform
Modified Stewart platform configuration

## Slide 9: DBQ Support enabled to reduce pre-alignment time from one day to 20 minutes
Simple shimming solution – slow (time 1 day)
New solution design – adjustable platform concept
  Stewart platform adaptation – 3 vertical and 2 horizontal supports
  Simplified structure – reduced number of parts
  Ergonomic – easy access
With DBQ support, time was reduced to 20 minutes

## Slide 10: Second possible use → option for the tunnel fast re-adjustment
The idea:
Motors
Gears
Trans-
missions
Position feedback
Controller
Portable motorised adapter needed
  Position and orientation feedback coming from the absolute tracker
  Option of permanent installation (remote adjustment)
    Pos. feedback sensors as eg. WPS needed

## Slide 11: Motorized adapter functional prototype designed and preliminarily tested
Mechanical design
  Light and compact
  Mobility – fast auto-lock mechanism
  Build-in sensors
Control algorithms adopted to automated and semi-manual use
  Feedback tunel measurements (eg. Laser tracker or position sensors)

## Slide 12: Motorized adapter functional prototype designed and preliminarily tested

## Slide 13: Standardized adjustment solution
Universal adjustment platform based on vertical/horizontal Stewart platform configuration
  Regulation knobs accessible on one side of platform
  Easy and ergonomic manual operation, fast manual adjustment
  Standardized interface to regulation knobs – possibility to easy connect the motorized adapter
Full remote adjustment control
  Upgrade in position sensors (eg. WPS, inclinometers, HLS)
  Easy integration of permanent motors

## Slide 14: Standardized adjustment solution
Standardization of alignment mechanics
Standardized vertical/radial actuators mechanics
Standardized regulation and blocking interface
Standardized way of joints design
Needed discussion with all interested users to recognize all requirements and future parameters:
  Mechanisms accuracies, resolution, stiffness
  Platform dimensions limitations, actuators dimensions
  Maximal loads, external forces, etc.
Validation of solutions chosen

## Slide 15: Case of collimators alignment
Universal adjustment platform can be easily adopted for adjustment solution for collimators
  Range of X-Y +/- 10mm and +/-10mrad of roll-pitch-yaw adjustment feasible
  Accuracy, resolution, stiffness to be defined
  Space below collimator seems sufficient to integrate the platform mechanics

## Slide 16: Proposed development schedule
Discussions with users interested, needs analysis → June-July 2017
Adjustment solution standardization specification → August - September 2017
Platform prototype(s) studies and initial design → October 2017 – January 2018
Adapter prototype studies and design → October 2017 – January 2018
Prototype platforms tests, components validations → February-September 2018
Final design report, standardized solution description → October-December 2018

## Slide 17: Summary
To increase safety of Survey personnel in radiation zones during components alignment - change of approach in design of adjustment supports is needed
  Intervention time optimization have to be taken as important factor during adjustment solutions design
We propose standardized, Stewart platform based 5DOF adjustment solution, allowing easy adjustment and motorisation of components if needed

## Slide 18
Back up

## Slide 19
Flexural vertical support
with wedge-profiled head
Threaded
wedge
Flexural vertical support
sliding bearing
Wedge sliding bearing
Belleville spring stack
Regulation screw
Regulation screw
bearing unit
(2 flat needle bearings
+ tightening screw)
Vertical regulation unit

## Slide 20
Differential thread
regulation screw
Flexural horizontal support.
One end threaded
(as a part of regulation screw)
DB Quad platform clamping block
Horizontal regulation unit

## Slide 21
Stiffness results
Maximum deformation along X axis is about 2.5 micron
And along Y axis is less than 0.5 micron
F=100N
Z
X
Force load in XZ plane

## Slide 22: Vertical movement (Y axis)

## Slide 23: Roll movement (Z axis angle)

## Slide 24: Roll movement (Z axis angle)

## Slide 25: Pitch movement (X axis angle)

## Slide 26: Pitch movement (X axis angle)

## Slide 27: Yaw movement (Y axis angle)

## Slide 28: Yaw movement (Y axis angle)

## Slide 29: XZ plane deformation

## Slide 30: XZ plane deformation

## Slide 31: XY plane deformation

## Slide 32: XY plane deformation

## Slide 33: YZ plane deformation

## Slide 34: YZ plane deformation