## Slide 1
GEM DETECTORS
20 YEARS OF DEVELOPMENTS AND APPLICATIONS
Fabio Sauli
TERA Foundation
CERN

## Slide 2: 1988: MICRO-STRIP GAS COUNTER (MSGC) (MSGC)
A. Oed,
Nucl. Instr. and Meth. A263(1988)351
THIN METAL STRIPS ON GLASS SUBSTRATE
RATE CAPABILITY ~ 1 MHz/mm2
POSITION ACCURACY ~ 40 µm
2-TRACK RESOLUTION ~ 500 µm
HERA-B MSGC INNER TRACKER ~ 200 MSGC 20x20 mm2
CMS CENTRAL TRACKER ~ 5500 MSGC
LIGHT AND COMPACT DETECTOR CONSTRUCTION
J. Bohm et al, Nucl. Instr. and Meth. A360(1995)34

## Slide 3: MSGC: DISCHARGE PROBLEMS
MILD OR SERIOUS DISCHARGE PROBLEMS!
S. Keller et al, Nucl. Instr. and Meth. A419(1998)382
HERA-B MSGC INNER TRACKER
50 sparks/min

## Slide 4: ~ 1990 TO PRESENT: NEW DEVELOPMENTS
MICRO-GROOVE
MICROMEGAS
Y. Giomataris,
Nucl. Instr. and Meth. A419(1998)239
MICRO-GAP
MICRO-WIRE
MICRO-PIN ARRAY
COMPTEUR A TROUS

## Slide 5: 1978: THE MULTISTEP CHAMBER (MSC)
UV PHOTONS DETECTION (RICH): MWPC WITH PHOTOSENSITIVE GAS (TEA)
G. Charpak and F. Sauli, Phys. Lett. 78B(1978)723
PREAMPLIFICATION
GAIN 103
MWPC
GAIN 105
TRANSFER
10%
TOTAL GAIN 107
SINGLE ELECTRON DETECTION
SIMULATED CHERENKOV RING (COLLIMATED UV SOURCE)
E605 RICH
MULTISTEP CHAMBER

## Slide 6: ~ 1995 : µVIAS DEVELOPMENT
POLYIMIDE ETCHING:
CONTACTS THROUGH FLEXIBLE PRINTED CIRCUITS
Angelo Gandi and Rui De Oliveira
CERN’s Printed Circuit Workshop (EST-DEM)

## Slide 7: 1996: MSC+µVIAS => GEM
F. Sauli, Nucl. Instr. and Meth. A386(1997)531
PRESENTED AT:
IEEE Nuclear Science Symposium & Medical Imaging Conference
Anaheim, CA November 3-9, 1996
THE GAS ELECTRON MULTIPLIER (GEM):
100 µm PITCH HOLES ON COPPER-CLAD POLYIMIDE FOIL

## Slide 8: GEM MANUFACTURING
50 µm Kapton
5 µm Cu
Metal etching
Kapton etching
Second masking
Metal etching
and cleaning
Photoresist coating, masking and exposure to UV light
DOUBLE MASK PHOTOLITHOGRAPHY
DOUBLE CONICAL
“HOURGLASS”
140 µm
70 µm
“STANDARD” GEM

## Slide 9: TWO-STEP DETECTOR
GEM
MSGC
MSGC WITH GEM PREAMPLIFIER
R. Bouclier et al, Nucl. Instr. and Meth. A396(1997)50
COMBINED GAIN CURVES

## Slide 10: HERA-B MSGC+GEM
Bagaturia et al,
Nucl. Instr. and Meth. A490(2002)223
Angelo Gandi
Rui De Oliveira
J-C Labbé
~ 200 GEM FOILS, 20x20 cm2
CERN’s Printed Circuit Workshop (EST-DEM)

## Slide 11: MPGD DISCHARGE STUDIES
~2000
GEM:
A. Bressan et al.Nucl. Instr. and Meth. A424(1999)321
~3000
MICROMEGAS:
GASEOUS a SOURCE: 232Th -> 232Rn+a (6.4 MeV) DE ~ 500 keV ~ 104 e I+
Q ~ 104.103 = 107 e I+
RAETHER LIMIT
THORIUM
MPGD

## Slide 12: MULTI-GEM STRUCTURES
DOUBLE GEM
TRIPLE GEM
HIGHER GAINS
REDUCED ION BACKFLOW
VGEM
S. Bachmann et al, Nucl. Instr. and Meth. A 443(1999)464
LOWER DISCHARGE PROBABILITY

## Slide 13: DISCHARGE STUDIES - ALICE GEM TPC
220Rn INTERNAL a SOURCE
TRIPLE GEM
P. Gasik RD51Coll. Meeting (CERN 2016)
3 104
NO
DISCHARGES

## Slide 14: BACK TO MULTIGEM DISCHARGES
WHAT ABOUT THE RAETHER LIMIT?
VERY LARGE GAINS OBSERVED IN PURE NOBLE GASES
CHARGE CONFINEMENT: HOLES ARE (QUASI) INDEPENDENT
A. Buzulutskov et al, Nucl. Instr. and Meth. A433(1999)471
DISCHARGE PROBABILITY ON ~ MeV a
IN MULTI-GEMs, THE CHARGE SPREADS BY DIFFUSION OVER MANY HOLES!
P. Bhattacharya, MPGD Workshop (Trieste 2015)
4-GEM SIMULATION (ALICE TPC)

## Slide 15: HYBRID DETECTORS
GEM
MICROMEGAS
S. Procureur et al, Nucl. Instr. and Meth. A659(2011)91
GEM + MICROMEGAS
1 GeV p BEAM
VGEM=280 V
8000
GAIN
DISCHARGE PROBABILITY
10-4
10-5
M. Vandenbroucke, JINST 7(2012)C05014
AVALANCHES SIMULATION
GEM+MICROMEGAS

## Slide 16: DISCHARGE STUDIES - ALICE GEM TPC
DISCHARGE PROPAGATION: LAST GEM TO ANODE
SECTORS POWERING: STANDARD
HVB
HVT
GEM
EIND
HVB
HVT
GEM
EIND
FLIPPED:
standard
flipped
DISCHARGE PROPAGATION PROBABAILITY:
P. Gasik RD51Coll. Meeting (CERN 2016)
DISCHARGE PROPAGATION DELAY:
standard
flipped

## Slide 17: SINGLE GEM X-RAY DETECTOR
HIGH PROPORTIONAL GAINS
FAST ELECTRON SIGNAL
READOUT PLANE AT GROUND POTENTIAL
PATTERNED AT WILL
2-DIMENSIONAL CARTESIAN STRIPS READOUT
A. Bressan et al,
Nucl. Instr. and Meth. A425(1999)254
6 keV RADIOGRAPHY

## Slide 18: MAIN GEM PERFORMANCES: MIPS
M. Alfonsi et al, Nucl. Instr. and Meth. A535(2004)319
A. Bressan et al,
Nucl. Instr. and Meth. A425(199)262
LOCALIZATION ACCURACY
TRIPLE GEM A-CO2-CF4
J. Benlloch et al, IEEENS-45(1998)234
SINGLE GEM RATE CAPABILITY
20 C/cm2
~ 4 1014 MIPS cm-2
M. Alfonsi et al, Nucl. Instr. and Meth. A518(2004)106
RADIATION RESISTANCE
DOUBLE GEM Ar-CO2
s ~ 40 µm
s ~ 4.5 ns
TIME RESOLUTION: LHCB MUON TRIGGER
1 MHz mm2
GEM+MSGC

## Slide 19: TRIPLE GEMs FOR COMPASS TRACKER
Honeycomb
plates
GEM foils
Readout
board
C. Altumbas et al,
Nucl. Instr. and Meth. A490(2002)177
HV TESTING DURING ASSEMBLY
~30 TRIPLE GEM 30x30 cm2 - 2D CARTESIAN READOUT
L. Ropelewski

## Slide 20: GEM SECTORS AND READOUT PATTERNS
CENTRAL BEAM KILLER
GEM SECTORS SEPARATION (200 µm)
M. Krämer et al, 2008 IEEE Nucl. Sci. Symp. Conf. Rec.
1x1 mm2 PIXELS AND STRIPS
MEASURED FLUX IN HADRON BEAM:
1.2 105 Hz/mm2

## Slide 21: TOTEM TRIPLE GEM FORWARD CMS TRACKER
M.G. Bagliesi et al, Nucl. Instr. and Meth. A617(2010)134
SEMI-CIRCULAR MODULES
TEN-GEM TOTEM FORWARD SECTOR

## Slide 22: CYLINDRICAL GEMS
GAS DETECTORS DEVELOPMENT
CERN
L. Ropelewski....M. Van Stenis.....
TRIPLE-GEM PROTOTYPE

## Slide 23: CYLINDRICAL GEM DETECTORS
KLOE-2 INNER TRACKER
A. Balla et al,
Nucl. Instr. and Meth. A732(2013)221
BES III DETECTOR at IHEP (Beijing)
R. Farinelli, RD51 Coll. Meeting (Aveiro 2016)

## Slide 24: CERN GDD: SPHERICAL GEM CHAMBERS
S. Duarte Pinto arXiv:1011.5528v1
IEEE 2011 Nucl. Sci. Symp. Conf. Rec.
“SPHERICAL” MULTIGEM AND READOUT BOARD
GDD

## Slide 25: LARGE SIZE GEM PRODUCTION
SINGLE MASK PHOTOLITOGRAPHY
R. De Oliveira, CERN EP-DT-EF
M. Alfonsi et al, Nucl. Instr. and Meth. A617(2010)151
Cu-clad Kapton
Single mask
Photoresist
Cu etching
Kapton etching
Second Cu etching
“CYLINDRICAL” HOLES

## Slide 26
DISMOUNTABLE MECHANICAL ASSEMBLY
EDGE STRETCHED GEM FOILS
CERN-INFN-BONN
CMS HIGH-h MUON DETECTOR UPGRADE
GEM MODULES: 100-120 cm x 22-45 cm
36 SUPERCHAMBERS IN EACH ENDCAP
B. Dorney, MPGD WORKSHOP (Trieste 2015)
M. Alfonsi et al, Nucl. Instr. and Meth. A617(2010)151
D. Abbaneo et al,
Nucl. Instr. and Meth. A732 (2013) 203
Archana Sharma, CMS GEM Upgrade Project Manager

## Slide 27
CMS HIGH-h MUON DETECTOR UPGRADE
B. Dorney, MPGD Workshop (Trieste 2015)
DESIGN GAIN: 5.103
LARGE PROTOTYPE IN TET BEAM

## Slide 28
ALICE GEM-TPC UPGRADE
Chilo Garabatos, Deputy Project Leader
A. Deisting, MPGD Workshop (Trieste 2015)
QUAD-GEM WITH STAGGERED HOLES

## Slide 29: ALTERNATIVE GEM STRUCTURES
H, Takahashi et al, Nucl. Instr. and Meth. A724(2013)1
GOOD GAIN UNIFORMITY
GOOD ENERGY RESOLUTION
NON-OUTGASSING MATERIALS
GLASS GEM

## Slide 30: THICK ELECTRON MULTIPLIER (THGEM)
MECHANICAL DRILLING OF METAL-CLAD PC BOARD
SELF-SUPPORTING
HIGH GAIN (?)
A. Breskin
R.Chechik et al, Nucl. Instr. and Meth. A535(2004)303
ALSO CALLED LARGE ELECTRON MULTIPLIER (LEM)

## Slide 31: THGEM: GAIN AND CHARGING UP
DEVELOPMENTS FOR THE COMPASS RICH-1 UPGRADE
LARGE RIM:
HIGH GAIN
CHARGING UP
0.1 mm rim
No rim
RIMLESS:
LOW GAIN
STABLE
M. Alexeev et al, Nucl. Instr. and Meth. A695(2012)159
MULTIPLE
STRUCTURES
GAIN
V (kV)
0
10 µm
100 µm
RIM:
GAIN VS TIME (CHARGING UP EFFECT):

## Slide 32: MULTIGEM GAIN AT VERY HIGH RATES
P. Everaerts, PhD Thesis Gent University (2006)
GAIN VS X-RAY RATE: TRIPLE GEM (2006)
GDD

## Slide 33: MULTIGEM GAIN AT VERY HIGH RATES
S. Franchino et al, IEEE 2015 Nucl. Sci. Symp. Conf. Rec.
P. Thuiner, PhD TU Vienna (2016)
SINGLE GEM
TRIPLEGEM
NEW MEASUREMENTS (2015)
SIMULATION: CHARGE DENSITIES VS RATE
GDD

## Slide 34: POSITIVE IONS BACKFLOW
MULTIGEMS:THE IBF VALUE DEPENDS ON GEOMETRY, FIELDS AND DIFFUSION:
POSITIVE IONS BACKFLOW (OR FEEDBACK):
IDRIFT
IANODE
IBF =
THE WISH:
ONE IBF ION PER PRIMARY
SINGLE GEM
~ 30%
ED/EI=25%
S. Backmann et a, l
Nucl. Instr. Meth. A438(1999)376
A. Bondar et al, Nucl. Instr. and Meth. A496(2003)325
0.05%
0.2%
Gain
DOUBLE GEM
TRIPLE GEM

## Slide 35: ION BACKFLOW REDUCTION: OFFSET HOLES
EXPLOIT THE DIFFERENCE BETWEEN IONS’ AND ELECTRONS’ DIFFUSION IN AN OFFSET DOUBLE GEM
e- I+ TRANSVERSE DIFFUSION:
F. Sauli et al, Nucl. Instr. and Meth. A560(2006)269
OFFSET SCAN:

## Slide 36
ALICE TPC GEM UPGRADE
ALICE TDR CERN-LHCC-2013-020
FOUR GEMS WITH STAGGERED HOLES
ENERGY RESOLUTION VS IBF:
GEM 1 & 4: STANDARD PITCH 140 µm
GEM 2 & 3: LARGE PITCH 280 µm
A.Deisting, MPGD Workshop (Trieste 20125)

## Slide 37: IBF SIMULATIONS FOR THE PANDA TPC
F.W. Bohmer et al,Nucl. Instr. and Meth. A719(2013)101
TRIPLE GEM OPERATED IN Ne-CO2 90-10
2 107 p-p ANNIHILATIONS GAIN M=2000 IBF 2.5 10-3
SPACE CHARGE DENSITY:
ELECTRIC FIELD DISTORTIONS:

## Slide 38: GAS DETECTORS SIMULATION TOOLS
P. Bhattacharya, RD51 Collaboration
MAGBOLTZ (Steve Biagi)
GARFIELD (Rob Veenhof)
+ ELECTRIC FIELD, ENERGY LOSS,...

## Slide 39: GAS DETECTORS SIMULATION TOOLS
P. Bhattacharya, MPGD Workshop (Trieste 2015)
ALICE GEM TPC SIMULATION

## Slide 40
GEM APPLICATIONS: NEUTRON DETECTORS
CASCADE: 10B-COATED GEM ELECTRODES
M. Klein and Ch. Schmidt, Nucl. Instr. and Meth. A628(2011)9
THERMAL NEUTRON RADIOGRAPHY

## Slide 41
NEUTRON DETECTORS
n
α
b-GEM:
TRIPLE GEM WITH ALUMINUM FOIL CATHODE COATED WITH 1 µm OF BORON CARBIDE
READOUT: 144 PADS, 8x8 mm2
G. Croci et al, Nucl. Instr. and Meth. A732(2013)217
2-D THERMAL NEUTRON BEAM PROFILE
SENSITIVITY TO GAMMA BACKGROUND:

## Slide 42
NEUTRON DETECTORS
BORON ARRAY NEUTRON DETECTOR (BAND-GEM)
Padded Anode
n
α
e-
10 cm
6 cm
2 mm
Triple GEM
Cathode
3D Lamella
System
Ed
48 LAMELLAS PROTOTYPE
Alumina Lamellas coated on both sides with 10B4C
G. Croci et al, MPGD Workshop (Trieste 2015)

## Slide 43: UV PHOTON DETECTION: CsI PHOTOCATHODES
REFLECTIVE CsI PHOTOCATHODE ON UPPER GEM ELECTRODE
NO PHOTON FEEDBACK
INSENSITIVE TO DIRECT IONIZATION
200 µm
55 µm rms
T. Meinschad, L. Ropelewski and F. Sauli, NIMA 535(2004)324
TRIPLE GEM
COLLIMATED SINGLE UV PHOTON SOURCE
POSITION ACCURACY
GDD

## Slide 44
PHENIX HADRON BLIND DETECTOR
e+
e-
E
Protons
C. Aidala et al, Nucl. Instr. and Methods A502(2003)200
Z. Fraenkel et al, Nucl. Instr. and Methods A546(2005) 466
“INVERSE FIELD” TPC

## Slide 45: COMPASS RICH 1 UPGRADE
THICK GEM CsI-COATED 30x30 cm2
M. Alexeev et al, Nucl. Instr. and Meth. A732(2013)264
TRIPLE THGEM PROTOTYPE
SINGLE EVENT (6 GeV p- BEAM)

## Slide 46: CHERENKOV RING IMAGING
COMPASS RICH-1 MPGD UPGRADE
M. Alexeev et al, MPGD Workshop (Trieste 2015)
DOUBLE STAGGERED THGEMS+MICROMEGAS

## Slide 47: GEM APPLICATIONS: POLARIMETRY
R. Bellazzini et al, Nucl. Instr. and Meth. A720(2013)173
5.9 keV PHOTOELECTRON (80 µm pixels pitch):
SOFT X-RAY POLARIMETRY
MEASURED ANGULAR MODULATION:

## Slide 48: GEM POLARIMETER IN SPACE
Toru Tamagawa, MPGD Workshop (Saragoza 2013)
NEW MISSION (2017):
POLARIMETRY FOR RELATIVISTIC ASTROPHYSICAL X-RAY SOURCES (PRAXyS)
W.B. Iwakiri et al, Nucl. Instr. and Meth. In press (2016)
GEMS MISSION CANCELLED BY NASA (2012)

## Slide 49: GEMPIX: GEM + MEDIPIX
F. Murtas et al, JINST10(2015)P11003
TRIPLE-GEM WITH MEDIPIX READOUT
256x256 pixels, 55x55 µm2
COMPTON ELECTRON:
RECORDED EVENTS:

## Slide 50: X-RAY FLUORESCENCE ANALYSIS
28x28 mm2 MICRO-HOLE AND STRIP PLATE (MHSP)
WITH RESISTIVE LINES 2-D READOUT
A.L.M. Silva et al, Spectrochimica Acta B86(2013)115
X-RAY TRANSMISSION IMAGE:
ELEMENTAL ANALYSIS:

## Slide 51: ENERGY-RESOLVED X-RAY FLUORESCENCE
J. Veloso, RD51 Special Workshop on Photon detection (CERN, 2015)

## Slide 52: OPTICAL IMAGING
TRIETHYLAMINE (TEA):
INTERNAL WAVELENGTH SHIFTER
G. Charpak, J.-P. Fabre, F. Sauli and M. Suzuki,
Nucl. Instr. and Meth. A258(1987)177
COSMICS
IMAGING CHAMBER (1987)

## Slide 53: OPTICAL IMAGING (2002)
a PARTICLES TRACKS
n INTERACTIONS IN 3He
CARBON TETRAFLUORIDE SCINTILLATION:
F.A.F. Fraga, et al, Nucl. Instr. and Meth. A478(2002) 357
He-CF4 GAS FILLING

## Slide 54: DOSE MONITORING IN HADROTHERAPY
E. Seravalli et al, Phys. Med. Biol. 53(2008)4651
DOUBLE GEM WITH OPTICAL DETECTION
BEAM PROFILE:

## Slide 55: OPTICAL IMAGING
Full energy
Pileup
Escape
55Fe source
F. Resnati , EP Detector Seminar (CERN, April 29, 2016)
55Fe 5.9 keV X-RAYS
a PARTICLES FROM 220Rn and 216Po
GDD

## Slide 56: ENERGY RESOLVED FLUORESCENCE ANALYSIS
Red
Green
Blue
X-ray tube
‘painting’
pin-hole
GEMs
shielding
Camera and lens
GDD
F. Resnati, MPGD Workshop (Aveiro, 2016)

## Slide 57: OPTICAL X-RAY IMAGING
JUMPING DRONE RADIOGRAPHY (30 keV)
11 kV
40 kV
GDD
SMALL DRONE-IN-THE BOX
F. Resnati, MPGD Workshop (Aveiro, 2016)

## Slide 58
X-RAY TOMOGRAPHY
IMAGE -> SINOGRAMS -> FILTERED BACK PROJECTION -> 3D IMAGE
GDD
F. Resnati, MPGD Workshop (Aveiro, 2016)

## Slide 59: CORRECTION OF THE PARALLAX ERROR
RADIAL CONVERSION AND DRIFT:
DRIFT
GEM 1
GEM 2
CATHODE
Computed with COMSOL Multiphysics
CONCENTRIC GRADED POTENTIAL RINGS ON CATHODE AND GEM ELECTRODES
F. Sauli, PCT Patent WO99/21211
PLANISPHERICAL GEM
PINHOLE CAMERA:
PARALLAX ERROR

## Slide 60: PLANISPHERICAL GEM WITH OPTICAL READOUT
CAD-CAM DESIGN
3-D PRINTING OF MOST PARTS
SEGMENTED GEMS MANUFACTURED AT CERN (R. De Oliveira)
10 cm Ø 10 cm FOCUS (ADJUSTABLE)
... F. Brunbauer.....M. Van Stenis.....
GDD

## Slide 61: PLANISPHERICAL GEM
55Fe 5.9 keV
MASK
MASK WITH 1 mm Ø HOLES PATTERN
UNIFORM DRIFT FIELD
RADIAL DRIFT FIELD
F. Sauli, MPGD Workshop (Aveiro 2016)
GDD

## Slide 62: PLANISPHERICAL GEM
FLUORESCENCE IMAGE OF A COPPER MESH 1mm STRIPS AT 5 mm PITCH
Florian Brunbauer, October 20
GDD
X-RAY TUBE
20 keV

## Slide 63: AND IF YOU WISH TO KNOW MORE.....
Thanks for your attention!