## Slide 1: HL-LHC Lay-out Optics version 1.3
Y. Muttoni, B. Vazquez de Prada, I. Zurbano
Thanks to all WPs collaborative effort
Presented by P. Fessia

## Slide 2: Summary
New collection of info via collaborative approach
What we have new in the lay-out
The lay-out in 5R
Status of the others lay-out
Lay-out timeline

## Slide 3: Trying to improve comment collection
Till now the large part of the information necessary to build lay-out were transferred orally, by mail, in small/medium meetings
The aim was to make the information available to more people in easier way and to record source of information
The target was a development collaborative effort in order to efficiently get to a level of definition ready to go through the standard HL-LHC/LHC quality approval in EDSM/CDD
Presently open to WP15 e-list (about 90 persons)

## Slide 6: Lay-out modifications
Where | what
Experiment side | New VAX unit
TAXS-Q1 | Ion pump added
Q1 IP extr. | BPM moved into the good measurement area, new (shorter) cold to warm transition
Q1 and Q3 | Shorten of 40 mm
Q1->CP | Moved to the IP because of the above mentioned cryoassembly modifications
Q1 to Q2a | BPM moved in good measurement area
Q2a and Q2b | Reduction distance dipole corrector to quad
BMQ DFX | Moved from inside DFX to warm
TAXN | New references for dimensions on drawing
TAXN/D2 | Revised vacuum lay-out
Crab cavities | Reduction from 4 modules to 2 modules
BPTX and APWL | moved in the area made available by the crab above
Q4 | Change from LQYY to LQYG
TCLMB | Mask added in front of Q4

## Slide 7: Lay-out modifications
Where | what
BBLR | Shorten because of need of space for surrounding equipment (5760 mm vs. 6000 mm flange to flange)
Q4 and Q5 | Now symmetric respect to the IP

## Slide 9: Lay-out drawing comments 5R

## Slide 10: Lay-out drawing comments 5R
To be modified when new baseline ready
BPM could be moved when DFX design and vacuum part refined
Need of the lay-out from top: 2 beam and staggered equipment
Present baseline probably no 5th axis and asked collimation to investigate alternative location for collimators

## Slide 11: Lay-out drawing comments 5R
Connection SC-link D2 to be updated when design is more advanced. Possible need to shift crab of 1 meter to the arc
Shorten BBLR to total mech length of 5760 mm
New mask, displaced APWL and BPTX
(location being optimized)

## Slide 12: Lay-out drawing comments 5R
Zone could be modified when we will know more about QRL-QXL connection

## Slide 13: Status of other lay-outs and time line Optics version 1.3
Lay-out | Status | Date for approval
5R and 5L LSS | Last discussion tomorrow in INT meeting then approval | 04/11/2016
1R and 1L LSS | First discussion next week at INT meeting | 18/11/2016
7R and 7L DS | To be started | 18/12/2016
2R and 2L DS | To be started | 14/01/2017
6L and 6R LSS | To be started | 28/01/2016
4R and 4L LSS | To be started | 28/04/2017
7R and 7L LSS | To be started | June 2017
3R and 3L LSS | To be started | June 2017

## Slide 14: Digression
We are running a de-installation and installation tasks/budget exercise. We want to end it for end of January. After C&S review we are going to ramp up in intensity. Please be responsive
Cabling: revision of cable needs. Please prepare your need estimation. We are not asking detailed list but we need to be sure that
  We have a good evaluation in the hands of EN-EL
  We are sure that cost wise have not been forgotten
  We can optimise integration targeting also these costs
  we have the work in the de and installation sequence
WP with electronics racks: we need to have good view of needs. If the person coming normally to the integration meeting has not the full view (and this is normal) please give us a reference name to contact. We need information to allow you having the space required in terms of quantity and quality