## Slide 1: Status and Plans of the AWAKE Experiment
Edda Gschwendtner
for the AWAKE Collaboration
SPSC 18 October 2016

## Slide 2: Outline
Introduction
AWAKE Facility and Equipment
AWAKE Beam Commissioning
Electron Acceleration Status
AWAKE Run 2 after LS2
Long-Term Perspectives for Proton-Driven Plasma Wakefield Accelerators
Summary

## Slide 3: Proton Drivers for Plasma Wakefield Acceleration
Proton drivers: large energy content in proton bunches  interesting for plasma wakefield accelerators
Drive beams:
  Lasers: ~40 J/pulse
  Electron drive beam: 30 J/bunch
  Proton drive beam: SPS 19kJ/pulse, LHC 300kJ/bunch
Protons drives wakefields over much longer plasma lengths  to reach high energies of a witness beam possible in few stages.
But: need short bunches  self-modulation instability
Witness beam
Drive beam: protons
Plasma cell

## Slide 4: Modulated Proton Bunch
Drive beam for AWAKE: 400 GeV/c SPS proton beam
SPS longitudinal beam size (sz = 12 cm) is much longer than plasma wavelength (l = 1mm)
 Immediate use of CERN SPS beam
 AWAKE Experiment is based on self-modulation instability
  Modulate long bunch to produce a series of ‘micro-bunches’ in a plasma with a spacing of plasma wavelength lp.
    Strong self-modulation effect of proton beam due to transverse wakefield in plasma
    Resonantly drives the wakefield
    Modulation should be seeded (with laser in AWAKE)

## Slide 5: AWAKE
AWAKE Collaboration: 16+3 Institutes world-wide:
Collaboration members:
John Adams Institute for Accelerator Science
Budker Institute of Nuclear Physics & Novosibirsk State University
CERN
Cockcroft Institute
DESY
Heinrich Heine University, Düsseldorf
Instituto Superior Tecnico
Imperial College
Ludwig Maximilian University
Max Planck Institute for Physics
Max Planck Institute for Plasma Physics
Rutherford Appleton Laboratory
TRIUMF
University College London
University of Oslo
University of Strathclyde
Novosibirsk
Vancouver
Oslo
Hamburg, Greifswald
Dusseldorf
Munich
CERN
Lisbon
Manchester
London
Glasgow
Associated members:
Ulsan National Institute of Science and Technology (UNIST), Korea
Wigner Institute, Budapest
Swiss Plasma Center group of EPFL
Further groups have also expressed their interest to join AWAKE.

## Slide 6: AWAKE at CERN
AWAKE Timeline
 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022…
Proton and laser beam-line |  |  |  |  |  |  |  |  |  | 
Experim-ental area |  |  |  |  |  |  |  |  |  | 
e- source and beam-line |  |  |  |  |  |  |  |  |  | 
Studies, design
Fabrication
Installation
Commissioning
Commissioning
Installation
Modification, Civil Engineering and installation
Study, Design,
Procurement, Component preparation
Study, Design,
Procurement, Component preparation
Data taking
Data taking
Phase 1
Phase 2
Long Shutdown 2
24 months
RUN 2
RUN 1
Advanced Proton Driven Plasma Wakefield Acceleration Experiment
  Final Goal: Design high quality & high energy electron accelerator based on acquired knowledge.
Proof-of-Principle Accelerator R&D experiment at CERN
Approved in August 2013
First beam end 2016
cont’d

## Slide 7: AWAKE: Experimental Program
Plasma electron density rplasma
Proton beam density rbeam
Self-modulated proton bunch resonantly driving plasma wakefields.
laser pulse
proton bunch
gas
plasma
J. Vieira et al PoP 19063105 (2012)
Laser
dump
SPS
protons
10m
SMI
Proton
beam
dump
Laser
Proton diagnostics
BTV,OTR, CTR
p
Phase 1: Understand the physics of self-modulation instability processes in plasma.
 Start with physics Q4 2016!

## Slide 8: AWAKE Experimental Program
Phase 1: Understand the physics of self-modulation instability processes in plasma.
Phase 2: Probe the accelerating wakefields with externally injected electrons.
Laser
dump
e-
SPS
protons
10m
SMI
Acceleration
Proton
beam
dump
RF gun
Laser
p
Proton diagnostics
BTV,OTR, CTR
e- spectrometer
Maximum amplitude of the accelerating field Ez as a function of position along the plasma. Saturation of the SMI at ~4m.
laser pulse
proton bunch
gas
plasma
electron bunch
Beams are co-propagating in this direction close to the speed of light
protons
electrons
A. Petrenko, CERN
 Start with physics Q4 2017!

## Slide 9: Outline
Introduction
AWAKE Facility and Equipment
AWAKE Beam Commissioning
Electron Acceleration Status
AWAKE Run 2 after LS2
Long-Term Perspectives for Proton-Driven Plasma Wakefield Accelerators
Summary

## Slide 10: AWAKE Planning 2016
Laser installation
HW commissioning p-line:
Diagnostics, magnets, PC, WIC
DSO tests
1st p-beam Comm.
Laser beam line installation
p-beam commissioning (+RF synch, + laser)
Plasma cell end flanges installation
Plasma cell HW commissioning
p-beam + plasma (Rb) + laser commissioning
First AWAKE physics
OTR/CTR comm.
Laser beam commissioning
Laser beam line installation
RF synchronization, streak camera commissioning, etc..
E.G. Preliminary version 0.5
TS1’
AWAKE physics
End of run
HW comm.
TS2
p-beam + plasma (no Rb) + laser commissioning
Dry-run1

## Slide 11: AWAKE Proton Beam Line
Proton beam line fully installed (Magnets, Instrumentation, Vacuum)
Hardware commissioning finished
Proton beam line upstream
Proton beam line downstream


## Slide 12: Laser and Laser Line
Laser beam line to plasma cell
  l = 780 nm
  t pulse = 100-120 fs
  E = 450 mJ
Diagnostic beam line (“virtual plasma”)
  l = 780 nm
  t pulse = 100-120 fs,
  E ≈ 5 mJ
Laser beam line to electron gun (to be installed in 2017)
  l = 260 nm
  t pulse = 0.3-10 ps
  E = 0.5 mJ
Laser system installed and commissioned:
  Laser, compressor, safety shutters, beam dumps, mirrors
  Control system  integrated in CERN control system
  Lots of efforts in commissioning of laser itself
Protons from SPS
Laser insertion
Point
Electron Source
Electron Merging Point
Common Beam Line
Start of Plasma Cell


## Slide 13: Laser and Laser Line
Protons from SPS
Laser insertion
Point
Electron Source
Electron Merging Point
Common Beam Line
Start of Plasma Cell
Laser safety shutters:
Linked with SPS access system
Laser, compressor in laser room
Mirrors in vacuum
plasma entrance
plasma centre
plasma exit
Laser profile on virtual transport line

## Slide 14: AWAKE RF Synchronization
BA3 surface
AWAKE
BA3
AWAKE
~3km
Deliver wide range of RF signals for laser, proton and electron beams
Precision trigger pulses for beam instrumentation
Active link stabilization to the ps-level for 3km transmission from AWAKE to BA3
Notes:     “fc and frep” divided signals are sent to the SPS to change the time of arrival of the proton beam with respect to the 10Hz laser pulse train.

## Slide 15: RF Hardware Development and Installation
Tests and validation steps done to synchronize protons with laser:
Use signals from AWAKE
  All frequencies in correct range
Coarse alignment of SPS proton bunch and laser pulse
  Proton bucket selection mechanism in AWAKE LLRF validated
Fine phase of protons at SPS extraction (within one ‘half bucket’)
  Temporary set-up works as expected
Synchro crate
AWAKE crate
Link compensation
Fast triggers
Distribution, frac. divider
Main divider, RF trains
TSG40
BA3/Faraday Cage
BA3 surface
AWAKE


## Slide 16: Self-Modulation Instability Detectors
SPS
protons
10m
SMI
Proton
beam
dump
Laser
p
BTV1
BTV2
Indirect SMI Measurement:
Measure the angle of the maximum defocused protons to indirectly prove the SMI development of the proton beam and reconstruct the saturation point of the SMI.
Measurements in the HiRadMat Facility
 Defined the choice for the BTV screens (1mm Chromox Al2O3:CrO2)
HiRadMat setup
Chromox screen
Measured proton beam on BTV2
Installed and commissioned

Notes: 1mm thick: highest light yield

## Slide 17: Self-Modulation Instability Detectors
SPS
protons
10m
SMI
Proton
beam
dump
Laser
p
BTV
BTV
sp ~ 400 ps
4 ps
CTR & TCTR
OTR
Direct SMI Measurement:
Radiation emitted by bunch when traversing dielectric material
 Streak camera
OTR/CTR table with installation
Light transport to streak camera
Streak camera
Installed and commissioned


## Slide 18: Plasma Cell
Circulation of Galden HT270 at 210 [°C] in plasma cell
Rubidium Vapour Source
Density adjustable from 1014 – 1015 cm-3, 10 m long, 4 cm diameter
Plasma formed by field ionization of Rb
  Ionization potential FRb = 4.177eV
  above intensity threshold (Iioniz = 1.7 x 1012W/cm2) 100% is ionized.
System is oil-heated ~ 210˚ C
  keep temperature uniformity at Top ± 0.1 [°C] over the 10 [m] cell length
  Keep density uniformity

## Slide 19: Why this Complex Plasma End Flange?
Revised solution for source ends
Valves resulted in long Rb density ramp and
slow refill time.  strong effect on electron capture!
 New solution: continuous flow through small aperture
 2016: final design and manufacturing
Pumping Group
Rb Recycling
Glovebox
Expansion chamber
Cold trap
Rb Flow path
View port
Alignment table
Argon Feed Valve
Notes: Main function:
Allow injection of Rb vapour into plasma cell at uniform and controlled temperature
Sub-functions:
Allow Rb loading and recycling
Allow Rb temperature control
Allow Rb density monitoring
Safety functions:
Prevent other equipment from Rb contamination
Allow remote chamber neutralization

## Slide 20: Plasma Cell: Current Status
10m long plasma cell installed in Feb 2016
For beam commissioning: Connected to vacuum system with spare vacuum tube

## Slide 21: Plasma Cell End Flange Integration
Plasma cell end flange installation

## Slide 22: AWAKE Plasma End Flanges
Clean Room Activities:
UHV vacuum reception tests
Alignment
Delivered to CERN in September 2016

## Slide 23: Plasma End Flanges in AWAKE Tunnel
Installed and aligned 17 October 2016


## Slide 24: EHN1 Surface Plasma Cell Test Area
Main Glove box
Plasma cell replica
Main activities
Control system: integration and test
Probes calibration
Rb handling processes: testing and rehearsal before Rb will be installed in the tunnel
Glove box
EHN1 surface test area

## Slide 25: AWAKE Control System
Built on architecture provided by the CERN accelerator controls group.
Strong collaboration between CERN controls groups, CERN equipment groups and institutes to develop technical solutions for integration of AWAKE specific equipment.
Beam line, magnets, beam instrumentation, electron source…
SMI, laser, spectrometer…
Validated during dry-run and commissioning run


## Slide 26: Outline
Introduction
AWAKE Facility and Equipment
AWAKE Beam Commissioning
Electron Acceleration Status
AWAKE Run 2 after LS2
Long-Term Perspectives for Proton-Driven Plasma Wakefield Accelerators
Summary

## Slide 27: AWAKE Planning 2016
Laser installation
HW commissioning p-line:
Diagnostics, magnets, PC, WIC
DSO tests
1st p-beam Comm.
Laser beam line installation
p-beam commissioning (+RF synch, + laser)
Plasma cell end flanges installation
Plasma cell HW commissioning
p-beam + plasma (Rb) + laser commissioning
First AWAKE physics
OTR/CTR comm.
Laser beam commissioning
Laser beam line installation
RF synchronization, streak camera commissioning, etc..
E.G. Preliminary version 0.5
TS1’
AWAKE physics
End of run
HW comm.
TS2
p-beam + plasma (no Rb) + laser commissioning
Dry-run1

## Slide 28: Proton and Laser Beam Commissioning 2016

## Slide 29: Results Proton Beam Commissioning
Stable beam at full intensity 3E11 p/bunch
Optimized trajectory at experiment
Standard deviation during stability run of ~60 μm
No beam losses at laser merging mirror
Proton beam line commissioned and running stable with full intensity and matching the specifications

Laser
dump
SPS
protons
10m plasma cell
SMI
Acceleration
Proton
beam
dump
Laser
OTRstreak
Proton
diagnostics
p
BTVstreak
BTV
BTV
BTV

## Slide 30: Results Laser Beam Commissioning
Operational Point: 11 mm
No losses on BLMs even with full intensity of 3E11 protons
Merging mirror scan across the proton beam
Laser
dump
SPS
protons
10m plasma cell
SMI
Acceleration
Proton
beam
dump
Laser
OTRstreak
Proton
diagnostics
p
BTVstreak
BTV
BTV
BTV


## Slide 31: Results Laser Beam Commissioning
Laser positioned on proton beam references to within 300 microns
Transversal alignment of proton and laser beam (spatial overlap)
Laser
dump
SPS
protons
10m plasma cell
SMI
Acceleration
Proton
beam
dump
Laser
OTRstreak
Proton
diagnostics
p
BTVstreak
BTV
BTV
BTV
p-beam
laser

Notes: Keep in mind: this is a ~50meter throw from the nearest optic
So 300 micron on a 50 meter throw is 6 urad pointing jitter

## Slide 32: Result Proton and Laser Beam Synchronization
laser
proton beam
1 ns
Laser
dump
SPS
protons
10m plasma cell
SMI
Acceleration
Proton
beam
dump
Laser
OTRstreak
Proton
diagnostics
p
BTVstreak
BTV
BTV
BTV
BTV upstream plasmas cell
SPS proton beam synchronized with AWAKE laser within ~20ps accuracy


## Slide 33: What We Want to See During Physics Run Dec. 2016
Laser
dump
SPS
protons
10m plasma cell
SMI
Acceleration
Proton
beam
dump
Laser
OTRstreak
Proton
diagnostics
p
BTVstreak
BTV
BTV
BTV
Proton beam undergoes Self-Modulation Instability when passing through plasma
Proton Beam Self-Modulation Instability

## Slide 34: Outline
Introduction
AWAKE Facility and Equipment
AWAKE Beam Commissioning
Electron Acceleration Status
AWAKE Run 2 after LS2
Long-Term Perspectives for Proton-Driven Plasma Wakefield Accelerators
Summary

## Slide 35: Electron Source in AWAKE
Electron source design finished, construction of hardware ongoing
Waveguide system: launched production
Shielding designed and decided to have a separate access zone for the electron source
Dismantling of PHIN will start next month


## Slide 36: Collaborations for Electron Source
Good progress in collaborations:
  TRIUMF BPM’s and Faraday Cup:
    First successful test in CALIFES
  Pepper pot from Manchester:
    Designed, most of equipment ordered
  Booster structure together with Lancaster and Cockcroft
    fabrication, prototypes accepted
Triumf BPM
Pepper pot
Booster structure

Length ~ 4 m
FC
E, DE
MS
BPR
Laser +Diagnostics
RF GUN
Emittance
Incident, Reflected Power and phase
Spectrometer
Corrector
MTV
VPI
FCT
Accelerator
MTV,
Emittance
Matching triplet
BPR
BPR
Incident, Reflected, transmitted Power
Klystron from CTF3
1m booster linac

## Slide 37: Status of the Electron Beam Line
Layout, specifications frozen
Magnets, power converters ordered
Cabling for BTVs done


## Slide 38: Electron Spectrometer
Design of the light transport line from the spectrometer screen to the CCD camera done
Spectrometer vacuum window design: 2mm Al
 no risk of buckling of the window
 scattering of electrons negligible compared to camera resolution

Notes: For energies of ~100 MeV and upwards, the width of the line spread function due to the window is negligible compared to the camera resolution.
  At 20 MeV: at 0 (45) degree incidence: RMS ~0.2 (0.4) mm  broaden distribution by ~4 (13) %.

## Slide 39: Electron Phase Master Schedule
p+ to PLASMA
p+ GLOBAL COMMISSIONING
p+ GLOBAL COMMISSIONING
p+ to PLASMA
p+ to PLASMA
HWC
EYETS
2016
2017
AWAKE
p+
and
e- PHYSICS
e- HWC
e- and p+ to PLASMA
e- GLOBAL COMMISSIONING
YETS
20172018
e- LASER: Studies and Purchasing
e- LASER Installation and HWC
Cabling
e- SOURCE: Studies, Purchasing and Production
PHIN SOURCE & Accelerating structure: Dismounting, Installation and HWC
RF:
Studies and Procurement
RF:
Installation and HWC
Beam Controls& Instrumentation:
Studies and Procurement
BE-CO & BI: Installation and HWC
e- Magnet Install
e- VSC:
Install.
e- Vacuum:
Studies, Procurement and Production
e- Phase
Experiment
Installation
2016 |  |  |  | 2017 |  |  |  | 2018 |  |  | 
Q1 | Q2 | Q3 | Q4 | Q1 | Q2 | Q3 | Q4 | Q1 | Q2 | Q3 | Q4
e- Beam line and Magnets
Studies, design, procurement, production and tests
Plasma Cell:
Installation and HWC
Cabling
CV & Infrastr.
p+ to PLASMA
on track
Laser
dump
e- spectrometer
e-
SPS
protons
10m
SMI
Acceleration
Proton
beam
dump
RF gun
Laser
Proton
diagnostics
p
Plasma cell


## Slide 40: Outline
Introduction
AWAKE Facility and Equipment
AWAKE Beam Commissioning
Electron Acceleration Status
AWAKE Run 2 after LS2
Long-Term Perspectives for Proton-Driven Plasma Wakefield Accelerators
Summary

## Slide 41: AWAKE Run 2 and Beyond
AWAKE Run 1 until LS2 : proof-of-concept experiment – fully funded
AWAKE Run 2:
Goals:
Accelerate an electron beam, while preserving beam quality as well as possible
Demonstrate scalability of the AWAKE concept
Requirement:
Compressed proton beam in SPS
Sustain gradient in SMI wake over long distance  density step for freezing modulation
Short electron bunch with higher energy for loading wakefield
Scalable length plasma sources
Laser
dump
Optimized
SPS
protons
10m plasma
SMI
Acceleration
Proton
beam
dump
RF gun
Laser
Proton diagnostics
BTV,OTR, CTR
e- spectrometer
~4m plasma
e- (~100 fs, > 20 MeV)
Bunch compression, increased acceleration
e- emittance
measurement

## Slide 42: Run 2: Example of Simulation Studies
Other Simulation studies:
Emittance preservation, tolerances, staging
Reach %-level of energy spread of the electron beam with beam loading.
Typical electron beam parameters:
  40 – 60 µm (100 fs) bunch length
  Few 100 A peak current
  > 50 MeV Injection energy
 Freezing the modulation:
Wakefield amplitude quickly drops after the beam gets modulated
Remedy: control the wave phase by the plasma density profile
1 m wide gap to inject electrons
Plasma cell (SMI)
Plasma cell (acceleration)
Plasma density
Accelerating gradient
4% density step
Notes: (defocusing regions keep on moving along the beam and destroys the bunches)

## Slide 43: Run 2: Options for Electron Injector
Modify phase 2 injector (S-band)
Can Run 1 AWAKE injector (PHIN S-band photo-injector) be modified to provide 50 MeV and 400 A, within space constraints ?
Modify phase 2 injector, upgrade with X-band
X-band structure? ~60 MV/m gives required boost
X-band gun? Based on best SLAC results could provide required energy and current in available space. Requires development work.
X
X
Laser wakefield acceleration injector
very short bunches possible (few um)
compact
AWAKE energy requirement (< 100 MeV) relaxed with respect to state-of-the-art (4 GeV)
 collaboration with LWFA-experts initiated
100+ MeV routinely reached with few MW Ti:Sa laser

## Slide 44: Run 2: Scalable Plasma Sources
Does not need laser ionization
Fully modular (no gaps)
Required density reached
Uniformity (spatial, temporal) needs work
Need to move from prototype to AWAKE-compatible technology
Helicon development
Current 1m prototype in Greifswald
 Collaboration between MPP Greifswald, EPFL SPC and CERN is being set up
Gas discharge development
3m prototype developed by Imperial College and IST (Lisbon)
Construction of prototype is pending funding

## Slide 45: Outline
Introduction
AWAKE Facility and Equipment
AWAKE Beam Commissioning
Electron Acceleration Status
AWAKE Run 2 after LS2
Long-Term Perspectives for Proton-Driven Plasma Wakefield Accelerators
Summary

## Slide 46: Fixed Target Experiments with High Energy Electron Beam
So far, no experimental hints on particle nature of dark matter.
Interest in low-mass particle solutions increasing; e.g., dark photons.
Light shining through walls experiments …
Here, use electron beam.
NA64 experiment
NA64: expect 106 electrons/spill; 1012 electrons for 3 months
AWAKE-like electron beam driven by SPS proton bunch. Assuming 109 electrons/bunch, would give 3 orders of magnitude increase.
M. Wing, Physics Beyond Colliders Kickoff Workshop, 7/Sep/2016, CERN
AWAKE
NA64

## Slide 47: Physics with an Electron-Proton or Electron-Ion Collider
Focus on QCD: Large cross sections  low luminosity enough (HERA level)
Many open physics questions !
 High energy ep collider: Ee up to O(50 GeV), colliding with LHC proton;
 e.g. Ee = 10 GeV, Ep = 7 TeV, √s = 530 GeV already exceeds HERA cm energy.
G. Xia et al., Nucl. Instrum. Meth. A 740 (2014) 173.
Create ~50 GeV electron beam within 50−100 m of plasma driven by SPS protons, But luminosity < 1030 cm-2 s-1.
LHeC-Like:
VHEeP: A. Caldwell and M. Wing, Eur. Phys. J. C 76 (2016) 463
VHEeP:
Choose Ee = 3 TeV as a baseline and with EP = 7 TeV yields √s = 9 TeV. Can vary.
Centre-of-mass energy ~30 higher than HERA.
Reach in (high) Q2 and (low) Bjorken x extended by ~1000 compared to HERA.
Opens new physics perspectives
Luminosity ~ 1028 − 1029 cm-2 s-1 gives ~ 1 pb−1 per year.

## Slide 48: Strategy for Run 2 and Beyond
Created a Run 2 Coordination Package
  Define goals, technology and work-packages
Gives opportunity to new institutes interested in joining.
CERN AWAKE Project Leader Mandate Extended:
  Leading the CERN AWAKE project towards and during Run 2
  Coordinating and organizing the general proton driven plasma wakefield acceleration studies at CERN
  Coordinating all resources associated with the AWAKE project and the proton driven plasma wakefield studies.
 Have a first proposal of Run 2 program ready by end 2017

## Slide 49: Summary
Great progress in installation and commissioning of AWAKE Run 1
On track for first AWAKE physics in 1st week in December 2016
On track with installation for electron acceleration phase in 2017
Run 2 and beyond:
  Preparation of proposal for Run 2
  Long-term prospects: Start to develop particle physics program that could be persued with an AWAKE-like beam.


