## Slide 1: 16 T Cosq DIPOLE Mechanical Analysis
STEFANIA FARINON
on behalf of INFN team:
G. Bellomo, P. Fabbricatore, B.CAIFFI, V. Marinozzi, M. Sorbi and G. Volpini

## Slide 2: Overview
Principal stresses and failure criteria
2D model: plain strain vs plain stress
2D mechanical optimization
Cosq 2D models:
CONFIGURATION 1 – vertical cut
CONFIGURATION 1I – horizontal cut
CONFIGURATION 1II – hybrid
CONCLUSIONS

## Slide 3: PRINCIPAL STRESSES
The principal stress s1, s2 and s3, defined for each single element, are those in which the stress-strain tensor is diagonal
(s3< s2< s1).
s3 ~ sx in block coil geometry
s3 ~ sq in cosq geometry
Von Mises stress is defined as:
Stress-strain tensor
In cartesian coordinate system
PRINCIPAL coordinate system: system in which the SS tensor is DIAGONAL

## Slide 4: STRESSES
sq
sVM
s1
s3
sr

## Slide 5: PLANE STRESS vs PLANE strain
Plain stress approximation is less conservative but more compatible with 3D simulation results.
Plane strain
Plane stress
Plane strain is a stress state that varies only in the X and Y directions. The strain in the Z direction is always zero, as are the XZ and YZ shear strains, since the boundaries are fixed.
Plane stress is a stress state that varies only in the X and Y directions. The stress in the Z direction is always zero, as are the XZ and YZ shear stresses.
Plane stress is generally used on flat, thin structures, where the deformation is assumed to be solely in the plane of the structure.

## Slide 6: 2d mechanical optimization
Cables undergo degradation if:
stress on conductors >150 MPa @room temperature;
stress on conductors > 200 MPa @cold;
stress on conductors > 150 MPa @cold after energization in the high field region → attention must be given in particular to first layers.
Tensile stress on the iron yoke at 4 K < 200 Mpa.
Contact pressure Ti pole-conductors > 2 MPa after energization at 16T.
41
435
829
1223
1616
2010
2404
2798
3192
3586
F[N]

## Slide 7: Material parameters
 | E modulus [GPa] (T=4K) | E modulus [GPa] (T=300K) | a (K-1) | νxy
Conductor | Ex=33 Ey=27.5 | Ex=30 Ey=25 | ax=3.08E-3/296 ay=3.36E-3/296 | 0.3
Steel | 210 | 191 | 2.8e-3/296 | 0.28
Iron | 224 | 204 | 2.0e-3/296 | 0.28
Aluminum | 79 | 72 | 4.2e-3/296 | 0.3
Copper | 110 | 100 | 3.4e-3/296 | 0.3
Resin | 27.5 | 25 | 2.5e-3/296 | 0.2
Titanium | 126.5 | 115 | 1.7e-3/296 | 0.3
+10%

## Slide 8: CONFIGURATION 1
ANSYS model
Al alloy
Iron
SS
key
C-clamp
Vertical cut
Bladder & key configuration
Key length= 20 mm, interference= 0.6 mm
Vertical cut both in the steel collar and in the iron yoke
C-clamp mandatory to achieve enough contact pressure at the pole, interference= 0.15 mm
55 mm
155 mm
40 mm

## Slide 9
B.Caiffi WP5 Coordination Meeting
Contact Pressure [Pa]
Contact Pressure [Pa]
Contact Pressure [Pa]
Cool Down
Assembly
Energization
Contact pressure and principal stress
Azimuthal Stress s θ [Pa]
Azimuthal Stress s θ[Pa]
Azimuthal Stress s θ [Pa]
s θ peak= -182 MPa
s θ peak=-195 MPa
sθ peak= -111 MPa

## Slide 10: CONFIGURATION 2
Horizontal cut
Al alloy
key
Bladder & key configuration
Key length= 20 mm, interference= 0.4 mm
Horizontal cut both in the steel collar and in the iron yoke
Iron
SS
45 mm
160 mm
30mm

## Slide 11: Contact pressure and principal stress
s θ peak=-206 MPa
s θ peak= -232 MPa
sθ peak= -97 MPa
Contact Pressure [Pa]
Contact Pressure [Pa]
Contact Pressure [Pa]
Cool Down
Assembly
Energization
Azimuthal Stress s θ [Pa]
Azimuthal Stress s θ[Pa]
Azimuthal Stress s θ [Pa]

## Slide 12: CONFIGURATION 2
Peak stress due to the edge
IVth layer shifted upward by 1 mm
IIIrd and IVth layers shifted upward by 1 mm
A
B

## Slide 13: Contact pressure and principal stress
s θ peak= -225 MPa
s θ peak=-187 MPa
sθ peak= -90 MPa
Contact Pressure [Pa]
Contact Pressure [Pa]
Contact Pressure [Pa]
Cool Down
Assembly
Energization
Azimuthal Stress s θ [Pa]
Azimuthal Stress s θ[Pa]
Azimuthal Stress s θ [Pa]

## Slide 14
Cable 1 (inner) | Cable 2 (outer)
22 | 36
1.1 mm | 0.712 mm
13.2 mm | 13.5mm
1.892 mm | 1.225 mm
2.072 mm | 1.343 mm
0.15 mm | 0.15 mm
0.5° | 0.5°
0.85 | 2.1
11200 A | 11200 A
1167 A/mm2 | 1154 A/mm2
86% | 86%
 | Cable 1 (inner) | Cable 2 (outer)
Strand number | 22 | 36
Strand diameter | 1.1 mm | 0.712 mm
Bare width | 13.2 mm | 13.5mm
Bare inner thickness | 1.892 mm | 1.225 mm
Bare outer thickness | 2.072 mm | 1.343 mm
Insulation | 0.15 mm | 0.15 mm
Keystone angle | 0.5° | 0.5°
Cu/NCu | 0.85 | 2.15
Operating current | 11180 A | 11180A
Copper current density | 1165 A/mm2 | 1143 A/mm2
Operating point on LL (1.9 K) | 86% | 86%
16T-22b-36-optd6f7
Wedge minimum
thikness: 0.86 mm
In LHC: 0.70 mm
In D11: 0.98 mm
Turn number:
Layer 1: 13
Layer 2: 20
Layer 3: 30
Layer 4: 38
Tot: 202/ap.
Field harmonics < 1 unit

## Slide 15: Tensile stress in the iron
Tensile stress peak in the iron (s1 peak) ~ 350 MPa

## Slide 16: CONFIGURATION 3
60 mm
150 mm
45 mm
Vertical cut
Horizontal cut
Bladder & key configuration
Key length= 20 mm, interference= 0.5 mm
Horizontal cut in the steel collar
→greater contact pressure at the pole
Vertical cut in the iron yoke
→smaller tensile stress on the iron
Iron
SS
Al alloy

## Slide 17: Contact pressure and principal stress
B.Caiffi WP5 Coordination Meeting
Cool Down
Assembly
Energization
s θ peak=-226 MPa
s θ peak= -219 MPa
sθ peak= -107 MPa
Contact Pressure [Pa]
Contact Pressure [Pa]
Contact Pressure [Pa]
Azimuthal Stress s θ [Pa]
Azimuthal Stress s θ[Pa]
Azimuthal Stress s θ [Pa]

## Slide 18: Contact pressure and principal stress
B.Caiffi WP5 Coordination Meeting
Cool Down
Energization
s θ peak= -216 MPa
s θ peak=-210 MPa
sθ peak= -102 MPa
Contact Pressure [Pa]
Contact Pressure [Pa]
Contact Pressure [Pa]
Assembly
Azimuthal Stress s θ [Pa]
Azimuthal Stress s θ[Pa]
Azimuthal Stress s θ [Pa]

## Slide 19: Conclusions
The mechanics of the 16T costheta dipole has been investigated, giving particular importance to the fulfillment of the following requirements: stress on conductors <150 MPa @room temperature, stress on conductors < 200 MPa @cold and contact pressure Ti pole-conductors > 2 MPa after energization.
Different configurations were considered, among those the more promising were presented:
CONFIGURATION 1- vertical cut in the steel collar and the in the iron yoke
Bladder&Key + C-clamp mandatory to achieve contact pressure at the pole
Almost fulfill stress limits on the conductor
Good contact pressure at the pole for all the layers
CONFIGURATION II – horizontal cut in the steel collar and in the iron yoke
Almost fulfill stress limits on the conductor
Good contact pressure at the pole for all the layers
Very high values for tensile stress on the iron (350 MPa)
CONFIGURATION III- hybrid solutions, horizontal cut in the steel collar and vertical cut in the iron yoke
Almost fulfill stress limits on the conductor
Good contact pressure at the pole for all the layers