## Slide 1
NA61/ perspectives for
open charm
measurements
M. Deveaux, Goethe Universität Frankfurt am Main
on behalf of the NA61/SHINE collaboration

## Slide 2: Introduction NA61/SHINE
Fixed target hadron spectrometer (8 TPCs)
Coverage of the full forward hemisphere
At CERN/SPS
Hadrons (π, K, p) and ions (Be, Ar, Xe, Pb)

## Slide 3: Open charm measurements with NA61/Shine
melting has been proposed as probe for deconfinement and the temperature of the fireball.
Most charm is produced as open charm.
Direct A-A → Open Charm + X measurements are needed for precise understanding.
H. Satz, arXiv:1303.3493v2 [hep-ph] 12 Apr 2013
Idea: Add vertex detector and detect open charm (D-mesons).
T. Matsui and H. Satz, 1986, Phys. Lett. B 178, 416

## Slide 4: Requirements on the vertex detector
Reconstructing open charm requires:
Excellent secondary vertex
resolution (~ 50 µm)
=> Excellent spatial resolution (~5 µm)
=> Very low material budget (few 0.1 % X0)
=> Detectors in helium
Primary Beam: 150 AGeV Pb Ions
Primary
vertex
Secondary
vertex
Short lived particle
D0 (ct = ~ 120 µm)
Detector 1
Detector2
Target
(Pb)
z
Reconstruction concept for open charm
A good time resolution to distinguish
the individual collisions
Good radiation tolerance
NA61 Pb+Pb collision

## Slide 5: Open Charm detection – Feasibility studies
5 cm
10 cm
15 cm
20 cm
 | Requirement | MIMOSA-26
Stations | 4 @ 5,10,15,20 cm | --
Spatial resolution | ~5 µm | 3.5 µm
Rate capability (156 AGeV Pb+Pb) | 80 Hz trigger 2 kHz coll. rate | OK
Time resolution | < 500 µs | 115.2 µs
Material budget | few 0.1% X0 | 0.05% X0
Simulated performance with NA61
Ideal - ID
No - ID
Simulation: ~ 1d beam
Simulation: D0 → K + π seems feasible, limited to Pb+Pb at top energy
MIMOSA-26
Simulation: Yasir Ali et. all, ACTA PHYSICA POLONICA B, Vol. 44 (2013)
Sensor: M. Deveaux et al., JINST 6.02 (2011): C02004

## Slide 6: Feasibility studies: Small Acceptance VD
Small acceptance VD
Observation: 16 out of 125 sensors cover:
35% of NA61 acceptance for D0+D0.
Full forward rapidity.
Build Small Acceptance Vertex Detector (SAVD)
~125 sensors
16 sensors
No cuts
Full VD
Small VD

## Slide 7: Sensors - tolerance to heavy ions
Sensors in first VD station exposed to direct beam ions.
Radiation damage?
Literature suggests:
Pb-hardness factor
Should be ok.
No empiric experience available  Test it
Ionizing and non-ionizinig radiation hardness OK, but heavy ions?
M. A. Xapsos, et al., IEEE TNS Vol. 51 (2004), P. 3250-3254
6 mm

## Slide 8: Sensors - tolerance to heavy ions
Location:
200m upstream
NA61 target.
Result: No significant integrated radiation damage.
Radiation tolerant positioning table
MIMOSA-34THR
Tower/Jazz 0.18µm CMOS
Dosimetry:
4x4mm² scintillator
Dose reached:
1.2x1010 Pb/cm² (30A GeV/c)

## Slide 9: Sensors - tolerance to heavy ions
MIMOSA-26 operated in direct 30A GeV/c ion beam for ~24h
Observation:
Pb-Ions generate clusters of ~200 fired pixels
No obvious loss of functionality.
Observed 3 latch-ups. One persisted several hours before discovery. Chip recovered after power cycling.
Pb-ion
 Sensor surprisingly robust
Worry: Losses of sensors observed in Au+Au @ STAR

## Slide 10: Official proposal to SPSC (Dec. 2015)

## Slide 11: Design iterations
5 cm
10 cm
15 cm
20 cm

## Slide 12: SAVD – External building blocks
MIMOSA-26AHR
1152x576 pixels of 18.4x18.4 µm²
3.5 µm resolution, 0.05% X0
Readout time: 115.2 µs
50 µm thin
PICSEL Group, IPHC Strasbourg

## Slide 13: SAVD – External Building blocks
Sensor integration, FEE,
initial firmware: CBM – MVD,
GU Frankfurt
DAQ: TRB-3 FPGA board
Project coordination, mechanics, NA61 software, system integration JU Krakow, AGH Krakow
ALICE ITS ladder
Ultra light carbon fibre
< 0.3 X0 incl. water cooling
St. Petersburg, CERN

## Slide 14: SAVD – External building blocks
CBM Micro Vertex Detector Prototype
Sensor integration techniques
Flex print cables, Front end board
Local DAQ (software/hardware)
Incl. TRB3 FPGA Board
Goethe Universität Frankfurt am Main, GSI

## Slide 15: System integration
C-frame
Helium box
Cooling
Moving engine
Services
DAQ-integration
Software
System integration and project leadership:
Jagiellonian University Krakow
supported by AGH Krakow, WUT Warsaw

## Slide 16: Detector installation 6th Dec. 2016
Guest device:
ALICE-ITS ladder
Commissioning run,
Pb+Pb, 150A GeV/c
Hope: See D0-peak

## Slide 17: First results: Jura Arm (Run 42, 7th December)
Observations:
15 over 16 sensors operational.
~10% corrupted frames in one arm (software issue, fixed meanwhile).
Detector worked for 1 week without damage.
Statistics:
Min-Bias trigger used (required for other NA61 detector tests).
~130k central events 150 A GeV/c Pb+Pb (after QA-cuts, preliminary).
Beam
Heavy ion hits
Mirrored view

## Slide 18: First results (Work in progress)
Spatial resolution (Hit – track): ~ 6µm
Correlation Projectile Spectator Detector -VD
First results look promising – More to come.
Preliminary
alignment
Primary
vertex
visible.
Target
SAVD-NA61
sync. works
SAVD-TPC track
matching successful

## Slide 19: Steps to the future: SHINE-2020 (1 kHz Pb+Pb)
ALICE - MFT
ALICE - ITS
Integration concept:
Spatial resolution
Material budget
Time resolution
OK
Tolerance to Heavy ions
 Test in Nov. 2017
Idea: Build detector components in synergy with ALICE-upgrade
Common technological platform – minimize modifications
Common mass production – minimize cost and efforts
To be decided
Use present ALICE TPC electronics to upgrade TPCs
Upgrade VD to obtain full acceptance and 1kHz rate
Sensor: ALPIDE

## Slide 20: Steps toward the future
 | SAVD (80Hz Pb+Pb) | VD-2020 (1kHz Pb+Pb)
2017 | Commissioning improved software/hardware Data taking p+Pb Data taking Xe+La Data analysis Pb+Pb 2016 | Test of ALPIDE in Xe-beam (robustness) Preparation of proposal for NA61 2020
2018 | Data taking Pb+Pb 2018 Data analysis Xe+La 2017 | Option: Upgrade/complement SAVD with ALPIDE-ladders
LS2 | Decommissioning Data analysis Xe+La 2018 | Construction
2020 (After LS2) |  | Commissioning/Data taking at 1 kHz trigger rate.

## Slide 21: Summary and conclusion
Adding a vertex detector to NA61/SHINE will allow for first
direct open charm measurements in A-A collision systems
at SPS top energy.
A Small Acceptance Vertex Detector (SAVD) has been built:
16 MIMOSA-26 CMOS sensors (32 cm², 10 MPixel).
ALICE ITS ladders (modified) <0.4% X0 / layer.
CBM-MVD DAQ and integration (adapted).
A commissioning beam time was performed in Dec. 2016. Hope
to extract open charm peak.
The SAVD will continue regular operation until end 2018 (LS 2).
Aim for upgrade during Long Shutdown 2

## Slide 22: The VD - team
Krakow:
JU: P. Staszel (Coordinator), Y. Ali, D. Larsen, M. Jablonski, A. Merzlaya R. Planeta
AGH: M. Baszczyk, P. Dorosz, W. Kucewicz, L. Mik
GU Frankfurt: M. Deveaux, M. Gazdzicki, M. Koziel, A. Snoch
Thanks to: P. Klaus, J. Michel, M. Wiebusch
Warsaw
WUT: W. Brylinski, D. Tefelski
UW: A. Aduszkiewicz,
St. Petersburg State University: G. Feofilov, S.Igolkin, T.Lazareva, V.Kovalenko,
A. Merzlaya, V.Vechernin
ETH Zürich: S. Di Luise
Thanks to:
And many others…
Thanks to:
PICSEL Group
TRB - collaboration

## Slide 23
50
100
150
200
200
400
600
800
1000
PSD energy [ADU]
Clusters [1]