Parameterization-based tracking
for the P2 experiment
Iurii Sorokin
PRISMA Cluster of Excellence /
Institute for Nuclear Physics, University of Mainz
CTD/WIT 2017, LAL (Orsay)

---
The Weak Mixing Angle
color red %theta_W
defnies the relative strength of electromagnetic and weak interactions

---
The Weak Mixing Angle
color red %theta_W
defnies the relative strength of electromagnetic and weak interactions
Standard Model

---
The Weak Mixing Angle
color red %theta_W
defnies the relative strength of electromagnetic and weak interactions
With a dark Z boson
arXiv:1507.00352 [hep-ph]
Standard Model

---
measurement
color red %theta_W
Detector
155 MeV
e- beam
        polarized
Liquid H2
target
elastic scattering on protons

---
measurement
color red %theta_W
Detector
155 MeV
e- beam
        polarized
Liquid H2
target
elastic scattering on protons
A_{PV}~ `=` { color blue {N downarrow} - color green { N uparrow } } over { color blue {N downarrow} + color green { N uparrow } } ~ `=` { color blue {%sigma downarrow} - color green { %sigma uparrow } } over { color blue {%sigma downarrow} + color green { %sigma uparrow } } `=` ~ { {G_F Q^2 } over {4 sqrt{2} %pi %alpha }} ( color red {Q_W} - F(Q^2))
color red Q_W = 1 - 4 cdot {{sin^2( color red %theta_W )} }
proton weak charge
Weak mixing angle

---
measurement
color red %theta_W
Detector
155 MeV
e- beam
        polarized
Liquid H2
target
elastic scattering on protons
A_{PV}~ `=` { color blue {N downarrow} - color green { N uparrow } } over { color blue {N downarrow} + color green { N uparrow } } ~ `=` { color blue {%sigma downarrow} - color green { %sigma uparrow } } over { color blue {%sigma downarrow} + color green { %sigma uparrow } } `=` ~ { {G_F Q^2 } over {4 sqrt{2} %pi %alpha }} ( {Q_W} - F(Q^2))
~ O (10–8)
nospace{ %DELTA A_{PV} } ~ `=` 1 over sqrt{ color blue {N downarrow} + color green { N uparrow } } ~ `<`` color red bold {6 cdot 10^{-10 }}
(2% relative)
=>
10 000 hours at
1011 events/s
color blue {N downarrow} + color green { N uparrow } ~ `approx` color red bold { 3 cdot 10^{18} }

---
The MESA accelerator
Mainz Energy-recovering Superconducting Accelerator
extracted beam mode:
150 µA @ 155 MeV
energy-recovering mode:
1 mA (later 10 mA)
@ 105 MeV

---
P2 setup
Integrating
Cherenkov
Detector
Tracking Planes
Sheild
Target
e–
γ (Brems-
strahlung)
Magnet

---
Why is tracking necessary?
“Measure” actual Q2 distribution
e-
Liquid H2 Target
60 cm

---
Why is tracking necessary?
“Measure” actual Q2 distribution
e-
Liquid H2 Target
A_{PV}~ `=` { color blue {N downarrow} - color green { N uparrow } } over { color blue {N downarrow} + color green { N uparrow } } ~ `=` { color blue {%sigma downarrow} - color green { %sigma uparrow } } over { color blue {%sigma downarrow} + color green { %sigma uparrow } } `=` ~ { {G_F color red Q^2 } over {4 sqrt{2} %pi %alpha }} ( {Q_W} - F(color red Q^2))
60 cm

---
Why is tracking necessary?
Validate the acceptance, alignment, and magnetic filed map
The magnetic field is anyways necessary,
even without tracking

---
Why is tracking necessary?
Montor the beam and the target conditions (e.g. boiling)
Continuously, at full rate,
but with small duty cycle.
On-line analysis

---
MuPix HV-MAPS
   ▸	pixel size 80 x 80 µm2 (latest version)
   ▸	digital readout
   ▸	time resolution 11 ns (measured)
   ▸	rate capability:
2.5 MHz/chip tested (DAQ limited)
30 MHz/chip
 or 280 MHz/cm2
   ▸	efficiency > 99% demonstrated
Originally developed for the Mu3e experiment, MuPix fits excellent to the needs of P2.
 Peric, Ivan Nucl.Instrum.Meth. A582 (2007) 876-885
Augustin, Heiko et al. Nucl.Instrum.Meth. A845 (2017) 194-198
theoretical
MuPix7
on a
readout board
Beam test of
4- and 8-plane
MuPix telescopes
at PSI (2016)

---
P2 setup
Integrating
Cherenkov
Detector
Tracking Planes
Sheild
Target
e–
γ (Brems-
strahlung)
Magnet
2 layers
HV-MAPS

---
GEANT4 simulation
(only relevant components displayed)
beam

---
Reconstruction frame (45ns)
at 1% beam rate
without the background from the beam
γ
e–
12
hits

---
Reconstruction frame (45ns)
at 1% beam rate
without the background from the beam
12
hits
γ
e–
10 cm
10 cm

---
Reconstruction frame (45ns)
at the full beam rate
with the background from the beam
1600
hits
γ
e–
10 cm

---
y-z view
e– beam
target
2 cm
2 cm
54 cm

---
Conventional track following
track
seed
e– beam
target

---
Conventional track following
track
seed
hit search window
e– beam
target

---
Conventional track following
1
2
e– beam
target

---
Conventional track following
extrapolation
e– beam
target

---
Conventional track following
B field
∫...dz
e– beam
target

---
Parameterization-based track finding
3
0
1
2
x2, y2
f( x2, y2, x3, y3 )
x3, y3
3rd order
polynomial
e– beam
target

---
Extrapolation
?
e– beam
target

---
Extrapolation with constraints
Search
window
e– beam
target

---
Using reference tracks
instead of extrapolation
Search
window
e– beam
target

---
Reference tracks:
 ▸	from MC
 ▸	brute-force reconstruction at low rate; select by χ2.
e– beam
target

---
How to construct the parameterizations?

---
Search window for plane 2
3
0
1
2
f(x3, y3)
x3, y3
?
e– beam
target

---
Search window for plane 2
3
0
1
2
 f(R3)
?
R3
e– beam
target

---
Take reference tracks
with the given R3
(with some tolerance)
 f(R3)
Optimal
search window
for the given R3
R3
e– beam
target

---
Collect large number of
reference tracks
e– beam
target

---
Group tracks
in R3 bins
R3
R3
R3

---
R3
R3
R3

---
R3
R3
R3

---
Search window for every R3 bin:
R3
R3
R3
Δy'32
Δy'32
Δy'32
Δx'32
position of hit 2
 relative to hit 3
position of hit 2
 relative to hit 3
Δx'32
position of hit 2
 relative to hit 3
Δx'32

---
Δy'32
Δy'32
Δy'32
R3 = value
R3 = value
R3 = value
Δx'32
Δx'32
Δx'32

---
Extract window position and size:
Δy'32
Δy'32
Δy'32
R3 = value
R3 = value
R3 = value
Δx'32
Δx'32
Δx'32
R3	xPOS	yPOS	xSIZE	ySIZE	φROT
...	...	...	...	...	...
	◾◾◾◾	◾◾◾◾	◾◾◾◾	◾◾◾◾	◾◾◾◾
	◾◾◾◾	◾◾◾◾	◾◾◾◾	◾◾◾◾	◾◾◾◾
	◾◾◾◾	◾◾◾◾	◾◾◾◾	◾◾◾◾	◾◾◾◾
…	...	...	...	...	...
value
value
value

---
R3	xPOS	yPOS	xSIZE	ySIZE	φROT
...	...	...	...	...	...
	◾◾◾◾	◾◾◾◾	◾◾◾◾	◾◾◾◾	◾◾◾◾
	◾◾◾◾	◾◾◾◾	◾◾◾◾	◾◾◾◾	◾◾◾◾
	◾◾◾◾	◾◾◾◾	◾◾◾◾	◾◾◾◾	◾◾◾◾
…	...	...	...	...	...
value
value
value

---
Fit
R3	xPOS	yPOS	xSIZE	ySIZE	φROT
...	...	...	...	...	...
	◾◾◾◾	◾◾◾◾	◾◾◾◾	◾◾◾◾	◾◾◾◾
	◾◾◾◾	◾◾◾◾	◾◾◾◾	◾◾◾◾	◾◾◾◾
	◾◾◾◾	◾◾◾◾	◾◾◾◾	◾◾◾◾	◾◾◾◾
…	...	...	...	...	...
value
value
value
xPOS=pol3(R3)
R3
xPOS

---
Fit
R3	xPOS	yPOS	xSIZE	ySIZE	φROT
...	...	...	...	...	...
	◾◾◾◾	◾◾◾◾	◾◾◾◾	◾◾◾◾	◾◾◾◾
	◾◾◾◾	◾◾◾◾	◾◾◾◾	◾◾◾◾	◾◾◾◾
	◾◾◾◾	◾◾◾◾	◾◾◾◾	◾◾◾◾	◾◾◾◾
…	...	...	...	...	...
value
value
value
φROT=pol3(R3)
yPOS=pol3(R3)
xSIZE=pol3(R3)
ySIZE=pol3(R3)
xPOS=pol3(R3)
R3
R3
R3
R3
R3
Fake plot.
For illustration
only.
xSIZE
ySIZE
yPOS
xPOS
φROT

---
Search window for plane 2
3
0
1
2
xPOS=pol3(R3)
yPOS=pol3(R3)
xSIZE=pol3(R3)
ySIZE=pol3(R3)
φROT=pol3(R3)
R3
e– beam
target

---
Search window for plane 1
3
0
1
2
f(Δx'23, Δy'23, R3)
Δx'23, Δy'23
R3
e– beam
target

---
R3	Δx'23	Δy'23	xPOS	yPOS	xSIZE	ySIZE	φROT
▪▪▪	▪▪▪	▪▪▪	▪▪▪	▪▪▪	▪▪▪	▪▪▪	▪▪▪
▪▪▪	▪▪▪	▪▪▪	▪▪▪	▪▪▪	▪▪▪	▪▪▪	▪▪▪
▪▪▪	▪▪▪	▪▪▪	▪▪▪	▪▪▪	▪▪▪	▪▪▪	▪▪▪
bin by
{R3, Δx'23, Δy'23 }
Fit (in 3D)
determine the search windows
     xSIZE	= pol3( R3, Δx'23, Δy'23 )
     ySIZE	= pol3( R3, Δx'23, Δy'23 )
     xPOS	= pol3( R3, Δx'23, Δy'23 )
     yPOS	= pol3( R3, Δx'23, Δy'23 )
     φROT	= pol3( R3, Δx'23, Δy'23 )

---
Search window for plane 0
3
0
1
2
Δx'13, Δy'13
f(Δx'13, Δy'13, R3)
R3
e– beam
target

---
distance
½ window size
plot:
Relative distance from the center
of the search window
search window
reference
track

---
Relative distance from the center
of the search window
search window
e– beam
target

---
Relative distance from the center
of the search window
Plane 0
search window
Search window
Plane 2
Plane 1
Search window
Search window
Overall about 90% efficiency (depending on settings).

---
Performance
Number of candidates per signal track
Fixed-size
search windows
(same efficiency)
N candidates
N signal
Parameterized
search windows
ideal

---
Performance
Number of candidates per signal track
Fixed-size
search windows
(same efficiency)
N candidates
N signal
Parameterized
search windows
ideal

---
Parameterization instead of fitting
Fit replaced by parameterization:
momentum = pol3( R3, ΔR31, Δφ31 )
Rigorous fit
Using GBL fit within the GENFIT framework
Kleinwort C. General Broken Lines as advanced track fitting method http://dx.doi.org/10.1016/j.nima.2012.01.024
GBL:
Rauch J., Schlüter T. GENFIT — a Generic Track-Fitting Toolkit
https://doi.org/10.1088/1742-6596/608/1/012042
GENFIT:

---
Summary
Parameterization-based tracking:
 –	replaces rigorous model calculations
by simple analytical parametric functions
– parameters can be tuned based on
real data or model (MC or deterministic with covariance)
–	enables accurate, efficient, and very fast track finding
–	can be used to estimate the kinematic parameters
–	works well in P2 due to narrow momentum range

---
Search window efficiency
using reconstructed tracks as a reference gives equally good results!

---
The Weak Mixing Angle
color red %theta_W
left( stack{{ color blue %gamma }# {color blue Z^0} } right) ` = ` left( matrix{ { cos color red %theta_W} # { sin color red %theta_W} ## {- sin color red %theta_W} # { cos color red %theta_W} } right) ` left( stack{{ color green B^0 }# {color green W^0} } right)
observable
fundamental
defnies the relative strength of electromagnetic and weak interactions