## Slide 1
High efficiency RF power sources.
I. Syratchev, CERN.

## Slide 2
Accelerator tunnel at the European XFEL (Picture: DESY)
Accelerator tunnel at the LHC (Picture: CERN)
‘TrueBeam’ X-ray radiotherapy
(Picture: Varian)
Accelerator tunnel at the C-band XFEL (Picture: PSI)
Every modern accelerator needs RF power sources to provide the electromagnetic field for the charged particle acceleration.

## Slide 3
The accelerators technology is very diverse and could require the RF signals in a wide range of the frequencies (few 100 MHz – 12 GHz), peak power levels (few 100 kW – 100 MW) and pulse lengths (CW -100ns).
The klystron amplifiers technology is the one that covers almost all RF frequency/power demands of the modern accelerators.
12 GHz, 50MW/SLAC-CLIC
3 GHz, 60MW/SLAC
6 GHz, 50MW/PSI
1.3 GHz, 10MW/DESY
0.7 GHz, 1.5MW/ESS
MBK
0.4 GHz, 0.3MW/LHC
Electro vacuum devices for science
USA
France
Japan
LHC
LHC
FCCee
CLIC
ILC
DESY
PSI
SACLA
SLAC
CLIC’k
SLAC-BF
Industrial/Medical
PAL
e-rings
injectors
IOT
single beam
SSA tower
Magnetron
(oscillator)
Frequency, GHz
Peak power, MW
electron & proton rings
SC e/p Linacs
electron Linacs
high intensity
high gradient
Klystrons
Pulsed
Continuous Wave
MBK
FNAL
Tetrode
KEK
NLC
J-PARC
ESS
CEPC

## Slide 4
1948. The first multi-megawatt (33 MW) S-band klystron ITT 2960 Mark III (Stanford, USA)
M. Chodorow
The klystrons have been used in the particle accelerators for more than 7 decades.
The experimental results from hundred’s of different devices have shown that higher efficiency is associated with lower perveance.
Accounting for technological and cost reasons (µA/V1.5>0.25), the 73% efficiency was predicted to be the utmost limit.
S-band
Industry
X-CERN
50 MW
X-CERN
6 MW
industrial empirical limit
X-KEK
PPM, 50 MW
L-MBK ILC,10 MW
L-MBK CLIC, 20 MW
UHF-LHC
0.3 MW
Klystrons for science
L-ESS,1.5 MW
UHF-B-factory
1.25 MW
(µA/V1.5)
ITT 2960
33 MW
L-SNS, 0.55 MW
S-SLAC
65 MW
Efficiency performance for the selected commercial klystrons. State of art.
S-SLAC
150 MW

## Slide 5
105 MW
Average RF power needs of the large-scale HEP Accelerators Projects
The klystron efficiency impact on the CLIC 3TeV power consumption.
Example of the efficiency upgrade from 70% to 85%.
Potential saving are 2.53 TWh in 10 years (152 MCHF in 10 years).
Reduced environmental impact (cooling and ventilation)
Reduced installation cost (stored energy in modulators).
Reduced maintenance cost (klystron life time).
R&D on increasing the useable efficiency is worth every penny/cent invested!
 | Klystron eff. 70% | Klystron eff. 85% | Difference
RF power needed for 3TeV CLIC | 180 MW |  | 
DC input power | 257 MW | 211 MW | -46MW
Waste heat | 77 MW | 31 MW | -46MW
Annual consumption (5500 h assumed) | 1413 GWh | 1160 GWh | -253 GWh
Annual cost (60 CHF/MWh assumed) | 84.8 MCHF | 69.6 MCHF | -15.2 MCHF
Electricity installation dimensioned for | 257 MW | 211 MW | -18%
CV installation dimensioned for | 77 MW | 31 MW | -60%
3.0 TeV CLICe+e- ; pulsed, 1.0 GHz, PRF total = 180 MW

## Slide 6
E field expansion in the drift tubes causes beam reacceleration when it leaves the output cavity.
Ohmic loses are proportional to the operating frequency.
Space charge depression is a partial conversion of the beam kinetic energy into the potential DC energy of beam traveling in the drift tube.
Bunch saturation is optimal, when all the elections populate only the useful RF phase bucket leaving the anti-bunch empty.
Bunch congregation is a normalized elections velocity spread along the bunch. It has an optimal value for every given bunch length.
Bunch stratification is a radial dependence of the bunch length and congregation. The ideal bunch should not have such a dependency.
Radial bunch expansion happens during beam deceleration in the output cavity in the presence of external solenoidal magnetic field.
Reflected electrons could be generated if some of the above effects are not balanced.
SLAC B-factory CW
0.478GHz, 1.25 MW
The factors limiting efficient RF power extraction from the bunched beam in RF cavity
bunch
<- arrival time (t/w)
Velocity Ve/c
Efficiency 61%
Arrival plane
0
2
Bunch phase space in the vicinity of the klystron output cavity
Driven by klystron general parameters.
Driven by RF design and space charge effects.

## Slide 7
The ultimate power extraction efficiency in the linear beam devices
Example of 0.8 GHz FCCee klystron. Voltage 133 kV, Current 12.6 A (µP=0.26 µA/V3/2)
Effect of the bunch length
Fully saturated bunch with optimised congregation
Optimised congregation for the different bunch lengths.
Optimum at L bunch  RF /3
Ultimate limit
90.1 %
E field expansion in the drift tubes
Ohmic Losses
Space charge depression
Bunch saturation
Bunch congregation
Bunch stratification
Radial bunch expansion
High efficiency Klystrons design objectives
Optimised RF bunching circuit
Ultimate limit

## Slide 8
The new bunching technologies have been developed to balance the space charge forces and RF impedances in order to provide the full bunch saturation with an optimal congregation:
Core Oscillation Method (COM) relies on the de-bunching/bunching alternation between space-charge forces and impedances of the RF cavities. COM requires the long bunching circuit. Cost effective solution for the high frequency devices.
Core stabilization Method (CSM) implies the RF cavities with higher harmonic number (2nd and 3rd) that allows the fast collecting of the peripheral electrons into the bunch. Most suitable for the low frequency devices.
The High Efficiency International Klystron Activity has been initiated at CERN (2013-2017) targeting the improvement of klystron efficiency performance through the development of the new electron bunching methods and the new reliable simulation tools adopted for the massive optimization processes.
The fast and reliable computer code for the klystron simulations (KlyC) has been developed at CERN. KlyC is in a public domain and now is adopted by Labs, Universities and industrial partners in Europe, USA, Japan, China, Russia and India.
Using the new tools and methods, a number of the high efficiency klystrons for the large scale accelerators (LHC, FCC and CLIC) has been developed at CERN and few completed designs have already been communicated to the industry for the technical evaluation and prototyping.

## Slide 9
High Efficiency (80%) 1.4 MW, 0.8 GHz, CW FCCee CSM klystron (CERN/Thales).
bunch
<- arrival time (t/w)
Velocity Ve/c
Arrival plane
0
2
Bunch phase space in the vicinity of the klystron output cavity
Particle-In cell simulations (MAGIC 2D)
79.9%
79.7%
1.5D
Particle-In cell simulations (CST 3D)
79.5%

## Slide 10
Parametric Scaling Procedure. High Efficiency (70%) 350kW, 0.4 GHz, LHC klystron upgrade.
Design of any new klystron is rather time consuming. It requires high level of the related experience/expertise.
The PSP was developed at CERN as a set of semi-analytical procedures that allow to scale the existing klystron design to the new one (beam power, frequency and perveance) and to preserve the bunching processes.
Design cycle ~ 6 month
Design cycle ~ 2 weeks
 | FCC
Frequency, GHZ | 0.8
Beam power, MW | 1.68
Perveance, | 0.26
RF power, MW | 1.34
Efficiency, % | 80
 | LHC | LHC/Thales
Frequency, GHZ | 0.4 | 0.4
Beam power, MW | 0.5 | 0.5
Perveance, | 0.72 | 0.72
RF power, MW | 0.35 | 0.30
Efficiency, % | 70 | 60
Cut-off view of the LHC CSM klystron
Re-used housing, electron gun and solenoid

## Slide 11
High Efficiency (65%) 50 MW, 12 GHz, CLIC COM klystrons (CERN/CPI).
Bunch phase space in the vicinity of the klystron output cavity
<- arrival time (t/w)
Velocity Ve/c
0
2
Arrival plane
 | VKX-8311A | HEX COM_2M/CERN | HEX COM/CERN
Voltage, kV | 410 | 400 | 400
Current, A | 310 | 190 | 190
Frequency, GHz | 11.994 | 11.994 | 11.994
Peak power, MW | 50 | 48.8 | 49.8
Sat. gain, dB | 48 | 58 | 58
Efficiency, % | 40 | 67.7KlyC/ 64.2CST | 68.7KlyC/ 65.5CST
Life time, hours | 30 000 | 85 000 | 85 000
Solenoidal magnetic field, T | 0.6 | 0.35 | 0.35
RF circuit length, m | 0.32 | 0.39 | 0.86
VKX-8311A
HEX COM_2M; 0.35T; 64.2%
HEX COM_2M
67.7%

## Slide 12
Tailored Technologies. High Efficiency (85%) 24 MW, 1 GHz, CLIC MBK/2S klystron.
Industrial CLIC MBK prototypes delivers ~70 % RF power production efficiency
Canon E37503
6 beams MBK
Thales TH1803
10 beams MBK
The new klystron bunching technologies cannot be directly adopted to the CLIC MBK:
COM requires very long (5m) RF circuit.
In CMS, the 3rd harmonic cavity is not compatible with MB-type cavities layout.
The CLIC MBK with two high voltage stages.
Electron efficiency measured in PIC simulations is 84%.
Bunching at a low voltage (high perveance). Very compact RF bunching circuit.
Bunched beam acceleration and cooling (reducing p/p) along the short DC voltage gap.
Final power extraction from high voltage (low perveance) beam. High efficiency.
Conceptual features:

## Slide 13
High Efficiency klystrons industrialization efforts.
The first ‘off shelf’ commercial 7.5 MW S-band (2.856 GHz) HE klystron by …….
Original design (5 cavities):
Voltage: 155 kV
Current: 109 A
Peak power: 7.5 MW
Efficiency: 45%
High efficiency COM upgrade (10 cavities):
Voltage: 140.2 kV
Current: 88 A
Peak power: 7.3 MW
Efficiency: 59.2%
Commercial prototype of the 50 MW HE X-band (11.424 GHz) COM klystron by BVERI (China)

## Slide 14
Efficiency
micro Perveance
Efficiency performance of the selected commercial klystrons and the new HE klystrons (July 2019).

## Slide 15
Special thanks to many colleagues from Labs, Universities and industry who have been actively involved into the high efficiency klystrons development:
T. Anno, A. Baikov, A. Beunas, O. Brunner, G. Burt, J. Cai, D. Constable, I. Guzilov, P. Hamel, V. Hill, A. Jensen, E. Jensen, T. Kimura, A. Leggieri, R. Kowalczyk, C. Lingwood, Z. Liu, R. Marchesin, C. Marrelli, J. Neilson, F. Peauger, J. Plouin, V. Teryaev, B. Weatherford…