## Slide 1: Cryogenic Engineering Conference Madison, WI
Experimental Effervescence Measurements of Nitrogen in Liquid Methane-Ethane Mixtures to Support an Extraterrestrial Submarine for Titan
Ian Richardson
July 10, 2017
Notes: Specifically Helium Dissolved in Liquid Hydrogen.

## Slide 2: Titan’s Cryogenic Environment
1. Titan is the only known body (other than Earth) within the Solar System with stable seas
  Stable hydrocarbon seas similar in size/depth as Great Lakes on Earth
  Liquid surface temperature 90-96 K; near freezing point of ethane and methane
  Seas ~96% Liquid (ethane or methane), 4% GN2
  Density variations of 30%

## Slide 3: Titan’s Cryogenic Environment
2. Only known moon with significant atmosphere
  Organic compounds accumulate to form thick haze, clouds
  1.5 atm, 95% GN2, 5% GCH4
  5x density of Earth
  14% of Earth’s gravity
3. GN2 solubility increases with increasing pressure, decreasing temperature and increasing mole fraction of methane
4. At Titan’s surface (95 K, 22 psia)
  15% dissolved GN2 in pure liquid methane
  3% dissolved GN2 in pure liquid ethane

## Slide 4: Titan Submarine
Light
X-Band Omni Antenna
Depth Sounder
Physical Properties Package
Meteorology Sensor
Surface Imager
Benthic Sample Acquisition
Side Scan Sonar Array
Doppler Velocimeter
Sonar Transducer
X-Band Phased Array Antenna
Hydrodynamic Skin
Thrusters
Ballast Tank
Stabilizer
Science
Control/Propulsion
Communication
1200 kg submarine
6m long x 1m wide x 2m high

## Slide 5: Design Challenges
When will effervescence occur?
How will the nitrogen bubbles behave?
What affects will nitrogen bubbles have on the ballast systems, scientific instruments, and propellers?

## Slide 6: Experimental Apparatus

## Slide 7: Effervescence Results
- Likelihood of effervescence increases with increased nitrogen content.
Data Point | CH4 [mol %] | C2H6 [mol %] | N2 [mol %] | Pressure [bar] | Sea Temp. [K] | Heater Surface Temp. [K] | Heat Flux at Bubble Incipience [W/m2]
1 | 87.1 | 0.0 | 12.9 | 1.546 | 96.2 | 101.4 | 10830
2 | 87.7 | 0.0 | 12.3 | 1.65 | 93.5 | 100.2 | 13029
3 | 82.5 | 0.0 | 17.5 | 1.782 | 95.9 | 99.6 | 3257
4 | 72.3 | 0.0 | 27.7 | 4.53 | 97.0 | 104.1 | 17915
5 | 0.0 | 97.3 | 2.7 | 1.73 | 103.6 | 118.7 | 28810
6 | 0.0 | 94.6 | 5.4 | 4.41 | 92.5 | 107.2 | 24559
7 | 50.6 | 44.2 | 5.2 | 1.85 | 97.8 | 108.7 | 18729
8 | 57.5 | 37.2 | 5.3 | 1.561 | 92.7 | 107.8 | 26448
9 | 47.6 | 30.9 | 21.5 | 3.21 | 91.9 | 97.8 | 11074
10 | 24.9 | 48.3 | 26.8 | 3.44 | 91.9 | 94.2 | 2475
11 | 27.0 | 61.4 | 11.6 | 3.85 | 91.8 | 98.8 | 10244
12 | 30.2 | 63.9 | 5.9 | 2.133 | 93.6 | 111.6 | 31758

## Slide 8: Freezing Point Depression Measurements
Freezing point measurements showed 16 K subcooling below the triple point temperature of methane (90.7 K) and ethane (90.4 K)
Data Point | Methane [mol %] | Ethane [mol %] | Nitrogen [mol %] | Pressure [bar] | Sea Temp. [K]
F1 | 61.0 | 25.6 | 13.4 | 0.290 | 71.5
F2 | 46.9 | 45.3 | 7.9 | 0.517 | 74.0

## Slide 9: Measurement Video
Video available at: http://hdl.handle.net/2376/12183

## Slide 10: Acknowledgements
Dr. Jason Hartwig (GRC)
Dr. Jacob Leachman (WSU)
NSTRF Grant NNX14AL59H
NASA Research Grant NNC16MF93P
Notes: Before closing I would like to thank Steve Barsi from NASA Glenn who has been my mentor over the last year as part of the NASA Space Technology Research Fellowship that funds this work and a special thanks to Mark McLinden at NIST who is a leading expert in density measurements and has been a tremendous help in everything from helping to troubleshoot our system to calibrating the sinker for us.

## Slide 11: THANK YOU