## Slide 1
BTVs @ ELENA Status 2016_10_27
Location of new BTVs
Between Septum and Kicker
Relocation of
DE.BTV7045 -> LNI.BTV.0015
AD Extraction line
LNR.BTV.0117
Circulating beam
LNR.BTV.0118
Injected beam
BTVs for ELENA
S.Burger, A.Guerrero

## Slide 2
LNI.BTV.0015
BTVs @ ELENA Status 2016_05_27
Installed Q1 2016
Operational – Waiting for beam...

## Slide 3
LNR.BTVPA.0117
LNR.BTVPA.0118
Final vacuum tests were OK. Installation in LNR20 was done in July 16.
BTVs in LNR20 section of ELENA ready for operation
BTVs @ ELENA Status 2016_05_27
Vacuum and bake out finished mid October.
Installation of:
  the pneumatic interfaces
  the push-pull external parts
  the ‘Cloches’ (cameras + filter wheels + lights)
EIS tests -> OK on BTV side (LNR.BTV0117 in the access chain)
Documentation for Safety file has been transmitted to C.Alanzeau
Operational- Waiting for the beam…

## Slide 4
BTV ELENA – Pressure measurement during BTV movement in Building 113
Magnetic Push-Pull from UHV with CERN modifications:
- replacement of FRELON© and PEEK© pieces by BeCu
- large grooves for better vacuum pumping
NEG Coated vacuum chamber
Initial vacuum pressure for this test in building 113 setup was ~3E-10 (1E11 reached after cooling a vacuum pump that was discovered still warm on the setup).
3 gauges for monitoring. 2 are represented here.
Chart: Pressure during BTV movements
| 14:43:41 | 14:43:51 | 14:43:52 | 14:43:53 | 14:43:54 | 14:43:55 | 14:43:56 | 14:43:57 | 14:43:58 | 14:43:59 | 14:44:02 | 14:44:07 | 14:44:09 | 14:44:10 | 14:44:12 | 14:44:13 | 14:44:14 | 14:44:15 | 14:44:16 | 14:44:17 | 14:44:18 | 14:44:21 | 14:44:27 | 14:44:36 | 14:44:38 | 14:44:54 | 14:45:01 | 14:45:02 | 14:45:03 | 14:45:04 | 14:45:05 | 14:45:07 | 14:45:08 | 14:45:09 | 14:45:12 | 14:45:14 | 14:45:15 | 14:45:17 | 14:45:18 | 14:45:19 | 14:45:20 | 14:45:21 | 14:45:22 | 14:45:23 | 14:45:25 | 14:45:28 | 14:45:37 | 14:45:41
Pe2 | 9.7e-10 | 9.7e-10 | 8.5e-09 | 1.7e-08 | 7.9e-09 | 3.9e-09 | 2.2e-09 | 1.5e-09 | 1.3e-09 | 1.1e-09 | 1e-09 | 1e-09 | 2.6e-09 | 2e-08 | 8.8e-09 | 4.1e-09 | 2.4e-09 | 1.6e-09 | 1.3e-09 | 1.2e-09 | 1.1e-09 | 1e-09 | 1e-09 | 1e-09 | 1e-09 | 1e-09 | 1e-09 | 8.8e-09 | 4.5e-09 | 2.5e-09 | 1.6e-09 | 1.3e-09 | 1.1e-09 | 1.1e-09 | 1e-09 | 1e-09 | 2.2e-09 | 5.8e-09 | 2.9e-09 | 1.8e-09 | 1.4e-09 | 1.2e-09 | 1.1e-09 | 1.1e-09 | 1e-09 | 1e-09 | 1e-09 | 1e-09
SVT neg | 3.5e-10 | 1.1e-09 | 1.1e-08 | 8.7e-09 | 3.7e-09 | 1.8e-09 | 9.9e-10 | 6.4e-10 | 5.1e-10 | 4.4e-10 | 3.9e-10 | 3.6e-10 | 3.6e-10 | 1.2e-09 | 4.2e-09 | 1.9e-09 | 1.1e-09 | 7.2e-10 | 5.6e-10 | 4.8e-10 | 4.5e-10 | 4e-10 | 3.8e-10 | 3.5e-10 | 3.9e-10 | 3.8e-10 | 1.2e-09 | 4.7e-09 | 2.1e-09 | 1.1e-09 | 7e-10 | 5.4e-10 | 4.6e-10 | 4.2e-10 | 3.8e-10 | 5.5e-10 | 6.4e-09 | 2.8e-09 | 1.3e-09 | 7.9e-10 | 5.8e-10 | 4.8e-10 | 4.4e-10 | 4.1e-10 | 3.9e-10 | 3.8e-10 | 3.5e-10 | 3.9e-10
Movement of BTV0117
Screen IN
Screen OUT
Movement of BTV0118
Screen IN
Screen OUT
Gauges
Conclusion
Pressure rising with a level between 5E-9 and 2E-8 during movement.
Vacuum gets back to initial values after few seconds.
Pe2
SVT Neg
2016_07_04 S.Burger/Y.Delaup

## Slide 5
Vacuum performance in LNR20
BTVs @ ELENA Status 2016_05_27
1E-9
1E-10
~5 to 10x less than in lab