## Slide 1: Linac4 ion source modelling codes: NINJA, ONIX, IBSimu
Stefano Mattei
ABP-CWG meeting 31/10/2017

## Slide 2: Linac4 short intro
Linac4 will be the new injector to the PSB, replacing Linac2
Linac2: 50 MeV proton beam
Linac4: 160 MeV H- beam
Currently in commissioning stage
160 MeV already achieved
More details: A. Lombardi THE LINAC4 PROJECT, Proceedings of HB2016, Malmö, Sweden
http://accelconf.web.cern.ch/AccelConf/hb2016/papers/moam2p20.pdf
The ion source is the first component of the accelerator, providing the H- ion current

## Slide 3: The Linac4 H- ion source
H2 gas
ONIX
Detailed model of the beam formation
Plasma
H2 H-
RF coil + Ferrites
Octupole cusp magnets
Filter magnets
-35 kV
0 V
0 V
+45 kV
45 keV
H- beam
-45 kV
NINJA
Modelling the
RF-plasma
heating
IBSimu
Extraction and beam transport

## Slide 4: NINJA code
Kinetic code (Particle-In-Cell) for the simulation of the
RF plasma heating in inductively coupled plasmas
Code developed in close collaboration with KEIO University in Japan
Applied for the simulation of CERN’s Linac4 and CHARLIE test bed at University of Augsburg
Simulate the RF-plasma heating
Investigate the effect of design and operational parameters on the plasma characteristics
Provide inputs to beam formation simulations (ONIX)

## Slide 5: NINJA code: physics
Particle-In-Cell
2.5 D in cylindrical coordinates:
2D EM field calculation (azimuthal symm.)
3D3V particle dynamics
Implicit integration scheme
Plasma species: e-, H+, H2+, H3+, H-
+ neutrals H, H2(v)
Coupling with static magnetic field simulations (Opera VectorFields) imported via 3D fieldmap
Monte Carlo Collisions
Set of over 200 cross-sections covering the most important reactions in hydrogen
electron – neutral
electron – ion
ion – neutral
Coulomb collisions

## Slide 6: NINJA code: specs
Programming language: Fortran90 + libraries Fortran77, Fortran90
OS: Linux
Compilers: successfully run with GNU, INTEL, NAG and PGI
we typically run with INTEL
Libraries: all open source
  NITSOL (Fortran77)
    BLAS (Fortran77)
    LAPACK (Fortran77)
  SPARSKIT (Fortran90)
Parallelization: MPI
Licensing: not open-source, discussion ongoing with collaborators at KEIO University
Documentation: A fully implicit Particle-In-Cell Monte Carlo code for the simulation of inductively coupled plasmas, in preparation for submission to “Journal Computational Physics”

## Slide 7: NINJA: application
Grid: Ng 104
Particles: Np 106-107
∆t = < 10-10 s
We need to simulate 10-20 µs
105-106 time steps
Computing time: 10 days on 12 cores (engpara on lxbatch)
Parameter scans required:
  RF power
  Gas pressure
  Magnetic configuration
  Antenna position
NINJA provides the plasma parameters (temperatures, densities and fluxes) over the volume of the plasma chamber

## Slide 8: ONIX
ONIX is a 3D Particle-In-Cell code for the simulation of the beam formation in a negative ion sources
Initially developed in the laboratory LPGP, Orsay, France in order to simulate the extraction region of an ITER-like negative ion source
S. Mochalskyy, J. Lettry, T. Minea, New journal of physics 2016
http://iopscience.iop.org/article/10.1088/1367-2630/18/8/085011
Applied for the simulation of the Linac4 H- ion source
Study the effect of volume/surface produced H- on the extracted current and beam emittance

## Slide 9: ONIX: specs
3D Particle-In-Cell Monte Carlo Collision electrostatic code
Owner: LPGP Orsay and IPP Garching
Parallelization: MPI
Performance: typical run is performed using 20 million macro particles with a meshing of 110x100×100 PIC nodes. The code performance is ~0.1 μs per day on 20 cores.
Normally 1-2 μs simulation time is sufficient to reach steady state.
Currently work in progress to reduce the cell size and improve parallelization to run on large clusters (~1000 cores)
Licensing: not open-source
Currently maintained by LPGP and IPP Garching

## Slide 10: ONIX: future
Finer resolution
fluxes
OFF-line coupling between NINJA and ONIX
Extract from NINJA the plasma parameters (ne, Te, flux of H0, etc) at the entrance of the collar region
ONIX: defines the resulting beam characteristics
Goal is the optimization of the plasma electrode geometry and puller optics
Work to be done in collaboration between CERN-KEIO-LPGP-IPP provided resource availability

## Slide 11: IBSimu
http://ibsimu.sourceforge.net/
An ion optical computer simulation package for ion optics, plasma extraction and space charge dominated ion beam transport using Vlasov iteration.
Used at CERN for 5-6 years: Linac3, Linac4, ISOLDE
Developed by T. Kalvas @ U. of Jyväskylä (Finland)
Solid geometry definition using 2D DXF files, 3D STL files, mathematical formulation, etc.
Finite Difference Method solver for 1D, 2D and 3D Poisson equations with edge smoothing.
Particle trajectory iteration in self-consistently calculated electric and imported magnetic fields.
Space charge density calculation from trajectories.
Vlasov iteration for self-consistent simulation of high space-charge beams.
Nonlinear plasma models for positive and negative ion extraction.

## Slide 12: IBSimu: specs
Programming language: C++
OS: Linux, Windows
Compilers: GNU
Libraries: several for background functionality (graphics, math, etc.) listed on the website
Parallelization: none
Licensing: open-source, GNU General Public License
Maintained by T. Kalvas
Documentation: http://ibsimu.sourceforge.net/index.html

## Slide 13: IBSimu: application
Beam transport given geometry and potentials
e- and H- beam
including space-charge, trajectories
Computing time: 1-2 days
Parameter variations:
Extracted currents, e- / H-, geometry, potentials. Typically 200-300 runs
Limitation of IBSimu is the plasma model  not suited for surface produced negative ions
Linac4 H- ion source extraction optics:
Daniel Fink: http://scitation.aip.org/content/aip/proceeding/aipcp/10.1063/1.4916433
Oystein Midttun: http://scitation.aip.org/content/aip/journal/rsi/85/2/10.1063/1.4824814

## Slide 14: IBSimu: future
NINJA-ONIX can provide the beam phase-space few mm from the plasma electrode
IBSimu can track it through the e- beam dump section and provide input to TRAVEL and PATH
Goal is the optimization of the overall ion source emittance
ONIX
IBSimu
NINJA
TRAVEL/PATH