## Slide 1: Overview of the GE2/1 & ME0 Chamber R&D
Production plans, synergies and Lessons Learnt from GE1/1 project
Michele Bianco (CERN) on behalf of CMS GEM group
Many thanks to: A.Sharma, R. De Oliveira, A. Conde, S. Brachet, A. Goldames Perez, M. Abbas, P. Aspel, G. De Lentdecker, P. Vitulo, L. Benussi, M. Maggi, I. Vai, J. A. Merlin, B. L. Dorney, …..

## Slide 2: Outline 1
GE2/1 Motivation for improved redundancy
Performance requirements
Baseline option as triple GEM detector
GE2/1 20 degrees: general constraints
GE2/1 chamber layout
Electronics for Read Out
Services
Synergies with other projects
Production schema and schedule
µ-RWELL Option: Motivation & Concept
µ-RWELL Technology description
µ-RWELL Prototypes developed & R&D plans and studies

## Slide 3: Outline 2
ME0 Baseline solution as triple GEM detector
Rate capability and discharge probability
Ongoing R&D
  Triple GEM Back-to-Back
  FTM Detector
ME0: general constraints and possible implementations
Electronics for Read Out
Synergies with other projects

## Slide 4: The upgrade of the CMS muon system in high h region in Phase 2
GEM Endcap GE1/1: station to be installed in LS2, 1.6 < |η| < 2.2  GEM technology
Muon Endcap ME0: station proposed for LS3, h < 3.8  2 technologies under consideration:
GEM: GE1/1-like station, with more layers to reject background - Baseline
FTM and BtoB - Option
GEM Endcap GE2/1: station proposed for LS3, h < 2.4 
2 technologies considered:
GEM technology - Baseline
mRWELL - Option

## Slide 5: GE2/1 Motivation
The performance of the endcap muon trigger relies on the optimal performance of L1 CSC trigger
Installation of new GEM chamber provide:
  Additional redundancy in the most difficult region (low B, highest rates)
  Similar to GE1/1, allows measurement of muon direction
    Improves L1 momentum measurement for prompt muons and reduces trigger rate
    Enables triggering on displaced muons
  Additional hits to recover lost CSC stubs
  Good spatial resolution can aid in matching L1 track trigger objects with L1 muons and offline reconstruction
GE2/1:
  20 degrees chambers
  18 super chamber per disk (36 total)
  2 chamber per station (super chamber)
   2 extra hits

## Slide 6: Triple GEM detector as baseline option for GE2/1
Triple GEM detector with the same “operational layout 3/1/2/1” adopted for the GE1/1 chambers has been chosen as baseline solution.
Well-known mature technology
Easy to be implemented
Match the detector requirement (GE1/1 even more demanding)
Time resolution of 8ns is adequate from simulation studies, (97% of single chamber hits associated to the correct)
Eco-friendly gas validated
YE2
YE1
Shielding
ME2/1 CSC
88 mm

## Slide 7: GE2/1 Geometrical constraint
The baseline GE2/1 station consists of 36 200 Super Chambers, the layout will be similar to GE1/1, but covering much larger surface.
Limits in space make the GEM technology
perfect candidate for GE2/1
Same technical solution successfully
adopted for the GE1/1
Each GE2/1 Superchamber realized
with two single chambers
YE2
YE1
Shielding
ME2/1 CSC
88 mm
Same thickness of GE1/1 chambers
36.4 mm

## Slide 8: GE2/1 Geometrical constraint
YE2
YE1
Shielding
ME2/1 CSC
88 mm
Similar thickness of GE1/1 chambers
1251 mm
1911 mm
1178 mm
1837 mm

## Slide 9: GE2/1 20 degrees: general constraints
An ideal detectors should:
Minimize the dead area ==> to increase the acceptance
Reduce the number of components ==> to make easy the construction
1251 mm
1911 mm
We have to deal also with the RO PCB segmentation, which should be closest as possible to the simulation
A unique module solution for the GE2/1 chambers would be very welcome, but:
GEM foil base material limited in size (max 610 mm wide)
PCB producer usually limit the size of the PCB to ~ 60 cm; for a single and double sided board 1550mm x 600mm panel; we can have a circuit of length 1500mm x 550mm
Chambers realized with several module ==> Easier solution

## Slide 11: GE2/1 20 deg. 4 horizontal modules
GE2/1 chamber segmented in 4 horizontal modules
Max PCB size about 1200 mm X 600 mm (M4)
M4 size comparable with GE1/1 Long chambers possible to fit in to the actual copper box
All detectors components available on the “Market”
Chambers coupled together trough external metallic profiles
Dead area between chambers limited to 35.5 mm ( staggered second chamber to eliminate dead area)
GEM foils production to be split between two(or more) production sites (several candidates)
M1
M2
M3
M4
1178 mm
502mm

## Slide 12: GE2/1 20 deg. 4 horizontal modules
Y1
Y2
Y3
Y4
YI4
YI3
YI2
YI1
8 modules configuration reduce the dead area
and get at least one GE2/1 hit for each muon
FOILS SENSITIVE AREA

## Slide 13
M1
M2
M3
M4
1178 mm
12 Strips groups
12 Strips groups
12 Strips groups
12 Strips groups
Adopted segmentation: 8 Eta / 6 phi partitions
Not really projective eta segmentation
~ 0.5 mrad
458.5 mm
458.5 mm
458.5 mm
458.5 mm
420 mm
420 mm
497 mm
497 mm
Int
Ext
GEB 4
GEB 5
GEB 3
GEB 2
GEB 1
OH
OH

## Slide 14: GE2/1 20 deg. 4 horizontal modules
Mechanical Summary
72 20 deg. Chambers == > 18 Super Chamber per end
288 Modules == > 8 different types
Max module size ~ 50 cm X 120 cm (comparable withGE1/1 long)
864 Foils == > 8 different types
42 Strips group per chambers equally distributed between the modules
Interconnections between Drift and RO PCB in modules M4, in M3 and M2 under evaluation

## Slide 15: GE2/1 20 deg. 4 horizontal modules
Front Chamber active area
Back Chamber active area
Overlapping active areas

## Slide 16: M4 Design (FEM Simulation)
Symmetry applied to reduce the number of elements

## Slide 17: M4 Design (FEM Simulation)
Pressure results, under 5mbar for no Pillar, 2 Pillars and 3 Pillars configuration

## Slide 18
M4 Design (FEM Simulation)
Pressure results, under 5mbar for no Pillar, 2 Pillars and 3 Pillars configuration
Number of Pillars | Max Deviation at 5 mbar | Def at rest for gravity and stretching
0 | 1.65 mm | 0.1 mm
2 | 0.52 mm | 0.07 mm
3 | 0.32 mm | 0.06 mm
Results for 3 pillars: Optimal position after the iterative process:
  Vertical direction: Middle of the active area
  Horizontal direction: At the symmetry plane and at 270 mm from the symmetry plane

## Slide 19: M4 Design: RO board, Foils, Frames and details
50 HV Sector of about 100 cm2 each
25 Left / 25 Right
HV connection middle top
Power distribution left/right side
RO Board External view

## Slide 20: M4 Design: RO board, Foils, Frames and details
Milling
Internal frame re-designed to increase the distance between the frames and the active area and avoid Spurious Signals
GE1/1 internal frames
Milling
GE2/1 internal frames
Internal frame
Old shape

## Slide 21: Module coupling and chamber assembly
Two transversal bars, which hold the modules have been added to increase the mechanical stability of the full chambers
Three stiffener bars to join the modules together

## Slide 22: Module coupling and chamber assembly
Transversal bar
GEB
RO PCB
External frame
Drift PCB
Pocket in the Drift PCB
Alu profile between modules
19.5 mm
chimney
18 mm

## Slide 23: GE2/1 Baseline option: prototyping schedule
ONE Prototype Schedule
Final Design Completed: 30th Nov 2016
Material Procurement: Mid Feb 2017
M4 Modules Assembly: End Feb 2017
Modules Tests in the Lab: End Apr 2017
Chamber Material Procurement: Mid June 2017
Chambers Assembly: End June 2017
Chamber Test and Cabling: End July 2017
In Time for TDR!!!
GE2/1 prototype strategy:
The detector technology is identical as GE1/1 chambers == > R&D Complete ! (performance, aging, …)
GE2/1 Mechanics very close to GE1/1
We have to optimize module coupling by building prototype
4 separate modules to be built, only one as “working module”, three dummy, enough to test the whole system from mechanics point of view.
Mechanical Mockup for integration tests completed (mid March)

## Slide 24: Electronics components
Numbers provided in next slide are based on the experience and solutions adopted with the GE1/1 chambers.
Actual GEB boards are limited in size (~ 1100 mm in GE1/1 will use GEB made by two separated pieces)
Opto-hybrid for GE1/1 can handle up to 24 VFAT chips

## Slide 25: Optimization of Electronics components for GE2/1 design
Four horizontal modules:
(components for the whole GE2/1 system)
3456 VFT3 chips (48 x 2 x 36)
144 OH with 24 VFAT3 input
5 different GEB boards per chamber: 1 x M1, 1 x M2, 1 (or 2) x M3, 2 x M4
360 (or 432 ) GEB in total for the GE2/1 project
1 GEB
1 GEB
1 GEB ( 2 GEB ?)
2 GEB
Opto Hybrid

## Slide 26: GE2/1 Baseline: services
2 HV Multi conductor cable
4 LV Cable from the PS to FEAST DCDC
4 Fibers to ME2/1 TMB
The TMB can’t accept more than 4 Fibers for each GE2/1 20 deg. super chamber

## Slide 27: GE2/1 Baseline solution HV/LV system
The base line Power HV power source will be A1515 from CAEN.
In the finest granularity one GE2/1 super-chamber can be powered with 4 modules.
• GE2/1 Detectors for will be equipped with VFAT3 front-end chip and OH every two moduls.
• The CERN FEST DCDC converter will be integrated on the GEB boards to provide LV power for the on detector electronics
Reducing the number of LV channels (cost) per detector
Having an option to use smaller power cables, sensitive for the GEM installation regions
As result of this approach DCS software will be identical to GE1/1.

## Slide 28: Synergies with other projects
The Baseline detector for the GE2/1 chambers, ( with the layouts presented here), shares several aspect with the ongoing GE1/1 project.
In the GE2/1 20 deg. the largest module will have dimensions comparable with the GE1/1 Long chambers == > tooling and setups prepared for the GE1/1 can be mostly re-used.
The new CMS GEM clean room & GEM QC Lab, in preparation in bd. 904 (Prevessin) is large enough to host the production & Quality Control of the GE2/1 chambers
Electronics developed for the GE1/1 (VFAT3) can be easily adapted to the GE2/1 chambers

## Slide 29: Synergies with other projects
The triple GEM detectors, the baseline option chosen for the GE2/1 modules, is the same technology used by GE1/1 this mean:
  Well known performances (GE1/1 expected rate higher than GE2/1)
  No additional aging test needed, the GE2/1 will use the material components adopted for the GE1/1 No different materials compared to GE11
  Production & QC Tooling and setup, (some of them quite expensive: X-ray, copper boxes, cosmic ray stand, …) prepared for the GE1/1 production to be reused for the GE2/1 production and tests.
  Crew trained for the production and test of the GE1/1 will be easily moved to the production and test of the GE2/1 baseline option.
  Production sites “certified” for the production of GE1/1 chambers don’t need to be certified again
  Production of GE2/1 modules can be seen as continuation of the GE1/1 chambers

## Slide 30: The µ-RWELL option
The µ-RWELL is composed by:
The µ-RWELL PCB and the drift cathode PCB + frame to seal the gas volume
The µ-RWELL PCB is realized by coupling:
a suitable kapton foil patterned with a µ-WELL acting as a single “amplification stage”
for discharge suppression & current sinking DLC sputtered in one Kapton surface
single resistive layer  surface resistivity ~100 M/☐
expected rate capability << 100 kHz/cm2:
a standard readout PCB with strips
µ-RWELL:
Has simple assembly steps
large area coverage can be easily obtained with the standard PCB splicing technique

## Slide 31: µ-RWELL Motivation & Concept
Motivation
  More efficient tiling of several modules in 20 degree GE2/1 chamber
Benefits
  Simplified mechanical structure and assembly procedure could translate in an effective cost reduction.
  Detector thickness fits space constraints for GE2/1 installation
Concept
  Single-stage amplification structure using a µ-RWELL
    Single amplification structure
    Resistive readout structure to protect the amplification stage against sparks

## Slide 32: GE2/1 µ-RWELL schematic
Four PCB (M1,..,M4) assembled together using splicing technique (0.5mm dead area between each sector)
One chamber is one gas volume.
1 HV channel/chamber. Very easy to increase the number of HV channel/chamber to increase granularity
Almost negligible dead area (<0.1% of the active surface)
Electronics and services needed for µ-RWELL will be the same of the one needed as for 3-GEM option

## Slide 33: Planned R&D Studies: Mechanical Design (1/2)
Four PCB µ-RWELL modules spliced with the same technique used for large ATLAS µM + only one cathode PCB closing entire chamber
Mechanical design of full-size detector (20 degree option)
Started finite element simulations for:
  PCB & cathode deformation studies under gas over-pressure due to gas flowing during operations (see next slide)
  Mechanical structure rigidity and robustness studies
  Optimization of FEE housing/cooling/services (to fit the available 7.4 mm for GE2/1 installation )

## Slide 34: Planned R&D Studies: Mechanical Design(2/2)
PCB deformation of the GE2/1 chamber (20 degree option)
Simulated structure 2x (FR4 1.6mm + HC 3mm + FR4 1.6mm) + Gap 5 mm + 9 pillars of 12 mm diameter
Max deformation 0.78 mm at 8 mbar gas over-pressure (expected 2~mbar during standard operation)
Detail of the µ-RWELL PCB around the splicing and pillar location
The pillars along splicing zone Pillars implementation in -RWELL is easy and introduces an overall dead area of <0.1%

## Slide 35: GE2/1 µ-RWELL summary
µ-RWELL has potential to simplify construction & assembly of largest GE chambers and to recover dead space between modules: simple construction and assembly procedure can probably reduce total cost
The electronics and services needed for µ-RWELL are not different from the one needed for 3-GEM
Still a lot of R&D work to do:
  Mechanical studies: planarity of the PCB r/o over a large area => produce mechanical mock-up of the chamber setup (will allow also to study FE housing/cooling..); finalize the studies on PCB and cathode deformation due to gas overpressure.
  Measure gain uniformity, space resolution, gas distribution uniformity and time resolution (over large areas)and discharge rate probability
  Aging test at GIF++. Outgassing studies to be done for all new materials introduced, if any.

## Slide 36: MEO Detector

## Slide 37: ME0 baseline option
Triple GEM detector 3/1/2/1 (as per GE1/1)
Eta Coverage 2.03 – 2.82
20 Degrees – 18 ME0 stacks per endcap
Chamber dimensions smaller than GE1/1 short
To be installed during LS3
36 ME0 super-modules plus all the services in UXC and USC

## Slide 38: Rate capability
Rate capability:
Modification of the electric field at high rate (space-charge effects)
  Measurements done with X-ray source, charge released by a converted gamma is about 10 times larger than the charge provided by MIP
  No effects up to 104 Hz/mm2 (stable gain)
  Increasing of the electron transparency between 104 and 105 Hz/mm2 (gain rise)
  Decreasing of the ions extraction around 106 Hz/mm2 (gain drop)

## Slide 39: Discharge probability: J. A. Merlin Thesis
Discharge probability:
Initiation of a streamer in case of heavy ionizing event (high charge density)
Can induce long dead time or damages
Protections against discharges:
- Asymmetric sharing of the gain
- GEM foils divided in small sectors
- Use of protection resistances
Procedure:
  - Detection of α-particles from Am241
    (perpendicular to the GEMs)
    - Identify pulses on the GEM and the RO with same polarity (typical discharge signals)
Results:
  10-5 to 10-3 at gains of 4-6 x 105
  Expected 10-10 at gain 1-2 x 104

## Slide 40: Discharge probability: New tests
Quite large uncertainties on the J. Merlin data extrapolation.
Several data over the years, not all of them with similar results. Different (by order of magnitudes ) discharge probabilities..
Different GEM configurations and beam configurations
Small detector size (10 x 10 cm2)
Tests for ME0 seem appropriate
Test Time required
Suppose we observe no Discharge Event (DE) in ∆𝑡. Upper limit for Zero events would be n=3 ( «Rule of three» : 𝑃 0,𝑛 = 𝑒−𝑛 ≥ 0.05 ) @ 95% CL
To quote a Discharge Probability (DP) of 10−7 = 3/h𝑛∆𝑡𝐴 , h𝑛 = 1 𝑘𝐻𝑧/𝑐𝑚2 neutron hit rate, 𝐴 = 102 𝑐𝑚2 detector area would take ∆𝑡 = 300 𝑠 (n.b. Neutron sensitivity is about 2 10−3 => Neutron Flux ~ 2 106 n/cm2 s)
To quote a Discharge Probability (DP) of 10−10 would take ∆𝑡 = 3.4 𝑑 (of continuous running)
Test running time of order of 1 week .

## Slide 41: New tests at CHARM facility @ CERN
Problems and Constraints
15 m cables from DUT to Patch-Panels
17 m cables from Patch-Panels to CRoom
50 m Gas line
This is not a standard TEST-BEAM
First time a gas Detector @ CHARM
Gas Bottle
PatchPanel
GEM
gas bottle into the CHARM buffer zone

## Slide 42: New tests at CHARM facility @ CERN
The GEM mounted on the RACK
RadMON installed by the Facility
Give information of Hadron Flux

## Slide 43: New tests at CHARM facility: DAQ
Data Analysis just started …

## Slide 44: ME0 detector in CMS
Space, space my kingdom for more space
In the actual layout 205 mm are available for the stack plus 15 for the base support

## Slide 45: ME0 detector in CMS
Ideas to gain space: (to be investigated)
Reduce the thickness of the base support -> 15 mm to 10 mm (not Aluminum anymore, Carbon Fiber?)
Modify the nose shape, Read structure inserted in the Grey support

## Slide 46: ME0 Baseline option, chamber geometry
If will not be possible to gain space than:
New design is in progress
3.2 mm Thick PCB replaced by 3 mm PCB
New chimney of 17.6 mm
Total chamber thickness 33.4 mm
Small enough to accommodate 6 chamber per stack in 205 mm
Here pictures from not updated layout, dimensions of active area and chambers surface unchanged
3 mm PCB is not standard size, an ad hoc production have to be required, feasible on large numbers as ME0 maybe will increase the chamber deformation under the gas pressure and mechanical stress

## Slide 47: ME0 Baseline option, stack geometry
Structure of 6 layer GEM* detectors, Base line technology is the triple GEM
* Other MPGD technologies are under study at the moment
Electronics Volume
DC/DC converter and OHs
Go-Out Services path

## Slide 48: ME0 position in CMS

## Slide 49: ME0 position in CMS
In order to assure overlap between two adjacent detectors, two subsequent stacks will be installed front-back each other

## Slide 50: ME0 chambers overlap
Detector overlaps
The mechanical overlap between two adjacent stacks will about 6.5 cm

## Slide 51: ME0 chambers overlap
Detectors overlaps

## Slide 52
Mechanical Summary
36 20 deg. Stacks == > 18 per side
216 Chambers == > unique type
Chamber size ~ 57 cm X 86 cm (Smaller than GE1/1 short)
648 Foils == > unique types
48 Strips group per chambers ( channels density twice GE1/1) to deal with the high rate and the necessary resolution performances
ME0 baseline option

## Slide 53: Electronics components for the ME0 baseline options
RO board not yet finalized
Possible option 6phi partitions x 8 partitions (48 group of 128 strip => ~0.5 mrad )
Challenging to fit 48 hybrids in such a small space (also reduced by the chimney )
10368 Front-End chips (VFAT) (48 x 6 x 36)
432 opto-hybrid with 24 VFAT input (2 per chamber or OH need to be completely redesigned)
Opto-hybrids “outside” the chamber, to be defined the available space for the OH
1 per chamber, 6 GEB per stacks
216 GEB in total for the ME0 project
48 VFAT
1 GEB
Two opto-hybrid x chamber

## Slide 54: Synergies with other projects
The Baseline detector for the ME0 chambers, ( with the layouts presented here), share several aspect with the ongoing GE1/1 project.
No different materials are expected to be used to build the ME0 w.r.t. the GE1/1
Chambers will have dimensions comparable with the GE1/1 short chambers == > tooling and setups prepared for the GE1/1 can be mostly re-used.
The new CMS GEM clean room, in preparation in bd. 904 (Prevessin) will be large enough to host the production of the ME0 chambers,
Electronics developed for the GE1/1 can be adapted to the ME0 chambers

## Slide 55: Synergies with other projects
The triple GEM detectors, the baseline option chosen for the ME0 modules, is the same technology used by GE1/1 this mean:
  Tooling and setup, (some of them quite expensive: X-ray, copper boxes, cosmic ray stand, …) prepared for the GE1/1 production can be reused for the ME0 production and tests.
  Crew trained for the production and test of the GE1/1 can easily move to the production and test of the ME0 baseline option.
  Production sites “certified” for the production of GE1/1 chambers don’t need to be certified again
  Production of ME0 modules can be seen as continuation of the GE1/1 and GE2/1 chambers

## Slide 56: R&D ongoing activity (B2B)
The detector is composed of two stacked triple-GEM detectors, each one with parallel readout strips
  One GEM has 256 strips in the x – axis
  One GEM has 256 strips in the y – axis
A single HV supply powers both the triple-GEM
On detector’s board

## Slide 57: B2B rate measurements
Chart: 109Cd - GEM1 readout
| 1445.0 | 1436.0 | 1427.0 | 1419.0 | 1409.0 | 1400.0 | 1391.0 | 1382.0 | 1373.0 | 1364.0 | 1355.0 | 1346.0 | 1337.0 | 1328.0 | 1319.0 | 1301.0 | 1283.0 | 1265.0 | 1243.0 | 1229.0
GEM1 readout - Source centered | 119.7667 | 121.0333 | 120.0667 | 117.5 | 116.7333 | 116.3667 | 113.85 | 111.3667 | 108.5 | 101.5333 | 100.9 | 92.9 | 89.0333 | 77.2167 | 50.15 | 31.9 | 18.55 | 9.1833 | 1.8167 | -0.2
GEM1 readout - Source in corner A | 108.0667 | 110.5 | 107.3 | 106.2667 | 103.5 | 102.4333 | 99.6833 | 96.6 | 82.0667 | 55.5 | 31.1833 | 19.7 | 9.85 | 3.4833 | 1.5833 | 0.43333
GEM1 readout - Different positions | 121.0333 | 110.5 | 117.2667 | 114.2333 | 113.7333 | 110.5667 | 111.2333 | 106.7 | 112.6
  Measurements performed with 109Cd source
  On both the triple-GEMs composing the detector
  Placing the source in different positions (red markers) on the active window to test the operation of the entire active area
Results show that the detector works properly and reaches a plateau.
Chart: 109Cd - GEM2 readout
| 1446.0 | 1436.0 | 1427.0 | 1419.0 | 1410.0 | 1400.0 | 1391.0 | 1382.0 | 1373.0 | 1364.0 | 1355.0 | 1346.0 | 1337.0 | 1328.0 | 1319.0 | 1301.0 | 1283.0 | 1265.0 | 1247.0 | 1229.0
GEM2 readout - Source centered | 124.7167 | 126.0833 | 122.4167 | 124.9833 | 121.8333 | 118.7167 | 118.2167 | 114.0667 | 114.4167 | 107.7167 | 102.7167 | 96.35 | 90.6 | 66.55 | 44.8333 | 29.7833 | 17.6667 | 7.2667 | 1.7167 | 0.4
GEM2 readout - Source in corner 1 | 122.9833 | 120.35 | 117.9 | 118.85 | 116.6 | 115.1833 | 111.55 | 108.2167 | 93.3833 | 82.9 | 36.6667 | 25.3167 | 15.1 | 4.4667 | 1.0167 | 0.6
GEM2 readout - Different positions | 126.0833 | 120.35 | 125.6833 | 123.15 | 121.8167 | 117.4833 | 121.0167 | 118.4833 | 121.55

## Slide 58: B2B tests
  Measurements performed with 109Cd source
  Placing the source in different positions on the active window to test the operationg of the entire active area (see below: values with multiple markers)
Chart: 109Cd - Gain vs Position
| center | corner1 | between corners 1-2 | corner2 | between corners 2-3 | corner3 | between corners 3-4 | corner4 | between corners 4-1
Gain at divider curr.=1435,95 µA | 8946.3267 | 8255.9918 | 8283.9345 | 8009.8965 | 8275.1674 | 6928.7322 | 7328.6719 | 6641.6565 | 7704.5498
Gain at divider curr.=1427,25 µA | 4454.3168 | 3317.7862 | 4085.2257 | 3658.6825 | 3345.7582 | 2312.0067 | 2709.5551 | 2061.4286 | 2882.5273
Mean gain at 1435,95 µA | 7830.6397 | 7830.6397 | 7830.6397 | 7830.6397 | 7830.6397 | 7830.6397 | 7830.6397 | 7830.6397 | 7830.6397
Mean gain at 1427,25 µA | 3173.8532 | 3173.8532 | 3173.8532 | 3173.8532 | 3173.8532 | 3173.8532 | 3173.8532 | 3173.8532 | 3173.8532
Gain at plateau varies between 15% (at 1435,95 µA divider current) and 40% (at 1427,25 µA divider current)
  Detector’s proper working demostrated
  Measured gain at plateau > 2000 (up to about 8000) depending on applied voltage
  Next:
  Analysis of data acquired at H2 test beam [gas mixture Ar/CO2 70/30)] from spatial point of view (spatial resolution, cluster size), efficiency calculation
  Test beam at H4 ongoing to test spatial and timing performance in gas mixture Ar/CO2/CF4 45/15/40

## Slide 59: Fast Timing Micropattern (RTM) R&D
The contribution to the time resolution of the drift velocity is:
With a drift gap of the order of 3-4 mm and with a proper choice of the gas mixture, these detectors can reach a time resolution of the order of 5-10 ns.
t=d/vd
st= (lvd)-1
The idea is to divide a single thick drift region in many thinner drift regions, each coupled to its amplification stage.
The reduction in time resolution is proportional to the number of stages ND employed
When the avalanche grows in one drift-amplification stage, the signal is induced on the top and bottom readouts.
The construction of consecutive drift-amplification stages is allowed by the use of resistive layers to polarize drift and multiplication volumes. The overall structure is then transparent to the signal, that can be extracted at every amplification stage.

## Slide 60: FTM first prototype
Reference:arXiv:1503.05330v1
European Patent Application 14200153.6
M. Maggi, A. Sharma, R. De Oliveira
The detector is composed by two independent drift-amplification stages (Layer 1 & 2 in the picture above)
Each amplification region is based on a pair of polyimide foils stacked due to the electrostatic force induced by the polarization of the foils:
The first foil, perforated with inverted truncated-cone-shaped holes (bases 100 mm and 70 mm, pitch 140 mm), is a 50 mm thick Apical KANECA, coated with diamond-like carbon (DLC) technique, to reach up to 800 MW/□ resistivity.
The second foil is 25 mm thick XC Dupont Kapton, with a resistivity of 2 MW/□.
The drift volumes are 250 mm thick, with planarity ensured by coverlay pillars, with diameter 400 mm and pitch of ~3.3 mm.

## Slide 61: FTM first prototype: timing results
The plots show the time distribution of the signal pickup from the drift electrode, with muon beam (top left) and pion beam (bottom right).
The time resolution is estimated from the sigma of the gaussian fit of the distribution.
The electronics chain used to readout the signals was composed by a Cividec broadband amplifier (x100) and a Lecroy linear amplifier (x7.5)  Different electronics from lab test: faster for timing measurement!

## Slide 62: Production Schedule GE2/1 and ME0
Preamble:
This schedule is related only for the baseline option, with the assumption that at the time of the production at least two vendors of GEM foils will be available and four production sites, all of them with similar capacity of chamber construction
GE2/1 | Tot Chambers: 72 |  | Total Modules: 288 |  | GEM foils needed: 864 |  | Foils Prod sites:2 |  | Prod. Lines : 4 | 
ME0 | Total Stacks: 36 |  | Total Chambers: 216 |  | GEM foils needed: 648 |  | Foils Prod sites:2 |  | Prod. Lines : 4 | 

## Slide 63: Production Schedule GE2/1
 |  | 2018 Q3 | 2018 Q3 | 2019 Q1 | 2019 Q2 | 2019 Q3 | 2019 Q4 | 2020 Q1 | 2020 Q2 | 2020 Q3 | 2020 Q4 | 2021 Q1 | 2021 Q2 | 2021 Q3 | 2021 Q4 | 2022 Q1 | 2022 Q2 | 2022 Q3 | 2022 Q4 | 2023 Q1 | 2023 Q2
 | GE2/1 Pre-prod ( CERN) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | GE2/1 Foils Prod (Site 1) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | GE2/1 Foils Prod (Site 2) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | GE2/1 Module Prod (Line 1) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | GE2/1 Module Prod (Line 2) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | GE2/1 Module Prod (Line 3) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | GE2/1 Module Prod (Line 4) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Chamber Assembly and tests |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | GE2/1 Contingency |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | GE2/1 Installation |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Implication:
PRR and EDR for material procurements have to be done in second half of 2018
Final version of Readout Electronic, as well as of cooling system and services on chambers have to be ready by Q1 2021

## Slide 64: Production Schedule ME0
 |  | 2021 Q4 | 2022 Q1 | 2022 Q2 | 2022 Q3 | 2022 Q4 | 2023 Q1 | 2023 Q2 | 2023 Q3 | 2023 Q4 | 2024 Q1 | 2024 Q2
 | ME0 Foils Prod (Site 1) |  |  |  |  |  |  |  |  |  |  | 
 | ME0 Foils Prod (Site 1) |  |  |  |  |  |  |  |  |  |  | 
 | ME0 Module Prod (Line 1) |  |  |  |  |  |  |  |  |  |  | 
 | ME0 Module Prod (Line 2) |  |  |  |  |  |  |  |  |  |  | 
 | ME0 Module Prod (Line 3) |  |  |  |  |  |  |  |  |  |  | 
 | ME0 Module Prod (Line 4) |  |  |  |  |  |  |  |  |  |  | 
 | ME0 Stacks Assembly and tests |  |  |  |  |  |  |  |  |  |  | 
 | ME0 Installation |  |  |  |  |  |  |  |  |  |  | 

## Slide 65: Backup

## Slide 66: Direction Measurement
Proposed granularity matches well trigger requirements and tracking requirements
  Two or Four strip pads (VFAT defaults) provide good direction measurements
    Table below shows trigger rate reduction for 20 GeV L1 muon trigger
    Good direction measurement is critical for displaced muons (next slides)
L1 muon momentum resolution can be improved with a second detector if we can measure the “bending angle”
Choice | 2-strip pad (1 mrad) | 4-strip pad (2 mrad) | 8-strip pad (4 mrad) | 16-strip pad (8 mrad)
GE21 1.6<h<2.1 | 2.5+/-0.2 | 2.4+/-0.2 | 2.0+/-0.2 | 1.7+/-0.2
GE21 2.1<h<2.4 | 1.5+/-0.05 | 1.49+/-0.05 | 1.38+/-0.04 | 1.25+/-0.04
GE2/1 granularity:
Min Radius 136cm Max Radius 320 cm strips/etapartition 768
pitch@Rmax 0.14 cm --> 0.45 mrad. pitch@Rmin 0.06 cm

## Slide 67: Trigger requirements
  Another important goal is aiding in resolving ambiguities in CSC reconstruction and improving efficiency
    Timing requirements are not too strict due to multiple redundancy of spatial and timing measurements (6 CSC layers + 2 GEM layers)
    Simulation results shown for local reconstruction used ~8 ns resolution
Charge 2b

## Slide 68: Trigger requirements
Algorithms for GEM-CSC integrated triggers developed for Technical Proposal using CMSSW 62X in PU140 non-aging conditions.
TP studies with GE2/1 trigger were carried out using single GE2/1 super chamber (2 hits)
Improvements to CSC stub building are significant!
Prompt Muons will be reconstructed with the tracker+muon system in Phase-II with excellent momentum resolution and dramatic rate decrease.
Triggering on non-prompt muons at L1 :
  Tracker is inefficient beyond dxy ~ 2mm
  Muon system is very efficienct up to large displacements!

## Slide 69: Trigger on displaced muons
L1 tracking trigger inefficient if dxy over a few mm.
Current L1Mu algorithm finds displaced muons, but the momentum assignment eliminates non-prompt muons as they look “bent” as soft muons
Can measure momentum for displaced muons by requiring muon directions to be aligned in different stations
  Need at least two direction measurements: GE2/1-ME2/1 is that second measurement (in addition to GE1/1-ME1/1)
  Requirements on precision are the same as for “bending angle”
    Proposed granularity is adequate for this purpose
Charge 2b

## Slide 70: “Non projective layout” (closest chamber to the IP)
All strips have the same lenght 
Different h angle covered by the strips
Different particle rate on all strips (h partition)
d hn
d hI
d hII
d h’ ≠ d h’’ ≠d h’’’ ≠ …….≠d hn
I.P.

## Slide 71: “Non projective layout” ( chamber far from the IP)
Strips in module 1 have same length of strips in module 2
Strips in module 3 have same length of strips in module 4

Different h angle covered by the strips
Different particle rate on all strips (h partition)
d hn
d hI
d hII
d h’ ≠ d h’’ ≠d h’’’ ≠ …….≠d hn
Module 1 and 2
Module 3 and 4
I.P.

## Slide 72: Readout Board internal view
Internal view
10 mm
0.2 mm strips separation both in phi and eta (0.2 phi 0.5 eta in GE1/1)
17 mm, the distance between the edge of the PCB and the first strip
19 mm, the distance between the edge of the PCB and the first strip

## Slide 73
HV schema for GE2/1 : Option A
28 ch. per chamber (56 ch. Per super-chamber)
Two HV Module, GE1/1 model, (multichannel system), to power one GE2/1 chamber.
Four HV Module for a super chamber
72 HV Modules (x 7 channel) per EndCap
144 HV Modules in total

## Slide 74
HV schema for GE2/1 : Option A
14 ch. per chamber (24 ch. Per super-chamber)
One HV Module, GE1/1 model (multichannel system), to power one GE2/1 chamber.
Two modules will be necessary to power a super-chamber which will cover 20 Deg.
36 HV Modules (x 7 channel) per EndCap
72 HV Modules in total

## Slide 75: Production organization
PCB production site (probably one)
Foils production site M1 / M2
Foils production site M3 / M4 (CERN)
Prod. Site M1
Prod. Site M2
Prod. Site M3
Prod. Site M4 (CERN)
Integrationsite (904)
CERN
Minor components procurements
(CERN)
To P5
Charge 8
M1
M2
M3
M4

## Slide 76: Discharge probability (ME0)
Consequences of discharging:
Accumulation of 450 discharges during the entire test, in few cm2
Thin deposition of copper oxide in the irradiated region (all GEM foils)
Superficial copper etching near the rim of the holes
These effects do not affect the operation of the detector (non-destructive discharges)
Conclusions:
~ 7500 discharges expected in the whole chamber during the entire ME0 life of the detectors
expected safe operation at gas gains up to several 104

## Slide 79
NETWORK
SY 1527 + A1515
A laptop has been configured under Linux OS to…
CONTROL the mainframe
MONITOR PICOAMMETER (RS232)
act as DATA LOGGER (store data)
MONITOR trend of currents and Voltages
GEM Phase 2 R&D: Neutron Discharge Probability
V-I Control and Monitor
A. Braghieri, INFN Pavia
Oct 17, 2016
GEM3 det
Keithley 6487 picoamm