## Slide 1: Studies on the beam induced effects in the FCC-hh
Ignasi Bellafont
WP4 Meeting 05
November 07th 2016

## Slide 2
OUTLINE
1. Previous status
2. Expanded thesis proposal
3. High power density issue in the beam screen - Absorber design
4. Low pumping speed issue - Beam screen optimization
5. Roughness role in the reflector design
6. Heat load on the cold bore
7. Pumping speed improvement
8. Reflectivity and PSD future studies
9. Conclusions, next steps

## Slide 3
LAST MEETING STATUS
The 6 months training of the resource allocated at CERN was already completed, according to the foreseen plan
ANKA setup synchrotron radiation power distribution, slits aperture, and pressure level were studied and found, including its variants, in a preliminary way. No major issues were found, and the pressure levels it will achieve were found to be adequate for the experiments
The power and flux distribution and the vacuum status of the FCC-hh bending magnets were studied, and the first simulations were performed. Some major issues were identified, as some high power density areas and a low pumping speed, meaning a high scrubbing time of operation until being able to achieve the necessary molecular density levels

## Slide 4
THESIS PLAN DETAILED PROPOSAL
After the received training, the project necessities were better identified and therefore the working plan and necessary studies were further detailed:
  FCC-hh cryogenic vacuum system - The pressure contribution of the beam induced effects will be studied, resulting in one total equivalent molecular density inside the BS for different system conditions of the FCC-hh
Beam induced vacuum effects
Photon stimulated desorption
Electron cloud
Ion induced desorption
Photon-stimulated desorption + Ion induced desorption
+ Electron induced desorption + Thermal outgassing
Total Pressure (P) =

## Slide 5
THESIS PLAN DETAILED PROPOSAL
  A final viability report regarding the vacuum status due to the beam induced effects, for the steady state status, will be then written, mainly focusing in the PSD effect
  ANKA prototype - The pressure evolution and the photon flux distribution will be analyzed for different prototype configurations and design options. These simulated results will be thus compared with the experimental ones, allowing their correctness a higher confidence with the simulations of the FCC-hh vacuum system
  General suggestions for the future work, mitigating measures for the identified issues and a comparison with the LHC cryogenic vacuum system will be included in the final report

## Slide 6
RADIATION ABSORBER
Due to the secondary chamber design and angle between dipoles, there is one region at the end of the beam screen where the radiation could reach power densities higher than 3kW/cm2, due to the forward reflection and direct radiation impact (for ideal beam). This could raise too much the temperatures and generate an excessive thermal stress
To deal with this high density, an absorber has been designed. Focusing the SR on this absorber would also improve the cooling efficiency and would lower the PSD
FCC-hh DIPOLE
FCC-hh DIPOLE
Beam direction
Affected area
W/cm2
Power distribution at the end of the FCC-hh beam screen
61 W SR power
Another spot of 40W at the end

## Slide 7
This 22mm long Cu/Glidcop absorber, would be placed out of the cryogenic region, at the beginning of the bending magnets interconnection
Its design and final position is still tentative, the final geometry of the interconnection still has to be defined
It can be symmetrical to avoid reverse mounting errors
Main idea proposed by C. Garion
RADIATION ABSORBER
Slope
SS covers
Cu main absorber

## Slide 8
RADIATION ABSORBER
S. steel, welded to the BS and brazed to the Cu
22mm long, 12.8o slope
Possible absorber location
Beam direction

## Slide 9
W/cm2
61 W (12.6% T P)
800W/cm2 max
For an ideal beam, this end absorber can reduce the maximum power density more than 4 times on the slope area, reducing the possibility to have a thermomechanical failure
Redirecting as much SR as possible to the absorber, not only the cooling efficiency improves, the total outgassing is also decreased. It can be done changing the reflector’s shape or reducing its roughness
Carnot efficiency of refrigerators
RADIATION ABSORBER
Beam direction

## Slide 10
LOW PUMPING SPEED ISSUE
Chart: Dynamic H2 PSD molecular density over time, for FCChh 50 TeV 500mA
| 1 | 24 | 72 | 168 | 336 | 504
Molecular density | 3321870000000000 | 707170000000000 | 410170000000000 | 266170000000000 | 184970000000000 | 151970000000000
FCChh requirement | 200000000000000 | 200000000000000 | 200000000000000 | 200000000000000 | 200000000000000 | 200000000000000
LHC requirement | 1000000000000000 | 1000000000000000 | 1000000000000000 | 1000000000000000 | 1000000000000000 | 1000000000000000
Chart: Dynamic H2 PSD molecular density over time, for FCChh 50 TeV 500mA
| 1 | 24 | 72 | 168 | 336 | 504
Molecular density | 3321870000000000 | 707170000000000 | 410170000000000 | 266170000000000 | 184970000000000 | 151970000000000
FCChh requirement | 200000000000000 | 200000000000000 | 200000000000000 | 200000000000000 | 200000000000000 | 200000000000000
LHC requirement | 1000000000000000 | 1000000000000000 | 1000000000000000 | 1000000000000000 | 1000000000000000 | 1000000000000000
336h (2 weeks)
1.86∙1014 H2/m3
Molecular desorption yield tendency example
In the last meeting we saw the molecular density coming from the PSD effect was too high, and the time to achieve the pressure requirements would take longer than acceptable
We had then to optimize the system to reduce the molecular density

## Slide 11
BS PUMPING SPEED OPTIMIZATION
To reduce the total molecular density inside the beam screen coming from the PSD contribution, we can:
  Trigger the PSD effect as far as possible from the main chamber
  Lower the outgassing, by redirecting the radiation to be absorbed in high flux density areas, or using low PSD yield materials
  Increase the conductance of the main chamber to the cold bore, increasing the pumping speed
One of the initial FCC-hh BS cross sections

## Slide 12
BS PUMPING SPEED OPTIMIZATION
For now, the most effective and with most potential solution is to increase the pumping speed of the system, easing the pass of the molecules to the cold bore:
  Increasing the size of the slot which divides the primary chamber and the secondary one, where photons are absorbed
  Increasing the size of the pumping holes. This size has a limit, since too much radiation can be leaked towards the cold bore surpassing its limit
One of the initial FCC-hh BS cross sections

## Slide 13
PUMPING HOLES OPTIMIZATION
The bigger they are, the higher the pumping speed, as the molecules have more probability to pass trough them towards the cold bore, were they are pumped.
However, we have three limitations:
  The beam cannot see the pumping holes, they have to be screened, as this could increase the impedance
  We can’t have asymmetry and make bigger the side where we don’t have SR, to reduce the risk of mounting the BS in a wrong way
  The bigger they are, the more radiation is also leaked and reaches the cold bore. So we had to find a maximum thermal radiation budget which will limit the slots shape and aperture
A previous FCC-hh beam screen geometry, with the pumping holes distribution

## Slide 14
PUMPING HOLES OPTIMIZATION
Beam gas scattering, average
0.035 W/m
Max conduction, sliding rings
Leaked radiation power
Gray body thermal radiation
0.0043 W/m
< 0.001 W/m
< 0.0001 W/m
Total heat load
FCC-hh cold bore heat load
0.046 W/m
0.049 W/m
?
0.0023 W/m
< 0.05 W/m
< 0.1 W/m
LHC cold bore heat load
The total thermal budget for the 1.9K cold bore is the 0.1W/m/aperture, (given by C. Kotnig, cryogenics team, internal communication)
Due to the electron shield in the LHC and the design of the FCC-hh BS, the thermal load due to the electron cloud in the CB has been neglected
For the leaked radiation, we have around 0.0027 W/m budget left, around 0.038W per dipole and beam

## Slide 15
PUMPING HOLES OPTIMIZATION
+
Proton (charge +)
Gas molecule
+
+
+
+
+
Cross-section area,
around 100mbarn for H2
Molecular
density
Beam
energy
Scattered protons warm up the cryogenic magnets
For a hydrogen equivalent density of 2∙1014 H2/m3, the total amount of scattered power is 0.05 W/m, with a beam gas lifetime of 463h
Around the 8% of this power is absorbed in the beam screen, though (M.I Besana, 2015), so the resulting power in the cold bore is 0.046 W/m

## Slide 16
PUMPING HOLES OPTIMIZATION
Power distribution in the reflector, in W/cm2
W/cm2
H2/m3
M. density order of magnitude
Exponential increase of power density
p+ beam
High radiation density area
We need to reduce the number of Cu rings!
Best area to place the pumping holes
Molecular density, in H2/m3

## Slide 17
PUMPING HOLES OPTIMIZATION
Taking advantage as much as possible of the thermal budget we found, the resulting holes found size has been 10mm, with a changed and optimized copper ring distribution allowing a 23.75mm length
Chart: Total leaked SR power per BM vs holes length
| 0 | 5 | 7 | 10
 | 0 | 0.009 | 0.01635 | 0.034
P(W) ≈ 2E-05x3 + 6E-05x2 + 0.0011x
0.038 W budget limit
Limit to the high radiation area, where there is no shadow from the ribs, change of slope
10mm
best size
Making the holes axially longer takes advantage of the space more efficiently

## Slide 18
REFLECTOR ROUGHNESS IMPACT
Increasing the roughness in the reflector, makes the radiation to be scattered in a more diffuse way, not being stopped by the ribs and being leaked to the cold bore
With higher reflector roughness, the budget is surpassed! So it should be polished
Better polished reflector
Higher pumping speed
Less pressure, less heat leaked to the cold bore and reduced operating costs!
Lower BS temperature
Specular probability of the incident radiation
A recommended manufacturing roughness shall be fixed!
Reflector roughness
200nm
Other areas
σ
T
σ/T
Cold bore P
5500nm
10nm
3100nm
0.036
0.0032
2.38 mW/m
Reflector roughness
200nm
Other areas
5500nm
0.036
5.31 mW/m
200nm
5500nm
0.036
Reflectivity used data - Pure Fe/Cu
(2.7mW/m budget)

## Slide 19
W/cm2
Cold bore leaked radiation ray tracing - The openings marks of the pumping slots are easily noticeable
LEAKED RADIATION TO THE CB
The transversal sides of the drilled holes act as a 2nd barrier to the radiation, as it hits them perpendicularly, keeping safer the cold bore
On the other hand, increasing the roughness of the ribs, could reduce the leaked radiation, decreasing their reflectivity
BS external surface, with the pumping holes
Cold bore internal irradiated surface
2.38 mW/m SR power

## Slide 20
TOTAL HEAT LOAD DISTRIBUTION
Beam gas scattering, average
Max conduction, sliding rings
Leaked radiation power
Gray body thermal radiation
Total heat load
FCC-hh cold bore heat load
0.046 W/m
0.049 W/m
0.00238 W/m
0.0023 W/m
0.09968 W/m
Under 0.1W, OK!
The first estimations show it is possible to achieve reasonably the maximum budget
Chart: 1.9K Heat load distribution
| Beam-gas scattering | Suports conduction | Leaked radiation | Thermal radiation
Beam-gas scattering Suports conduction Leaked radiation Thermal radiation | 0.046 | 0.049 | 0.00238 | 0.0023
The heat load with the highest potential to be reduced is the conduction of heat from the beam screen to the cold bore through the metallic supports, as it is highly geometry and material dependent

## Slide 21
The slot can’t be indefinitely increased, as opening it too much would result in an excess of radiation being backscattered to the main chamber
Besides, opening it worsens the impedance and the mechanical resistance during a quench
It has to cover, at least, most part of the main reflected radiation, while guaranteeing an optimal conductance
Monte Carlo simulation tools can help us to find an optimal size
Specular reflection
Diffuse reflection
Slot size
Plane normals
MAIN BEAM SCREEN SLOT SIZE

## Slide 22
After testing many configurations, it was seen the optimal size for a 72h max photon dose is around 4.2mm
However, as Synrad does not take into account the photon energy, and the scattered radiation to the main chamber has low one, the effect of the backscattered radiation is in fact lower. Taking also into account possible misalignments, we would recommend a 5mm slot
5mm best size, for now
Time lapse
72h
Pumping holes size
7mm
PSD data
Bk. 316SS H2 293K 4 keV
Reflector roughness
σ/T = 0.0032
MAIN BEAM SCREEN SLOT SIZE
Chart: Average MD vs slot size
| 3 | 4 | 5 | 7 | 7.6
 | 135000000000000 | 116000000000000 | 119000000000000 | 143000000000000 | 159000000000000

## Slide 23
GEOMETRY COMPARISON
Previous geometry, July 2016
WP4 5th meeting November 2016
Holes length
∼5.3mm
Holes width
1.5mm
Central slot
2.28mm
Av. H2 p. speed 50K
∼127 l/s/m
Previous
10mm
23.75mm
5mm
∼ 530 l/s/m
Current
x4!

## Slide 24
MOLECULAR DENSITY RESULTS
9.88·1013 H2/m3
Pumping Holes length
10mm
Holes area coverage
67’6 %
Reflector roughness
σ/T = 0.0032
Average arc density
Time lapse
72h
Average arc pressure
6.56 ·10-10 mbar
Main slot aperture
5mm outwards
Beam direction
Drift space between dipoles
1.43m
Bending magnet 14.3m
PSD data
Bk. 316 SS H2 293K 4 keV
Ribs
60K
Main reflector
Cold bore
Inner copper
60K
1.9K
47K
Other areas
50K
End absorber
100K
Temperatures
4.97·10-6 mbar·l/s
Outgassing per BM
Molecular density
profile only PSD H2

## Slide 25
PUMPING SPEED IMPROVEMENT
Due to the cleaning effect, the PSD decreases gradually with time
If only this effect was rising the pressure, and counting only hydrogen, in less than one day of maximum dose in nominal conditions, the required density would be met (SS room temperature PSD data)
Further studies with all gases and the remaining effects will be carried out
Chart: PSD H2 molecular density over time, for FCC-hh BS 50 TeV 500mA
| 1 | 24 | 72 | 168 | 336 | 504
Previous geometry | 3321870000000000 | 707170000000000 | 410170000000000 | 266170000000000 | 186170000000000 | 151970000000000
New geometry | 786790000000000 | 164720000000000 | 98800000000000
FCChh requirement | 200000000000000 | 200000000000000 | 200000000000000 | 200000000000000 | 200000000000000 | 200000000000000
LHC requirement | 1000000000000000 | 1000000000000000 | 1000000000000000 | 1000000000000000 | 1000000000000000 | 1000000000000000
Chart: PSD H2 molecular density over time, for FCC-hh BS 50 TeV 500mA
| 1 | 24 | 72 | 168 | 336 | 504
Previous geometry | 3321870000000000 | 707170000000000 | 410170000000000 | 266170000000000 | 186170000000000 | 151970000000000
New geometry | 786790000000000 | 164720000000000 | 98800000000000
FCChh requirement | 200000000000000 | 200000000000000 | 200000000000000 | 200000000000000 | 200000000000000 | 200000000000000
LHC requirement | 1000000000000000 | 1000000000000000 | 1000000000000000 | 1000000000000000 | 1000000000000000 | 1000000000000000
336h (2 weeks)
1.86∙1014 H2/m3
∼17h
1.90∙1014 H2/m3

## Slide 26
MISALIGNEMENT STUDY
To perform an approach to the real geometry conditions, a misalignment study has been carried out, moving the beam 1mm upwards
The leaked power is slightly lower, while the molecular density is slightly worse
The radiation is directed forward with a narrower angle, increasing the absorber power
W/cm2
Molecular density 72h
Cold bore power
Absorber power
Aligned
9.88·1013 H2/m3
0.034 W
63 W
Misaligned
9.93·1013 H2/m3
0.032 W
86 W
Inner copper power
3.3 W
3.7 W
Ribs power
165 W
73 W
Stretching the sharp point of the reflector can produce the same effect in ideal conditions

## Slide 27
RAY TRACING FAST RESULTS
W/cm2
Ribs
32.9%
Reflectors
Cold bore
Inner copper
29.3%
0.007%
6.56%
End absorber
12.6%
% of Total BM Power, 502W
Drift space
8.1%
68% of the incident power is reflected on the reflector

## Slide 28
RAY TRACING FAST RESULTS
Photons/s/cm2
Ribs
29.6%
Reflectors
Cold bore
Inner copper
21.4%
0.27%
4.9%
End absorber
12.8%
% of Total BM Flux, 2.1E18 ph/s
Drift space
5.9%
78% of the incident flux is reflected on the reflector

## Slide 29
REFLECTIVITY STUDIES
There is no experimental data of the reflectivity of the FCC-hh’s beam screen steel in the X-Ray range. Knowing accurately its reflectivity properties would increase the reliability of the performed simulations
Some measurements are foreseen to be performed at BESSY II, Germany, by the end of the year by R. Cimino with the samples provided by CERN, and if allocated the beamtime, more measurements will be done next year
Special thanks to H. Kos for the machining
Three materials with different roughness will be analyzed: SS P506 (FCC and LHC steel, most important one), 316LN (ANKA steel) and copper with SALT treatment

## Slide 30
PROJECT NEEDS - FURTHER DATA
All these molecular density simulations have been performed with the SS data for room temperature, so they are still not very accurate
As done for the LHC, we should characterize the PSD yield at the BS cryogenic temperatures, around 40K-70K, for stainless steel (P506 better..)! The difference could be of an order of magnitude
Ideally, the critical energy should be as close as possible to 4.3keV
The initial yield would be lower, but the cleaning rate would be slower, too
PSD yield dependence of temperature example
(V. Baglin et al, Vacuum 67, 421-428)

## Slide 31
CONCLUSIONS
The FCC-hh beam screen pumping speed has been increased, being the new design capable of meeting the pressure requirements for nominal conditions in a much shorter amount of time
The heat load on the cold bore has been analyzed, still existing potential to reduce it
The surface finishing plays an important role in the manufacturing specifications, it should be rough were the radiation has to be absorbed, and smooth were reflected
The future reflectivity measures, and a possible PSD yield measurement for P506 stainless steel, will allow a higher reliability and accuracy in the simulations

## Slide 32
NEXT STEPS
Detailed design of the end absorber, and the drift space design, to deal with the directly irradiated areas
The total pressure contribution of the electron and ion induced desorption shall be studied, as done with the PSD, to completely study all the beam induced vacuum effects
The beam screen design will be further improved and reanalyzed, following possible future geometry changes, to maximize the pumping speed and thus reducing the pressure
The pressure contribution of the outgassing generated when warming up some possible beam screen coatings will be studied

## Slide 33
THANK YOU FOR YOUR ATTENTION !