## Slide 1: Optimisation of the CLIC Damping rings for the project re-baselining
H. Ghasem, S. Papadopoulou,
F. Antoniou and Y. Papaphilippou
CLIC implementation meeting
November 4th, 2016

## Slide 2: CLIC DR challenges and adopted solutions
High-bunch density in all three dimensions
  Intrabeam Scattering effect reduced by choice of ring energy, lattice design, wiggler technology and alignment tolerances
  Electron cloud in e+ ring mitigated by chamber coatings and efficient photon absorption
  Fast Ion Instability in the e- ring reduced by low vacuum pressure and large train gap
  Space charge vertical tune-shift limited by energy choice, reduced circumference, bunch length increase
  Other collective instabilities controlled by low –impedance requirements on machine components
Repetition rate and bunch structure
  Fast damping times achieved with SC wigglers
  RF frequency reduction @ 1GHz considered due to many challenges @ 2GHz (power source, high peak and average current, transient beam loading)
Output emittance stability
  Tight jitter tolerance driving kicker technology
Positron beam dimensions from source
  Pre-damping ring challenges (energy acceptance, dynamic aperture) solved with lattice design

## Slide 3: Adapting the DR complex to a new CLIC baseline
Pre-damping rings revision
  Potentially remove the electron pre-damping ring
  Potentially replace the positron pre-damping ring with a booster ring
Review DR based on recent design developments and collaboration effort in the low emittance rings community (both beam dynamics and technology)
    New DR arc cell (longitudinally varying bends) and SC wigglers for circumference reduction (collective effects)
    RF frequency choice and LLRF technical development
    Stripline kicker + pulser tests
    SC wiggler tests and developments

## Slide 4: 1 vs. 2 GHz RF system
The cost difference due to the RF frequency choice in the DR (scaled with the total voltage) is minor
The cost impact of an additional delay loop for 1 GHz is small (but non negligible)
The technological risk of choosing the 2 GHz option, after conceptual design of A. Grudiev, is equivalent with the train recombination for the 1 GHz option
Choose 2 GHz as baseline and work with low emittance rings community to prove efficient handling of beam loading transients
  Collaboration with ALBA (F. Perez et al.) and LBNL (J. Byrd et al.) for the conceptual design of a 1.5 GHz active RF system
  Collaboration with T. Mastorides (CalPoly) for longitudinal beam dynamics and LLRF (T. Argyropoulos, A. Grudiev)

## Slide 5: Emittance targets
2008

## Slide 6: Emittance targets
2016

## Slide 7
Parameters, Symbol [Unit] | uniform
Circumference, C [m] | 427.5
Norm. horiz. emittance , gex [nm-rad] * | 657
Current design of the main CLIC DRs, E=2.86 GeV
The aim
Reduce the number of arc TME cells->longitudinally variable bends
Reduce the number of wigglers->higher wiggler field
500 nm (700 nm) required output emittance
*The emittance is calculated using the Bjorken-Mtingwa formalism through MADX.
Using the Piwinski form., the original design (with the uniform dipoles) reaches the target horizontal emittance.

## Slide 8
The parameterization of the emittance reduction factor FTME with the bending radii ratio r and the lengths ratio l, always for l>0.1.
Step profile
Trapezium profile
Longitudinally variable bends
Emittance reduction factor
Bending radii ratio
Lengths ratio

## Slide 9
Optimization of the arc TME cell
Parametrization with the phase advances
The parameterization of the detuning factor er (er = ex /eTME) and of the horizontal and vertical chromaticities (xx and xy) with the horizontal and vertical phase advances mx and my , only for the trapezium profile.
Parametrization with the drift lengths
The horizontal chromaticity xx is parameterized with the drift lengths s1, s2, s3 for the TME, for the step (left) and the trapezium (right) profile

## Slide 10
Optimization of the arc TME cell
When properly using the variable bends, lower emittances than the current design’s ones are reached. This gives us the flexibility to reduce the existing arcs’ TME cells, till the point we get the required output parameters (because the aim is not only to get a lower emittance, but also a shorter ring).
removing TME cells
checking the output parameters
procedure followed in MADX
The optimal solutions are found to be Nd=96 for the step and Nd=90 for the trapezium profile, instead of the existing arc’s cell that are Nd=100.

## Slide 11
Optimization of the wiggler FODO cell
When increasing the wigglers’ peak field Bw up to a certain point, the emittance and the IBS effect are lowered [3].
Removing some FODO cells from the existing straight section (NFODO=13 per section) is possible.
NFODO=10 per straight section
Results obtained after the optimization of the arc TME cell.
Based on the technological restrictions, a new working point for the damp. wiggler is proposed to be at 3.5T (prev. 2.5T), with 49mm period length[4]
Step profile
Trapezium profile
Parametrization of the steady state emittance and the IBS effect with the wiggler’s peak field Bw
Nb=4.07e+09

## Slide 12
Parameters, Symbol [Unit] | uniform | step | trapezium
Number of arc cells/wigglers | 100/52 | 96/40 | 90/40
Dipole field (max/min), B [T] | 0.97/0.97 | 1.77/1.01 | 1.77/0.73
horiz. /vert. chromaticities xx/xy | -113/-82 | -135/-76 | -126/-72
Wiggler peak field Bw [T] for length Lw =2m | 2.5 | 3.5 | 3.5
Wiggler period, lw [cm] | 5.0 | 4.9 | 4.9
Mom. compaction, ac [10-4] | 1.3 | 1.3 | 1.2
Energy loss/turn, U [MeV/turn] | 4 | 5.7 | 5.7
Energy spread (rms), sd [%] | 0.12 | 0.13 | 0.13
Bunch length (rms), ss [mm] | 1.8 | 1.6 | 1.6
Long. emittance , el [keV m] | 5.9 | 6.1 | 6.0
Damp. times, (tx, ty, tl) [ms] | (2.0, 2.0, 1.0) | (1.2, 1.3, 0.6) | (1.2, 1.2, 0.6)
IBS factors hor./ver./long. | 2.2/1.5/1.2 | 1.4/1.5/1.1 | 1.4/1.5/1.1
Norm. horizontal emittance (with IBS), gex [nm] | 681 | 502 | 500
Norm. vertical emittance (with IBS), gey [nm] | 5 | 5 | 5
Circumference, C [m] | 427.5 | 374.1 (-14%) | 359.4 (-19%)
-Collaboration with the Advanced Light Source ALS (LBNL) for their machine upgrade.
-Magnet design, based on the variable bends specifications, is studied in CIEMAT, Spain.
Nb=4.07e+09
DRs parameters, 2GHz and E=2.86 GeV

## Slide 13
Parameters, Symbol [Unit] | uniform | step | trapezium
Number of arc cells/wigglers | 100/52 | 96/40 | 90/40
Dipole field (max/min), B [T] | 0.97/0.97 | 1.77/1.01 | 1.77/0.73
horiz. /vert. chromaticities xx/xy | -113/-82 | -135/-76 | -126/-72
Wiggler peak field Bw [T] for length Lw =2m | 2.5 | 3.5 | 3.5
Wiggler period, lw [cm] | 5.0 | 4.9 | 4.9
Mom. compaction, ac [10-4] | 1.3 | 1.3 | 1.2
Energy loss/turn, U [MeV/turn] | 4 | 5.7 | 5.7
Energy spread (rms), sd [%] | 0.12 | 0.13 | 0.13
Bunch length (rms), ss [mm] | 1.8 | 1.6 | 1.6
Long. emittance , el [keV m] | 5.9 | 6.1 | 6.0
Damp. times, (tx, ty, tl) [ms] | (2.0, 2.0, 1.0) | (1.2, 1.3, 0.6) | (1.2, 1.2, 0.6)
IBS factors hor./ver./long. | 2.8/1.8/1.2 | 1.6/1.8/1.1 | 1.3/1.8/1.1
Norm. horizontal emittance (with IBS), gex [nm] | 883 | 568 | 541
Norm. vertical emittance (with IBS), gey [nm] | 6 | 6 | 6
Circumference, C [m] | 427.5 | 374.1 (-14%) | 359.4 (-19%)
DRs parameters, 2GHz and E=2.86 GeV
-Collaboration with the Advanced Light Source ALS (LBNL) for their machine upgrade.
-Magnet design, based on the variable bends specifications, is studied in CIEMAT, Spain.
Nb=5.7e+09

## Slide 14
The DRs’ layout has a racetrack shape and consists of two arcs and two long straight sections.
The arcs are composed of theoretical minimum emittance (TME) cell with longitudinally variable bends and the straight sections are based on FODO cell filled with high field super conducting damping wigglers.
Each arc/straight section includes of 42 TME/10 FODO cells and there are totally 90 dipoles and 40 superconducting wiggler magnets in the whole DR.
There are four matching sections grouped in two types to match the optics of straight section to the optics of arc section and vice versa.
General layout of CLIC damping ring (DR)

## Slide 15
Parameters | Value
Energy (GeV) | 2.860
Circumference (m) | 359.440
Tune (-/-) | 45.2895/8.3133
Natural emittance (pm.rad) | 75.8924
Natural chromaticity | -128.789/-61.832
1st order mom. com. factor | 1.2478E-4
Energy spread | 1.2745E-3
Energy loss per turn (MeV) | 5.721
Damping time (ms/ms/ms) | 1.179/1.199/0.604
TME cell;
Length= 2.45 m
ψx/2π= 0.442
ψy/2π= 0.042
FODO cell;
Length= 5.969
ψx/2π= 0.238
ψy/2π= 0.096
wiggler (l=2 m, B=3.5 T, λ=49 mm)
Dispersion suppressor;
Length= 8.56
ψx/2π= 0.851
ψy/2π= 0.709
Dispersion suppressor;
Length=8.57
ψx/2π= 0.851
ψy/2π=0.726
Optical functions and parameters

## Slide 16
ΔP/P=0
ΔP/P=0.3%
ΔP/P=-0.3%
DA: The Physical stable space for the particles
The injected beam normalized emittance and energy spread;
For electron DR: εxn=10 μm and εyn=10 μm, δ=0.1%
For positron DR: εxn=65 μm and εyn=10 μm, δ=0.1%
Phase space & DA
Electron DR
Positron DR

## Slide 17
ΔP/P=0
ΔP/P=0.3%
ΔP/P=-0.3%
Frequency Map Analysis

## Slide 18
 | Order | Multipole | Systematic | Random
Dipole, Bn/B1 @ 10 mm | 2 | Quadrupole | 1.00 *10-4 | 1.00*10-3
 | 3 | Sextupole | 1.50*10-4 | 1.00*10-3
 | 4 | 8-pole | 0.00 | 1.00*10-3
 | 5 | 10-pole | 5.00*10-5 | 1.00*10-3
 | 6 | 12-pole | 0.00 | 1.00*10-3
 | 7 | 14-pole | 5.00*10-4 | 1.00*10-3
 | 8 | 16-pole | 0.00 | 1.00*10-3
Quadrupole, Bn/B2 @ 10 mm | 3 | Sextupole | 0.00 | 1.00*10-3
 | 4 | 8-pole | 0.00 | 1.00*10-3
 | 5 | 10-pole | 0.00 | 1.00*10-3
 | 6 | 12-pole | 1.00*10-6 | 1.00*10-3
 | 7 | 14-pole | 0.00 | 1.00*10-3
 | 8 | 16-pole | 0.00 | 1.00*10-3
 | 9 | 18-pole | 0.00 | 1.00*10-3
 | 10 | 20-pole | 1.00*10-7 | 1.00*10-3
 | 11 | 22-pole | 0.00 | 1.00*10-3
 | 12 | 24-pole | 0.00 | 1.00*10-3
 | 13 | 26-pole | 0.00 | 1.00*10-3
 | 14 | 28-pole | 1.00*10-8 | 1.00*10-3
 | 15 | 30-pole | 0.00 | 1.00*10-3
 | 16 | 32-pole | 0.00 | 1.00*10-3
 | 17 | 34-pole | 0.00 | 1.00*10-3
 | 18 | 36-pole | 1.00*10-8 | 1.00*10-3
Sextupole, Bn/B3 @ 10 mm | 4 | 8-pole | 0.00 | 1.00*10-3
 | 5 | 10-pole | 0.00 | 1.00*10-3
 | 6 | 12-pole | 0.00 | 1.00*10-3
 | 7 | 14-pole | 0.00 | 1.00*10-3
 | 8 | 16-pole | 0.00 | 1.00*10-3
 | 9 | 18-pole | 1.00*10-6 | 1.00*10-3
 | 15 | 30-pole | 1.00*10-7 | 1.00*10-3
 | 21 | 42-pole | 1.00*10-6 | 1.00*10-3
 | 26 | 54-pole | 5.00*10-7 | 1.00*10-3
 | 33 | 66-pole | 1.00*10-7 | 1.00*10-3
 | 39 | 78-pole | 5.00*10-8 | 1.00*10-3
 | 45 | 90-pole | 1.00*10-8 | 1.00*10-3
DA & multipoles
Electron DR
Positron DR

## Slide 19
Misalignments- Combined dipole
Combined Dipole bare magnetic field
Combined horizontal dipole
generated by
Horizontal displacement (Δx), Roll (θ)
Skew quadrupole
generated by
Roll (θ)
Vertical constant term dipole
generated by
Vertical displacement (Δy), Roll (θ)
Combined Dipole magnetic field in presence of alignment errors (Δx, Δy, θ)
Ignoring Δxsinθ and Δysinθ terms

## Slide 20
Quadrupole magnetic field
Orthogonal quadrupole
generated by
Roll (θ)
Skew quadrupole
generated by
Roll (θ)
Horizontal/vertical constant term dipole
generated by
Horizontal/vertical displacement (Δx/Δy), Roll (θ)
Quadrupole magnetic field in presence of alignment errors (Δx, Δy, θ)
Ignoring Δxsinθ and Δysinθ terms
Misalignments- Quadrupole

## Slide 21
Sextupole magnetic field
Orthogonal sextupole
generated by
Roll (θ)
Skew quadrupole
generated by
Vertical displacement (Δy), Roll (θ)
Orthogonal quadrupole
generated by
Horizontal displacement (Δx), Roll (θ)
Sextupole magnetic field in presence of alignment errors (Δx, Δy, θ)
Ignoring Δxsinθ and Δysinθ terms
Skew sextupole
generated by
Roll (θ)
Misalignments- Sextupole

## Slide 22
Correctors installed
242 vertical; (84 per arc, 8 per DS-I, 9 per DS-II, 20 per LSS)
262 horizontal; (84 per arc, 8 per DS-I, 9 per DS-II, 30 per LSS)
Correctors
Monitors installed
262 BPM; (84 per arc, 8 per DS-I, 9 per DS-II, 30 per LSS)
Skew quads
2 sextupole families in the arcs
Skew quads installed as windings in the sextupoles.

## Slide 23
The variation of the vertical orbit at the BPM position sj resulting from the corrector kick θi at si is expressed by;
Correction method – orbit response matrix
Feed misalignment error

## Slide 24
Correction method- vertical dispersion
The differential equation for vertical dispersion with coupling (to first order, corrector kick neglected) is
which assumes quadrupole rolls and skew quadrupoles as major coupling contributors, ϕ is the roll angle of a normal
quadrupole, S is the skew quad strength and ηx is the horizontal dispersion at the coupling source point.
The self-consistent solution of dispersion when a skew quad strength changes by Δ(kl) is
This is the response of dispersion function to a unit change in skew quad strength.
Feed misalignment error

## Slide 25
Accumulated histogram;
For 100 machine samples, the vertical emittance due to the dipole vertical displacement up to 200 μm is below than 1 pm rad.
For the case of Δy = 150 μm;
Dipole vertical offset

## Slide 26
Accumulated histogram;
Dipole roll up to 1 mrad is tolerable.
For the case of Δϕ = 500 μrad;
Dipole roll

## Slide 27
Accumulated histogram;
Vertical emittance is very sensitive to misalignment of quads.
Vertical emittance due to the quad vertical offset up to 20 μm is below than 1 pm rad for 100 machine samples.
For the case of Δy = 20 μm;
Quadrupole vertical offset

## Slide 28
Accumulated histogram;
For 100 machine samples, the vertical emittance up to 200 μrad quadrupole roll is below than 1 pm rad.
For the case of Δϕ = 150 μrad;
Quadrupole roll

## Slide 29
Accumulated histogram;
Vertical emittance is very sensitive to misalignment of sextupoles.
For 100 machine samples, vertical emittance due to the sextupole vertical offset up to 20 μm is below than 1 pm rad
For the case of Δy = 25 μm;
Sextupole vertical offset

## Slide 30
Accumulated histogram;
The vertical emittance for the 100 machine sample s is below than 1 pm rad.
For the case of Δϕ = 250 μrad;
Sextupole roll

## Slide 31
Vertical emittance
For 95% of machine samples,
vertical emittance is below than 0.7 pm rad.
Error | Unit | Value
Dipole/quadrupole/sextupole/BPM vertical misalignment | μm | 35/20/20/50
Dipole/quadrupole/sextupole roll | μrad | 80/50/50
BPM roll | μrad | 50
BPM noise | nm | 200

## Slide 32: Next steps
Complete analysis of collective effects with new DR parameters
  Ions, space-charge, e-cloud, impedance budget, feedback specs
Investigate the possibility to replace e-linac by a booster
Continue collaboration with low emittance rings community for experimental tests
  Modeling and protyping of variable dipole bends with CIEMAT (F. Toral)
  Test existing wiggler at ANKA and finalise Nb3Sn short wiggler model
  Test stripline and pulser at ALBA
  Design of a 1.5 GHz active harmonic RF system for ALBA and adapt it to 2 GHz CLIC DR RF system

## Slide 33
Back up slides

## Slide 34: CLIC DR complex challenges
DR complex challenges
  Large injected emittances and energy spread  Requirement of large DA and MA
  Ultra low emittance at extraction
  Repetition time of 20 ms  Fast damping requirement
PDR  efficient injection of the large incoming beams
Main DR  ultra-low emittance generation
The positron beam needs at least 8 damping times to reach equilibrium (w/o taking into account injection, IBS, etc)
   The positron PDR is necessary!
Injected Parameters | e- | e+
Bunch population [109] | 4.7 | 6.4
Repetition frequenzy [Hz] | 50 | 50
Bunch length [mm] | 1 | 9
Energy Spread [%] | 0.1 | 1
Long. emittance [eV.m] | 2000 | 257000
H/V norm. emittance [nm-rad] | 100 x 103 | 7 x 106
Extracted Parameters | PDR e-/e+ | DR e-/e+
Bunch population [109] | 4.1-4.4 | 4.1
Bunch length [mm] | 10 | 1.4
Energy Spread [%] | 0.5 | 0.1
Long. emittance [eV.m] | 143000 | 5000
Hor. Norm. emittance [nm-rad] | 63000 | 500
Ver. Norm. emittance [nm-rad] | 1500 | 5
F. Antoniou

## Slide 35: Electron linac requirements
For non-Gaussian beams the minimum required acceptance:
To avoid an e- PDR:
  In horizontal Rmin < 1 mm-rad
  In vertical Rymin < 1.2 mm-rad
Required emittances from the electron injection linac in order to remove electron PDR
  εxrms= 25 μm-rad
  εyrms= 50 μm-rad
DA of the main DR
F. Antoniou

## Slide 36: The CLIC DR CDR design
Performance parameters of the CLIC DR for the 1 GHz and 2 GHz options in comparison to the V06
  Increased energy (2.4242.86 GeV)
  Reduce the circumference by 15%
  Ultra-low emittances in all 3 planes
  Reduced IBS effect (from 3 to 1.5)
  Reduced space charge tune shift (-0.2  -0.1)
  Lower RF stable phase (70o51o (62o))
F.Antoniou

## Slide 37
Parameters | Highest field section | Lowest field section
Length (cm) | 4.1825 | 5.0550
Field (T) | 1.7666 | 0.8366
Radius (m) | 5.4000 | 11.4028
Def. angle (Deg.) | 0.4438 | 0.2540
K (m-2) | -1.1000 | -1.1000
Gradient (T/m) | -10.4937 | -10.4937
The dipole total length is set to L = 0.58 m as the optimized value.
Each trapezium field profile dipole bends the beam 4 Degrees.
Trapezium field profile dipole

## Slide 38
Two families of sextupole magnets both with the same length of 15 cm in the TME cell are considered to correct the natural chromaticity of ring to +1.
Parameters | SF | SD
Length [cm] | 15 | 
Pole radius [mm] | 15 | 
Sextupole strength [m-2] | -362.6698 | 416.5494
B” (T/m-2) | -3459.7589 | 3973.7531
Pole tip field (T) [R=15 mm] | -0.3892 | 0.44705
Small variation of tune point up to ±0.3 % energy deviation reveals that present sextupole arrangement was good a starting point to perform nonlinear beam dynamics.
Chromaticity correction-Tune shift with energy

## Slide 39
ΔP/P=0
ΔP/P=0.3%
ΔP/P=-0.3%
DA & lost particles
Electron DR
Positron DR

## Slide 40
RF frequency: 2 GHz
Natural radiation loss per turn: 0.57 MeV
Parasitic energy loss per turn: 50 keV
Harmonic number: 2398
RF voltage: 6.055 MV
Over voltage factor: 9.74
RF acceptance: 6.17 %
No essential requirement for the aperture for the DR vacuum system in view of acceptance.
10 mm residual vertical dispersion and 1.5% momentum acceptance are assumed.
εi is assumed to be 10 times larger than the injected beam and the “i” indicates horizontal and vertical directions.
Acceptance
Electron DR
Positron DR

## Slide 41
The IBS algorithm is based on the Bjorken and Mtingwa’s * formula.
Assumed parameters;
No. Particles:4E9
Bunch charge:0.72 nC
Vertical emittance: 0.73 pm
RF voltage=6.055 MV
Harmonic=2398
Length=1.577 mm
Parameters | Without IBS | With IBS | Growth rate (%)
Natural emittance (pm.rad) | 73.752 | 89.847 | 21.823
Energy spread | 1.275E-3 | 1.303E-3 | 2.196
Bunch length (mm) | 1.577 | 1.612 | 2.194
* J.D. Bjorken, S.K. Mtingwa
Intrabeam Scattering, Part. Acc. Vol. 13, 1983, 115-143.
Calculated with ELEGANT
Intra beam scattering

## Slide 42
Closed orbit & vertical dispersion

## Slide 43
Corrector’s strength

## Slide 44
Coupling coefficients

## Slide 45
Tune shift

## Slide 46
Corrected chromaticity

## Slide 47
Misalignments- Vertical offset & roll
Dipole
Quadrupole
Sextupole

## Slide 48
Error | Unit | Value
Dipole/quadrupole/sextupole/BPM vertical misalignment | μm | 80/17/17/50
Dipole/quadrupole/sextupole roll | μrad | 250/80/80
BPM roll | μrad | 50
BPM noise | nm | 200
For 95% of machine samples,
vertical emittance is below than 0.7 pm rad.