## Slide 1: TECHNICAL CHALLENGES OF ACCELERATOR COMPONENTS
Antti Kolehmainen
Tommi Mikkola
on behalf of CERN EN/MME

## Slide 2: CERN EN-MME GROUP
“The mandate of the MME group is to provide to the CERN community specific engineering solutions combining mechanical design, fabrication and material sciences.”

## Slide 3: NEW ACCELERATOR
ELENA:
PROPOSAL 1980’s
PROJECT LAUNCH 2011
1ST BEAM 2016

## Slide 4: FIRST VERSION
MME CONTRIBUTION:
MATERIAL DEVELOPMENT
SIMULATIONS

## Slide 5: DESIGN PHASE
EN-MME CONTRIBUTION:
DETAILED DESIGN OF THE EQUIPMENT
SOURCE SUPPLIERS FOR COMPONENTS
CONSULT THE EQUIPMENT OWNERS ON MANUFACTURING, PLAN MANUFACTURING OF THE REQUESTED EQUIPMENT

## Slide 6: GEOMETRIES
CHALLENGES:
COMPLEX GEOMETRY TO MODEL, DRAW AND MANUFACTURE
TIGHT TOLERANCES, PERFECTION DESIRED
DIFFERENT MATERIALS

## Slide 7: GEOMETRIES
STANDARDIZED PRESENTATION
“LEGAL DOCUMENT”

## Slide 8: MANUFACTURING
REMOVE MATERIAL BY CUTTING
ADDING DEGREES OF FREEDOM ALLOWS MORE COMPLEXE GEOMETRIES
FORM MATERIAL
BEND / ROLL / DRAW
MELT PARTS TO BE JOINED LOCALLY

## Slide 9: MEASURING
WHAT IS THE REQUIRED RESOLUTION?
WE CAN GO TO 0.X μm(1/1000 mm)

## Slide 10: BEAM AND MAGNET ENERGY
ONE LHC BEAM ENERGY ~ TGV TRAIN
DILUTE THE BEAM -> SPREAD INTO A GRAPHITE CYLINDER(EN-MME MATERIAL DEVELOPMENT)
RADIATION IN CERTAIN AREAS
SUPERCONDUCTING MAGNETS INVOLVE CRYOGENICS, SUPERCONDUCTIVITY AND VACUUM IN ONE DEVICE
CHALLENGES:
STOP THE HEAT LOAD – 1 W REMOVED FROM HELIUM NEEDS 1000 W IN ROOM TEMPERATURE
RETAIN COILS WITH HIGH FORCES STATIC
  154 LHC DIPOLES STORED ENERGY~ AIR-CRAFT CARRIER @ 20 km/h
MANAGE THE THERMAL CONTRACTION/EXPANSION

## Slide 11: VACUUM
ULTRA HIGH VACUUM(UHV) = 10-13 bar ~ DEEP SPACE PRESSURE OR ~ 1/10 OF THE PRESSURE IN THE MOON
THE LOWER THE PRESSURE THE LESS UNWANTED COLLISIONS
MATERIAL REQUIREMENTS LEAD OFTEN TO STAINLESS STEEL OR COPPER
MATERIAL QUALITY CLOSELY FOLLOWED
TREATMENTS TO IMPROVE VACUUM
VACUUM FIRING
NEG COATING
CRYO-PUMPING
FOR DESIGNER:
THE LESS CONNECTIONS THE LESS POSSIBLE LEAKAGES
AVOID TRAPPED VOLUMES

## Slide 12: INTEGRATION & PROJECTS
CHALLENGES:
LIMITED SPACE
MANAGE ALL THE COMPONENTS
  FOLLOW-UP OF THE DESIGN
  WORK TOGETHER WITH EVERYONE INVOLVED

## Slide 13: INSTALLED ACCELERATOR
EN-MME CONTRIBUTION:
DELIVERY OF THE MANUFACTURED AND PURCHASED COMPONENTS
INSTALLATION FOLLOW-UP AND SUPPORT
COMPLETE THE DOCUMENTATION

## Slide 14
? / !
QUESTIONS / THANK YOU FOR YOUR ATTENTION