## Slide 1: Methodology of Real-Time Space Radiation Dose Estimates Using Onboard Vehicle Dosimeters
Christopher J. Mertens and Tony C. Slaba
NASA Langley Research Center
Hampton, Virginia USA

## Slide 2: Motivation
Need to Assess Biological Impacts to Astronauts in Real-Time during Solar Energetic Particle (SEP) Events
NASA Real-Time Dose Assessment Guideline
  Minimize the Dependence on Physics Transport Codes
  Maximize Use of Onboard Dosimeter Data
The General Approach
  Optimize Use of Vehicle Dosimeter Measurements to Estimate Body Dose Quantities at Crew Location
  The Body Dose Quantities are Inputs to Acute Radiation Risk Models Used to Assess Biological Impacts
    Predict incidence/severity of Acute Radiation Syndrome (ARS)
    Predict incidence/magnitude of Performance Decrement
This Real-Time Approach will be Tested on the EM-1 Flight

## Slide 3: Main Objective & Assumptions
Focus of this Study
  Part I of General Approach to Real-Time Biological Impact Assessment
  Estimate of SEP Absorbed Dose at Crew Locations Using Measurements at the Dosimeter Locations
Main Objective
  Evaluate Two Independent Methodologies for Estimating Dose at Crew Locations Using Dosimeter Measurements
Assumptions
  Dosimeter Measurements are Simulated (HZETRN code)
  A 15% Standard Deviation is Assumed for Measurement Noise
  Only Absorbed Dose in Silicon is Estimated at Crew Locations
  SEP Events Assumed Isotropic

## Slide 4: Outline
Method 1: Dosimeter Dose-Depth Fit
  Description of Method
  Test Method 1 for EM-1 Dose at Crew Locations from Distribution of SEP Event-Accumulated Doses
Method 2: Dosimeter Dose-Database Fit
  Description of Method
  Test Method 2 for EM-1 Dose at Crew Locations from Distribution of SEP Event-Accumulated Doses
Down Select to One Operational Method
Assess Operational Methodology for Time-Dependent SEP Events
Summary & Next Steps

## Slide 5: Description of Method 1: Dose-Depth Fit

## Slide 6: Dose-Depth Fit: Basic Approach
Fit Power-Law in Depth to Onboard Dosimeter Measurements
Dose measurement from detectors (i)
Effective depth of detector (i)
Dose delivered to detectors at position xi by “true” radiation environment along ray paths Ω

## Slide 7: Dose-Depth Fit: Basic Approach
Dose-depth power-law representation requires iterative approach to obtain self-consistent solution of these two equations
Determination of Fit Parameters:
Effective depth expansion coefficients for each detector (i):
  Di =
  Determine xeff and  from large database of SEP simulations and fit xeff to polynomial in 
Power-Law Parameters (A, ):
  Real-time fit to D(i) measurements using Bayesian statistical inversion

## Slide 8: The Inverse Problem
Vector of Measurements
Model of Measurement
Measurement Error
Statement of inverse problem: Find model parameters x that “optimally estimate” the measurements y to within the measurements error 
Solution of inverse problem: Find model parameters x, given the measurements y, that maximize the posteriori pdf P(x|y)
(Bayes’ theorem on inverse probabilities)

## Slide 9: The Inverse Problem
Assuming Gaussian Statistics
Measurement noise variance matrix
a-priori
a-priori variance matrix
Define the cost function
Solution: the maximum likelihood solution xs to the Bayesian statistical inverse problem satisfies (i.e., minimizes the cost function):

## Slide 10: Optimal Solution of Inverse Problem
Solution Vector:
Solution Covariance Matrix:
Forward Model Approximation:
Jacobian Matrix:

## Slide 11: Develop Effective Depth Parameterizations for EM-1 Vehicle

## Slide 12: EM-1 Effective Depth
Calculate Database of Dose-Depth Curves (0-100 g/cm2) for 65 Historical SEP Events Using HZETRN
  SEP/GLE Database (1956-2006): Tylka et al. (38th COSPAR Assembly)
Calculate Dose at EM-1 Dosimeter & Crew Locations for the Same 65 Historical SEP Events Using HZETRN
From Dose-Depth Curve, Find Effective Depth that Reproduces Dose at EM-1 Dosimeter & Crew Locations for Each SEP Event
Catalogue (xeff, ) for Each SEP Event at the Dosimeter & Crew Locations
Use (xeff, ) Catalogue to Fit Effective Depth (xeff) to Polynomial in Power-Law Index () for Each Dosimeter & Crew Locations

## Slide 13: EM-1 Cumulative Depth Distribution
Vehicle Dosimeter Locations
Storm Shelter Crew Locations

## Slide 14: Effective Depth: EM-1 Detectors

## Slide 15: Effective Depth: EM1 Crew Locations

## Slide 16: Test Dosimeter Dose-Depth Fit Approach for EM-1 Vehicle

## Slide 17: Test Set-Up -1
Simulate EM-1 Dosimeter Measurements (HZETRN)
Estimate Dose at EM-1 Crew Locations
  Use Dose-Depth Fitting Method to Derive Parameters (A, ) Based on Simulated EM-1 Dosimeter Measurements
  Estimate Dose at Crew Locations Using Fit Parameters (A, ) and Effective Depth Parameterization
Simulate Dose at EM-1 Crew Locations (HZETRN)
Compare Dose-Depth Fit Estimate of Dose at Crew Location with Simulated Dose (HZETRN)
Simulated SEP Event Test Cases Based on Random Selection of SEP Spectral Parameters

## Slide 18: SEP Spectra for Algorithm Testing

## Slide 19: Estimated vs “True” Si-Dose
Storm Shelter Crew Locations

## Slide 20: Estimated vs “True” Si-Dose Diff
Storm Shelter Crew Locations
Absolute Average Difference < 3%
Maximum Difference < 10%

## Slide 21: Test Set-Up -2
Simulate EM-1 Dosimeter Measurements (HZETRN)
  Perturb measurements by random noise (15% STD)
  50 Random Samples
Estimate Dose at EM-1 Crew Locations
  Use Dose-Depth Fitting Method to Derive Parameters (A, ) Based on Simulated EM-1 Dosimeter Measurements
  Estimate Dose at Crew Locations Using Fit Parameters (A, ) and Effective Depth Parameterization
Simulate Dose at EM-1 Crew Locations (HZETRN)
Compare Dose-Depth Fit Estimate of Dose at Crew Location with Simulated Dose (HZETRN)
Simulated SEP Event Test Cases Based on Random Selection of SEP Spectral Parameters

## Slide 22: Estimated vs “True” Si-Dose Diff
Storm Shelter Crew Locations
Absolute Average Difference < 35%
Maximum Difference ~ 1200%

## Slide 23: Description of Method 2: Dose-Database Fit

## Slide 24: Dose-Database Fit: Basic Approach
Compute Normalized Variance-Weighted Average Measured Dose
Compute Normalized Dose Calculated from the SEP Event Database at the Dosimeter Locations
Find SEP Event that Minimizes the Square Residual Between the Measured & Database Normalized Average Dose

## Slide 25: Optimal Solution for General LSQ
Define the cost function
Solution: the maximum likelihood solution xs to the Bayesian statistical inverse problem satisfies (i.e., minimizes the cost function):
Solution Vector (General LSQ):

## Slide 26: Test Dosimeter Dose-Database Fit Approach for EM-1 Vehicle

## Slide 27: Estimated vs “True” Si-Dose Diff
Storm Shelter Crew Locations
Absolute Average Difference < 4%
Maximum Difference ~ 10%

## Slide 28: Estimated vs “True” Si-Dose Diff
Storm Shelter Crew Locations
Absolute Average Difference < 7%
Maximum Difference ~ 10%

## Slide 29: SEP Database with Time Evolution
Down Select to Dose-Database Fit Approach as Operational Approach
  More robust (less sensitive to noise perturbations in dosimeter measurements) compared to Dose-Depth Approach
  Straightforward Approach to get Body Dose Quantities
Test Dosimeter Dose-Database Fit Approach for EM-1 Vehicle Using Time-Dependent SEP Event Database
  Database Based on IMP-8/GME Measurements (Jim Adams)
  479 SEP Events (1973-2001)
  ~190,000 30-Minute Time Intervals

## Slide 30: Estimated vs “True” Si-Dose
Storm Shelter Crew Locations
Event Accumulated Dose

## Slide 31: Estimated vs “True” Si-Dose Diff
Storm Shelter Crew Locations
Absolute Average Difference < 20%
Maximum Difference ~ 80%
Error bars are STD Over
Event Sub-Intervals

## Slide 32: Example SEP Anisotropy: GLE69
Highly collimated proton beam during initial phase of GLE
Anisotropy persists at ~10-30% for more than 12 hours after peak flux
GLE69 Parameterization: Bombardieri et al., Astrophys. J., 682, 1315-1327, 2008

## Slide 33: Summary
Comparisons of the Two Methods With (simulated) “True” Dose (Si) at Crew Locations
  No Noise Added to Simulated Dose Measurements
    Maximum Absolute Difference for Single Event 10%
    Average Absolute Difference over all Events
  Noise Added to Simulated Measurements
    No Appreciable Change in Robustness and Reliability of Dose-Database Method (same error characteristics as above)
    Dose-Depth Method can Fail Badly in Estimating the Dose
Down Select To the Dose-Database Method as the Real-Time Approach for Estimating Crew Dose from Dosimetry Measurements
  Proven to be more Robust for Realistic Measurements
  Body Dose can be Obtained Straightforwardly from the Optimal SEP Database Index (j*) and the Dosimeter Measurement Fit Parameters
  Database can be Expanded to Include Anisotropic Effects

## Slide 34: Next Steps
Expand Database of Dose-Database Method
  Include Anisotropic Effects
  Include Wider Range of SEP Spectral Shapes Using the IMP-8 Time-Dependent Event Database
  Include Body Dose Quantities and Integrate Dose Output with Acute Radiation Risk Models
Re-evaluate Updates to Dose-Database Method

## Slide 35: Backup Slides

## Slide 36: Solution Diagnostics
Estimated Relative Parameter Error:
Convergence Test and Quality Control:
Limited value (even misleading); doesn’t account for correlated errors
Goodness Test:
Includes correlated errors
Probability close to one means the optimally estimated parameters fit the measurements better than any other set of parameters