## Slide 1: Micro-pattern Gaseous Detectors GEM for Upgrade of the CMS Muon System
Archana Sharma
CERN
Vilnius (Lithuania)
14-12-2016

## Slide 2
LHC future scenarios
GE2/1, ME0, RPC installation
300 fb-1
PU ∼50
>3000 fb-1
PU ∼140-200
CMS Upgrade
Phase I Upgrade
Phase II Upgrade
LHC:
Run2:
L=1.7e34, PU 40factor 2 increase wrt 2012
L=1x design lumi by LS2
Run3:
L=2x design lumi by LS3, and integrate 300fb-1 by 2022
Use PU=50 for upgrade studies
HL-LHC:
• Lumi-level at 5x design and integrate 3000 fb-1
PU=140 for upgrade studies
Run 1
Run 2
Run 3
Run 4
30 fb-1
PU ∼40

## Slide 3
Compact Muon Solenoid

## Slide 4
  Eta coverage:
  |η|<1.6: 4 layers of CSCs and RPCs, DTs
  the |η|≥1.6: CSCs only;
3 technologies:
Drift Tubes and Cathode Strip Chambers (for tracking and triggering);
Resistive Plate Chambers (for triggering).
GOALS:
robust, redundant and fast identification of the muons
Level-1 trigger has access to muon information only
Momentum measurement: the muon system is relevant for high pt muon (>100 GeV) and in the high η region (large lever arm of the muon system)
The CMS Muon system
Highly hermetic and redundant muon system, with at least four stations on a muon path in all directions

## Slide 5: High h region upgrade with MPGD for Phase 2
Objectives:
  Sustain triggering at current trigger thresholds
  Increase offline muon identification coverage
  Maintain existing envelope by mitigating aging effects

## Slide 6
Drift Tubes (DT)
Central coverage: |η | < 1.2
Measurement and triggering
12 layers each chamber: 8 in φ, 4 in z
Cathode Strip Chambers (CSC)
Forward coverage: 0.9 < |η| < 2.4
Measurement and triggering
6 layers each chamber: each with φ, z
Resistive Plate Chambers (RPC)
Central and Forward coverage:
|η | < 2.1
Redundancy in triggering
2 gaps each chamber, 1 sensitive layer
Gas Electron Multiplier (GEM)
Fast triggering and precise tracking
Endcap coverage : 1.6 < |η| < 2.4
CMS: Gas Detector technologies
Phase-II

## Slide 7
The forward region |h|1.6 is very challenging
  Redundancy: the highest rates in the system vs fewest muon layers  few handles for the new Track finder postLS2 and for the track-trigger in HL-LHC
  Rate : in 10’s of kHz/cm2 and higher towards higher eta and worse momentum resolution
  Longevity: Accumulated charge after many years of LHC operation
  Electronics: High occupancy/rate and latency increases exceed capabilities of the existing electronics
Forward Muon system : challenges
The issues affect already the postLS2 operations and will be exacerbated in Phase 2
  Eta coverage:
  |η|<1.6: 4 layers of CSCs , RPCs, DTs
  the |η|≥1.6: CSCs only;
High luminosity can adversely affect muon system performance

## Slide 8: CMS GEM Endcap Chambers
The currently un-instrumented high- RPC region of the muon endcaps presents an opportunity for instrumentation with a detector technology that could sustain the radiation environment long-term and be suitable for operation at the LHC and its future upgrades into Phase II: GEM Detectors
GE1/1
in nose of
first Endcap Yoke
CMS Detector
GE1/1 simulation
geometry

## Slide 9: New handle: bending angle
X3 reduction
Forward trigger for |h|>1.6 relies entirely
on the CSC system:
• Measurement driven by internal chambers:
least scattering, strong B field.
GEM detector in front of CSC can measure muon bending angle in magnetic field and add redundancy
maintain 15 GeV online threshold, keep < 5 kHz rate, high efficiency
Lever arm - trigger

## Slide 10
• Maximum geometric acceptance within the given CMS envelope :
• Rate capabilities up to 100’s kHz/cm2 .
• Single-chamber efficiency > 98 % for mips
• Gain uniformity of 10% or better across a chamber and between chambers and no loss due to aging effect after 3000 fb-1
• High spatial and good time resolution
Micro-Pattern Gas Detectors (MPGD) due to their proven performance at HEP experiment (high rate capability and fine space resolution, high gain stability) are ideal tools. Dedicated studies for the large CMS detector:
Detector requirements
10
Triple GEM
GEM

## Slide 11: The GE1/1 design
10o
superchambers
short
long
  GE1/1 in high-η region 1.5<|η|<2.2
  100 trapezioidal triple-GEM Superchambers
  Long (1.5<|η|<2.2) and short (1.6<|η|<2.2) version
  36 superchambers in each endcap
Muon
Endcap
Station 1
GE1/1
Front-end
Chamber
Installation in LS2
11

## Slide 12
Challenge 1

## Slide 13
Challenge 1 ..

## Slide 14
Challenge 2

## Slide 15: 3rd GE1/1 Prototype:: NS2
GEM tensioning
GEM foil in inner frame assembly
GEM foil with inner & outer frame
Inside of readout board with O-ring seal
Chamber closed by
readout board with
Panasonic connectors
for frontend electronics
compact HV divider
Vias for strips sealed w/ kapton
HV noise
filters
-sector with
384 radial readout strips (12.4 cm long)
base pcb with drift electrode
CERN
2012
No spacers in active volume

## Slide 17: Full-size GE1/1 Detector Prototypes
GEM active area: 990 mm
 (220-445) mm
Single-mask technology
1D radial strip read-out with
3  8  128 = 3,072 channels
35 HV sectors
3/1/2/1 mm gap sizes
Gas mixtures:
  Ar/CO2 (70:30; 90:10)
  Ar/CO2/CF4 (45:15:40;
  60:20:20)
Gas flow ≈ 5 l/h

## Slide 18: GE1/1 Project development
2015
YETS 2016
2016/17
2017/18
2018/19
Prototyping, DAQ &trigger and QC procedure of detectors. First prototype of VFAT3
electronics&chamber prototype installation-
Slice and trigger commissioning.
Full-production of
chambers and electronics started
Full installation of GE1/1 with final electronics
Production GE1/1 chambers with final electronics
18
2010
Generation I
The first 1m-class detector ever built but still with spacer ribs and only 8 sectors total.
2011
Generation II
First large detector with 24 readout sectors (3x8) and 3/1/2/1 gaps but still with spacers and all glued.
2012
Generation III
The first sans-spacer detector, but with the outer frame still glued to the drift
2014
Generation V
Stretching apparatus that is now totally inside gas volume.
test beam campaign for final performance measurements.
2014/2015
Generation VI
Latest detector design; Optimized final dimensions for maximum acceptance and final eta segmentation.
Generation IV
First detector with complete mechanical assembly; no more gluing parts together!
2013
2014
2012
2011
2010
2015

## Slide 19
GE1/1-V
-> Optimization of the mechanics
-> stretching apparatus inside the gas volume
-> single-mask technology
-> 99x(22-45) cm2
-> 3072 readout channels
-> gap config. 3/1/2/1
-> No glue/no spacers
GE1/1-VI
-> Optimization of the mechanics
-> single-mask technology
-> design for long and short detectors
-> 99x(22-45) cm2
-> 120x(20-50) cm2
-> 3072 readout channels (new mapping)
-> gap config. 3/1/2/1
-> No glue/no spacers
GE1/1-I
-> first 1m-class GEM detector ever built
-> single-mask technology
-> 99x(22-45) cm2
-> 1024 readout channels
-> gap config. 3/2/2/2
-> use of spacer grid and glue
GE1/1-II
-> Optimization of the electric field configuration
-> single-mask technology
-> 99x(22-45) cm2
-> 3072 readout channels
-> gap config. 3/1/2/1
-> use of spacer grid and glue
2010 2011 2012 2013 2014 2015
GE1/1-III
-> first use of the self-stretching technique
-> single-mask technology
-> 99x(22-45) cm2
-> 3072 readout channels
-> gap config. 3/1/2/1
-> No spacers but glue on the external frame
GE1/1-IV
-> Optimization of the mechanics and assembly
-> single-mask technology
-> 99x(22-45) cm2
-> 3072 readout channels
-> gap config. 3/1/2/1
-> No glue/no spacers
Toward production phase
R&D phase
TDR
CHAMBERs
Project
Approved
30.9.2015

## Slide 20
GE1/1-VII (slice test)
-> Optimization of the mechanics
-> Optimization of the grounding
Optimization of the HV distribution
-> single-mask technology
-> 99x(22-45) cm2
-> 120x(20-50) cm2
-> 3072 readout channels
-> gap config. 3/1/2/1
-> No glue/no spacers
-> External (w.r.t . CERN) production sites certification and chamber components shipment
-> GE1/1 chamber assembly and certification
-> Super chamber mechanics optimization
-> First test with final front-end electronics
2016 2017 2018 2019 2020
Production phase & installation
Slice test installation
-> GE1/1 super chamber assembly and certification with final front-end electronics
-> First batch of Superchamber shipped to P5
GE1/1 super chambers ready in P5 for installation
Installation and cabling of all super chambers
Commissioning in situ with cosmic muons
Super chamber characterization in situ with cosmic muon
First data with LHC beam
To Super CHAMBERs
First SC
GE1/1-VIII (LS2)

## Slide 21
￼
￼

## Slide 22
CMS GEM GE1/1 - 3V5&2V6 :
CERN SPS
Beam Test 2014-16
Beam Tests at CERN and Fermilab

## Slide 23: Resolutions for CMS GEM detector at eta sector 5
σ= 86μrad
σ= 111μrad
VFAT test beam
86 (111) μrad or 160 (207) μm
P. Barria

## Slide 24: GEM GE1/1 Activity at the GIF++

## Slide 25: Slice test in YETS2016
DAQ system will be integrated in CMS DAQ;
combined CSC+GEM trigger
Operation procedure implemented
reconstruction included in official CMS software;
  validation done with standard tool;
  background and noise rate included in simulation.
gain integration experience
reduce the GEM commissioning period:
- Back-end electronics installed and commissioned in advance of the installation of the FE electronics.
- All components (Incl. detectors) will have been qualified beforehand at the TIF
trigger commissioning and performance check “CSC-TF”
background measurement.
opportunity to cross-check with data what expected by simulation.
4 super chambers in slots 1,2,35, 36 on YE-1
Motivations:
Installation of 4 SuperChamber during 2016 YETS
INSTALLATION WINDOW : Early January (10.1.2017 – 31.3 March 2017
INSTALLATION WINDOW :LS2
GE1/1 Week 15 onwards – until Ready for beam minus 30 weeks)

## Slide 26: GEM Detector Production
Slice Test
Assembled 2 of 8 detectors for P5!
Commissioning of quality control test stands on-going
Price inquiries for the LS2 chambers components are running
Slice Test chamber assembled

## Slide 27: Toward the full production Training and production site qualification

## Slide 28: CMS: Industrialization of GEM Foils
Mecharonics: Korea M.Choi , I. Park
Tech Etch Florida USA : Collaboration with B. Surrow & M. Hohlmann
Micropack : India
L. Pant
P. Menon
Completed:
Technology transfer license agreement with CERN signed
Foils made
Detectors made
Tests ongoing
A. Sharma 22092015
40x40 cm2
40x40 cm2

## Slide 29: Production site readiness
6 production sites are ready for final production, all have assembled GE1/1-IV prototypes , QC procedures have been initiated
https://www.youtube.com/watch?v=Ssuqh5GAVZ4
Luigi Benussi
Brian Dorney
Michele Bianco
Many others !!
Delhi University
SINP
Panjab University
Site Visits
Scheduled
Chamber
Production Sites
QC Sites

## Slide 30
QA and QC:

## Slide 31: CMS GE1/1 Electronics System
VFAT3 front-end ASIC development
GEM Electronic Board (GEB)
Opto-Hybrid (OH)
GBT
Versatile Link
MP7
μTCA
AMC13, MCH
Use of many common developments such as GBT, Versatile Link, μTCA backend
VFAT2
Trig data
(encoded)
TMB
uTCA
FPGA: Concentrator
E-links @ 320Mbps
“s” signals
@ 320Mbps
3.2Gbps
24 VFAT3
FPGA performs “concentrator” and drives the optical link @ 3.2Gbps.
FPGA programming and timing via the GBT.
GBT
GBT
Data PATH
Full granularity
(non zero suppressed)
1GBT for 8 VFATs
4.8Gbps
320Mbps
3.2Gbps
Trigger
GBT
GBT
The control, readout and power to/from the VFAT3 hybrid are delivered via electrical signals (E-links) running through the GEB to the opto-hybrid.

## Slide 32: 904: GE1/1 : Integration

## Slide 33: Power Budget and Cooling
The GE1/1 Super-chamber will take cooling from the RBX loops. It will give an negligible impact to the cooling system in the YE1
The cooling circuit is designed such to provide direct thermal contact with all heat sources in the GE1/1 chamber.

## Slide 34: 904: GE1/1 : Integration
GE1/1 inside
The cooling box
ME1/1
GE1/1 Setup for VFAT and GEB tests.
Alignment sensors
Zoltan Zillasi
Andrey Marinov

## Slide 35: Cooling Tests Ongoing
In CMS
The physical space of the GE1/1 Installation slots in YE1 is very compact.
No air flow or convection can be used for evacuating the heating power of the detector and the electronics.
In b 904
The GE1/1 chamber is placed in wooden box with cover to stop any airflow. It should simulate the same ambient conditions as it will be in CMS
The flow of the water trough the cooling pipe will be the same as in CMS – 2liters per minute.

## Slide 36: Integration into CMS
Four superchambers in
their final position
on endcap yoke
Installation sequence:
A. Conde Garcia
Mounting on yoke disk
Superchamber
(Two Triple-GEMs)

## Slide 37: Trial Installation in CMS

## Slide 38: High h region upgrade with MPGD for Phase 2
Objectives:
  Sustain triggering at current trigger thresholds
  Increase offline muon identification coverage
  Maintain existing envelope by mitigating aging effects

## Slide 39
ME0 requirements and technical choices
Detector requirement:
Multilayer structures
High rate capability O(MHz/cm2)
time resolution for triggering
No green house gases
Good spatial resolution O(100 mm) for tracking and triggering
  Baseline : Six layers of triple-GEMs
  Option : Fast Timing Micropattern
    gas detector (FTM)

## Slide 40: New generation of MPGD:FTM
The overall structure is transparent to the signal
Signal can be extracted in each amplification stage
Standard MPGD
Resistive MPGD
Multi-layer Resistive MPGD

## Slide 41
50 m thick Apical KANECA
800 M/ resistive layer
2 M/ resistive kapton
250 m thick gas gap
400 m pillars diameter & 3.3 mm pitch
Detector Layout & Parameters
500 V amplification
stage
2 kV/cm drift gap
Fullly resistive amplification stage:
Signals picked up by the external electrodes;
High rate capability;
Sub ns time resolution with several gaps in cascade;
DLC coating on the top
Perforated foils
Antistatic polymide foils
Two layers separated by Pillars
Pick-up electrode
Structure of the FTM detector
Reference:arXiv:1503.05330v1
European Patent Application 14200153.6
M. Maggi, A. Sharma, R. De Oliveira

## Slide 42
GE2/1 Detector requirements

## Slide 43
27
GE2/1 Detector requirements
For GE21 (only 88 mm available)
YE2
YE1
Shielding
ME2/1 CSC
88 mm
Foil stretching without spacers and NS2 technique developed for GE1/1
should be validated for the larger area of GE2/1
The baseline GE2/1 station consists of 36 200 SuperChambers with the layout will be similar to GE1/1, but covering much larger surface. It will be the largest GEM detector ever built.

## Slide 45
Vilnius University:
Valdas Rapsevicius: DB, DB loader, WBM framework (xfer from online to offline DB), etc.
Andrius Juodagalvis, Vytautas Mickus: Offline DB & interfacing with DPG
ENHEP (Egypt)
Ola Aboamer: DB GUI, DB, & WBM interface to DB
Safaa Salem: WBM interface to DB
Delhi University
Muhammad Hasib: DB & interface to detector construction
Texas A&M University
Alfredo Castaneda: DB & DAQ interface
Fermilab
Umesh Joshi: DB
Detector & DAQ Experts:
Brian Dorney, Michele Bianco, Jeremie Merlin, Jared Sturdy, etc.
GEM Database Current Activities - People

## Slide 46
Store all GEM construction data of chambers for the Slice Test in DB and access & display all QC test data using WBM
Status
  The DB GUI has been used to store & “build” detectors in the DB
  All 6 super chambers have been constructed
  In the process of storing QC data & publish using WBM interface
Use DB to enable the DAQ system to configure the Slice Test detector using GEM DB
  Status: The DAQ group is working on using the DB to configure the system for the cosmic test stand and Slice Test
GEM offline conditions DB & WBM interface (developed by Valdas & his group)
  Goal: Have this system working for the Slice Test
Use the GEM Online DB (inP5) to store & publish all construction data from the various stations around the world
  Goal: enable physicists in all test stations around the world to automatically synchronize & store construction & QC data in the GEM online DB in P5
GEM DB Near Term Goals

## Slide 47
1 ft3
active
volume
30 cm
Florida Tech Cubic-Foot MT Prototype
Triple GEM for Muon Tomography
Principle of Muon Tomography (MT) based on Cosmic Ray Muons: Five targets with various Z
U
W
Pb
Fe
Sn
GEM Muon tomography in The Economist:
http://www.economist.com/node/21552169
Muon Tomography for Homeland Security

## Slide 48
GEM combined with a scintillation gas (CF4) is used.
Very good spatial resolution in the method, shown on the right
Luggage inspection, food inspection, defect scanners

## Slide 49
Radiography of a bat, recorded with a GEM detector
Improving Digital Imaging

## Slide 50
GEM Countries - 16
Korea
China
India
Pakistan
Egypt
Qatar
Italy
Switzerland
Germany
Finland
Hungary
Colombia
USA
Bulgaria
Belgium
Lithuania

## Slide 51
GEM Institutes ~ 40

## Slide 52
A lot of students !!

## Slide 53: Summary
Several projects in the pipeline
GE11 to be delivered for LS2
GE21 & ME0 TDR in ~ 1 year
Promising outlook for a lot of work….
By the collaboration